## Slide 1: sPHENIX
OUTLINE
Technical/LESHC-PCSS review Dec 5.

## Slide 2: PRESENTATION OUTLINE
Project Summary System review summary/overview and charges
Present summary of previous reviews: LESHC of the magnet safety issues
Magnet Power and quench protection System
  Vapor cooled Leads & Cooling
  Burn out time
  Voltage tap locations
  Quench detection system
    Fast discharge: τ = XX seconds
    Slow Discharge: τ = 40 min
System requirements
System description and layout
  PFD
  P&ID’s
Action items list from Jan 2018 Technical Review by External Committee
Summary of Design ratings
Pressure drop profile calculations, updated
  Cooldown/Warmup 293K Supply 1010 Compressor, 45K supply RHIC 45K wave
  4.5K operation
  100K Hold summershutdown
  LN2 Exchanger design results
Layout
  1008B valvebox and interface
  Transfer line system
  IP8 valvebox
  Jumper adjustment: Solenoid physics location range / Cradle platform adjustment
    ±1, ± 1, ± 1 ??
Address Action items list from Jan 2018 Technical Review
Controls logic summary
  Control logic during normal operations
  Control logic during Quench
    Dump valve and Reliefs
    Return to RHIC protection
LN2 transfer line system:
  Layout and rating specifications
  Procurement later in 2019.
ODH Analysis and Summary
  ODH sensing and fan capacity: 34,500 CFM
APPENDIX/BACKUP SLIDES
  Slides from Jan 2018 Review

## Slide 3: Past reviews: Magnet&Cryogenics
Review | Date | Description | Outcome
Directors Review | Mar 7, 2014 | Directors Review sPHENIX project | Recommend full current high power test.
BNL Internal Committee | Dec 16, 2014 | NPP Review: sPHENIX magnet review: a. Acceptance tests/plans of the Magnet in Building 912 b. Design modifications to the Magnet “Chimney” and its interfaces to subsystems hadronic calorimeter c. Verify that the hadronic calorimeter acts as a flux return and magnet can be operated without end plugs: asymmetric forces? d. Identified a technical and management team. | Magnet Chimney extension approved, and proceed with Low and High power test in 912
BNL Internal Committee | May 14 2015 | Mechanical Design Review: Magnet Valve Box Extension a. Is Extension design ready for fabricaction for full field test in 912 and final install in IP8? b. Mechanical design adequate and are new parts easiliy available. c. Good understanding between disciplines and responsibilities. | Mechanical Chimney extension approved for IP8 Integration
BNL LESHC 15-05: PCSS committee | May 22, 2015 | Review the Magnet (testing) in Building 912 SOLENOID History and Design, Documentation, Location and Assembly Work in Building 912, 912 Cryogenic System to Cool Solenoid, Low Current <100A Test at 4.5K. | Approved for Low power testing in building 912
C-AD ASSRC Accelerator System Safety Review Committee | Dec 2015 | Review sPHENIX Solenoid 912 Low power Test | Approved for Low power testing in building 912
C-AD Internal Committee | Mar 15, 2017 | sPHENIX Quench Detector Review | Approved for High power testing in building 912
C-AD ASSRC Accelerator System Safety Review Com. | July 2017 | Review sPHENIX Solenoid 912 High Power Test | Approved for High power testing in building 912
External Committee [SLAC, Fermi, Ansaldo, NSLS2] with BNL staff | Jan 18, 2018 | Review of cryogenics system for IP8 Review requirements, design and layout, operating modes, interfacing with RHIC cryogenics. | Proceed with design. Address Action items

## Slide 4: Project Summary & Charge(s)
LESHC-PCSS Committee Approval(s)
  Does the new cryogenic system design and interfacing to existing RHIC equipment and to sPHENIX IP8 equipment meet the laboratory safety requirements?
  The Helium system will be released for procurement in Spring and will be specified to be manufactured to meet pressure vessel code and process piping code. Does the design and specification meet the laboratory pressure and safety standards.
  The LN2 transfer line system be released for procurement in Summer. Final route and support locations to be worked out. Does the design and specification meet the laboratory pressure and safety standards.
Technical Committee Charge (s)
Have all the items from the January 2018 External Review been addressed?
Does the cryogenic system hardware and controls provide operational capability and flexibility for all modes of operation, cryogenic safety, and magnet protection and interlocks, and minimal interruption of RHIC cryogenic operations?

## Slide 5: Items from the Jan 2018 Technical-Review
Care must be used in the warm-up of the magnet. There should be monitoring and controls to limit the differential temperature across magnet.
  This is currently part of the control logic for a controlled cooldown and warmup, with alarms and interlocks, which has been functioning properly during the bldg 912 low field and high field test.
The lead flow may not have sufficient flow [pressure drop operating budget] due to the return pressure. The use of an small compressor may be required.
  Solution proposed: Operate the solenoid bath at higher pressure, which means higher bath temperature.
  Technical committee magnet expert has reviewed the new proposed operating conditions and concluded that the magnet should be able to operate at the the higher bath temperature of 4.65K at 1.45bar. The Current Sharing Temperature Tcs, i.e. the temperature at which a defined electric field is detected in the cable due to the superconducting-to-normal state transition. This temperature depends on the magnetic field and on the ratio between operating current and critical current. At 4600 A the peak field in the winding is at 2.3T. When considering the Ic(B) curve of the conductor, one can find Tcs=7.28 K. The temperature margin between the Tcs and the operating temperature T0 =2.78K. The real parameter is the enthalpy margin defined as the energy for unit volume (J/m^3) which can be dissipated in the winding without causing a transition. For this conductor the margin is 3635 J/m^3 if T0=4.5 K. If the coolant temperature increases, the enthalpy margin decreases. At a T0= 4.65 K, the enthalpy margin only decreases by 2.5 %.
  We will be able to operate, with the return valve and control logic, the solenoid return separator at a higher boiling point pressure, e.g. 1.45 bar which will give us 250 mbar DP budget for the current lead flow circuit and warm return piping. We will swap to “Low Pressure Drop” Sierra Mass flow Controllers from the current MKS mass flow controller.
  The 400 Liter supply reservoir will be operated at 1.65 bar. 4.85K

## Slide 6: Items from the Jan 2018 Technical-Review
The quench pressure transient should be analyzed to ensure the burst disk does not rupture before the opening of mechanical and pneumatic controlled valves.
  We have done a full energy quench during the high field test, and the fast dump valve, set at a pressure of 2.2 atm opened; burst disk did not rupture.
The burst disks should be arranged in an assembly that allows the replacement of a burst disk while another is in an operations state.
  We will implement a switchover valve but replace burst disks with reliefs valves to ensure
Temperature sensors should be installed on the relief devices exit line to monitor helium leakage.
  Temperature sensors have been engineered in for the solenoid reliefs and the reliefs for the reservoir vessel.
It should be determined if the Quench Pressure Dump valve should be directly interlocked with the fast shutdown or quench interlock.
  The dump valve operated on pressure interlock okay during the high field quench test, but this interlock with the quench detection system can be implemented easily. The quench dump valve is set to respond quickly to the pressure rise and it may not be necessary to open faster than the pressure response of the system.
It should be analyzed if the fast discharge rate will be sufficient to protect the gas cooled leads from damaged if cooling flow is stopped.
  The burn out time that the manufacturer of the vapor cooled leads give is 87 seconds. The fast discharge rate is XXX seconds??
  [An in-house calculation check to raise the temperature of the copper lead to 250F gives 115 seconds.
The design and process of removing the cryogenic transfer lines between the shield wall to the interface valve box should be reviewed in detail.
  This has been reviewed with Facilities support/System, and the blocks can be removed. The rectagular opening dimsnsions will be verified to allow a Z-shape jog in the cryo piping to go through the opening.
RHIC cryogenics system operations [return line] should be protected from a quench disturbance.
  The Control valves for the RHIC’s R/U header and WR header will be throttled based on pressure and temperature