## Slide 1: JLEIC Machine Parameters Critical for Polarimetry
Vasiliy Morozov
Inaugural Meeting for the EIC Polarimeter WG
November 30, 2018

## Slide 2: Outline
Electron polarization
  Electron beam parameters and bunch structure
  Polarization scheme
  Polarization life time and top off
  Polarimetry setup
Ion polarization
  Polarization scheme
  Zero-integer spin resonance
  3D spin rotator
  Bunch structure
  Polarimetry setup and calibration

## Slide 3: Electron Beam Parameters
Electron beam
  3 A at up to 7 GeV
  Normalized emittance 58 µm @ 5 GeV
  Synchrotron power density < 10 kW/m
  Total power up to 10 MW
Beam energy | GeV | 3 | 5 | 6.9 | 9 | 10 | 12
Beam current | A | 3 | 3 | 3 | 1 | 0.69 | 0.33
Total SR power | MW | 0.4 | 2.7 | 9.6 | 9.3 | 9.8 | 9.7
Energy loss per turn | MeV | 0.12 | 0.88 | 3.2 | 9.3 | 14.2 | 29.4
Energy spread | 10-4 | 2.8 | 4.6 | 6.4 | 8.4 | 9.3 | 11.1
Transverse damping time | ms | 389 | 84 | 32 | 14 | 11 | 6
Longitudinal damping time | ms | 194 | 42 | 16 | 7 | 5 | 3
Normalized Emittance | um | 13 | 58 | 152 | 337 | 462 | 799

## Slide 4: Electron Bunch Structure
Electron injection scheme: fring / fCEBAF = 476.3 MHz / 1497 MHz = 7 / 22
Bunch structure in the electron collider ring
14.69 ns, 68.05 MHz (22 CEBAF buckets, 7 ring buckets)
68.05MHz bunch train, 3.6µs 247 bunches (Ipulse up to 1 mA @ 5GeV)
injector pulse train up polarization from gun
……
injector pulse train down polarization from gun
1ps, 14.7 pC bunch
……
Waiting for damping or kicker recovery 10-400ms
2.1ns, 476.3 MHz (1 ring bucket)
Iave = 44 nA
Waiting for damping or kicker recovery 10-400ms
…
…
2.1 ns (476.3 MHz)
7.52 s (132.9 kHz, ~2.26 km, 2.8 A)
3.6 s (1714 bunches, 5.9 nC/bunch up to 7 GeV)
rms bunch length is 1 cm
0.16 s
(78 empty bunches)
3.6 s (1714 bunches, 5.9 nC/bunch up to 7 GeV)
rms bunch length is 1 cm
0.16 s
(78 empty bunches)

## Slide 5: Electron Polarization
Two highly polarized bunch trains maintained by top-off
Universal spin rotator
  Minimizes spin diffusion by switching polarization between vertical in arcs and longitudinal in straights
  Two polarization states with equal lifetimes
  Basic spin match

## Slide 6: Radiative Polarization Effects
Sokolov-Ternov polarization change rate
is the invariant spin field, a 1-turn periodic unit 3-vector field over the phase space satisfying the T-BMT equation along particle trajectories, is a unit vector along the particle velocity, and is Planck’s constant.
Depolarization rate due to spin diffusion
is the spin-orbit coupling function
Total polarization change rate
Equilibrium polarization
where is the value of ensemble average of independent of and is the initial polarization
Average over phase space,
emittance dependent

## Slide 7: Spin Tracking
Spin tune scan using a spin tuning solenoid in SLICK/SLICKTRACK
Demonstrates suppression of synchrotron sideband spin resonances
Verified by Zgoubi’s Monte-Carlo spin tracking
s=0.01 (optimum spin tune)
s=0.027 (synchrotron tune)
Spin tracking using ZGOUBI.
~ 3x,y
Spin tune scan using SLICKTRACK
Synchrotron sideband spin resonances suppressed compared to a racetrack
Spin tuning solenoid

## Slide 8: Polarization Lifetime and Continuous Injection
Estimated polarization lifetime
Constant polarization is maintained by continuous injection of highly polarized electron beam from CEBAF
Equilibrium polarization
A relatively low average injected beam current of tens-of-nA level can maintain a high equilibrium polarization in the whole energy range
Beam lifetime must be balanced with the beam injection rate and
Energy (GeV) | 3 | 5 | 7 | 9 | 12
Lifetime (hours) | 116 | 9 | 1.7 | 0.5 | 0.1

## Slide 9: Polarization Measurement
Dipole chicane downstream of IP: same polarization at laser as at IP due to zero net bend
Compton polarimetry: non-invasive monitoring of electron polarization
Optics optimized for polarimetry

## Slide 10: Discussion of Electron Polarization Measurement Requirements
Ideally, one would like to have a bunch-by-bunch luminosity and polarization measurement. However, this is difficult and one should consider relaxing this requirement.
The two electron polarization states have the same life times. Beam lifetime is short compared to Sokolov-Ternov time. Even in case of error, equilibrium asymmetry would be negligible. Any error in spin rotator setting would manifest itself in reduction of polarization life time. It would be beneficial to have a direct measurement of vertical polarization in the arcs for spin rotator setup. This also have the benefit of cross checking the Compton polarimeter.
Polarizations of the bunches in each train should be the same. Processes that can vary polarization along the train are:
  Systematic variation of polarization along the injected train. This can be tested experimentally.
  RF transient and collective effect such as ion instability. They do not affect the polarization directly. The impact on polarization may come through change in emittance. This can be studied in simulations.
With the above caveats, it may be sufficient to measure the average polarization of each train.

## Slide 11: Ion Polarization
Figure-8 concept: Spin precession in one arc is exactly cancelled in the other
Without additional fields, spin rotation is a priori unknown and occurs only due to closed orbit excursion and beam emittances
Spin stabilization by small fields: ~3 Tm vs. ~1200 Tm for deuterons at 100 GeV
  Criterion: induced spin rotation >> spin rotation due to orbit errors
3D spin rotator: combination of small rotations about different axes provides any polarization orientation at any point in the collider ring
No effect on the orbit
Polarized deuterons
Frequent adiabatic spin flips
n = 0

## Slide 12: Zero-Integer Spin Resonance and Spin Stability Criterion
Total zero-integer spin resonance strength
is composed of
  coherent part due to closed orbit excursions (due to imperfections); it does not lead to depolarization but causes coherent spin rotation about a priori unknown direction
  incoherent part due to transverse and longitudinal emittances (proportional to beam emittance), it causes spin tune spread potentially leading to depolarization
Spin stability criterion
  the spin tune induced by a spin rotator must significantly exceed the strength of the incoherent part of the zero-integer spin resonance
  for proton beam
  for deuteron beam

## Slide 13: Incoherent Part of Zero-Integer Spin Resonance Strength
, at 200 GeV/c are sufficient to stabilize the polarization
Assuming normalized vertical beam emittance of 0.07 m rad

## Slide 14: Coherent Part of Zero Integer Spin Resonance Strength
The coherent component does not depolarize the beam. However, it has to be compensated or taken into account when setting the polarization direction.
Assuming RMS closed orbit distortion of ~200 m

## Slide 15: 3D Spin Rotator in Ion Collider Ring
IP
ions
3D spin rotator
Provides control of the radial, vertical, and longitudinal spin components
Module for control of radial component (fixed radial orbit bump)
Module for control of vertical component (fixed vertical orbit bump)
Module for control of longitudinal component
Can be placed anywhere and has no effect on optics

## Slide 16: Polarization Control in Ion Collider Ring
100 GeV/c figure-8 ion collider ring with transverse quadrupole misalignments
Example of vertical proton polarization at IP. The 1st 3D rotator:  = 10-2 , ny=1. The 2nd 3D rotator is used for compensation of coherent part of the zero-integer spin resonance strength
2nd 3D rotator for compensation
1st 3D rotator for control
with compensation
without compensation

## Slide 17: Spin Flipping
Adiabaticity criterion: spin reversal time must be much longer than spin precession period  flip >> 1 ms for protons and 0.1 s for deuterons
Vertical (hy) & longitudinal (hz) spin field components as set by the spin rotator vs time  Spin tune vs time (changes due to piece-wise linear shape)
is the number of particle turns
Vertical & longitudinal components of proton polarization vs time at 100 GeV/c
Zgoubi
simulation

## Slide 18: Ion Bunch Structure
Ion bunch formation
  Injection bunches may be prepared with different polarizations
Each injection bunch is split in half up to 7 times
Bunch structure in the ion collider ring

## Slide 19: Ion Polarimeter Location
Ion polarization in the straight section upstream of the IP is the same at the IP, however:
  Polarimeter target would generate detector background
  Polarimeter only measures transverse polarization, placing polarimeter upstream does not help with measurement of the longitudinal polarization
Polarization is rotated at any other potential polarimeter location
Determining polarization at IP becomes a question of knowing
  Polarization rotation angle from IP to polarimeter
  Polarization orientation at the polarimeter
  Calibration of the spin rotator

## Slide 20: Extracting Polarization at IP
Polarization rotation from IP to the polarimeter
should be small, e.g. polarimeter placed in the straight downstream of IP
What precision level of polarization alignment is required at the IP?
Polarization orientation at the polarimeter and spin rotator calibration
Experimentally measure as a function of and and extract calibration of in terms of and

## Slide 21: Spin Rotator Calibration
Without limiting the generality, assume that the spin rotator is in the same straight as the polarimeter and consider polarization on the orbit plane
Polarization at the polarimeter
where
are the spin rotations (normalized to ) in the radial and longitudinal modules of the spin rotator
The polarimeter measures
Polarization angle at the polarimeter

## Slide 22: Spin Rotator Calibration
Assume that polarization behaves according to formula on previous page
Assume typical parameters of a 100 GeV/c proton beam
Assume that polarization is measured with a random error of 0.02 rms
Fit randomly generated data to formula and extract input parameters
Parameter | Input | Fit
(Tm) |  | 
(Tm) |  | 
Parameter | Input | Fit

## Slide 23: Discussion of Ion Polarization Measurement Requirements
It is difficult to resolve individual bunches in a polarimeter with JLEIC’s short bunch spacing
It may be possible to measure polarizations of individual bunch trains
  There are 26 trains of 128 bunches each
  Individual bunches within each train have identical polarizations because of the way they are formed
  Polarimeter data may be gated during transitions between trains
Variation of the bunch polarization along a train can be caused by variation in the bunch emittances due to RF transient and beam instabilities. However, impact of emittance on the polarization stability is negligible. We were not able to observe any effect of higher-order spin resonances in simulations.
The RHIC scheme with a fast relative polarimeter and a slow absolute polarimeter appears adequate.
Since it is hard to distinguish the individual bunches, one may consider using scalers counting all particles for each train and then calibrating detection efficiencies and effective analyzing powers. This may be adequate if the polarimeter background is constant.
To simplify polarized beam setup, there should be additional polarimeters at the source, after the linac, and in the booster.

## Slide 24: BACKUP

## Slide 25: Electron Spin Rotators with Doglegs
Universal spin rotator
  Sequence of solenoid and dipole sections
  Geometry independent of energy
Sol. 1 + dec. skew quads + matching quads
Vertical dogleg 1
Horizontal DBA 1
Vertical dogleg 2
Sol. 2 + dec. skew quads + matching quads
Horizontal DBA 2
IP
Arc
Vertical dogleg 1
Vertical dogleg 2
E | Solenoid 1 |  | Dipole set 1 | Solenoid 2 |  | Dipole set 2
 | Spin Rotation | BDL | Spin Rotation | Spin Rotation | BDL | Spin Rotation
GeV | rad | T·m | rad | rad | T·m | rad
3 | π/2 | 15.7 | π/3 | 0 | 0 | π/6
4.5 | π/4 | 11.8 | π/2 | π/2 | 23.6 | π/4
6 | 0.62 | 12.3 | 2π/3 | 1.91 | 38.2 | π/3
9 | π/6 | 15.7 | π | 2π/3 | 62.8 | π/2
12 | 0.62 | 24.6 | 4π/3 | 1.91 | 76.4 | 2π/3