## Slide 1: Development of LArTPCs for Neutrino Physics
Xin Qian
BNL
http://lar.bnl.gov/

## Slide 2
Chart: Energy Budget of the Universe
| Dark Energy ~73% | Dark Matter ~23% | Visible Matter ~4% | Neutrino >~ 0.3%
Sales | 73 | 23 | 4 | 1
As fundamental particles in the standard model of particle physics, neutrinos are the second most abundant (known) particles in our universe
Notes: For every proton/neutron/electron the Universe contains a billion of neutrinos from the Big Bang

## Slide 3: Neutrinos from the Universe
99% of the energy in a core collapse supernova explosion is carried away by neutrinos
1038 νe/s are produced by the sun
Notes: A mole of neutrino passing through your body through your lifetime

## Slide 4
1973-2012-Now
1998-2012-Now
Non-zero neutrino mass and mixing is evidence of physics beyond the standard model
Notes: Maximal violation of parity

## Slide 5: Big Questions in Neutrino Physics
Are neutrinos responsible for the large matter anti-matter asymmetry?

## Slide 6: Big Questions in Neutrino Physics
Are neutrinos responsible for the large matter anti-matter asymmetry?
What’s the neutrino mass hierarchy?
Review of “Neutrino Mass Hierarchy”
XQ and P. Vogel, Prog. Part. Nucl. Phys. 83, 1

## Slide 7: Big Questions in Neutrino Physics
Are neutrinos responsible for the large matter anti-matter asymmetry?
What’s the neutrino mass hierarchy?
Do sterile neutrinos exist?
Symmetry magazine

## Slide 8: Big Questions in Neutrino Physics
Are neutrinos responsible for the large matter anti-matter asymmetry?
What’s the neutrino mass hierarchy?
Do sterile neutrinos exist?
Are neutrinos Dirac or Majorana particles?

## Slide 9: Big Questions in Neutrino Physics
Are neutrinos responsible for the large matter anti-matter asymmetry?
What’s the neutrino mass hierarchy?
Do sterile neutrinos exist?
Are neutrinos Dirac or Majorana particles?
What is the neutrino mass?
…

## Slide 10: Big Questions in Neutrino Physics
Are neutrinos responsible for the large matter anti-matter asymmetry?
What’s the neutrino mass hierarchy?
Do sterile neutrinos exist?
Are neutrinos Dirac or Majorana particles?
What is the neutrino mass?
…
Precision neutrino oscillation measurements with man-made accelerator neutrinos are crucial to answer these questions
Review of “Long-Baseline Neutrino Experiments”, M. V. Diwan, V. Galymov, XQ, A. Rubbia, Annu. Rev. Nucl. Par. Sci. 66, 47

## Slide 11: Liquid Argon Time Projection Chambers (LArTPCs) for neutrino physics

## Slide 12: Early History of LArTPC Development
W. Willis and V. Radeka, Liquid argon ionization chambers as total absorption detector, NIMA 120:221 (1974)
D. R. Nygren, The Time Projection Chamber: A New 4π Detector for Charged Particles. eConf. C740805:58 (1974)
H. H. Chen et al. A Neutrino detector sensitive to rare process. I. A study of neutrino electron reactions. FNAL-Proposal-0496 (1976)
C. Rubbia, The liquid argon time projection chamber: a new concept for neutrino detector, CERN-EP/77-08 (1977)
V. Radeka
D. R. Nygren
H. H. Chen
C. Rubbia

## Slide 13: Principle of Single-Phase Liquid Argon Time Projection Chamber (LArTPC)
time
~mm scale position resolution with multiple 1D wire readouts
Particle identification (PID) with energy depositions and topologies
Drift velocity 1.6 km/s  several ms drift time
Made by Bo Yu (BNL)

## Slide 14: Unique capability to identify νe charge-current interactions in LArTPC
Gap Identification + dE/dx to separate e/γ
Comparison of PMCS and PRange to separate low-energy e/µ for νe charge-current interaction
Michel e
Stopped muon
Dead ch.

## Slide 15: Short-Baseline Neutrino Program
Search for light sterile neutrino(s) through anomalous νμνe oscillation motivated by LSND and MiniBooNE anomalies

## Slide 16: Deep Underground Neutrino Experiment (DUNE)
Search for new CP violation and determine the mass hierarchy through precision measurement of (anti)νμ(anti)νe oscillation
Also search for proton decay and detection of supernova neutrinos

## Slide 17: Path to 10s kT LArTPCs

## Slide 18: Why massive LArTPC?
O(1)% measurement  O(1000) events

## Slide 19: Why massive LArTPC?

## Slide 20: Why massive LArTPC?
  Neutrino flux ~ 1017 /m2/1020 (Proton On Target)
LBNF beam: 60-120 GeV proton beam 1.2 MW, upgradeable to 2.4 MW

## Slide 21: Why need massive LArTPC?
  Neutrino cross section ~ 10-38 cm2 x Energy (GeV)
J. A. Formaggio and G. P. Zeller, Rev. Mod. Phys., 84:1307 (2012)

## Slide 22: Why massive LArTPC?
Neutrino oscillation in Daya Bay
Appearance
Survival
m1
m2
ν Flavor Eigenstate
ν Mass Eigenstate
Neutrinos are produced and detected by the weak interaction, but propagate as mass eigenstates

## Slide 23: Why massive LArTPC?
Neutrino interaction rate is approximately independent of neutrino energy and baseline
We need at least 10s kTons of target mass for O(1000) events
Four 10 kT fiducial (17 kT total) LArTPCs 4850 feet underground

## Slide 24: The First 10 kT Module of DUNE
Cryostat
150 APAs with 2560 readout channels each within three (1D) wire planes (~ 5 mm pitch)
Cost and power consumption of electronics in LAr
Anode Plane Assembly (APA)

## Slide 25: Path towards 10 kT Single-Phase LArTPCs
ICARUS
LBL
SBL
35-ton prototype
MicroBooNE
Also ArgonNeuT
2014-2018
2018-2020
SBND
ProtoDUNE (NP04)
DUNE reference design
46 times larger than ICARUS
Also development of dual-phase technology
2001-2012

## Slide 26: Technology Development in MicroBooNE
Physics motivation:
  Understand the low-energy excess in MiniBooNE
  Measure ν-Ar cross sections
  Develop LArTPC technology

## Slide 27: TPC Signal Formation
Wire pitch
Energy deposition
Recombination
Attenuation due to attachment
Induction U bipolar shape
Collection Y unipolar shape
Induction V bipolar shape
Small ionization signal in LAr  multiple wire planes with non-destructive induction readouts
Bo Yu
Enabling technology: cold electronics
Yichen Li
Brett Viren
Nature of induction (long-range, position-dependent, following superposition principle)  smaller induction plane signals

## Slide 28: Cold Electronics
1st International Workshop towards the Giant Liquid Argon Charge Imaging Experiment (2011)
JINST 12 P08003
Placing the preamplifier inside LAr significantly reduced the electronics noise
  5-6 times compared to past warm electronics  60:1 MIP peak-to-noise ratio in the collection
  Significantly improve the performance of induction wire plane  An enabling technology

## Slide 29: Excess Noise Removal
Excess noise during initial phase caused by voltage regulator and HV power supply
Software mitigation
JINST 12 P08003 (2017)
Identified noise sources and developed both hardware fix and software mitigation
Jyoti Joshi
Mike Mooney
Brian Kirby
Notes: Regulartor and HV power supply noise … 1 year

## Slide 30: Improved Signal Processing: “2D Deconvolution”
Drift Time
Wire number
JINST 13 P07006/7 (2018)
Number of ionized electrons
Signal on Wire Plane
Field Response
Signal to be digitized by ADC
Electronic Response
Number of ionized electrons
(Signal Processing)
Hanyu Wei Brooke Russell
Deconvolution technique with fast Fourier transformation (FFT)
  O(N2.4~3)  O(N logN) with N = 2400 (ch.) x 8256 (time) ~ 2x107
Applied signal processing concepts to general data unfolding problem:
  “Data Unfolding with Wiener-SVD Method”, W. Tang, X. Li, XQ, H. Wei, C. Zhang, JINST 12, P10002
Wei Tang Xiaoyue Li

## Slide 31: 3D image reconstruction

## Slide 32: Traditional Reconstruction Approach: 2D matching  3D
2D pattern recognition
Matching to 3D objects
Error made in pattern recognition will propagate to the later reconstruction steps

## Slide 33: Wire-Cell Tomographic Event Reconstruction
“Three-dimensional Imaging for Large LArTPCs”, XQ, C. Zhang, B. Viren, M. Diwan, JINST 13, P05032 (2018)

## Slide 34: Solving: usage of Charge, Sparsity, Positivity, Connectivity
The goal is to differentiate the true hits from fake ones by using the charge information
  ~ large charge  true hits ~ zero charge  fake hits
Sparsity, positivity, and connectivity information are added through compressed sensing (L1 regularization)
E. Candes, J. Romberg, T. Tao
arXiv-math/0503066
Brett Viren
Chao Zhang

## Slide 35: Demonstration of Charge Matching
Old 1D
Signal Processing
JINST, 13, P07007
New 2D
Signal Processing
Mike Mooney
Brian Kirby
Notes: One set of plots … First time ever in LArTPC to reach charge matching …

## Slide 36: Wire-Cell on the MicroBooNE Data
2015, after several hours of CPU running
2018, 3 mins of CPU running
Bee link
Bee link
(lower) 2D deconvolution + L1 regularization
(upper) 1D deconvolution + L0 compressed sensing
JINST 13, P05032 (2018)
Notes: Significant improvement in SP and … write something … why is better ??? Remove last line, more dots  more hits, high efficiency …

## Slide 37: Wire-Cell on MicroBooNE Data
A set of 3D clustering algorithms is developed based on data events
The damage of 10% dead channels can be sufficiently mitigated in the reconstruction
Hanyu Wei Xiangpan Ji

## Slide 38: Neutrino Selection and Particle Identification

## Slide 39: Challenge in Selecting Neutrinos
4.8 ms drift window
20-30 TPC activities
LArTPC is a slow detector, running on surface leads to significant challenges in selecting neutrinos
The key is to associate the correct T0 (light info.) to the corresponding TPC cluster
  Compressed Sensing with L1 regularization!

## Slide 40: Before and After L1 Matching
Side view
Top view
Front view
Charge-Current νμ candidate
Prediction
Flash Observation
More details in MICROBOONE-NOTE-1040-PUB
Brooke Russell
Chao Zhang

## Slide 41: Before and After L1 Matching
CC νe candidate
Prediction
Flash Observation
Over 98% matching accuracy evaluated with cosmic muons
Side view
Top view
Front view
Brooke Russell
Chao Zhang

## Slide 42: Current Focus: Development of Particle Identification
Development of precision PID with dE/dx information is critical for LArTPC technology
Preliminary
Wenqiang Gu
London Cooper-Troendle

## Slide 43: Stay tuned for physics results from MicroBooNE!
MicroBooNE: 70 Ton
ProtoDUNE: ~ 420 Ton

## Slide 44: ProtoDUNE @ CERN
Prototype of DUNE with six APAs  validating design, prototyping production/installation procedure, demonstrating long-term operation stability
Test beam + cosmic data  detector response + cross section measurements

## Slide 45: APA and Cold Electronics
< 1% dead channels combining wires and electronics
ENC < 750 e as expected without software noise filtering
Maura Spanu’s particle physics seminar this Thursday
Major success of the BNL electronics team!

## Slide 46: The Enabling Technology for Giant LArTPCs: Cold Electronics
MIP Signal for 5x5 mm Sense Wire Spacing
CMOS at 77K: ENC< 103 e rms
ProtoDUNE (89 K)
ENC~750 e rms
DUNE with warm electronics (300K)
ENC~6x10^3 e rms

## Slide 47: 7 GeV beam proton
7 m

## Slide 48
Made by Chao Zhang (BNL)

## Slide 49: History of Large Liquid Scintillator Detector
1950s
Reines & Cowan
Discovery of ν
2000s
KamLAND
Solving solar ν problem on Earth
2010s
Daya Bay
Discovery of non-zero θ13
Year | Experiment | Goal
1950s-1970s | Reines & Cowan | Search for νs
1980s-1990s | Bugey, Reines and co., Gosgen … (~28 experiments) | Search for ν oscillation at L<100 m
1990s-2000s | CHOOZ and Palo Verde | Measurement of θ13 L ~ 1 km
2000s | KamLAND | Measurement of Δm221 L~ 180 km
2010s | Daya Bay/ RENO/ Double Chooz | Measurement of θ13 L~ 2 km
2018 | NEOS/DANSS/PROSPECT/STEREO … | Search for sterile ν at O(10) m
Petr Vogel arXiv:1902.03281 and also review on “Physics with Reactor Neutrinos”, XQ, J. C. Peng Rept. Prog. Phys. 82, 036201 (2019)

## Slide 50
MicroBooNE
SBND
ProtoDUNE SP
DUNE FD, SP
Noise Filtering &
ADC Mitigation
TPC Signal Processing
3D Image Reconstruction
3D Clustering
TPC/PMT flash matching
Trajectory fitting and dE/dx reco.
3D Pattern Recognition
Track/shower separation, PID & Event ID
Neutrino Energy Reconstruction
LEE and Cross section analyses
LArTPC is a crucial detector technology to answer many remaining questions in neutrino physics
The development of LArTPC technology is building a solid foundation for next discoveries with neutrino oscillation in coming decades
Summary

## Slide 51
Thanks for your attention

## Slide 53: Signals from a Track Segment

## Slide 54
Tensor R is Toeplitz
  Response only depends on the relative positions between signal and measurement
(RTR)-1 can be achieved through the deconvolution technique with fast Fourier transformation (FFT)
  O(N2.4~3)  O(N logN)
  One of top 10 algs. in 20th century
Immense dimension of M and S: 2400 (chs.) x 8256 (time bins) ~ 2 x 107
Extreme challenge in matrix inversion!
Matrix Inversion and Deconvolution
  1D deconvolution SP in LArTPC described in B. Baller JINST 12, P07010

## Slide 55
Fourier transformation
Time domain
Frequency domain
Back to time domain
Inverse Fourier transformation
Deconvolution Technique
Wiener filter: optimized by power of signal and noise in freq. domain
N. Wiener (1964)
Example taken from X. Li et al. JINST 12, P10002
Also PMT SP in Daya Bay: NIMA, 895, 48

## Slide 56: 2D Deconvolution
JINST 13 P07006/7 (2018)
Measured waveform
1-D deconvolution
2-D deconvolution
  R1 represents the induced signal from (i+1)th wire signal to ith wire
The inversion of matrix R can again be done with deconvolution  2-D Fast Fourier Transformation

## Slide 57
Quantitative evaluation of the signal processing chain  inefficiency for prolonged tracks (large-angle) track
  4-wire plane proposal for DUNE
Signal Processing Evaluation
JINST, 13, P07006

## Slide 58: Calibration of Electronics Response
Observed imperfect response due to “imperfect pole cancellation”
  Significantly reduced in the newer generation of ASICs
Developed a procedure to calibrate out imperfect electronics response
  Being applied to protoDUNE for ADC nonlinearity calibration
SP part II: JINST, 13, P07007
Led by BNL in collaboration with CSU
Notes: Get rid of this one

## Slide 59: L1 Signal Processing
L1 (compressed sensing)  a good solution to the signal processing in the V-Y shorted region
Thorough understanding of MicroBooNE detector achieved!
JINST, 13, P07007
E. Candes, J. Romberg, T. Tao
arXiv-math/0503066
Notes: Math and computing (important technique developed, BNL brought in these for LArTPC PS and reconstruction), underdetermined system

## Slide 60: SP for shorted-Y region
L1 (compressed sensing) became a good solution to the signal processing in the V-Y shorted region
  Powerful new technique first introduced in LArTPC by BNL group
Thorough understanding of MicroBooNE detector achieved!
JINST, 13, P07007
Notes: Math and computing (important technique developed, BNL brought in these for LArTPC PS and reconstruction), underdetermined system

## Slide 61
Noise (ENC) vs TPC Sense Wire and Signal Cable Length for CMOS at 300K and 89K MIP Signal for 3x3 and 5x5 mm Sense Wire Spacing
CMOS at 77K: ENC< 103 e rms
MicroBooNE
ENC~400 e rms
DUNE with warm electronics (300K)
ENC~6x10^3 e rms

## Slide 62: Challenge in Selecting Neutrinos
4.8 ms drift window
Coin. with ν beam
20-30 TPC activities
40-50 PMT activities
LArTPC is a slow detector, running on surface leads to significant challenges in selecting neutrinos
The key is to associate the correct T0 (light info.) to the corresponding TPC cluster
  Compressed Sensing with L1 regularization!