## Slide 1: Path forward toward p+A collisions in RHIC Wolfram Fischer
8 January 2013
Workshop on p+A collisions at RHIC, BNL
Notes: 09:00, 45 min

## Slide 2: Content
What do we have for p+Au collisions?
What do we still need for p+Au collisions?
Luminosity projection

## Slide 3: What do we have for p+Au collisions?
RHIC was designed for p+Au collisions
  Independent rings except DX magnets
  DX magnets movable (~1 shift)
With stochastic cooling initial Au beam size is at its maximum
  Allows for DX move in IR6 and IR8 only (~1 shift)
Solutions for lattice, injection and acceleration
  Lattice takes advantage of stochastic cooling
Machine with fast setup (beam-based feedbacks), good reliability
Experience with asymmetric collisions (d+Au, Cu+Au)
Proton beam with Nb = 2x1011, P = 55% with upgrades (OPPIS): Nb = 3x1011, P = 65%
Au beam with Nb = 1.3x109
with upgrades (EBIS/Booster/AGS/RHIC): 2.0x109 (emittance?)

## Slide 4: RHIC Design Manual
Run-11: Lavg = 30×1026cm-2s-1
Run-12: Lavg = 10.5×1031cm-2s-1 (with Pavg = 53%)

## Slide 5: RHIC Design Manual (July 1998)
IR design with beam splitting DX dipoles first
DX dipole
D0,Q1—Q3
DX dipoles
Lmag = 3.7 m, Bmax = 4.3 T
large aperture (18 cm coil ID)
only magnets that need training (~5 for IR6/8 only)
Notes: MAKE REAL CALCULATION FOR DX MOVE

## Slide 6: Now have full 3D stochastic cooling for heavy ions
M. Brennan, M. Blaskiewicz, F. Severino, PRL 100 174803 (2008); PRSTAB, PAC, EPAC
longitudinal kicker (closed)
horizontal kicker (open)
horizontal and vertical pickups
longitudinal pickup
5-9 GHz, cooling times ~1 h
vertical kicker (closed)
Notes: Frequency range: 5-8 GHz transverse, 6-9 GHz longitudinal

## Slide 7: Cu-Au store – new mode in 2012
10%/h
transverse emittances
luminosities
beam loss rates
25 mm.mrad
120x1026cm-2s-1
Cu and Au have different - intrabeam scattering growth rates (~Z4Nb/A2) rIBS,Au ≈ 2x rIBS,Cu
- cooling rates (~1/Nb) rSC,Au ≈ 3x rSC,Cu
Stores start with large e after undergoing instability at transition
Possible with stochastic cooling
Increase bunch intensity until loss at transition
Notes: Fillno 16991 06/15/12, last night

## Slide 8: p+Au easier with stochastic cooling
only need to accommodate initial Au emittances
sufficient to move IR6 and IR8 DX magnets
S. Tepikian, D. Trbojevic, C-A/AP/447 (Jan. 2012)
colliding IR move DX by 1cm

## Slide 9: p+Au easier with stochastic cooling
non-colliding IR
no DX move
S. Tepikian, D. Trbojevic, C-A/AP/447 (Jan. 2012)

## Slide 10: Beam control improvement – feedbacks on ramp
Blue orbits
xmean
ymean
xrms
yrms
M. Minty, A. Marusic et al.
Qx
Qy
Qy = 2/3
DQy = 0.006
x,yrms ≈ 20 mm (!) ≈ 3% of rms size
Orbit feedback on every ramp allows for
Smaller yrms (smaller imperfection resonance strength)
Ramp reproducibility (have 24 h orbit variation)
Tune/coupling feedback on every ramp allows for
Acceleration near Qy = 2/3 (better P transmission compared to higher tune)
0.7
0.66
-0.2
0.3
Orbit [mm]
Tune
Notes: Fillno 15443, one of best stores

## Slide 11: Time-in-store as fraction of calendar time
Run-12 with low failure rates in all systems
Highest time-in-store ratios to date even with increased APEX time during 255 GeV protons, and few weeks per species
85%
60%

## Slide 12: What do we still need for p+Au?
Demonstrate DX move by 1 cm
  Can be done at end of Run-13
  Move for p beam in Yellow, Au beam in Blue (different from d-Au)
If p beam in Blue is needed (and Au beam in Yellow)
  Modify vacuum pump stands in IR6 and IR8
  Modify shielding IR6 and IR8
Operate with new injection and acceleration scheme
  Inject and accelerate Au to intermediate level above transition Then inject p and accelerate both beams

## Slide 13: Moving IR6 and IR8 DX magnets by 1cm
Bellows allow for 1 cm movement
Installed shielding creates tight spaces but acceptable “6:00 the bellows and ion pump stand were swapped to make space for the shielding, … cannot be moved because of the ion pump stand” (M. Mapes)
Easier to do have p in Yellow, Au in Blue (different from d-Au!)
Can be done in ~ 2 shifts (i.e. during a run) when properly prepared in previous shut-down

## Slide 14: p+Au injection and acceleration
time
Lorentz factor g
107.4
25.4
10.5
injection Au
injection p
acceleration Au (cross transition)
acceleration p, Au
collision p+Au
Note: now tolerate ion beam instabilities at transition obtain higher intensity (can be cooled down again), not possible with p+Au since have smaller aperture available

## Slide 15: Asymmetric collisions (p+Au)
p+Au energies: 100.8 GeV p on 100.0 GeV/nucleon Au (gp = gAu = 107.4)
For energy scan need to match Lorentz factor g of both beams
LNN/week, min/max pb-1 15 37

## Slide 16: Summary
p+Au is possible max energy 100 GeV/nucleon for both beams
Stochastic cooling helps: DX move only in IR6 & IR8, no Au beam growth
DX move in ~2 shifts possible upgrade for pp2pp in IR6 requires change of DX bellows will reduce flexibility, cannot move DX magnets during run
New injection/acceleration scheme store Au beam above transition for ~15 min
Luminosity estimate based on p beam available (anticipated), and Au beam available (anticipated)
  LNN = 15 pb/week min (now) LNN = 37 pb/week max (few years)