## Slide 1
Modular aerogel RICH (mRICH)
Goal:
FY 19:
Analyze and publish the mRICH test beam data taken in June/July 2018.
Use the mRICH to develop an integrated readout sensor electronics solution for all Cherenkov systems (mRICH, dRICH, DIRC).
Plan for a 3rd (final?) mRICH test beam in FY20.
Search for best, radiation hard materials for Fresnel lens.
Optical characterization of Fresnel lens and aerogel.
Compact PID device with momentum coverage up to 10 GeV/c for /K and e/ up to 2 GeV/c.
First aerogel RICH with lens-based focusing (for performance and cost)

## Slide 2
Lens-Based mRICH Design |  | 9GeV/c pion beam launched at the center of xy plane in simulation Smaller and thinner ring image
Two-Layer Proximity Focusing Design (BELLE-2 ARICH) |  | EIC mRICH designed for K/pi ID up to 10 GeV/c BELLE-2 ARICH aims to separate pion and kaon up to 4 GeV/c
9 GeV/c pion beam launched at the center of xy plane in simulation
mRICH – lens-based focusing aerogel detector design
Smaller, but thinner ring improves PID performance and reduces length
Aerogel
Fresnel lens
Sensor plane
Notes: The modular RICH detector consists of a block of aerogel, Fresnel lens, mirror set and sensor plane.

## Slide 3
Lens-Based mRICH Design |  | 9 GeV/c pion beam launched at the center of xy plane in simulation Smaller and thinner ring image
Two-Layer Proximity Focusing Design (BELLE-2 ARICH) |  | EIC mRICH designed for K/pi ID up to 10 GeV/c BELLE-2 ARICH aims to separate pion and kaon up to 4 GeV/c
9 GeV/c pion beam launched at the center of xy plane in simulation
mRICH – lens-based focusing aerogel detector design
Smaller, but thinner ring improves PID performance and reduces length
Notes: This lens-based design generates smaller and sharper ring image compare to the state of art proximity focusing deisng.

## Slide 4
Lens-Based mRICH Design |  | 9 GeV/c pion beam incident at third quadrant (star) in simulation Ring image is center on the middle of the sensor plane
Two-Layer Proximity Focusing Design (BELLE-2 ARICH) |  | 9 GeV/c pion beam incident at third quadrant (star) in simulation Ring is centered at point of incidence
mRICH – lens-based focusing shifts image to center
Ring centering of lens-based optics reduces sensor area (main cost driver)
Notes: Furthermore, the Cherenkove photons generated at off the optical principle can be shifted to the middle of sensor plane by the lens. These results to less required sensor plane area.

## Slide 5: 2nd mRICH Beam Test
Another very successful mRICH prototype beam test at Fermilab (6/25 to 7/6/2018)
Group photo (missing two members)
– the first confirmed ring image
Notes: The first beam test results from last fiscal year will be published in NIM A.

## Slide 6: 1st and 2nd Beam Test Comparison (120 GeV Proton Beam)
Images from 120 GeV
Proton beam
Simulated Images
Using GEANT4
1st mRICH prototype was tested at Fermilab Test Beam Facility in April 2016
The 1st test beam result verified mRICH working principle and validated simulation
2nd mRICH prototype was tested at Fermilab Test Beam Facility in June/July 2018
New features: a) separation of optical and electronic components; b) longer focal length (6”); c) 3mm x 3mm photosensors.

## Slide 7: Completed Data QA Analysis for the 2nd Beam Test
Left: ring images formed by 120-GeV primary proton beam incident on the center of mRICH. White gaps are the PMT frames.
Examples of cumulative ring images from the second mRICH prototype beam test
Middle: ring images from 120-GeV primary proton beam incident at an angle of 11° toward the lower section of mRICH.
Right: images from an 8-GeV meson run. The challenge of this analysis is to determine the beam position since the beam hodoscope readout was not ready for this test.
Four Hamamatsu H13700 PMTs (3mm x 3mm pixel size; 16x16 channels) were used in these test runs. Each costs ~$5k. These sensors will NOT work in high magnetic field!!!

## Slide 8: mRICH Ring Images from SiPM Sensors (a FIRST!)
To meet the requirement of operating photosensors in high magnetic field in EIC experiment, we successfully demonstrated ring imaging construction using mRICH in the 2nd beam test. There were only three Hamamatsu SiPM matrices available at the time of this test. Given the limited beam time, we only took data with the primary proton beam at 120 GeV with cooling temperature settings at
-30oC, -20oC, -10oC, 0oC and room temperature.
See details in the progress report
-20oC
0oC
Room
temp
SiPM
SiPM matrix: 16 x 16 channels, 3mm x 3mm pixel size

## Slide 9: mRICH in an EIC Detector Built Around the sPHENIX Solenoid

## Slide 10: mRICH – FY19 activity (part one)
Data analysis of the 2nd mRICH beam test and publish the new results – verify the PID performance at 2, 5 and 8 GeV/c
Projected e/pi separation of mRICH 2nd prototype detector (blue solid line)
2nd prototype detector can achieve 3-sigma e/pi separation up to 2 GeV/c
Projected K/pi separation of mRICH 2nd prototype detector (Green dots)
2nd prototype detector can achieve 3-sigma K/pi separation up to 8 GeV/c
Data sets taken during the second mRICH beam test at Fermilab in June/July 2018

## Slide 11: mRICH – FY19 activity (part two)
Study of the radiation hardness of Fresnel lens (i.e., address the committee concern!) in spring 2019 at BNL using 60Co source together with DIRC team to confirm the earlier test result shown below. Have purchased more lens samples from Edmund for this test.
Simulation study of mRICH performance in the Forward sPHENIX experiment at BNL (ongoing effort).
Simulation study of mRICH performance in the electron endcap in JLEIC (ongoing effort).
Work with dRICH group to develop a plan for a join dRICH/mRICH beam test.
Tested by Greg Kalicy. 2 mm-thick acylic mRICH lens sample. A small drop of transmission was observed below 500 nm. This material seems surprisingly radiation hard even after a dose of 750 krad.