## Slide 1
MCP-PMT/LAPPDTM
Goal:
FY 19 Progress:
[1] Produce and test 6cm MCP-PMT with Incom 10 µm pore size MCPs, the spacing is the same as current standard design;
[2] Order glass components (side wall and spacer), design and prepare for another 10 µm MCP-PMT with reduced spacing;
[3] Convince Incom management to devote efforts on delivery of the pixelated LAPPDTM;
[4] Transfer SLAC MCP-PMT scanning system to ANL, establish 2D single photoelectron efficiency and TTS timing scan capability;
[5] Enhance MCP-PMT simulation effort to guide MCP-PMT design for high magnetic field;
[6] Perform an initial test of newly produced LAPPDTM without magnetic sensitive components.
Adapt LAPPDTM to the EIC requirements:
Highly pixelated LAPPDTM working at 2~3 Tesla, to be used as photosensors
for mRICH, dRICH, and DIRC detectors, as well as TOF applications.

## Slide 2
Fabrication of MCP-PMTs with 10 μm pore size MCPs

## Slide 3
MCP-PMT performance improvement with 10 μm MCPs
- Same stack height, no spacing reduction yet
Rise time
Gain
version 2: IBD design 20 μm
version 3: IBD design 10 μm

## Slide 4
MCP-PMT performance improvement with 10 μm MCPs
- Same stack height, no spacing reduction yet
Timing resolution (SPE)
Magnetic field tolerance
System: σ1 = 37.2 ps
Laser jitter: σLaser = 30 ps
Electronics: σEle. = 7 ps
10 μm MCP-PMT: σ = 20 ps
20 μm MCP-PMT | 10 μm MCP-PMT
0.7 Tesla | 1.3 Tesla
σTTS ~ 63 ps
σTTS ~ 20 ps
version 2
version 3

## Slide 5
Enhanced communication with Incom on LAPPDTM
The advices and recommendations from the committee and feedbacks from EIC user groups were well explained and emphasized during ANL-Incom bi-weekly meetings.
Pixel LAPPDTM is available for the first time, negotiating one to be delivered at ANL.
Current demonstrated pixel size: 25 mm x 25 mm
QE uniformity issue was solved here!

## Slide 6
Magnetic field test on new LAPPDTM -without magnetic sensitive components
A new LAPPDTM without magnetic sensitive components was delivered at ANL for a one day test.
SBIR Phase I was fulfilled, Phase II will be submit at end of Jan. 2019.
preliminary
preliminary
preliminary
5 HV bias connection
The B field tolerance can also be further enhanced by adjusting the HVs, further study planned.
LAPPDTM shows better B field tolerance than the 6cm one with individual HV biases.