## Slide 1
Amitoj Singh
USQCD All-Hands Collaboration Meeting
26-27 April 2019
Fermilab Facilities Report

## Slide 2: Introduction
To be deployed and existing Fermilab LQCD clusters.
Storage (disk and tape).
Allocation year 2018-2019 (PY18-19) Job statistics.
New user web portal.
Upcoming upgrades and changes.
User support.

## Slide 4: I of VI: Fermilab FY19 LQCD Cluster – LQ1
Total 112 nodes connected by a 2:1 oversubscribed Intel Omni-Path network.
Per node configuration:
  dual socket Intel Xeon 6248 “Cascade Lake” 2.5 GHz
  20-cores/socket .. 40-cores total
  192GB 2933 memory
  Intel Omni-Path EDR (100Gbps)
  ~0.9 TB local scratch space
  333 GFlops/node**
$0.02/MFlop ($0.03/MFlop++ for BNL-SKL).
CentOS 8.
Omni-Path attached to ~960TB of Lustre file-system.
Worker nodes have public net access via host router.
Release to “friendly user mode” June 14 and release to “production” July 1.
** average of P. Boyle’s Grid Benchmark for MILC and DWF on a single-node.
++ price adjusted for current memory pricing.
LQ1 July 2019

## Slide 5: I of VI: Fermilab FY19 LQCD Cluster – LQ1
1 CSL node-hour = 1.14 SKL node-hour
1 CSL node-hour = 220 Jpsi core-hour
LQ1 rating:
  981K node-hours
  1.1 M SKL node-hour
  215 M Jpsi core hours
Pi0 rating:
  113.6 M Jpsi-core-hours

## Slide 6: I of VI: Age of Fermilab LQCD clusters
Today
ds
bc
pi0g
LQ1
ds
dsg
pi0
pi0
pi0
Lustre

## Slide 7: II of VI: Storage – Existing Clusters
776 TB
14.5 TB
250 GB
Internet

## Slide 8: II of VI: Storage – LQ1
14.5 TB
LQ1#fnal
LQ1.fnal.gov
LQ1-Lustre
900 GB
960 TB
Host Router
Internet

## Slide 9: II of VI: Tape data migration
Urgent push to migrate data on existing tape media to LTO8 !! Estimated cost of migrating ALL data is ~$69k. Please review and delete legacy data under /pnfs/lqcd.
2004-2012
2012-YTD
LTO4 Media (0.8TB) Total: ~1.3 PB, 1,617 tapes
T10K Media (8.4TB), Total: ~4.2 PB, 564 tapes
Maintenance
$5.6k/year
Migration to LTO8
$6,400
Maintenance $12.4k/year
Migration to LTO8
$63,000

## Slide 10: II of VI: Tape data migration
Support for LTO4 tape media ends and replacement parts not available after September 2019.
Costly to USQCD to have all data migrated.
Data on tape is a mix of long-term data and short-term data.
We will need to help from users to...
  Identify long-term data of lasting scientific value such as gauge ensembles that need to be migrated to new media.
  Remove short-term data past its useful life, e.g., propagators, etc. belonging to projects that have ended.
We will be contacting affected projects shortly.

## Slide 11: III of VI: Job & Memory Size Distribution (conventional) in PY18-19
32 node jobs
128GB/node 32 nodes = 4TB

## Slide 12: III of VI: Job Size Distribution (accelerated) in PY18-19
Single node (4 GPU) jobs
Multi node multi GPU jobs

## Slide 13: IV of VI: New web portal for Fermilab resources
Tape Usage
Jobs List
Allocation Used
Overview
http://www.usqcd.org/fnal/clusterstatus

## Slide 14: V of VI: Upcoming upgrades and major changes
During the start of FY20 we plan to upgrade ALL existing clusters to CentOS 8 to match the OS on LQ1. This will require a prolonged downtime, stay tuned for details.
pi0 cluster:
  Starting Oct 1, 2019 70% of pi0 and all of pi0g cluster will no longer be available as an allocated resource.
Batch queueing system
  We are adjusting SLURM configuration to better manage dispatch priority using QoS (Quality of Service) parameter:
    Billable partitions (pi0, pi0g) use normal and opp QoS
    Non-billable partitions (bc, ds, dsg) use fifo QoS
    User’s can use test QoS for short test jobs (<=30 min, max 2 nodes) at high priority
  The default wall-time limit for users has been 24 hours, which is the maximum wall-time allowed. To improve scheduling, we are changing the default to 8 hrs.
    It is much easier to backfill idle nodes with smaller jobs of shorter duration.
    There is a demonstrated advantage when using realistic estimates of the wall-time needed for your jobs.

## Slide 15: VI of VI: User Support
https://www.usqcd.org/fnal/ServiceDesk.html
  Please send email to lqcd-admin@fnal.gov as this autogenerates a support ticket.
    We may convert INCidents (something broken) to REQests (something asked for).
    Benefits:
      Escalations / SLA for INC tickets is 4 business hours, management gets reports on response and resolution times.
      Tracked to completion - Nothing falls “off-the-plate”
      Assigned to a staff member – Responsibility/owner of the issue
      We can add additional users to a Watchlist – Helps improve communication
  Please avoid sending support related emails directly to support staff members.

## Slide 16: Questions?

## Slide 17: Backup Slides

## Slide 18: Fermilab LQCD Clusters
Name | CPU | Nodes | Cores GPUs | Network | Online
ds | Quad 2.0 GHz Opteron 6128 (8-core) | 153 | 4,896 | Mellanox QDR | Sept 2010 Oct 2010
dsg | Dual NVIDIA M2050 GPUs+Intel 2.53 GHz E5630 (4-core) | 38 | 304 Cores 0 GPUs | Mellanox QDR | Mar 2012
bc | Quad 2.8 GHz Opteron 6320 (8-core) | 217 | 6,944 | Mellanox QDR | July 2013
pi0 | Dual 2.6 GHz Xeon E2650v2 (8-core) | 314 | 5,024 | Mellanox QDR | Sept 2014 Apr 2015
pi0g | Dual NVIDIA K40 GPUs+Intel 2.6 GHz E2650v2 (8-core) | 32 | 512 Cores 128 GPUs | Mellanox QDR | Sept 2014
LQ1 | Dual 2.5 GHz Xeon 6248 (20-core) | 117 | 4,480 Cores | Omni-Path EDR | July 1, 2019
Unallocated resource operated in DNR (Do Not Resuscitate) mode

## Slide 19: Future Fermilab Institutional Cluster Model
LQ1
LQ2
Resource demand spikes that cannot be met by on-prem resources can be satisfied by routing jobs to commercial clouds, OSG resources or LCF’s.
NOvA using HEPCloud to claim ~1M cores at NERSC to perform a large-scale analysis over a short timeframe.

## Slide 20: II of VI: Storage Details
Global disk storage:
  960 TB (raw) Lustre file-system for LQ1 (not backed up)
  For existing clusters and will not be accessible from LQ1.
    776 TB Lustre file-system at /lqcdproj. (not backed up)
    14.5 TB “project” space at /project (backed up nightly)
    6 GB per user at /home on each cluster (backed up nightly)
Robotic tape storage is available via dccp commands against the dCache filesystem at /pnfs/lqcd.
  Some users will benefit from direct access to tape by using encp commands on lqcdsrm.fnal.gov or LQ1-IO.
  Please email us if you plan on transferring a large number of small (< 200MB) or big (>1TB) files. We may want to guide how these are written to avoid wasted space on tape.
Globus Online endpoint:
  lqcd#fnal - for transfers in or out of /lqcdproj Lustre file system.
  LQ1#fnal– for transfers in or out of LQ1 Lustre file-system.
Data integrity is your responsibility.