## Slide 1
eRD14 – EIC PID consortium
- An integrated program for particle identification (PID) for a future Electron-Ion Collider (EIC) detector.
M. Alfred, B. Azmoun, F. Barbosa, M. Boer, W. Brooks, T. Cao, M. Chiu, E. Cisbani, M.Contalbrigo, S. Danagoulian, A. Datta, A. Deldotto, M. Demarteau, A. Denisov, J.M. Durham, A. Durum, R. Dzhygadlo, D. Fields, Y. Furletova, C. Gleason, M. Grosse-Perdekamp, J. Harris, M. Hattawy, X. He, H. van Hecke, T. Horn, J. Huang, C. Hyde, Y. Ilieva, G. Kalicy, A. Kebede, B. Kim, E. Kistenev, M. Liu, R. Majka, J. McKisson, R. Mendez, I. Mostafanezhad, P. Nadel-Turonski, K. Peters, R. Pisani, W. Roh, P. Rossi, M. Sarsour, C. Schwarz, J. Schwiening, C.L. da Silva, N. Smirnov, J. Stevens, A. Sukhanov, X. Sun, S. Syed, R. Towell, G. Varner, R. Wagner, C. Woody, C.-P. Wong, W. Xi, J. Xie, Z.W. Zhao, B. Zihlmann, C. Zorn.
Contacts:
P. Nadel-Turonski <turonski@jlab.org>,
Y. Ilieva <jordanka@physics.sc.edu>
Generic Detector R&D for an Electron Ion Collider
Advisory Committee Meeting, BNL, January 24-25, 2019

## Slide 2
Abilene Christian University (ACU)
Argonne National Lab (ANL)
Brookhaven National Lab (BNL)
Catholic University of America (CUA)
City College of New York CCNY)
College of William & Mary (W&M)
Duke University (Duke)
Georgia State University (GSU)
GSI Helmholtzzentrum für Schwerionenforschung, Germany (GSI)
Howard University (HU)
Institute for High Energy Physics, Protvino, Russia
Istituto Nazionale di Fisica Nucleare, Sezione di Ferrara, Italy (INFN-Ferrara)
Istituto Nazionale di Fisica Nucleare, Sezione di Roma, Italy (INFN-Rome)
Istituto Superiore di Sanità, Italy (ISS)
Jefferson Lab (JLab)
Los Alamos National Lab (LANL)
North Carolina A&T State University (NCAT)
Old Dominion University (ODU)
Stony Brook University (SBU)
Universidad Técnica Federico Santa María, Chile (UTFSM)
University of Hawaii (UH)
University of Illinois Urbana-Champaign (UIUC)
University of New Mexico (UNM)
University of South Carolina (USC)
Yale University (Yale)
Participating institutions

## Slide 3
eRD14: an integrated program for PID at an EIC
3. Consortium synergies (including reduction of overall R&D costs)
2. A cost-effective sensor and electronics solution
1. A suite of detector systems covering the full angular- and momentum range required for an EIC detector
Different technologies in different parts of the detector
Focus on hadron ID with an electron ID capability
Development and testing of photosensors (to satisfy EIC requirements)
Development of readout electronics needed for prototyping
Close collaboration within the consortium, with coordinated goals and timelines (e.g., DIRC & LAPPD, mRICH & dRICH, etc).
Strong synergies with non-EIC experiments and R&D programs (PANDA, CLAS12, GlueX, PHENIX, commercial LAPPDs) resulting in large savings.

## Slide 4
The maximum hadron momentum in the endcaps is close to the electron and ion beam energies, respectively.
The momentum coverage need in the central barrel depends on the desired kinematic reach, in particular in Q2 – important for QCD evolution, etc.
  Weak dependence on beam energies
Hadron kinematics at an EIC

## Slide 5
A PID solution for the EIC
e-endcap
h-endcap
barrel
10x100 GeV
Q2 > 1 GeV2
DIRC
Aerogel RICH
Dual-radiator RICH
p/A
e
GeV
rapidity
h-endcap: A RICH with two radiators (gas + aerogel) is needed for
  /K separation up to ~50 GeV/c
e-endcap: A compact aerogel RICH which can be projective
  /K separation up to ~10 GeV/c
barrel: A high-performance DIRC provides a compact and cost-effective way to cover the area.
    /K separation up to ~6-7 GeV/c
TOF and/or dE/dx in a TPC: can cover lower momenta.
Photosensors and electronics: need to match the requirements of the new generation devices being developed – both for the final system and during the R&D phase

## Slide 6
PID in the EIC concept detectors and integration of eRD14 systems

## Slide 7
hadronic calorimeters
RICH detectors
silicon trackers
GEM trackers
3T solenoid cryostat
-3.5 < h < 3.5: Tracking & e/m Calorimetry (hermetic coverage)
magnet yoke
9.0m
Micromegas barrels
TPC
e/m calorimeters
hadrons
electrons
BNL BeAST EIC detector
A. Kiselev, EIC UG meeting, July 2016
eRD14 dRICH implementation ongoing
eRD14 mRICH
electron endcap implementation ongoing
eRD14 DIRC in barrel implementation to begin soon
2016 changes made integration with eRD14 systems much easier!

## Slide 8
BNL ePHENIX EIC detector
The DIRC, mRICH, and TOF systems already part of the current concept. An implementation in Geant4 (Fun4All) is ongoing.
In addition, either the eRD14 dRICH and eRD6 gas RICH could be used. The two options have been compared in a collaborative effort.
2016 layout shown!

## Slide 9
JLab EIC central detector showing PID integration
EMcal
Dual-radiator RICH
sensors
aerogel
gas
EMcal
DIRC & TOF
EMcal (Sci-Fi)
e/π Cherenkov?
Central tracker
Vertex (Si pixel)
TOF
EMcal
PWO4
GEM
tracker
Modular aerogel RICH
DIRC camera
mirror
Field shaping coils for RICH
Solenoid coil
All eRD14 systems (DIRC, mRICH, dRICH, and TOF) are part of the baseline JLab detector concept.

## Slide 10
High-resolution TOF
Goals:
The R&D goals have been achieved.
No funding requested for FY19.
Explore the possibility of achieving very high timing resolution (~10 ps)
Demonstrate 20 ps mRPC resolution in the lab.
Progress in 2nd half of 2018:

## Slide 11
Dual-radiator RICH (dRICH)
Goal:
Progress in 2nd half of 2018:
  Refinements on:
    Global particle ID reconstruction
    Evaluation of performance in a realistic physics case
  Moving towards a prototype implementation
Provide hadron identification (p/K/p) from 3 to 50 GeV/c (3 sigma) and electron identification (e/p) up to 15 GeV/c, in the forward ion-side endcap of the EIC detector, covering polar angles up to ~25 deg.

## Slide 12
dRICH is in magnetic field (3T central field in simu)
First dual-RICH to demand excellent performance from aerogel radiator!

## Slide 13
The PID capability fulfills the design goals
Momentum Threshold (GeV/c) |  | 
Particle | Aerogel (1.02) | C2F6 (1.0008)
e | 0.003 | 0.013
pi | 0.694 | 3.49
K | 2.46 | 12.3
p | 4.67 | 23.5
one of the six dRICH sectors
dRICH performance for a key process (Semi-Inclusive DIS)

## Slide 14
Nt : tracks (+ background «dummy track»)
Nh : photon hits
Nr : radiators (aerogel and gas)
Np : potential particle types (e,pi,K,p)
Global «brute force» approach: explore all possible combinations of:
Track  Particle type : Np^Nt
Photon hits  (Track  Radiator + Background) : (Nt*Nr+1)^Nh
Each combination has an associated Likelihood; take the one that maximize it.
Our approach:
Determine (by IRT) the possible emission angles corresponding to each photon hit
Associate, in sequence, each photon hit to (tracks  radiator) driven by a Likelihood (L1) that depends on emission angle and a-priori (previous associations) probability; number of combinations drops to (Nt*Nr+1)*Nh
Once all hits are associated, estimate a global Likelihood (L2) for each (track  particle) combination; choose the combination that maximize L2
PID problem: associate to each track a particle type (based on some sort of Likelihood)
Brute Force: up to 488 billion combinations
Our approach: 1200 combinations
Example: event with
2 tracks and 15 hits
Inverse Ray Tracing: global reconstruction

## Slide 15
Why: evaluate critical aspects of the proposed solutions; tune relevant parameters used in MC and consolidate the estimated performances
The prototype must:
mimic the performances of the proposed dRICH components, minimizing modeling and assumptions
be cost effective (trade-off between small scale, versatility and measurable quantities)
The preliminary prototype vessel size (with spherical mirror of 2 m radius) driven by two main considerations:
reasonable (order of 10) photoelectrons from gas per particle; depend almost linearly on the thickness (length) of the gas and therefore of the vessel.
catch the aerogel ring (20 cm radius) in order to estimate its angular resolution; constraints the transverse size of the vessel.
We also need to minimize vessel volume, sensor area, isolate aerogel from gas …
… going to start the detailed definition in coming months
Aerogel
Sensors
plane
Mirror
100 cm
30 cm
dRICH prototype

## Slide 16
Activity | T1 | T2 | T3 | T4 | Funding (USA+ITA) kUSD (1  1USD) |  | 
Finalize the event based (global) IRT reconstruction (article!) |  |  |  |  | Post Doc | Mat erial | Travel
Design the small scale prototype |  |  |  |  | 30* |  | 2.5*
Implement the prototype |  |  |  |  |  | 4.2 | 
Study the interface between gas and aerogel (and long term aerogel characterization, if able to get samples!) |  |  |  |  |  | 1.5 | 
(m+d)RICH - electronics: consolidate design and test SiPM sensor matrix with proper cooling and thermal stability; setting up the lab laser test bench for characterization (also for irradiation campaigns); follow SiPM ongoing development toward rad hard solutions |  |  |  |  |  | 3* | 
(m+d)RICH - electronics: implement Hawaii (TARGETX/SiREAD) + JLab/CLAS12 readout on chosen front-end; integration/test of the JLab backend and SiREAD |  |  |  |  |  | 2* | 
Important components (electronics and sensors) of the dRICH prototype are shared with the mRICH development
CLAS12 infrastructures available in Ferrara will be used for aerogel-gas studies
* (m+d)RICH
FY19 outlook

## Slide 17
Modular aerogel RICH (mRICH)
Goals:
Progress in the 2nd half of 2018:
Completed data quality assurance analysis of the mRICH 2018 test data.
Implemented mRICH detector array in Geant4 simulation built around the sPHENIX solenoid. The results of this effort were included in an EIC detector design study which was submitted to BNL management in October 2018.
Purchased more samples for studying Fresnel lens radiation hardness.
Compact PID device with momentum coverage up to 10 GeV/c for /K and e/ up to 2 GeV/c.
First aerogel RICH with lens-based focusing (for performance and cost)

## Slide 18
Lens-Based mRICH Design |  | 9GeV/c pion beam launched at the center of xy plane in simulation Smaller and thinner ring image
Two-Layer Proximity Focusing Design (BELLE-2 ARICH) |  | EIC mRICH designed for K/pi ID up to 10 GeV/c BELLE-2 ARICH aims to separate pion and kaon up to 4 GeV/c
9 GeV/c pion beam launched at the center of xy plane in simulation
mRICH – lens-based focusing aerogel detector design
Smaller, but thinner ring improves PID performance and reduces length
Aerogel
Fresnel lens
Sensor plane
Notes: The modular RICH detector consists of a block of aerogel, Fresnel lens, mirror set and sensor plane.

## Slide 19
Lens-Based mRICH Design |  | 9 GeV/c pion beam launched at the center of xy plane in simulation Smaller and thinner ring image
Two-Layer Proximity Focusing Design (BELLE-2 ARICH) |  | EIC mRICH designed for K/pi ID up to 10 GeV/c BELLE-2 ARICH aims to separate pion and kaon up to 4 GeV/c
9 GeV/c pion beam launched at the center of xy plane in simulation
mRICH – lens-based focusing aerogel detector design
Smaller, but thinner ring improves PID performance and reduces length
Notes: This lens-based design generates smaller and sharper ring image compare to the state of art proximity focusing deisng.

## Slide 20
Lens-Based mRICH Design |  | 9 GeV/c pion beam incident at third quadrant (star) in simulation Ring image is center on the middle of the sensor plane
Two-Layer Proximity Focusing Design (BELLE-2 ARICH) |  | 9 GeV/c pion beam incident at third quadrant (star) in simulation Ring is centered at point of incidence
mRICH – lens-based focusing shifts image to center
Ring centering of lens-based optics reduces sensor area (main cost driver)
Notes: Furthermore, the Cherenkove photons generated at off the optical principle can be shifted to the middle of sensor plane by the lens. These results to less required sensor plane area.

## Slide 21: 2nd mRICH Beam Test
Another very successful mRICH prototype beam test at Fermilab (6/25 to 7/6/2018)
Group photo (missing two members)
– the first confirmed ring image
Notes: The first beam test results from last fiscal year will be published in NIM A.

## Slide 22: 1st and 2nd Beam Test Comparison (120 GeV Proton Beam)
Images from 120 GeV
Proton beam
Simulated Images
Using GEANT4
1st mRICH prototype was tested at Fermilab Test Beam Facility in April 2016
The 1st test beam result verified mRICH working principle and validated simulation
2nd mRICH prototype was tested at Fermilab Test Beam Facility in June/July 2018
New features: a) separation of optical and electronic components; b) longer focal length (6”); c) 3mm x 3mm photosensors.

## Slide 23: Completed Data QA Analysis for the 2nd Beam Test
Left: ring images formed by 120-GeV primary proton beam incident on the center of mRICH. White gaps are the PMT frames.
Examples of cumulative ring images from the second mRICH prototype beam test
Middle: ring images from 120-GeV primary proton beam incident at an angle of 11° toward the lower section of mRICH.
Right: images from an 8-GeV meson run. The challenge of this analysis is to determine the beam position since the beam hodoscope readout was not ready for this test.
Four Hamamatsu H13700 PMTs (3mm x 3mm pixel size; 16x16 channels) were used in these test runs. Each costs ~$5k. These sensors will NOT work in high magnetic field!!!

## Slide 24: mRICH Ring Images from SiPM Sensors
To meet the requirement of operating photosensors in high magnetic field in EIC experiment, we successfully demonstrated ring imaging construction using mRICH in the 2nd beam test. There were only three Hamamatsu SiPM matrices available at the time of this test. Given the limited beam time, we only took data with the primary proton beam at 120 GeV with cooling temperature settings at
-30oC, -20oC, -10oC, 0oC and room temperature.
See details in the progress report
-20oC
0oC
Room
temp
SiPM
SiPM matrix: 16 x 16 channels, 3mm x 3mm pixel size

## Slide 25: mRICH in an EIC Detector Built Around the sPHENIX Solenoid

## Slide 26: mRICH – FY19 activity (part one)
Data analysis of the 2nd mRICH beam test and publish the new results – verify the PID performance at 2, 5 and 8 GeV/c
Projected e/pi separation of mRICH 2nd prototype detector (blue solid line)
2nd prototype detector can achieve 3-sigma e/pi separation up to 2 GeV/c
Projected K/pi separation of mRICH 2nd prototype detector (Green dots)
2nd prototype detector can achieve 3-sigma K/pi separation up to 8 GeV/c
Data sets taken during the second mRICH beam test at Fermilab in June/July 2018

## Slide 27: mRICH – FY19 activity (part two)
Study of the radiation hardness of Fresnel lens (i.e., address the committee concern!) in spring 2019 at BNL using 60Co source together with DIRC team to confirm the earlier test result shown below. Have purchased more lens samples from Edmund for this test.
Simulation study of mRICH performance in the Forward sPHENIX experiment at BNL (ongoing effort).
Simulation study of mRICH performance in the electron endcap in JLEIC (ongoing effort).
Work with dRICH group to develop a plan for a join dRICH/mRICH beam test.
Tested by Greg Kalicy. 2 mm-thick acylic mRICH lens sample. A small drop of transmission was observed below 500 nm. This material seems surprisingly radiation hard even after a dose of 750 krad.

## Slide 28
Paolo Carniti
@ RICH 2018
I. Balossino et al.
NIMA 876 (2017) 89
T. Tsang et al.
JINST 11 (2016) P12002
T= 84 K
109 neq cm2
Annealing at 250 oC
T= 0 C
few 109 neq cm2
Studies of SiPM radiation toleranace
The viability of using irradiated SiPMs for single-photon detection at the EIC will be the focus of future R&D on this topic.
Notes: Fare una immagine del PMT sulla risoluzione

## Slide 29
Laser head +
diffuser
MAPMT holder
JLab
632 nm picosecond pulsed laser light
Light diffuser to illuminate the whole MaPMT surface
Standardized system with CLAS12 electronics
H8500 6x6 mm2 pixel sensor so far
Ferrara
632 nm and 407 nm picosecond pulsed laser light
Light concentrator to scan the pensor surface
Flexible layout supporting various sensors and
Front-End electronics
Detailed characterization
Sensors: gain, efficiency, cross-talk, radiation tolerance
Electronics: gain, cross-talk, thresholds, time resolution
Laser head +
collimator
MAPMT holder
Pulsed laser test benches
Notes: Fare una immagine del PMT sulla risoluzione

## Slide 30
High-performance DIRC
Goals:
Successful radiation hardness study of lens materials at BNL
Order process for two custom-made 3-layer lenses using sapphire and PbF2 as the middle layer is close to completion
Successful beam test of the PANDA Barrel DIRC prototype performed at CERN
Very compact device with coverage up to 10 GeV/c for p/K, 6 GeV/c for /K, and 1.8 GeV/c for e/, pushing performance well beyond state-of-the-art
First DIRC aiming to utilize high-resolution 3D (x,y,t) reconstruction (performance and cost)
Progress in 2nd half of 2018:

## Slide 31
3-layer lens
DIRC – overview
Radiation hardness test in 60Co source
Detailed radiation hardness study was performed at BNL, five materials were tested up to 750 krad.
Sapphire and PbF2 were confirmed to be very radiation hard.
Radiation hard 3-layer lens prototypes
Both sapphire and PbF2 present new manufacturing challenges that have to be addressed by potential vendors.
Discussions are at final stage to complete the purchase of two custom-made 3-layer spherical lenses using sapphire and PbF2 as the middle layer.
Reducing sensor coverage
The successful beam test of the PANDA Barrel DIRC prototype identified the potential for a significant reduction in the number of sensors required to cover the detector plane.
Sapphire
PbF2

## Slide 32
60Co irradiation setup at BNL
Radiation damage quantified by measuring the transmission in the 190-800 nm range in a monochromator.
Five materials studied.
Sapphire and PbF2 confirmed to be radiation hard.
Radiation Hardness Test
Co60 Chamber
Tested samples
Monochromator

## Slide 33
60Co irradiation results
Radiation damage quantified by measuring the transmission in the 190-800 nm range in a monochromator
Five materials studied
Radiation hardness of sapphire and PbF2 confirmed
Radiation Hardness Test
Tested samples
Sapphire
PbF2

## Slide 34
Radiation Hardness Test
Tested samples
S-YGH51 (NLaK33 equivalent)
mRICH Fresnel lens material
60Co irradiation results
Radiation damage quantified by measuring the transmission in the 190-800 nm range in a monochromator
Transmission loss of alternate lanthanum crown glass material (S-YGH51) confirmed
Acrylic glass samle for mRICH Fresnel lens quite radiation hard.

## Slide 35
PANDA Barrel DIRC prototype at CERN PS in July/Aug 2018: reduced number of MCP-PMTs.
Caveat: larger sensor pixels, slower electronics than EIC DIRC → PANDA goal: 3σ π/K separation @ 3.5 GeV/c
Optics similar to EIC DIRC design: narrow bar, fused silica prism, 3-layer spherical lens
Reduced MCP-PMT coverage by 33% compared to 2017, gaps near prism sides (data analysis ongoing)
Measured key quantities: photon yield, Cherenkov angle resolution per photon and per particle, and /K separation power – all in good agreement with simulation (used for EIC DIRC)
PID performance in 2018 close to 2017 results (photon yield lower but π/K separation still > 3σ)
Impact of reducing number of sensors promising, has to be tested in EIC simulation.
Reducing sensor coverage
2x4 MCP-PMT arrangement
Example of hit pattern
π/p separation power at 7 GeV/c
(equivalent to π/K @ 3.5 GeV/c)
preliminary

## Slide 36
Two more radiation hardness tests planned for winter/spring and summer 2019 with the goal to produce NIM publication draft by the end of FY19.
Two new prototype lenses with sapphire and PbF2 will be build and studied on test bench to qualify their imaging properties.
The laser setup for the 3D mapping of the focal plane will be upgraded to improve measurement precision with the goal to produce NIM publication draft by the end of FY19.
Simulation studies of the reduced sensor coverage and of the impact of the very good timing precision (rms of 100ps or better) of the LAPPD sensors prototypes on the PID performance will be performed.
Administrative aspects and detailed plans of the transfer of the DIRC prototype from GSI to CUA will be finalized.
FY19 outlook

## Slide 37
Photosensors and Electronics
Goals:
Activities:
Evaluation of photosensors in high-B fields at JLab.
Adaptation of LAPPDs to EIC requirements at ANL.
Adaptation of readout electronics (U. Hawaii and INFN-Ferrara) to detector PID prototypes.
To evaluate commercial photosensors for EIC PID detectors and to develop alternative, cost-effective photosensors (LAPPDs).
To develop readout electronics for PID detector prototypes.

## Slide 38
Sensors in High-B Fields
Identify the limitations of current MCP-PMTs and provide guidance for development of new photo-sensors.
Find the optimal location and orientation of sensors in the EIC detector.
  Example: tilt angle with respect to the local B-field; different sensor options
Investigate suitable parameters for operations in high magnetic fields.
Construction, installation, and commissioning of a timing upgrade for timing measurements (fast laser system, electronics).
Efficiency evaluation of a 10-μm Planacon MCP-PMTs as a function of field, orientation, and HVphotocathode-MCP1.
Ion feedback measurement as a function of HV and B-field magnitude.
Goals:
Progress in 2nd half of 2018:

## Slide 39
Results from Summer 2018 Efficiency Studies
10-μm Planacon: Relative efficiency and Relative gain
Efficiency: ε = N1phe/Nped.
At θ=20° between the sensor and the B-field axes, the efficiency drops continuosly as B increases even though the gain shows a maximum at 0.3 T.
An increase of HVphotocathode-MCP1 by 200 V (close to maximum allowed) recovers only about 13% of the efficiency (θ=20°).

## Slide 40
Results from Summer 2018 Ion-Feedback Studies
10-μm Planacon: Ion Feedback
The accuracy of the extracted ion-feedback rate strongly depends on the noise of the signal line. The value of the threshold amplitude defining a signal, Athr, critically affects the estimate of ion feedback rate.
noise with large amplitude
t (ns)
t (ns)
t (ns)
t (ns)
A (ADC ch.)
A (ADC ch.)
Athr
Athr
Athr
Athr
time interval
probed for
delayed (ion) signals
signal no ion signal
signal
ion signal
ion signal
noise with large amplitude
signal no ion signal
signal
Athr=233

## Slide 41
Results from Summer 2018 Ion-Feedback Studies
10-μm Planacon: Ion Feedback
Too low Athr leads to an overestimate of the ion-feedback rate due to some noisy waveforms. Athr=233 is the best empirically found value for Summer 2018 data.
Problem: Waveforms where Asignal < A thr or/and Aions < A thr are not taken into account.
Rate is evaluated over a range of Athr. Rate(Athr=Pedestal) is obtained from a linear fit to the high-Athr tail. This is the best estimate of the true ion rate, i.e. as would be obtained if there were no noise on the waveform, but only signal(s).

## Slide 42
Results from Summer 2018 Ion-Feedback Studies
10-μm Planacon: Ion Feedback
Δ=Rate(Athr=Pedestal)−Rate(Athr=233). Reported above:
At all voltages the ion rate is below 2%.
Results suggest that ion-feedback is primarily driven by HV.
Ion-feedback rate dependence on B-field magnitude is relatively weak.
−2.7 kV
−2.65 kV
−2.6 kV
−2.55 kV
−2.5 kV
Hvmax = −2.8 kV

## Slide 43
Planned FY19 activities
Timing measurements of a 10-μm Planacon.
Some gain and efficiency measurements to understand trends observed in 2017-2018.
Work on a simulation for optimization of MCP‒PMT design parameters as time permits.
Outlook

## Slide 44
MCP-PMT/LAPPDTM
Goal:
Progress in the 2nd half of 2018:
Produced and tested 6cm MCP-PMT with Incom 10 µm pore size MCPs, the spacing is the same as current standard design
Ordered glass components (side wall and spacer), designed and prepared for another 10 µm MCP-PMT with reduced spacing
Enhanced communication with Incom, Inc on LAPPDTM, much stronger ties
Initiated MCP-PMT simulation effort to guide MCP-PMT design
Performed initial test of newly produced LAPPDTM compatible in high magnetic field
Establishing 2D single photoelectron efficiency and TTS timing scan capability
Adapt LAPPDTM to the EIC requirements:
Highly pixelated LAPPDTM working at 2~3 Tesla, to be used as photosensors
for mRICH, dRICH, and DIRC detectors, as well as TOF applications.

## Slide 45
Fabrication of MCP-PMTs with 10 μm pore size MCPs

## Slide 46
MCP-PMT performance improvement with 10 μm MCPs
- Same stack height, no spacing reduction yet
Rise time
Gain
version 2: IBD design 20 μm
version 3: IBD design 10 μm

## Slide 47
MCP-PMT performance improvement with 10 μm MCPs
- Same stack height, no spacing reduction yet
Timing resolution (SPE)
Magnetic field tolerance
System: σ1 = 37.2 ps
Laser jitter: σLaser = 30 ps
Electronics: σEle. = 7 ps
10 μm MCP-PMT: σ = 20 ps
20 μm MCP-PMT | 10 μm MCP-PMT
0.7 Tesla | 1.3 Tesla
σTTS ~ 63 ps
σTTS ~ 20 ps
version 2
version 3
V3 achieved 100 ps rms timing, which is critical for future DIRC applications!

## Slide 48
Enhanced communication with Incom on LAPPDTM
The advices and recommendations from the committee and feedbacks from EIC users were well explained and emphasized during ANL-Incom bi-weekly meetings.
Pixel LAPPDTM is available for the first time; negotiating for one to be delivered to ANL.
Current demonstrated pixel size: 25 mm x 25 mm
QE uniformity issue was solved here!

## Slide 49
Magnetic field test on new LAPPDTM - without magnetically sensitive components
A new LAPPDTM without magnetic sensitive components was delivered at ANL for a one day test.
SBIR Phase I was fulfilled, Phase II will be submit at end of Jan. 2019.
preliminary
preliminary
preliminary
5 HV bias connection
The B field tolerance can also be further enhanced by adjusting the HVs, further study planned.
LAPPDTM shows better B field tolerance than the 6cm one with individual HV biases.

## Slide 50
FY19 plans and outlook
Achieve great improvement from 0.7 T to 1.3 Tesla, and ~ 20ps timing (SPE) (Done)
2nd magnetic field testing of 20 cm LAPPD (Done)
Laser setup and approval (Done)
SBIR Phase II application (Jan. 29, 2019)
Fabrication and testing of MCP-PMT with 10 um MCPs and reduced space
Detailed testing and comparison of ANL version 2, 3, 4 MCP-PMTs in B field with fast laser setup
Establish uniformity scan capability
MCP-PMT simulation

## Slide 51
Readout Electronics
Goals:
Develop an suite of readout electronics for all photosensors used by the Cherenkov detector prototypes.
  Need to read out MCP-PMTs and SiPMs with 3 mm pixels
  The DIRC also requires good timing (< 100 ps)
Progress in 2nd half of 2018:
Maroc-based CLAS12 front end was used for the first two mRICH beam tests, demonstrating 3 mm pixel compatibility, and is currently utilized for ongoing mRICH, dRICH, and SiPM R&D
  Maroc is not an option for the DIRC due to its poor timing
A front end based on TARGETX (used in Belle II) is being developed in Hawaii to meet the requirements of all detectors, including the DIRC.
  TARGETX will eventually be replaced by the new SiREAD chip
A generic DAQ system for all the consortium needs is deing developed by INFN

## Slide 52
Derived from CLAS12 RICH readout:
1024 channels
MAROC 64 channel parallel digitalization
FPGA generated 1 ns timestamp
DAQ protocol based on VME/VSX SSP
Custom adapter boards
- Compact distribution
Use of existing MAROC boards
Light and gas tightness
MaPMT (H13700) readout used in the mRICH beam test
Notes: Fare una immagine del PMT sulla risoluzione

## Slide 53
53
Contalbrigo M.
SiPMs might offer a cheaper and more efficient solution, expecially in the longer term, potentially providing a device with low sensitivity to magnetic fields.
However, despite improvement in dark rate (and cost), radiation hardness remains an issue.
Challenge: cooling integrated into the sensitive readout
Custom cooling plate
Soldered to the board
Peltier cell cooling
Down to -30o in N2
eRD14 PID Consortium – 01/07/19
Dedicated board for readout and cooling
of a surface Mounting SiPM Matrix
SiPM readout used in the mRICH beam test
Notes: Fare una immagine del PMT sulla risoluzione

## Slide 54
  Mechanical fitting and PCB routing
  4 TARGETX chips on one daughtercard
  SCROD (s6 FPGA) boards already fabricated and tested
  Interconnect card purely passive routing
  Reuse KLM detector readout FW and SW
  Can readout all 256 PMT channels
  Compatible with mRICH layout (2x2 PMTs)
TARGETX-based electronics for mRICH, Rev 1.0 design
4x64 channel building block
full 1024 channel (4x256) readout block

## Slide 55
TARGETX-based beam hodoscope readout
  Used in 2018 beam test at Fermilab

## Slide 56
  Specialized full waveform sampling SiPM/PMT readout System-on-Chip
    initially 32 channels (prototype), but could be expanded to 64 channels
    timing properties match for all Cherenkov detectors, including the DIRC (< 100 ps)
    1 GSa/s, Region of Interest (RoI) readout capable
  Initial testing of SiREAD complete
    Results presented at IEEE NSS - Sydney
  Various small ‘bugs’ found in chip that require re-submission
  Next beam test in FY19:
    Front-end electronics operation (ideally with SiREAD rev2),
    Using SiREAD 1.0 is possible if mated with a ‘co-processing’ FPGA – Design is under way
    DAQ verification,
    different photosensors (including MCP-PMTs / LAPPDs )
Transition from TARGETX to SiREAD
– a common readout for all Cherenkov detectors

## Slide 57
eRD14 FY19 budget (including overhead)
5.9 Budget by project
5.10 Budget by institution
 | requested | approved | fraction
dRICH | 52,000 | 31,200 | 60.0%
mRICH | 77,300 | 61,840 | 80.0%
DIRC | 112,000 | 61,140 | 54.6%
high-B | 39,200 | 31,360 | 80.0%
LAPPD | 95,000 | 76,000 | 80.0%
Electronics | 86,000 | 60,200 | 70.0%
Total | 461,500 | 321,740 | 69.7%
 | requested | approved | fraction
ANL | 95,000 | 76,000 | 80.0%
CUA + GSI | 112,000 | 61,140 | 54.6%
GSU | 69,800 | 53,840 | 77.1%
INFN | 95,500 | 64,400 | 67.4%
JLab | 7,600 | 7,636 | 100.5%
U. Hawaii | 50,000 | 35,000 | 70.0%
U. SC | 31,600 | 23,724 | 75.1%
Total | 461,500 | 321,740 | 69.7%
Please note that the rollover funds from FY18 are very small. There was some confusion in this regard due to slow reporting and, in two cases, PI grants being charged by universities rather than the R&D accounts, but all these administrative issues are being addressed.

## Slide 58
Thank you!
http://phynp6.phy-astr.gsu.edu/eRD14/index.php/Main_Page
Also, please visit the eRD14 wiki

## Slide 59
Backup

## Slide 60
Electronics – Maroc (used for FY17-18 mRICH beam tests)
SSP Fiber-Optic DAQ
Adapter
& Asics
Boards
FPGA
Board
SiPMs
✓ Mass production technology
✓ Photon counting
✓ Excellent time resolution
✓ Compatible with magnetic field
✓ High dark rate
✓ Low radiation tolerance
Work at low temperature
CLAS12 RICH electronics

## Slide 61: Electronics – TARGETX
1st generation 1024 channel compact readout for the mRICH prototype (and hodoscope) based on existing TARGETX chip:
  Initial sensor: 4 x H13700 MaPMTs, each with 256 channels
  1 GSa/s full waveform sampling
  16 us trigger buffer
  16 channels
  Built-in comparator generates trigger primitives
  Low cost 250nm CMOS
  Readout close to PMT avoids costly cabling and amplification
Technology already used in 3 projects – developed FW/SW base:
  Belle II KLM upgrade, ~20k SiPM channels
  Borehole Muon Detector (BMD) prototype: ~100 SiPM channels
  Hawaii Muon Beamline (HMB): ~60 SiPM channels
  Cherenkov Telescope Array (CTA) ~2k SiPM or PMT /telescope
Firmware development underway at Hawaii and Nalu Scientific