## Slide 1: Pythia Detection, Localization, and Diagnosis of Performance Problems using perfSONAR
Constantine Dovrolis (PI),
Partha Kanuparthy, Sajjad Zarifzadeh, Madhwaraj GK
Warren Matthews, Danny Lee
Georgia Institute of Technology

## Slide 2: Basics
Pythia is a data-analysis tool.
  We will talk mostly about the implementation using perfSONAR data
  Other active measurements could be used
  Pythia does not use NetFlow, SNMP, syslogs or customer trouble tickets.
Our focus: performance problems.
Objectives: detection, localization, diagnosis.
Funded by DoE: started Sep/2011.

## Slide 3: Goals
Short-term events
  Major outages are easy
Near real time
  troubleshoot problems
  And plan upgrades.
Scalable
Configurable
Visualize useful summaries
Internet
Performance
Pathology
Definitions
Detection
Diagnosis
Agent
One-way delays, loss, reordering
Agent
Agent
Agent
Agent
Agent
Agent
Agent
Key: Lightweight agents!

## Slide 4: Detection
Look for statistically significant deviations from baseline One-Way Delays
  But, baseline can change abruptly
  Scalability requirement: only a single pass through OWAMP time series is allowed
Baseline
One-Way Delay Between Two PerfSONAR hosts.
baseline
Deviation
Type | Baseline
Delay | Propagation + TX delay + noise
Loss | No loss
Reordering | No reordering

## Slide 5: Diagnosis
Pythia uses a model-based approach to associate each root-cause with an expected set of symptoms (signatures)
Which pathologies do we currently consider?
  Various congestion types
  Routing events and anomalies
  Various loss-episode types
  Reordering causes
  Various end-host effects
Need to exclude problems with the end-host (monitor) itself to find network problems

## Slide 6: Pythia Diagnosis Tree
End-host
effects
NTP vs.
route events
Loss events
Congestion
Reordering
nature
Input:
Detected Events
(delay, loss, reordering)
Not shown:
Unknown type

## Slide 7: Common Pathologies
End-host effects
Congestion & buffers
  significant backlog for long periods
Loss events
Routing changes
Reordering events
600ms rise!
large triangles
Overload
Bursty
Delay-correlated losses
Random losses
Engineers know what congestion looks like

## Slide 8: Localization
Network Tomography: Localization of performance anomalies using active end-to-end measurements
Pythia is not able to localize each individual diagnosed event. It tries to identify links that are most likely the cause of problems.

## Slide 9: Motivation for Range Tomography
S1
S3
S2
S5
1
2
3
4
5
Constantine used this example
Analog tomography models path/link performance as continuous random variables
Very sensitive to noise, needs long measurement
Binary (boolean) tomography models path/link performance as “good” vs “bad”
Limited resolution

## Slide 10: Boolean Tomography
S1
S3
S2
S5
1
2
3
4
5
Boolean tomography would infer that (4,5) was the only lossy link because this is the only common hop for multiple measurements showing loss.
If we have several lossy links:
Measure 15% loss (1,5)
And 5% between (2,5)
And 7% between (3,5)

## Slide 11: Range Tomography
Remember:
Measure 15% loss (1,5)
And 5% between (2,5)
And 7% between (3.5)
Range tomography gives best of analog and boolean.
P(1,4)=10% (8-10%)
P(4,5)=5% (5-7%)
P(3,4)=2%
S1
S3
S2
S5
1
2
3
4
5
10
2
To match a localization event with diagnosis events, look for significant overlaps in time.
5

## Slide 12: Pythia – System Architecture
Pythia pulls data from perfSONAR (OWAMP, traceroute, ..)
Traceroute
MA
OWAMP
MA 1
OWAMP
MA 2
OWAMP
MA 3
BWCTL
MA
...
MA
Preprocessing
Detection
Localization
Diagnosis
Pythia
Bring it all together:

## Slide 13
I joined the project last year because of my operational experience.
New Work
Danny has been working on scaling and optimizing the database. Now 2.8m entries.
Partha implemented the detection and diagnosis on live data. Previously he had used captured owp files.
Partha also developed some initial visualization tools. Visualization remains under development.
Danny Lee joined the project too and implemented the localization on live data.

## Slide 14
We installed the Pythia agent code on hosts in the GAMMON project, 15 machines on multiple networks around Georgia.
The Georgia Measurement and Monitoring (GAMMON) project studies network and application performance between K-12 school districts. Green represents districts with servers, blue are districts that have expressed willingness to host a server, and yellow is targeted for the next phase of deployment.
Georgia does not have an education network serving schools. AT&T provide connectivity for most districts but GAMMON sites have 8 different service providers.
Our Testbed - GAMMON

## Slide 15: Front-End Visualization

## Slide 16: Heatmap Table
Filter diagnosis type
time frame
Total of 1,380,318 events in February:
EndHostNoise 751,294 (54%)
  does not seem to be related to hardware
DelayCorrelatedLoss 218,725 (16%)
RandomLoss 114,860 (8%)
Unknown 93,185 (7%)

## Slide 17: Diagnosis History
Intention was to track long-term trends, find issues that may otherwise disappear in the noise.

## Slide 18: Localization
End host at Dawson
Brighter means more problems

## Slide 19: Root Cause

## Slide 20: Summary: Work In Progress
Last year, Constantine reported that we would:
  Diagnose more performance problems and improve existing tests ✔
  Unsupervised clustering to identify unknown events ✗
  Open-source system implementation of Detection, localization, diagnosis with a real-time data collection framework on ESnet, I2, PL-testbed, broadband networks ✔
  Create front-end for users/operators ✔
    The front-end is viewable at http://pythia.cc.gatech.edu
Other Achievements
  Contributed to owamp source
  Packaged pythia-agent for easy install

## Slide 21: Further Work
Further Deployment
  ESNET
  Internet2
  Others
Continue to improve near-real time analysis.
Continue to improve front-end performance.
We will continue to talk to IT directors, network administrators, upstream providers – Does Pythia help solve their problems?
We expect these to happen after the release of perfSONAR 3.3.
}

## Slide 22: Project Publications
Sajjad Zarifzadeh, G. Madhwaraj, Constantine Dovrolis, “Range Tomography: Combining the Practicality of Boolean Tomography with the Resolution of Analog Tomography”. At the ACM IMC conference, 2012
Sajjad Zarifzadeh, Constantine Dovrolis, “Localization of Network Performance Problems with Multi-Level Discrete Tomography”. At the IEEE ICCCN conference, July 2012
Partha Kanuparthy, Constantine Dovrolis, “Pythia: End-to-End Diagnosis of Wide-area Performance Problems”. Under peer-review submission, 2013.

## Slide 23: Any Questions?
constantine@gatech.edu