## Slide 1: JLEIC IR Summary
Vasiliy Morozov
EICUG IR Working Group meeting on Luminosity Measurement February 15, 2019

## Slide 2: Full Acceptance Detector Concept
Would like to get ~100% acceptance for the whole event
Ion beamline
Electron beamline
Central Detector/Solenoid
Dipole
Dipole
Forward (Ion) Detector
Scattered Electron
Particles Associated
with Initial Ion
Particles Associated with struck parton
Forward photon

## Slide 3: Schematic of Full-Acceptance Detector
50 mrad crossing angle
Forward hadron detection in three stages
  Endcap
  Small dipole covering angles up to ~2-3
  Far forward, up to ~10 mrad, for particles passing through accelerator quads
Low-Q2 tagger
  Small-angle electron detection

## Slide 4: JLEIC Interaction Region Layout
Most recent changes occurred in the ion IR due to redesign for 200 GeV/c ion momentum
Streamlined updates of GEMC and GEANT4 detector region models
Continued development of an engineering design of the detector region
Forward hadron spectrometer
low-Q2 electron detection
and Compton polarimeter
p
(top view in GEANT4)
e
ZDC
IP
e
ions
forward e detection
Compton polarimetry
dispersion suppressor/
geometric match
spectrometers
forward ion detection

## Slide 5: Modifying IR Design for 200 GeV/c
Constraints
  Maximum pole-tip fields at 200 GeV/c of 4.6 T
  Minimum impact on the forward hadron tagging performance compared to the 100 GeV/c design
  Minimum impact on the luminosity performance compared to the 100 GeV/c design
  Minimum impact on the beam dynamics compared to the 100 GeV/c design
Modification strategy
  Increase the FFQ lengths to drop the pole-tip fields
  Switch from a triplet to doublet final focusing configuration
  First “quadrupole” in the doublet is two independent quadrupoles that can be run in a doublet mode up to 100 GeV/c

## Slide 6: JLEIC Ion IR 100 GeV COM Design
±10 mrad angular aperture acceptance in the whole energy range up to 100 GeV COM with a secondary focus in combination with high dispersion point downstream of spectrometer dipole
Conventional Nb-Ti technology Final-Focusing Quadrupole technology
Same high luminosity and detection performance as the 65 GeV COM design
Shorter- and longer-focus configurations at lower and higher energies, respectively
65 GeV COM
100 GeV COM

## Slide 7: Ion IR Optics
Multipole and orbit correction spools
Multipole and orbit correction spools
x/y kickers
IP
Secondary focus for Roman Pot

## Slide 8: Electron IR Optics
IP
Compton polarimeter

## Slide 9: Low Tagger in JLEIC
Dipole chicane for high-resolution detection of low-Q2 electrons
Compton polarimetry has been integrated to the interaction region design
  same polarization at laser as at IP due to zero net bend
  non-invasive monitoring of electron polarization

## Slide 10: IR Layout

## Slide 11: IR Layout
Compton polarimeter
+
Luminosity monitor
Need a hole in the dipole yoke for photons

## Slide 12: GEANT4 Model (Y. Furletova)

## Slide 13: GEANT4 Model (Y. Furletova)

## Slide 14: Development of IR Magnet Specifications
IR magnet engineering design/analysis
  Design of the multipole correction scheme in the IR region, relate LARP experience
  Identify limits in magnet parameters which directly affect the IR performance
  Relate existing magnet data to the EIC performance requirements including scaling to the IR design
  Heat and radiation loads on IR magnets
  Perform magnetic analysis and initial optimization, considering LARP design, BNL EIC IR quadrupole prototype, and others
  Mechanical and magnetic design of an optimized IR quadrupole
  Incorporate optimized IR quadrupole lessons/features and finalize IR layout