## Slide 1: EIC Physics and IR Design II
CFNS Summer School 2019
August 3, 2019
Vasiliy Morozov
on behalf of JLEIC design team

## Slide 2: Outline
Full acceptance detector concept
Magnetic optics of the interaction region
Engineering design of the interaction region magnets
Detector background
Detector acceptance
Tagging for heavy ions
  Coherent diffraction
  quark propagation and hadronization
EIC software highlights

## Slide 3: EIC Physics Highlights
An EIC aims to study the sea quark and gluon-dominated matter
  3D structure of nucleons
    How do gluons and quarks bind into 3D hadrons?
    How does the mass of a nucleon emerges?
  Role of orbital motion and gluon dynamics in the proton spin
    Why do quarks contribute only ~30%?
  Gluons in nuclei (splitting/recombining)
    Does the gluon density saturate at small x?
Need luminosity, polarization and good acceptance to detect spectator & fragments

## Slide 4: Full Acceptance Detector Concept
e
e’
p/A
For typical collider experiments, measurements are performed mainly in central region
Would like to get ~100% acceptance for the whole event

## Slide 5: Schematic of Full-Acceptance Detector
50 mrad crossing angle
Forward hadron detection in three stages
  Endcap
  Small dipole covering angles up to ~3
  Far forward, ~10 mrad, for particles passing through accelerator quads
Low-Q2 tagger
  Small-angle electron detection
mrad
mrad
Low tagger
Secondary
focus
Roman pots
End caps
Central detector

## Slide 6: Streamlining IR Updates
With many parties involved, need to find a way to reliably synchronize the IR models between accelerator, detector and engineering groups.
Accelerator Lattice
MAD-X
Detector Model
GEMC
Engineering Design
CAD
Largely
automated
Largely
automated

## Slide 7: Ion Interaction Region
High luminosity and acceptance performance in the whole energy range
Conventional NbTi technology
Secondary focus with high dispersion

## Slide 8: Ion Beam Envelope & 99%p Trajectory
Assuming beam momentum of 100 GeV/c, ultimate normalized x/y emittances of 0.35/0.07 m, and ultimate momentum spread of 310-4
The horizontal size includes both betatron and dispersive components
Ignoring effect of the crab tilt

## Slide 9: JLEIC Ion IR 100 GeV COM Design
±10 mrad angular aperture acceptance in the whole energy range up to 100 GeV COM with a secondary focus in combination with high dispersion point downstream of spectrometer dipole
Conventional Nb-Ti technology Final-Focusing Quadrupole technology
Same high luminosity and detection performance as the 65 GeV COM design
Shorter- and longer-focus configurations at lower and higher energies, respectively

## Slide 10: Ion IR Optics
Space reserved for multipole and orbit correctors
Correction of solenoid orbital effect consistent with full acceptance requirement
Multipole and orbit correction spools
Multipole and orbit correction spools
x/y kickers
x kickers
IP

## Slide 11: Orbit Correction
Orbit is centered inside the FFQs
The ion orbit has a vertical angle of 0.15 mrad to minimize the downstream corrector fields
IP
IP

## Slide 12: Coupling Compensation
Rotated frame technique: skew quads of the correction packages provide rotation effect
Interaction plane is rotated to account for the vertical angle of the ion orbit
Global coupling compensation
Detector solenoid
Anti-solenoids
IP

## Slide 13: Ion IR Element Parameters

## Slide 14: Electron Interaction Region
Downstream chicane for low- tagging and polarimetry

## Slide 15: Electron Coupling Compensation
Rotated frame technique
Global decoupling and local decoupling at the IP to simplify matching crab planes
Nested skew quads providing rotation effect
Detector solenoid
Anti-solenoids

## Slide 16: Low Tagger in JLEIC
Dipole chicane for high-resolution detection of low-Q2 electrons
Compton polarimetry has been integrated to the interaction region design
  same polarization at laser as at IP due to zero net bend
  non-invasive monitoring of electron polarization

## Slide 17: IR Layout
Compton polarimeter
+
Luminosity monitor
Need a hole in the dipole yoke for photons

## Slide 18: Electron IR Element Parameters

## Slide 19: JLEIC Interaction Region Layout
Streamlined updates of GEMC and GEANT4 detector region models
Continued development of an engineering design of the detector region

## Slide 20: Development of IR Magnet Specifications
IR magnet engineering design/analysis
  Design of the multipole correction scheme in the IR region, relate LARP experience
  Identify limits in magnet parameters which directly affect the IR performance
  Relate existing magnet data to the EIC performance requirements including scaling to the IR design
  Heat and radiation loads on IR magnets
  Perform magnetic analysis and initial optimization, considering LARP design, BNL EIC IR quadrupole prototype, and others
  Mechanical and magnetic design of an optimized IR quadrupole
  Incorporate optimized IR quadrupole lessons/features and finalize IR layout

## Slide 21: First Ion Spectrometer Dipole
By: 1.32 T x 1.5 m
Bx: 0.22 T x 0.75 m and –0.19 T x 0.75 m

## Slide 22: Upstream Ion Corrector
By: –0.019 T x 0.3 m
Bx: 4.5 T x 0.3 m

## Slide 23: Downstream Hadron Quadrupoles
200 GeV/c
protons
10 GeV/c electrons
mrad
Parameter | Unit | iQDS1a | iQDS1b | iQDS2
Lmagnetic | m | 2.25 | 2.25 | 4.5
Rclearbore | mm | 92 | 123 | 177
Router | mm | 231 | 310 | 444
Rgoodfield | mm | 40 | 40 | 40
Gnormal | T/m | -37.2 | -37.2 | 26.0
Gskew | T/m | -1.23 | 0.0 | 0.0
G x Rinner | T | 3.4 | 4.6 | 4.6
Main design requirements and features:
Provide neutron cone acceptance of ± 10 mrad
Clear bore up to 177 mm, add ~8 mm for coil radius
Design is based on collared cos2q NbTi coil: very large magnets but experience with CEBAF Hall C SHMS-Q2
50 mrad crossing angle allows more transverse space for shielding: no shift/tilt, separate electron magnets
iQDS2

## Slide 24: Magnet Length Optimization
Longitudinal space allocation is very tight:
Coil end geometry has to be optimized for winding the Rutherford cable
Spacers to control peak field and field quality make the coil end less compact
Include space for engineering features: leads, axial force support, cryostat
Estimate field quality and allocate space for correctors based on DA calculations
Option to increase operating gradient is limited by NbTi properties
Example: iQDS1a (JLEIC) end field quality
Integrated b6:
-43.3 units
over 406.3 mm
Integrated b6
is zero
Baseline (compact) end
With additional spacer
+17mm

## Slide 25: Detector Beam Pipe
Detector beam pipe may serve a resonator excited by the beams. One must absorb the energy of excited resonances to prevent their build up.
One must minimize the impact of multiple scattering on particles existing the beam pipe.
Focusing by the electron quadrupoles causes synchrotron radiation, which may cause detector background and increase vacuum pressure in the beam pipe. The synchrotron radiation must be properly masked.
200 mm
1924 mm
Ion beam
e beam
64.4 mm ID
60 mm ID x2
22.4 mm ID x2
Synchrotron mask

## Slide 26: Background Studies
Project leads: Latifa Elouadrhiri and Charles Hyde

## Slide 27: Detector Background
Performance of ZEUS at HERA was limited by background in the Central Tracking Detector (CTD)
  No careful background simulations prior to running
Background was generated by ion beam scattering on residual gas generated by electron beam’s synchrotron radiation
Background was monitored using a small scintillator counter C5
Simulation tools and procedures validated using HERA data (L. Elouadrhiri et al.)
C5 rate as a function of HERA e beam current for different p beam current
Results of our simulations
Be (65%), Al (35%)
10-8 mbar
10-10 mbar
10-10 mbar

## Slide 28: Shadow Diagram
Ion beam tube

## Slide 29: Far-Forward Acceptance for Charged Fragments
Δp/p = -0.5
Δp/p = 0.0
Δp/p = 0.5
(protons rich fragments)
(exclusive / diffractive recoil protons)
(tritons from N=Z nuclei)
(spectator protons from deuterium)
(neutron rich fragments)

## Slide 30: Far-Forward Angular & Momentum Acceptance
Transmission of particles with initial angular and p/p spread
  Quad apertures = B max / (fixed field gradient @ 100 GeV/c)
  Uniform particle distribution of 0.7 in p/p and 1 in horizontal angle originating at IP
  Transmitted particles are indicated in blue (the box outlines acceptance of interest)

## Slide 31: Far-Forward Acceptance to Neutrals
Transmission of neutrals with initial x and y angular spread
  Quad apertures = B max / (fixed field gradient @ 100 GeV/c)
  Uniform neutral particle distribution of 1 in x and y angles around proton beam at IP
  Transmitted particles are indicated in blue (the circle outlines 0.5 cone)

## Slide 32: Far-Forward Angular Acceptance
Quad apertures = 9, 9, 7 T / (By /x @ 100 GeV/c), dipole aperture = -30/+50 40 cm
Uniform distribution of 1 in x and y angles around proton beam at IP for a set of p/p
The circle indicates neutrals’ cone

## Slide 33: Momentum & Angular Resolution
Protons with p/p spread are launched at different angles to nominal trajectory
Resulting deflection is observed at the second focal point
Particles with large deflections can be detected closer to the dipole

## Slide 34: Momentum & Angular Resolution
Protons with different p/p launched with x spread around nominal trajectory
Resulting deflection is observed 12 m downstream of the dipole
Particles with large deflections can be detected closer to the dipole

## Slide 35: Acceptance for Protons from Diffractive Processes
Simulated acceptance for protons generated at the interaction point having energies of and having up to

## Slide 36: Example: DVCS Recoil Proton
Kinematics: 5 GeV e- on 100 GeV p at a crossing angle of 50 mrad.
  Cuts: Q2 > 1 GeV2, x < 0.1, E’e > 1 GeV, recoil proton 10σ outside of beam
DVCS generator: MILOU (from HERA, courtesy of BNL)
GEANT4 simulation: tracking through all magnets done using the JLab GEMC package
e- beam at 0 mrad
low-t acceptance
p beam at 50 mrad
Proton angle at IP
10σ beam size cut:
  p < 99.5% of beam for all angles
  θ > 2 mrad for all momenta
high-t acceptance
High-t acceptance limited by magnet apertures
-t = 1.9 GeV2 ±14 mrad

## Slide 37: Key EIC Measurements with Heavy Nuclei
Coherence and gluon saturation
  At low and , the probe interacts coherently with all gluons in its path
  The gluon density can be increased by going to lower x (higher cm energy), or increasing the nuclear thickness
    Heavy nuclei + selection of large path lengths through geometry tagging
    Extra boost from non-spherical nuclei?
Quark propagation and hadronization
  Knowing the path length will greatly improve our understanding of what happens when a quark propagates through nuclear matter.
    Energy loss, broadening, etc.
pT
q
h
g*
e'
e

## Slide 38: Coherent diffraction can reveal the spatial gluon distribution
Coherent diffraction may be the only way to image the transverse gluon distribution in nuclei, but the incoherent background is large
  Efficient veto is needed
Momentum transfer t is conjugate to transverse coordinate b T. Toll and T. Ullrich, Phys. Rev. C 87, 024913 (2013)
Notes: Coherent distributions can be used to obtain info about gluon distribution in impact parameter space by taking fourier transform of cross-section

## Slide 39: Coherent diffraction is also sensitive to gluon saturation
(Smaller) shows little sensitivity and can serve as a reference for (Larger) , which shows significant sensitivity to saturation (at moderate Q2) T. Toll and T. Ullrich, Phys. Rev. C 87, 024913 (2013)

## Slide 40: Incoherent diffraction cross-section dominates
The challenge for coherent diffraction is to suppress the much larger incoherent background; requires a combination of detection methods
Signal-to-noise ratio of 2:1 at the 3rd dip requires a veto efficiency of 99.9% (M. Baker, 2017)

## Slide 41: How Far in 𝒕 do we need to measure?
T. Ullrich and T. Toll
Fourier: large  small
BAD
GOOD

## Slide 42: Event generators
We also want to thank M. Ungaro for adding support for the event generator formats in the GEMC (Geant4) package

## Slide 43: BeAGLE
Feynman diagram and structure of BeAGLE

## Slide 44: Simulation process flow
Coherent events and their relative contribution from Sartre
Incoherent events from BeAGLE
GEMC for simulation of background suppression efficiency

## Slide 45: Tracking generated events in detector
BeAGLE and Sartre event generators interfaced to a GEMC detector model
e+Pb208 collisions at 10 x 40 GeV/u
10 mrad acceptance through FFQs
20 mrad acceptance through first spectrometer dipole
Cyan: electrons
Blue: neutrons
Black: photons
Red: protons
Grey: residual ion

## Slide 46: Vetoing incoherent diffractive events
Exclusive vector meson incoherent diffraction for 10 x 40 GeV e+Pb in BeAGLE
  Sample includes any vector meson: , , ,
  = 9 fm
  5.7 mb
  Significant fraction of the incoherent background events have no evaporation neutron: P(Nn = 0) = 11.3%
  Rejection factor using a ZDC alone is two orders of magnitude too low

## Slide 47: Vetoing inefficiency
Central veto: any of ( MeV), , , , or at mrad
ZDC: any of ( MeV), , , , or through FFQs
Full veto: Central + ZDC + any of , , or after the first dipole
Full + photons: Full + ( MeV) through the first dipole
fm
fm

## Slide 48: Applying the veto
fm
fm

## Slide 49: Gluon spatial distribution
Full veto + photons reproduces model distribution fairly well
Detection of A-1 nuclei, photons can also improve the veto efficiency
Notes: Magenta: reference input distribution; black: bSat model with including errors in t measurement; blue: full veto + photons with geometry tagging

## Slide 50: Collision geometry can be reconstructed from final state
Geometry tagging is the use of information from the nuclear breakup to categorize the geometry of the collision
By detecting nuclear fragments and particles in the ion direction, we can:
  Determine the impact parameter b and the effective nuclear thickness T(b) at lower x
  Determine the path length d in the nucleus after the primary interaction
Tagging allows us to select events for which the average T(b) and d are very different from their averages over the entire nucleus
Intra-nuclear cascading increases with d (forward)
Evaporation of neutrons from excited nucleus (very forward)
Without tagging, average d in a nucleus scales as the radius (A1/3)

## Slide 51: Tagging in b and T(b)
Geometry tagging using only evaporation neutrons: can select events with larger average nuclear thickness, at cost of lower statistics
Selecting 1.1% of events with largest average nuclear thickness (measured by evaporation neutrons only) equivalent to increasing the accelerator energy by a factor 3.2
e+Pb208 collisions at 10 x 40 GeV, Q2 > 1 GeV2, y < 0.95, x < 0.002
Notes: Plot on left shows saturation scale Q^2 as a function of x for ep, eCa, eAu for min bias and central (eAu only). For fixed Q2, eAu collision has similar saturation reach as ep collision but with 300x larger energy. At fixed x, geometry tagging to isolate central events from min bias events enhances saturation reach -

## Slide 52: What if we also detect the charged particles?
Detecting protons and light ions (d and 4He) in addition to neutrons increases the selectivity in b and the effective nuclear thickness T(b)
For a 1% yield cut, the increase in equivalent collision energy is about 40% (magenta curve on right) compared with using evaporation neutrons only
n, p, d, multiplicities

## Slide 53: What if we identify the residual ion?
A, Z and d and multiplicities
Kinematic reach can be extended by detecting the residual ion together with charged particles
Best result: measurement of Z in addition to A/Z (inferring A) – this would require a PID system for the ion (e.g. additional dE/dx if the dE/dx from the tracker is insufficient)
Compared to no geometry tagging, the total energy increase factor is 4.8

## Slide 54: Detection requirements
A, Z and d and multiplicities
Best results obtained by detecting the residual ion (tracking + dE/dx) and light ions (easy for all except Z = N nuclei)
A neutron ZDC can provide additional information or a useful measurement on its own
Also beneficial to detect protons – requires larger magnet apertures but is also needed for spectator tagging with light nuclei

## Slide 55: Further increasing the effective thickness: vs
Further energy boost is possible with using Uranium ions
Additional 1.4x factor gives total effective energy increase of 6.7
on is easier than on since only one axis needs to be aligned
JLEIC
M. Baker, 2017
8% in the tail

## Slide 56: Tagging in
+208 collisions at 10 x 40 GeV
 | IP | 2nd dipole | 
Evaporation Neutrons | 330216 | 330216 | 100.0%
Cascading Neutrons | 66968 | 39438 | 58.9%
Hard collision Neutrons | 40314 | 8199 | 20.3%
Total | 437498 | 377853 | 86.4%

## Slide 57: Tagging in at higher
For quark propagation and hadronization studies, it is more important to know d than to maximize it
Plots below illustrate sensitivity with yield. Binning for different values of average is straightforward.
Same detection criteria apply.
A, Z and d and multiplicities

## Slide 58: Software chain
Fast
detector
simulation
Full
detector
simulation
Reconstruction and analysis
MC generators

## Slide 59: Software chain
Generators
Fast simulation
Full simulation
Reconstruction & analysis
g4e JLEIC in Geant4
Geant4 Fast mode
Eic smear
Generators Database
Pythia
Beagle
Herwig
…
ejana – EIC JANA(2)
BNL & Jlab effort on
Fast detector prototyping
ejana = EIC Jana
Community reference reconstruction
g4e = Geant 4 EIC
C++ genue GEANT4 with JLEIC detector in it
Database with various MC samples

## Slide 60: Software for detector simulation and reconstruction
GEMC Geant 4 based simulation
Plain Geant 4 C++ for √s 100 GeV design (Driven by the community request)
For those who prefer scripting over compilation
Geant 4 python can be used

## Slide 61: Geant 4 EIC
The codename g4e – stands for Geant 4 EIC
Beta stage
√s 100 GeV design is implemented
Imports CAD, accelerator group data
Exports final Geometry in various formats
Plain flattened analysis ready ROOT files
For those who prefer scripting over compilation
Geant 4 python can be used

## Slide 62: Entry Point for EIC = EPIC
Workflow oriented interactive environment based on Jupyter
Contact:
Dmitry Romanov
romanov@jlab.org