## Slide 1
EIC Detector Design
Alexander Kiselev
CFNS Summer School
Stony Brook University August,1-9 2019

## Slide 2: Outline
Introduction
EIC detector concepts
Tracking
Calorimetry
Particle identification
Summary
Wednesday
Thursday
*Input from E.Aschenauer, M.Chiu, R.Erbacher, Y.Furletova, K.Gnanvo, T.Horn,
U.Langenegger, V.Manzari, P.Nadel-Turonski, B.Page, D.Pitzl, J.Repond, L.Ruan,
F.Sefkow, M.Stanitzki, B.Surrow, M.Vandenbroucke, H.Wennloef, P.Wintz, C.Woody,
R.Yoshida and other colleagues used in this lecture

## Slide 3
Introduction

## Slide 4: EIC Physics
Key questions:
How are the sea quarks and gluons, and their spins, distributed in space and momentum inside the nucleon?
How does the nuclear environment affect the distribution of quarks and gluons and their interactions in nuclei?
Where does the saturation of gluon densities set in? Does this saturation produce matter with universal properties?
Precision study of quark and gluon dynamics inside nucleon and nuclei
A.Acardi et al, EPJ A 52 9 (2016)

## Slide 5: Typical EIC experimental measurements
(A) Inclusive Reactions in ep/eA:
Structure Functions: g1, F2, FL
(B) Semi-inclusive Reactions in ep/eA:
TMDs, Helicity PDFs, FFs (with flavor separation); di-hadron correlations; Kaon asymmetries, cross sections
(C) Exclusive Reactions in ep/eA:
DVCS, exclusive VM production (GPDs; parton imaging)
e’
t
(Q2)
e
gL*
x+ξ
x-ξ
H, H, E, E (x,ξ,t)
~
~
g, p,J/Y
p
p’

## Slide 6: Example (A): scattered e- acceptance
Typically use pseudo-rapidity h = -ln(tan(q/2)) rather than q
Scattered electron {h,p} for various Q2 ranges at the same set of beam energies
h=4 ~ 20
h=0 ~ 900
In principle need to cover at least -4 < h < 2 range with appropriate tracking and e/m calorimetry

## Slide 7: Example (B): kinematics of SIDIS pions
Cuts: Q2>1 GeV2, 0.01<y<0.95, p>1GeV
-> -3.5 < h < 3.5 covers entire kinematic region in hadron pt (transverse momentum) and z (virtual photon energy fraction), which are important for physics
(no difference between p±, K±, p±)

## Slide 8: Example (C): DVCS photons & protons
e’
t
(Q2)
e
gL*
x+ξ
x-ξ
H, H, E, E (x,ξ,t)
~
~
g
p
p’
DVCS photon {h,E} for 10 GeV electrons and various proton beam energies
Need e/m calorimetry coverage in -4 < h < 2 range
RP
275 x 18 GeV
~10s away from beam line
100 x 10 GeV
first quad aperture & beam pipe
B0
41 x 5 GeV
vacuum system ~20mrad cone
DVCS proton Pt (by far forward spectrometers B0/RP ); range up to ~1.3 GeV/c required by physics
20mrad vacuum system cone opening from IP to B0 magnet suffices, except for the lowest energy combination

## Slide 9: DIS kinematics reconstruction basics
p/A
e
e'
Electron method
“Classic” way to determine {x,Q2}
Obviously diverges at small y
-> only scattered electron
information is used
Scattered electron
Proton (ion) remnants
Struck quark fragmentation products
qe’

## Slide 10: DIS kinematics reconstruction basics
p/A
e
e'
Scattered electron
Proton (ion) remnants
Struck quark fragmentation products
Jacquet-Blondel method
-> only hadronic final state
information is used
Relatively poor resolution (yet better than nothing)
The only way to reconstruct {x,Q2} for charged current
events (since neutrino in the final state can not be detected)
-> FYI: “mixed” reconstruction methods exist as well (see e.g. next slide)

## Slide 11: DIS kinematics reconstruction example
Lepton tracking only
Double-angle method
Describes migration between kinematic bins
Important to keep it close to 1.0 for successful unfolding
“Straightforward” lepton tracking can hardly help at Y<0.1
Hadronic final state accounting allows to recover part of the high Q2 range
{PYTHIA events 20x250 GeV} -> {BeAST detector; full GEANT simulation} -> {Kalman filter track fit}
Bremsstrahlung turned on here (and it matters even for detector with ~5% X/X 0!)

## Slide 12
EIC detector concepts

## Slide 13: Detector requirements: ideal vs real life
The “ideal” detector (for a given process):
Detect all final state particles of interest with 100% efficiency
Determine their type (PDG) with high confidence level
Measure all 4-momenta precisely
Real life:
Only 13 particle species have ct > 500mm -> have to deal with the decay products, secondary vertices, invariant mass peaks
Never get 100% efficient acceptance (cracks, support system, beam pipe, sub-detector frames, ...)
Never get 100% detection efficiency (detector imperfectness, reconstruction algorithms, DAQ limitations, ...)
Particle identification is never perfect
Have to deal with the finite detector resolutions (detector size and technology limitations, costs, ...)
Background processes spoil the picture

## Slide 14: How do we detect particles?
Long-lived: through their interaction with the detector material
Tracking (“gentle” measurement)
Calorimetry (destructive measurement)
& PID detectors
Short-lived: through measuring their decay products

## Slide 15: Emerging practical implementation
Caveats:
Calorimetry measurement is destructive, therefore tracking system should be the closest to the IP
EIC physics also requires hadron species p/K/p identification!

## Slide 16: Illustration: CMS detector at LHC

## Slide 17: EIC detector concept: JLEIC
Jefferson Laboratory (JLab) “green field” detector

## Slide 18: EIC detector concept: BeAST
hadronic calorimeters
RICH detectors
silicon trackers
GEM trackers
3T solenoid cryostat
iron yoke
up to 9.0m
TPC
e/m calorimeters
hadrons
coils
electrons
trackers
Brookhaven Laboratory (BNL) “green field” detector

## Slide 19: EIC detector concept: ePHENIX
Brookhaven Laboratory sPHENIX-based implementation

## Slide 20: EIC detector concept: TOPSiDE
Argonne Laboratory (ANL) all-silicon implementation

## Slide 21: EIC Detector Concepts
Common features:
  Compact design
  (Almost) 4p hermetic acceptance in tracking/calorimetry/PID
  Vertex + central + forward/backward + far forward tracker layout
  Low material budget in the tracker volume
  Strong central solenoid field
  Moderate momentum resolution (~1% level)
  Moderate EmCal and HCal energy resolution
Note:
  Community wants two general-purpose detectors

## Slide 22
Tracking

## Slide 23: Tracking basics: idea
Charged particles lose energy via ionization when passing through media (a gas volume, a silicon layer, …):
Tracking detector:
  Amplify this “electron signal” if needed
  Discretize it according to the detector design
Track fitting algorithm:
  Use the resulting N discrete “space points”, their respective covariance matrices (error estimates) and knowledge about the underlying dynamics (magnetic field, material distribution) in order to estimate track parameters at the detector location
  Extrapolate to the interaction point and build vertices
Bethe-Bloch formula

## Slide 24: Tracking basics: momentum measurement
- 3 points
- N equidistant points
solenoidal field
Important observations:
-> resolution becomes worse
with increasing momentum
-> want high single point
resolution, large field
and large size
add 3 measurements

## Slide 25: Tracking basics: Kalman filter algorithm
  Originally developed by R.Kalman in 1960 for spacecraft radar applications
  Formulated for charged particle tracking and vertex fitting by R.Fruehwirth in 1987

## Slide 26: EIC detector tracking: systems & options
Vertex detector
  MAPS
Central tracker
  TPC (+ MM)
  All-silicon tracker
  A set of MM cylinders
  Drift chamber
  Straw tube tracker
Endcap trackers
  Large-area GEMs (MM, mRWELL, GEM-TRD, sTGC)
Forward & backward trackers
  MAPS
  (Very) high resolution GEMs
Close-to-beamline instrumentation
  Roman Pots, B0 magnet tracker, low-Q2 tagger, …

## Slide 27: Expected “typical” EIC tracker performance
Radiation length scan
Momentum resolution
~2.0m
H1 : 0.6%*Pt + 1.5%
ZEUS : 0.5%*Pt + 1.5%

## Slide 28: “Traditional” Si detectors (here: CMS strips)
Planar sensor from a high purity silicon wafer (here n-type).
Segmented into strips by implants forming pn junctions.
Strip pitch 20 to 200 μm, high precision photolithography.
Bulk is fully depleted by a reverse bias voltage (25-500V).
Ionizing particle creates electron-hole pairs (25k in 300 μm; 3.6eV/pair).
Electrons and holes are separated by the electric field and collected on the implanted strips
High spatial resolution (dozens of microns, pitch-dependent)
Fast (~10ns collection time)

## Slide 29: “Traditional” Si detectors (CMS)
Impressive system: 107 channels; 200 m2!
Bump-bonding to a (separate
from sensor) readout chip …
  … this blows up the material budget (no good for EIC)!

## Slide 30: Monolithic active pixel sensors
Hybrids
Sensitive volume and readout electronics on separate chips
Most commonly used in silicon vertex trackers
Radiation tolerant and fast
Monolithic Active Pixel Sensors (MAPS)
Sensitive volume and readout electronics on same chip
Made using commercial CMOS technology
Thin and fine granularity
Slow (charge collection partly via diffusion)

## Slide 31: Monolithic active pixel sensors (ALICE)
Upgraded ALICE Inner Tracker System (ITS2)
Based on novel MAPS ALPIDE (vs ITS1)
10 m2 active silicon area, 12.5 G-pixels
Smaller pixels: ~5 μm in rφ and z directions (vs 12 μm and 100 μm)
Power density < 40mW / cm2
Less material: ~0.3% X0 for Inner Barrel (vs 1.1% X0)
Faster readout: 100 kHz Pb-Pb (vs 1 kHz)
artistic view of charge
collection process

## Slide 32: Monolithic active pixel sensors (ALICE)
Upgraded ALICE Inner Tracker System (ITS2)
Layers 4,3 & 5
Outer barrel stave, 102 million pixels

## Slide 33: Depleted monolithic active pixel sensors
Depleted Monolithic Active Pixel Sensors (DMAPS)
Utilizing high voltage/high resistivity CMOS technology
Depleted volume intended to be as large as possible
Depletion gives faster (drift mode) and more uniform charge collection compared to standard MAPS
Standard process (MAPS)
Modified process (DMAPS)

## Slide 34: Why small pixels are required?
Open charm reconstruction
Signature: displaced Kp vertex
Simulated vertex tracker
|η| < 0.5 (barrel region)
η = 3 (forward region)
  Smaller pixels provide better pointing resolution …
Pointing resolution plots

## Slide 35: Central tracker: Drift Chamber
Multi Wire Proportional Chamber (MWPC)
G.Charpak 1968, Nobel prize 1992
Typical parameters: L=5~8 mm,
d=2mm, anode wire diameter =20 μm.
MWPC: address of fired wire(s) give one dimensional information and σx ≈ d/√12
Drift chamber: use drift length time information, typical resolution ~200 μm
Resolution limits: drift and diffusion effects

## Slide 36: Central tracker: Drift Chamber (issues)
Remember, error of momentum measurement:
⇒ L has to be large ⇒ detector has to be wide (small Rin, large Rout)
Also: want large η coverage ⇒ z dimension has to be large ⇒ detector has to be long
-> a drift chamber with several thousand long wires
-> problems with both construction and maintenance
Solution#1: encapsulate each anode wire in a separate cylindrical volume ⇒ straw tracker
Solution#2: let the electrons drift over long distances
⇒ TPC: essentially a huge gas filled box

## Slide 37: Central tracker: Straw Tubes (PANDA)
4636 straw tubes in 2 separated semi-barrels
23-27 radial layers in 6 hexagonal sectors
  15-19 axial layers (green) in beam direction
  4 stereo double-layers: ±3° skew angle (blue/red)
Volume: Rin / Routr= 150 / 418 mm, L~ 1650 mm
  Inner / outer protection skins (~ 1mm Rohacell/CF)
Ar/CO2 (10%), 2 bar, ~ 200ns drift time (2 T field)
Time & amplitude readout
  sr ~ 150 µm, sz ~ 2-3 mm (isochrone)
  (dE/dx) < 10% for PID (p/K/ < 1 GeV/c)
p /p ~ 1-2% at B=2 Tesla (STT + MVD)
X/X0 ~ 1.25% (~ 2/3 tube wall + 1/3 gas)

## Slide 38: Central tracker: Straw Tubes (PANDA)
Material budget at lowest limit (2.5 g per assembled straw)
thinnest Al-mylar film, d=27µm, =10mm, L=1400mm
thin wall endcaps, wire fixation (crimp pins), radiation-hard
self-supporting modules of pressurized straws (p=1bar)
  close-packed (~20 µm gaps) and glued to planar multi-layers
  replacement of single straws in module possible (glue dots)
strong stretching (230kg wires, 3.2tons tubes)*, but no reinforcement needed

## Slide 39: Central tracker: Time Projection Chamber
STAR TPC
140,000 electronics channels (pads)
512 time bins
140,000 x 512 = 72 million 3D “pixels”
Inner sectors were instrumented in 2019
Gating Grid concept:
Designed to reduce Ion Back Flow (IBF) from the amplification stage, and respective space charge of positive ions in the TPC volume (gate open by trigger only for the time needed to collect all electrons – several ms only)

## Slide 40: STAR TPC, legacy pictures
STAR event display, {r,f} view
STAR event display, side view

## Slide 41: “New generation” TPCs: attack IBF problem
MWPC-based TPC drawbacks
No other means to suppress IBF other than gating grid
This in particular excludes TPC usage in a continuous readout mode (and in a high luminosity environment)
Solution: replace MWPC amplification stage
by either quadruple GEM (ALICE upgrade &
sPHENIX TPC) or a GEM+mMegas hybrid; carefully tune gas mixture, GEM foil configuration & HV
dE/dx resolution vs IBF
IBF vs uMegas mesh voltage
sPHENIX TPC: ALICE approach

## Slide 42: Large (here 2D) planar detectors: GEM
GEM: Gas Electron Multiplier
Primary ionization in a short (few mm) drift gap
Multi-stage (3-5 50mm thick foils) amplification in a high field
Direct coupling to readout strips (or pads)
EIC Detector R&D program
U-V strips charge sharing

## Slide 43: Large (1D) planar detectors: GEM
via
  Low mass, stretched carbon fiber frames
  High spatial resolution & low channel count zigzag charge sharing readout
EIC Detector R&D Program

## Slide 44: Large planar detectors: mMegas
ATLAS New Small Wheel
4 Types of detectors => 4 constructions sites
Technology: 1200 m2 of resistive Micromegas
2M channels
Primary ionization in a short (few mm) drift gap
Single-stage amplification in a high field 128mm gap
Capacitive coupling to readout strips through the resistive layer

## Slide 45: Medium-size cylindrical tracker: mMegas
CLAS12 vertex tracker upgrade
Silicon
MM
TOF
Neutron Det.
Same technology: 4 m² of mMegas detectors
Light-Weight Detectors (~0.5% of X0 per layer)
Limited space (~10 cm for 6 layers)
High magnetic field (5T)
Variable geometry (6 Layers with different R)
High enough spatial resolution (~100mm)

## Slide 46: mRWELL trackers
µRWELL with 2D X-Y readout
µRWELL in FNAL Test Beam
µRWELL
Modern technology, competing with GEM & mMegas:
  Simple, low mass, no stretching, low cost
  1D & 2D configurations, flat & cylindrical
Primary ionization in a short (few mm) drift gap
Single-stage amplification in a high field 50mm gap (foil)
Capacitive coupling to readout strips through the resistive layer

## Slide 47
End of day one!