## Slide 1: EICUG Polarimetry WG – Inaugural Meeting
November 30, 2018
Morning
JLEIC Machine parameters critical for polarimetry,
Vasiliy Morozov (JLAB)
Requirements for Lepton and Hadron Polarimetry,
Christoph Montag (BNL)
Requirements for Lepton and Hadron Polarimetry,
Elke Aschenauer (BNL)
Electron Polarimetry Today,
Dave Gaskell (JLAB)
Fast detectors for electron detection for Compton polarimetry,
Alexandre Camsonne (JLAB)
Discussion on Electron Polarimetry at an EIC
Hadron Polarimetry Today and Improvements for EIC,
Oleg Eyser (BNL)
A Polarimeter for Light Ions,
Nigel Buttimore (Trinity College, Dublin)
Needed Improvements to the H-Jet for an EIC,
Andrei Poblaguev (BNL)
Needed improvements for Hadron Polarimeters,
Charles Hyde (Old Dominion University)
Alternative Hadron Polarimeter Concept,
William Schmidke (BNL)
Discussion on Hadron Polarimetry
Afternoon
https://indico.bnl.gov/event/5376/
Primary meeting goal: Prioritized list of R&D projects, both experiment and simulation

## Slide 2: Accelerator Polarimetry Requirements
Themes common to both JLEIC and eRHIC
Multiple polarimeters helpful for beam setup.
At JLEIC, measuring vertical e- pol. in arcs useful, ion polarimeters at
source, after linac and in booster.
At eRHIC, RCS likely needs additional polarimetry
polarization lifetimes decreases with lepton beam energy.
18 GeV@eRHIC: 0.4 h 12 GeV@JLEIC: 0.1h
Polarimeter locations more-or-less identified in both designs in rings.
eRHIC-specific issues:
Rapid Cycling Synchrotron (RCS) requires special electron polarimeter
JLEIC-specific issues:
Ions not always vertically polarized in ring – spin precesses through ring.
Ion polarimeters only sensitive to transverse polarization –> need to
carefully constrain spin direction

## Slide 3: Accelerator Related R&D
Understand origins of difference in polarization for colliding/non-colliding bunches at HERA
Study the degree of expected polarization profiles at EIC
Quantify the degree to which bunch-by-bunch and profile-dependent variations of polarization impact physics observables

## Slide 4: Electron Polarimetry
Method:
Electron polarimetry via Compton should be able to meet precision requirements for EIC (1% or better)
 JLEIC Compton design focuses on detection of scattered electron, long. polarization near IP. Longitudinal measurements have regularly yielded high precision
eRHIC will measure transverse polarization at dedicated IP. Transverse Compton polarimeters not as common, have not achieved high precision
Issues:
Backgrounds from Bremsstrahlung, synchrotron, and beam halo can be significant
Percent-level precision has been achieved for longitudinal Compton polarimetry, but not yet for transverse
Bunch-by-bunch polarization measurements may be challenging

## Slide 5: Electron Polarimetry R&D
Simulation/software
Further studies of synchrotron and other backgrounds
  Benchmark GEANT4 simulations
  Mitigation studies
High precision transverse Compton polarimetry
  Detailed simulations with realistic analysis/polarization extraction
Simultaneous measurement of longitudinal/transverse polarization
  Position sensitive detector ++
Hardware/detector
Fast electron detectors - proof-of-principle
Fabry-Perot cavity with mode-locked (pulsed) laser

## Slide 6: Hadron Polarimetry
Hadron polarimetry at EIC will build on experience gained at RHIC
H-Jet provides absolute polarization measurements, but requires a long time (hours)
p-Carbon polarimeter provides fast measurements – must be calibrated by H-Jet.
  Provides information on polarization profile, lifetime and bunch-by-bunch polarization
Identification of recoiling proton (or carbon) uses correlation between time and signal size
Short bunch spacing at EIC will make this basically impossible without further information
– “prompt” background from different bunch (n+1) in particular a problem
Several ideas discussed to address this issue (improved timing/energy resolution, 2nd layer for vetoing background from high energy particles)
Polarized Deuterium Beam Measurement: Analyzing power for Deuterium only 10% of proton one

## Slide 7: Hadron Polarimetry R&D
Theory
more theory calculation for He-3 and D
  can one recover the full analyzing power if one detects all decay products
2. need help with analyzing powers for alternative polarization measurement ideas.
Simulation/analysis
Develop a Monte Carlo of the RHIC polarimeter setup
  Can one reproduce the pC and pp ToF – ADC spectra and such understand the origin of the “prompts”?
Extend these simulations to polarized deuterium and He-3 beams
Analyze the RHIC data to understand the bunch polarization as function of different beam parameters, i.e. emittance. Verify these dependencies can be absolutely reproduced with beam simulations.

## Slide 8: Hadron Polarimetry R&D
Hardware/detector
In the upcoming polarized pp run in 2021 introduce a 2nd layer of Silicon to investigate the prompts can be vetoed by requiring no punch through
Investigate an alternative option for the carbon fiber targets
Develop silicon detectors with higher timing and energy resolution
Is there an alternative detector technology to the Si?
Investigate whether a technical solution for the alternative polarization methods is feasible
Investigate a technical solution for the He-3 and deuterium polarimeters