## Slide 1: sPHENIX Director’s Review Tracking Simulations
sPHENIX Director's Review
April 9-11, 2019
BNL
April 9-11, 2019
Tony Frawley, Florida State University

## Slide 2: Functions of the Tracker
sPHENIX Director's Review
Momentum measurement
Provided by TPC measurement of sagitta
Need precise interaction vertex for best accuracy
obtained by adding MVTX hits
Pileup event disambiguation
provided by 2 hermetic layers of INTT silicon strips (can resolve 1 beam crossing)
Precise track vertex for DCA measurement
Provided by MVTX pixels
April 9-11, 2019
MVTX
INTT

## Slide 3: Tracking Simulations
sPHENIX Director's Review
Tracker configuration now finalized
Full Geant IV model of the tracker components
Conversion of G4 hits to readout values
Including all effects that contribute to resolution
Apply thresholds, dynamic range, digitization
Clustering
Tracking
Evaluation of performance using truth information
Realistic occupancy due to charge storage in TPC and MVTX
Event pileup from random min-bias collisions at specified collision rate
April 9-11, 2019

## Slide 4: Tracking Simulations
sPHENIX Director's Review
April 9-11, 2019
b-jet in sPHENIX
HF event in MVTX
HF event in MVTX + INTT

## Slide 5: TPC simulations
sPHENIX Director's Review
Single gas volume
Charge diffusion parameterized vs drift length
Space charge distortion correction uncertainty added
Readout:
GEM charge dispersion in rφ added
Charge distributed between pads using model of zigzag pads
SAMPA chip shaping folded with drift-diffusion time distribution
Z bins from realistic ADC binning of time distribution
Produces realistic occupancy effects in TPC
April 9-11, 2019

## Slide 6: Track Reconstruction
sPHENIX Director's Review
All subsystems provide a standard cluster format
  Weighted mean + full covariance matrix
  Clustering optimized for high occupancy
Fast initial Z-Vertexing based on triplet tracks in inner tracking system
- Developed, not implemented yet
Seeding based on a Hough transformation of a subset of TPC layers
  Seeding iterations
    progressively looser seed requirements - redundancy for high occupancy
    4 hits out of 7 layers
    6 hits out of 12 layers
Trajectory building and Track fitting based on state of the art Kalman filter
  Derived from Open Source GENFIT package
3D Track Fitting using RAVE package
Optional track refit including reconstructed vertex
Useful for prompt signals such as Upsilons
April 9-11, 2019

## Slide 7: Collaborators (current and recent)
sPHENIX Director's Review
Anthony Frawley, Florida State U. (simulations, tracking, coordination)
Jin Huang, BNL (consultant, sPHENIX simulations oversight)
Sanghoon Lim, LANL (vertexing)
Sookhyun Lee, Iowa State University (vertex finding, tracking)
Darren McGlinchey, LANL (MVTX simulations, tracking)
Yasser Corales, LANL (MVTX simulations)
Takahito Todoroki, RIKEN (INTT simulations)
Carlos Perez, SUNY SB (TPC simulations)
Chris Pinkenburg, BNL (simulations, consultant)
Christof Roland, MIT (Tracking)
Veronica Canoa Roman, SUNY SB (TPC simulations)
Sourav Tarafdar, Vanderbilt University (QA)
Yorito Yamaguchi, RBRC (pileup studies)
Haiwang Yu, BNL (Tracking)
April 9-11, 2019

## Slide 8: Status and Highlights - I
sPHENIX Director's Review
Effort in the last 12 months to enhance realism in the simulations.
TPC modeled as a single gas volume, with realistic transport of electrons to readout plane.
Implemented ADC readout and digitization for the TPC that includes all details as planned for the real detector, including noise.
Implemented realistic readout and digitization for INTT and MVTX.
The tracking detector model fully reflects the configuration agreed on following the tracking task force study.
April 9-11, 2019

## Slide 9: Status and Highlights - II
sPHENIX Director's Review
Careful study of out-of-time track rejection using matching to the INTT+MVTX
Critical for tracking in p+p running
Requiring 2 MVTX and 1 INTT hit per track provides rejection of 44,000 for out-of-time (event pileup) tracks
More than good enough
April 9-11, 2019

## Slide 10: Status and Highlights - III
sPHENIX Director's Review
Just completed a major upgrade of the tracking simulation and reconstruction software.
Simulations code modularized, and separated by subsystem.
More accessible to maintenance by subsystem experts
Tracking code modularized by function.
Facilitates adding new vertexing, seeding, track propagation and track fitting methods.
New hit and cluster storage containers and association maps implemented.
Easier and faster association to geometry details and to truth information.
Resulted in factor of two reduction in memory use.
This positions us for a big push in the next year to greatly improve code speed and memory use.
April 9-11, 2019

## Slide 11: Tracking Efficiency
sPHENIX Director's Review
Track reconstruction efficiency in various occupancy scenarios.
Uses 100 pions embedded in Hijing events with different event pileup rates.
Efficiency in worst case occupancy is workable. Most likely can be improved with
Better clustering
More iterations
April 9-11, 2019

## Slide 12: Momentum Resolution
sPHENIX Director's Review
Comparison of pT resolution in low and high multiplicity events.
Some deterioration of pT resolution in worst case occupancy scenario.
April 9-11, 2019

## Slide 13: DCA Resolution
sPHENIX Director's Review
Comparison of DCA resolution in the bend direction for low and worst case occupancy cases.
Very robust against occupancy effects.
April 9-11, 2019

## Slide 14: Upsilon Mass Resolution
sPHENIX Director's Review
Embedded Υ(1S) mass spectrum
Low occupancy events: 78 MeV
AuAu Central + 200 kHz pileup: 129 MeV
Low occupancy events (100 pions/event)
AuAu central + pileup from 200 kHz collision rate
April 9-11, 2019

## Slide 15: Issues and Concerns
sPHENIX Director's Review
Mar 6-8, 2018
In worst case occupancy events (central event with 200 kHz rate pileup)
Tracking efficiency remains acceptable
But momentum resolution deteriorates somewhat, pushes Upsilon mass resolution beyond our goal of 100 MeV
Possible solutions:
Improvements to clustering algorithm in high occupancy
There is still room for improvement in determining CG of TPC clusters
Improving usable luminosity while reducing total luminosity
Currently, only about 1/3 of total luminosity is in our tracking acceptance
Discussing crossing angle and other options with CAD

## Slide 16: Summary
sPHENIX Director's Review
Implement newly developed code to do initial vertex finding using MVTX + INTT
Implement scheme to track to multiple vertices/event using these seed vertices
Current tracking works, but is too slow and memory intensive
Investigate new track seeding algorithms
Investigate new track fitting algorithms
Example ACTS (open source ATLAS tracking package)
Reducing speed and memory consumption to levels needed for data reconstruction is feasible, and is a high priority for the near future.
April 9-11, 2019

## Slide 17: Back Up
sPHENIX Director's Review
April 9-11, 2019