## Slide 1
Rachid Nouicer, BNL
April 9-11, 2019
sPHENIX Director’s Review
WBS: 3.01
sPHENIX Intermediate Tracker (INTT) Overview/Management

## Slide 2
Strong Commitments of RIKEN/RBRC for INTT
INTT funded by RIKEN/RBRC

## Slide 3: 3.01 The sPHENIX INTT
- INTT has a unique role in the sPHENIX tracking system being the only detector with sufficiently fast time response to be able to associate individual tracks and events.
Mass Resolution
Y(1S,2S,3S)  e+e-
Event generator (simulated data): event pile up
TPC
Tracking System: MVTX+INTT+TPC
iHCAL
- Charged Tracking in sPHENIX:
MVTX provides vertexing
TPC provides p-resolution
INTT provides matching
MVTX
INTT: Two Silicon Strip Barrels
EMCAL

## Slide 4: INTT Technical Overview: Two Barrels Specification
Two Barrels
Barrel | Center of Sensor Tangent Radius (mm) | Pseudo rapidity | QTY of Ladders | Angle (deg) | Coverage (PHI) (%) | Overlap (%) | Clearance (mm) | Chip Power Dissipation (W) | Stave Rad Length (%) | Barrel Rad Length (%)
1 | - | - | 24 | - | 100 | 1.8 | 2.0 | 79.88 | 0.50 | 2.16
1a (Inner) | 71.88 | 1.37 | 12 | 0 | 52.7 | 0 | 0.6 | 39.94 | 0.25 | 1.08
1b (Outer) | 77.32 | 1.31 | 12 | 0 | 49.4 | 0 | 3.4 | 39.94 | 0.25 | 1.08
2 | - | - | 32 | - | 100 | 1.8 | 2.0 | 106.50 | 0.50 | 2.16
2a (Inner) | 96.80 | 1.12 | 16 | 0 | 52.4 | 0 | 0.6 | 53.25 | 0.25 | 1.08
2b (Outer) | 102.62 | 1.07 | 16 | 0 | 49.4 | 0 | 2.8 | 53.25 | 0.25 | 1.08
Total | - | - | 56 | - | - | - | 11.88 | 186.38 | 1.00 | 4.32

## Slide 5: INTT Technical Overview – Ladder Components and Assembly
Chips (FVTX)
HDI
(High Density Interconnect)
CFC Stave
(M55J)
Stave Endcap
(Carbon PEEK)
Silicon Sensors
Cooling Barb
(304 Stainless Steel)
For Details See INTT Talks: Ladder/Det. Assembly
by Connor Miraval
Ladder = 1 CFC Stave + 2 HDIs + 52 Chips + 4 Silicon Sensors
Cross Section of Ladder
CFC-Stave

## Slide 6: INTT Technical Overview
For Details See INTT Talks: 1) Electronics
by Itaru’s Nakagaya
2) Ladder/Det. Assembly
by Connor Miraval
3) Mechanics/Integration & Infrastructure
By Dan Cacace
2019 Beam Test
Final Design and Safety Review (ladder)
Ladder = 1 CFC-Stave + 2 HDIs + 4 Silicon sensors + 52 chips

## Slide 7: INTT Technical Overview (Components)
FVTX Chips Packaging 2018
ROC Available (24): need 12 + 4
Silicon sensors Preproduction: February 2019
HDI Preproduction: March 2019
Prototype Bus Extender: 2019

## Slide 8: INTT Technical Overview: Silicon Sensors and Chip
Type A: Single sensor = 8 x 2 cells
Type B: single sensor = 5 x 2 cells
Type A
Type B
Silicon Strip Sensor:
Very fine pitch (9.984/128 = 78 μm in f), for good spatial resolution
High efficiency (>99%) and low noise for excellent tracking
Excellent time resolution [-20 ns, 60 ns], for no pileup
Thin-sensor/low mass, 320 μm (~0.34% X0), for less multiple scattering
FVTX Chip:
p-implant on n-bulk, Ac-coupled, 1.5 MΩ polysilicon resistors
Depletion voltage < 100V, Resistivity 3 to 5 kΩ-cm
Single cell geometry (active region):
128 strips (better resolution in f-direction)
Strip width = 78 mm
f-length = 78 mm x 128 strips x 2 cells =19.968 mm
z-length = A: 16 mmx 8=128 mm (B: 20 mm x5=100 mm)
Photo FVTX chip

## Slide 9: INTT Scope and Deliverables By RIKEN/RBRC
3.01.01: INTT Construction
Ladder (Silicon Sensors + HDI + 52 Chips) Assembly: 100 Ladders
Endcap Rings (Carbon-Peek): 6 Support Structures to Build Barrels
Support Rails (Carbon-Fiber-Composite): 4 Support Rails Carrying Barrels
Barrels Assembly: 2 Barrels (4 sub-layers)
INTT Assembly: 2 Barrels + Extender/Conversion cables + ROCs + Survey
3.01.02: INTT Electronics
Design and Fabrication of Silicon Strip Sensors (Hamamatsu co.) : 400 Silicon Sensors
Testing and Evaluation of Silicon Sensors, and Implementation in Database
High Density Interconnect (HDI) Design and Fabrication (Yamashita co.) : 200 HDI Cables
Extender Cables (TAIYO-KOSAKUSHO co. ) and Conversion Cables: 200 Cables
FPHX Chips = 5,200 Chips
3.01.03: INTT Integration in sPHENIX
Temperature/Humidity Monitoring, Low and High Power Supplies, Optical Fibers, and Commissioning
Barrels
3 Half Ladders
Front View

## Slide 10: INTT Collaborators
Edward O’Brien (BNL)
Institutions:
BNL, RIKEN, RBRC, Purdue University,
Nara Woman’s University (NWU), and
National Central University (NCU)
Team:
Professors: Takashi Hachiya, Wei Xie, Chia-Ming Kuo
Physicists: Rachid Nouicer, Itaru Nakagawa, Yasuyuki Akiba, Jin Huang, John Haggerty, Martin Purschke, Eric Mannel
Physics Associates: Rob Pisani, Takahito Todoroki
Chief Engineer: Russ Feder
Mechanical Engineers:
Dan Cacace, Connor Miraval
Mechanical Technicians:
Mike Lenz, Bill Lenz
Designers: Rich Ruggiero
Electrical Engineer: Steve Boose
Electrical Technician: Sal Polizzo, Donald Pinelli
Yasuyuki Akiba (RIKEN/RBRC)
Consultant
Dan Cacace (BNL)
L3 Manager
Connor Miraval (BNL)
L3 Manager
Takashi Hachiya (NWU)
L3 Manager
Rachid Noicer (BNL)
Itaru Nakagawa (RIKEN)
L2 Manager
Wei Xie (Purdue U.)
L3 Manager
Chia-Ming Kuo (NCU)
L3 Manager
Ayaka Suzuki
+Undergrads
L4 Manager
Mechanical Design
Assembly
Bus Extender
Testing, Monitoring
Silicon Testing, Database
L1 Manager

## Slide 11: INTT Schedule Drivers
Schedule is being driven by the funds RBRC/RIKEN (Japanese fiscal year) has available for purchasing the INTT components:
  Silicon Sensors, HDIs, Extender Cables, and CFC Staves
Secondary driver, time of processing procurements (RIKEN/Japan) for the INTT components.
Need additional BNL engineering and technician FTEs to support delivery of INTT components which will be paid for by RIKEN/RBRC:
  ROC (need electronic engineer, more details in Itaru’s Nakagaya talk):
    Reuse of 5 years of operation, some broken function in some ROCs, many components are discontinued, original FPGA coder left the field long time ago.

## Slide 12: INTT Cost Drivers: RIKEN Funded

## Slide 13: INTT Basis of Estimate & Resource-Loaded Schedule
One file per L3 (5 for 03.01.02 total for INTT)
One Summary/Details
Consistent w/ P6

## Slide 14: INTT Status and Highlights
Highlights from March 2018: INTT Telescope (Prototype Silicon Modules) Beam Test at FNAL Proton Beam 120 GeV
Successful Beam Test
Status: June 2019: 120 GeV Proton beam test at FNAL using Pre-production silicon modules
Full readout chain (including prototypes bus extender and conversion cable)
More detail study of the detector performance and tracking resolution.
Silicon Module
Bus extender
Conversion Cable

## Slide 15: INTT Status and Highlights
Highlights from March 2018: INTT Telescope (Prototype Silicon Modules) Beam Test at FNAL Proton Beam 120 GeV
Successful Beam Test
Status: June 2019: 120 GeV Proton beam test at FNAL using Pre-production silicon modules
Full readout chain (including prototypes bus extender and conversion cable)
More detail study of the detector performance and tracking resolution.
Silicon Module
Bus extender
Conversion Cable
Status: 2018: - Prototype INTT components- silicon sensors + chips +HDI cable Successful tests (source test + beam test)
Plan:
2019: - Preproduction of INTT components (beam test)
 Final Design and Safety Review Summer 2020: - Mass production of electronics components, and detector assembly.

## Slide 16: INTT Issues and Concerns
There is a need for students/Post-docs for ladder and barrel tests, evaluation and data entry in the database during assembly.

## Slide 17: Summary
• The INTT has a unique role in the sPHENIX tracking system being the only detector with
sufficiently fast time response to be able to associate individual tracks and events.
• The INTT has essential roles in the aspects of tracking pattern recognition, and in matching TPC tracks to MVTX hits.
• Excellent progress in many fronts:
  - Prototype silicon sensors and HDI: design and fabrication achieved successfully (beam test)
  - Preproduction underway and preparation for next beam test June 2019.
• INTT conceptual design meet the scientific objectives, near completion, and achieved in coordination within the sPHENIX integration task force (Office System Integration).
• RIKEN has committed to delivering the INTT.

## Slide 18: Back Up

## Slide 19
Outline
INTT Two Barrels Layout Active Area: Simulation
Simulation set up
1.4T magnetic field
100 pi+ per event
Most recent INTT ladder configuration (sensor position)
100% phi coverage: only silicon active area shown
INTT geometry update in Simulation
Stave: done
Carbon-Peek Endcap Rings: done
Rails: done
HDI outside Endcap Rings: in progress
Bus Extender: in progress
Notes: 19
Le titre de l’expose est: