## Slide 1: Tracker for the mu2e Experiment at Fermilab
Aseet Mukherjee Bob Wagner

## Slide 2: Why µe?
See Rob Kutschke’s talk for more
Muons captured on a target to form a muonic atom
40% undergo the normal decay while in orbit (DIO)
  LOTS of electrons at … with a small tail to higher
60% capture on the nucleus, causing a nuclear breakup
  p, n,  produced in the breakup
We are looking for a small fraction of neutrinos-less conversions …
Signature: Mono-energetic electrons
  105MeV, depending slightly on nucleus
Rate in standard model is very low (BR ~10-54)
A signal indicates physics beyond the standard model

## Slide 3: Why mu2e?
Selection Window
at detector
Far from the first such search! So how do we do better?
More intense beam
Pulsed beam with excellent extinction (fraction of protons out of time)
Expect 104× better than previous limit
Distributions simplified for illustration

## Slide 4: Beam Line
Production Solenoid
Production Target
Transport Solenoid
Detector Solenoid
Collimators
Proton Beam
Uniform 1T field
Graded field,
2T  1T

## Slide 5: Detector Solenoid
Incoming µ-
MeV
Stopping Target
Tracker
Calorimeter
Cosmic Ray Veto (CRV, not shown) surrounds detector solenoid and much of the transport solenoid.

## Slide 6: Importance of Resolution
Steeply falling DIO background
Signal
Other Backgrounds ~flat
Reconstructed Momentum
The narrower the signal window, the better the signal to background

## Slide 7: Why annular?
Reconstructable
No Hits
Minimum mass at r<380mm  Vacuum
Some hits but limited acceptance & reduced efficiency
r>700mm: Mass OK
Decay in Orbit (DIO)

## Slide 8: Tracker Design
No mass at r<380mm
  Ambient vacuum  Detector most handle ~15psi pressure differential
Very light active region, 400<r<700mm Partial coverage for 380<r<400mm
Light, inactive region for 700<r<720mm to reduce hits from photon conversion and stopped neutrons decaying
Move mass out to r>720mm
Selected Solution: Straw tracker
  18 Stations distributed along beam direction Optimization of number of stations in progress
  A Station has 2 Planes.
  A Plane has Panels with varying rotation for stereo reconstruction
  Each Panel has 96 Straws of varying length

## Slide 9: Straw
5mm OD, 15µm thick metalized Mylar tube as cathode
  Metalized on inner & outer surface
  400Å Aluminum outer surface
  400Å Aluminum + 200Å Gold inner surface
  25µm gold-plated tungsten wire as anode
Notes: Fixed brass pin dimensions (previously labeled as 2mm OD)

## Slide 10: Leak Tests
Conventional methods
In air, straw at 15psig
  Test time: several days
In vacuum, straw at 15psia
  Measures exactly what we want
  Test time >1day
  Test setup too expensive to make many
Can do large batches but lose sensitivity
Using CO2 sensor
CO2 leaks through plastic faster than most gases
Fill straw with Ar-CO2 (80:20), purge test vesel with N2, and monitor CO2 level
Test time to required sensitivity: <1hour
Test setup cost: <$100, can have many setups
Needs to be calibrated against vacuum method

## Slide 11: CO2 Leak Test
Copper pipe for straw
Another in back (not seen) for circulation
Container for CO2 sensor and circulation fan

## Slide 12: CO2 Leak Tests
Sample results for straws with and without being pressurized
Leak rates well below limit of 3.5e-4 ccm

## Slide 13: Straw Creep
Like all plastics, the Mylar straws creep: loose tension over time
Our best fit, extrapolated to several years, shows detector is fine (over 200g) indefinitely if we install at 700g tension
Fit:

## Slide 14: Straw Creep
Extrapolation from <1year to many years is tricky
Alternative fits indicate a lifetime of >6years
Fine for mu2e … maybe not mu2e-II
Alternative: Add a stiffening carbon fiber line radially across the panel
Fit:

## Slide 15: Panel
All electronics are in drift gas to simplify cooling
Preamps to be tested for gas contamination, and may need coating
Digitizers are in the exhaust gas  don’t need to worry about outgassing
Digitizer region can be accessed while operating straws (not in the vacuum, of course)

## Slide 16: Gas Manifold
Gas tight while allowing access to electronics
Three separate covers, one each for preamps and one for digitizers

## Slide 17: Gas Manifold
Prototype had <0.24ccm leak rate
Small compared to allowed total of 7ccm
O-ring
Latch on this side (no room for screws)
Screws on this side
Aluminum plate for thermal and electrical conductivity
Composite Inner Ring
Stainless Steel Outer Ring
Brass Cover
Refrigerant

## Slide 18: Gas Manifold Inner Ring
96 straws/panel ×6 panels/plane × 36 planes  ~20K straws  40K precision holes
Alternative: Mold the holes in carbon fiber
Carbon Fiber
Stainless Steel
O-ring groove

## Slide 19: Plane
Self-supporting panels assemble into a plane

## Slide 20: Plane

## Slide 21: Plane
Switch to simpler representation

## Slide 22: Station
Two planes back-to-back

## Slide 23: Station
Optimal Stereo order still under study

## Slide 24: Tracker
18 stations tentative … optimal number being studied

## Slide 25: Tracker
18 stations + Support Structure

## Slide 26: Tracker
18 stations + Support Structure

## Slide 27: Tracker
18 stations + Support Structure
Support beams also serve as cable trays

## Slide 28: Front End Electronics
Commercial Analog ICs
FPGA
FPGA
ASIC (1)
Discrete (1)
FPGA
ADC
TDC
TDC
PCB transmission line
Preamp
Preamp
Readout Controller
DAQ
Straw
 & ∫
Baseline
Discrete
Output Control & Buffer
Alternate

## Slide 29: Time Division
Difference caused by noise and large pulses from 55Fe, while 90Sr pulses are close to what we expect.
Continuing to work on reducing noise to bring the two closer together
Use difference in signal arrival time at straw ends to estimate position along wire
Resolution much worse than stereo (<1mm)
Needed for stand-alone pattern recognition (not using calorimeter for timing)

## Slide 30: Mu2e Tracker & Project X
Mu2e-II: 10× rate increase
  3× instantaneous rate
    Affects performance directly (higher occupancy)
    Can study via simulations Already studied up to ×4 background rates as part of understanding mu2e robustness
  3× duty factor
    No direct affect on performance
    Concern is radiation damage (aging)
Mu2e-III: 100× rate increase
  Unlikely this tracker can survive

## Slide 31: Efficiency
Mu2e
Mu2e-II
<5% loss in efficiency

## Slide 32: Resolution
Mu2e-II No change in apparatus
Mu2e
Loose cuts … not resolution used for most analysis
Key point: No significant change

## Slide 33: Rebuild
Thinner walls
  8µm instead of 15µm
  Less scattering
  Fewer conversions & δ-rays
Run sub-atmospheric
  8µm unsafe for 15psid
  Fine for 8psid
Side benefit: shorter ion drift time
  Less space charge
Cannot operate at nominal gas density in air
Harder to test
But … by then we’ll have more experience

## Slide 34: Summary
Mu2e has a tracker design well suited for operation starting ~2019
For mu2e-II, the detector is expected to continue to operate adequately, but rebuilding with thinner straws may be better
Mu2e-III will require an entirely different design