## Slide 1
Magnetic Fields: Hazards and Effects on Human Health
M Buzio
07.06.2013
1

## Slide 2: Overview
Contents: subset of a safety training course held at CERN since 2010 to alert all categories of personnel about the risks inherent in working close to strong magnetic field.
Technical hazards Indirect, linked to materials and equipment
Health hazards Interaction between magnetic field and human health

## Slide 3
Part I - Technical hazards

## Slide 4
Projectile effect – what can happen ?

## Slide 5
Relatively common accidents in the MRI (Magnetic Resonance Imaging) field.
One fatality on record (O2 bottle)
Worst case at CERN: LEP’s L3 0.5 T magnet (currently in ALICE) none injured.
Collision hazard examples

## Slide 6
Example: projectile effect in CERN’s CMS experiment
Peak force ≈ 50 kgf  0.5 m Kinetic energy ≈ 250 J Max. speed ≈ 70 m/s
100 g magnetic steel screwdriver (μr = 500)
max. BdB/dz ≈ 3 T2/m
Courtesy B. Dalena in L.P. Sun, LHC PN 426
Skull fracture energy  50 J

## Slide 7
Electronic equipment tolerance in a magnetic field
J. Hourtoule, “Magnetic compatibility of standard components for electrical installations”, Fusion Engineering & Design, 2005
Examples of results from:
ITER component tests
tests of tilt sensors (error: ~1 mrad) and angular encoders (OK) in LHC dipoles up to 9 T

## Slide 8
Vulnerability of magnetic stripe cards
Magnetic stripe cards come in two basic varieties (as per ISO 7810-7813)
Low-Coercivity (300 Oe) Fe2O3 stripe, usually light-brown: shorter lifespan, frequent rewrites, cheap writing device; e.g. membership cards, tickets, hotel cards …
High-Coercivity (2750 Oe) BaFe12O19 stripe, usually black: frequent usage e.g. access badges, ID cards, bank cards
 | Min. | Typ. | Max.
Coercivity [Oe] | 300 | 2750 | 4000
Full demagnetization [mT] | 30 | 275 | 400
Max. tolerable field [mT] | 3 | 27 | 40
2750
HiCo stripe
LoCo stripe
=1.4  10%
[Tm ]
H [Oe]
300

## Slide 9
Radioprotection instrumentation and magnetic fields
individual dosimeters = passive sensors → no problem
fixed induced activity monitors may be affected (e.g. CERN ATLAS) → calibrated in situ
portable survey meters, electronic dosimeters: impact of B varies by type → may fail or give inaccurate readings
CERN + Politecnico di Milano are developing field-compatible dosimeters ( 1 T for now) → 4 prototypes made

## Slide 10
Interference with welding process
plasma arc- or electron beam-based welding processes are sensitive to local and ambient magnetic field
lower-current methods (e.g. TIG) tend to be most sensitive
problems appear already between 1 and 4 mT: instability, “arc blow” (deflection), molten metal spray  arc welding impossible above 20 mT
example: moderate arc blow
(source www.twi.co.uk)

## Slide 11
Faulty current lead connection (1/2)
Accident occurred on a CERN SPS main dipole test bench in bldg. 867, during a 6kA rampup (2012)
6kA current leads
fluxmeter
MB dipole
6kA copper connection box

## Slide 12
Faulty current lead connection (2/2)
molten Cu
connection fault copper melts  circuit opens  electrical arc  explosion, flame
fastening bolts
just broken
broken since a long time (cause of the fault)

## Slide 13
Part II – Magnetic fields and human health
Etibar Elchiyev , “human magnet”

## Slide 14
How magnets affect human health: an old concern …
Lodestone (magnetite, Fe3O4) first documented to attract iron by Thales of Miletus (585 BC)
Many weird medical applications based on attraction/repulsion analogies thru the ages
Effective treatments: lodestone powder used as a styptic or laxative, or for surgical extraction of iron shards from the eyes
Dioscorides of Anazarbus, 40-90 AD
B ut of ye Load-stone that which draws iron easily is ye best, & of an azure-like colour & thick, but not too heavy. It hath a faculty of drawing out gross humors being given with melicrate ye weight of 3 Oboli.
They say that this hath a discerning faculty of a woman that is chaste & of her that plays ye adulteress with another man, for if any do set it secretly upon the beds for ye chaste woman, who loves her husband, she being overborne into sleep, with a certain natural faculty of ye stone both opens her hands towards her husband, and cleaves close to him; but the other being troubled in dreams with foul labours, falls out of ye bed.
Also when two men carry this, it freeth them from all strife, & it causeth concord, and being born on ye breast, it assuageth people.
Excerpt of “De Materia Medica” from: R.T. Gunther, The Greek Herbal of Dioscorides, 1934 (transl. by J. Goodyer, 1655)

## Slide 15
Can you eat (permanent) magnets ?
No particular harm from a single permanent magnet
Two or more may pinch the bowels obstruction, volvulus, necrosis, peritonitis
Surgery is needed, the outcome may be fatal
5 cases/y in the USA only  more and more frequent due to increasing popularity of rare-earth PM based toys

## Slide 16
… YES if you are a bovine
“cow magnets” trap tramp iron, barbed wire, nails etc.. and prevent the so-called hardware disease

## Slide 17
Magnetic field and human health
Magnetic therapy: many references online …
Most advertised effect is blood supply increase - is it true ?
use at your own risk … but what happens in reality ?
“When blood flows through this magnetic field, the blood cells spin then separate from each other giving each cell more surface area to carry much more oxygen and vital nutrients. The magnetic field also widens your blood vessels allowing more blood to flow through.
The second benefit comes from Germanium which emits negative ions (also known as "Air Vitamins") and Far Infra-Red Rays (also known as "Growth Rays")”

## Slide 18
Medical applications of magnetic fields
Established medical applications and therapies :
Magnetic imaging (e.g. monitoring magnetic nanoparticle markers to study motility in the digestive system)
Drug delivery (capsules operated magnetically) and targeting (drug associates with magnetic nanoparticles)
Device guidance (e.g. catheters for cardiac electrophysiology, capsule endoscopy)
Transcranial Magnetic Brain Stimulation (localized eddy currents to activate specific neuronal circuits)
Pulsed EMF for bone nonunions (fractures that do not heal): inductively generated E field in connective tissue has similar effects to mechanical stress  promotes bone cell growth

## Slide 19
Forces on magnetic tissues
Magnetite crystals in many animal and human tissues possible role as sensors (e.g. for homing)
Iron in human blood: 3 g (red cells) 1 g (ferritin) (typ. adult male values) isolated atoms, no ferromagnetic domains  small forces
T. Higashi et al., “Orientation of erythrocytes in a strong static magnetic field,” J. Blood 82, 1328 1993
small mechanical effects  no health hazard at CERN field levels
Haemoglobin contains 4 × Heme groups with Fe
r  1+3.5×10-6 (venous) , 1-6.6×10-7 (arterial)
Erythrocytes in a field orient with their disk plane parallel to the field (A) Apparently due to the shape (diamagnetic membrane)
B
Magnetite (Fe3O4) crystals in human cerebellum and magnetotactic bacteria

## Slide 20
Voltage across blood vessels
Conducting medium moving in a magnetic field  electric voltage
blood is an electrolyte moving in a field  charge separation (Hall effect)
Heart J. et al., Evaluation of blood flow velocity in the ascending aorta and main pulmonary artery of normal subjects by Doppler echocardiography, 1984
no voltage drop across nerves or muscle cells
no biological effects
v = flow speed (max  2-3 m/s in the ascending aorta)
B = magnetic field (worst case = horizontal)
E=v×B electric field
V=E induced voltage
(experimental: 40 mV @ 2.5 T)

## Slide 21
Slowing down the bloodstream
fluid elements see variable field vector  induced currents  magnetic friction
World Health Organization - Environmental Health Criteria 232, 2006
DW Chakeres, “Effect of static magnetic field exposure up to 8T on sequential human vital sign measurement”, J. Magn. Reson. Imaging, 2003
B
v
physiologic rise
+ 6%
slight increase of systolic pressure to compensate for viscous drag no change to diastolic pressure, heart rate, body temperature
pressure gradient p=vB2 flow slows down (1% @ 5T)  blood pressure increases (3% @ 8T)
v
v

## Slide 22
Other interaction mechanisms
very subtle effects, inconsistent experimental evidence
no reason to believe in a health hazard
Free radical chemistry Vast class of reactions involving highly reactive species with unpaired electrons as intermediate products. Well-known effect: rates of certain radical pair recombination reactions can be affected by magnetic fields up to 50%. However, no known biochemical reaction meets the necessary requisites (one exception observed in a type of photosynthetic bacteria)
Ion cyclotron resonance of enzymatic metal cofactors Inconclusive evidence
Magnetic field driven DNA damage investigated in vitro, on animal models and in humans: inconclusive evidence

## Slide 23
Safety of Magnetic Resonance Imaging
Large body of safety-related evidence from MRI community
0.5~3.0 T widespread, up to 7 T commercially available
400 M scans since 1985, 20 M scans/year (2.5% of population in industrialized countries)
no long term/delayed effects epidemiologically observed
patient/occupational exposure deemed safe up to 8 T (US FDA)
full-body MRI trials @ 9.4 T ongoing 11.7 T foreseen end 2014
small vertebrates routinely tested up to 21 T
no harm observed or expected even at those levels

## Slide 24
Interaction of AC field with human tissues (1/2)
Basic mechanism: dB/dt in a conducting medium (1 m)  induced voltage  eddy currents  excitation of nerve cells (E  6 V/m) and muscles (V  40 mV)
Possible subjective reversible effects:
Dizziness/vertigo/headache: AC: typical thresholds is 2T/s for 1 s. DC mechanism: differential susceptibility of vestibular structures (46 T2/m  perceived 1% g)
Acidic/metallic taste: provoked presumably by electrolytic reactions due to eddy currents in the tongue, effect felt by 15% of test subjects @3T. Threshold dB/dt2.3 T/s (e.g. shaking head @ 0.6 Hz in a 0.5 T fringe field). May be contrasted by opening the mouth.
Magnetophosphenes: perceived flickering lights caused by electrical stimulation of the retina/optical nerve. (0.2 mV). Threshold dB/dt 2T/s for 50 mS (max. sensitivity 20 Hz)

## Slide 25
Interaction of AC field with human tissues (1/2)




OK
peripheral nerve stimulation
extra systoles, fibrillation
Eddy current density:
sensation threshold
fast movement inside experimental magnets
ATTENTION: moving in a DC field = standing in a AC field

## Slide 26
DC effects on implants
orthopedic implants plates, screws, rods
neural/bone
stimulators
infusion pumps
heart valves, pacemakers
hearing aids
IUD
eye implants
splinters
implants may malfunction or dislodge (especially if recent)
magnetic anus
needles
bullets, shrapnel
Co-Cr implants braces
jewelry, piercings

vascular clips (e.g. for aneurysms)


## Slide 27
Magnetic fields and pacemakers
Normal pacemaker function: sense electrical cardiac pulses, if needed provide pulses at an appropriate intensity and rate
A reed switch can be magnetically closed from outside to:
- disable pulse sensing and go into fixed-frequency mode (asynchronous pacing)
- go into programming mode
Uncontrolled switch behavior if B > 0.7 mT  competitive rhythms  discomfort, arrhythmia, death
AC fields may interfere with pulse detection/generation electronics
pacemakers, implantable defibrillators (ICD) etc
exposure to B > 0.5 mT is absolutely forbidden
reed switch
external field  magnetization and closure of contacts
field sources > 0.5 mT are ubiquitous (office magnets, electrical components, machinery ….)

## Slide 28
AC effects on implants
orthopedic implants: plates, screws, rods
heart valves
dental fillings
real concern only for fast-pulsed MRI fields generally safe at detector levels (4T)
also: high current  burns when touching conducting objects
large implants may give rise to heating and mechanical loads

## Slide 29
Summary: CERN rules
B  0.5 mT
B  10 mT
B  200 mT
heart implant (pacemaker, defibrillator)
general public (generic implants)
employees (all categories)
(need authorization)
B > 200 mT