## Slide 1: Polarized Proton Acceleration
Thomas Roser

## Slide 2: RHIC – First Polarized Hadron Collider
STAR
PHENIX
AGS
LINAC
BOOSTER
Pol. H- Source
Spin Rotators
(longitudinal polarization)
Siberian Snakes
200 MeV Polarimeter
Int. Polarimeter
pC Polarimeters
Absolute Polarimeter (H jet)
pC Polarimeter
10-25% Helical Partial Siberian Snake
5.9% Helical Partial
Siberian Snake
Spin Rotators (long. pol.)
Spin flipper
Siberian Snakes

## Slide 3: Spin Dynamics in Rings
Precession Equation in Laboratory Frame:
(Thomas [1927], Bargmann, Michel, Telegdi [1959])
dS/dt = - (e/gm) [(1+Gg)B + (1+G) BII ]  S
Lorentz Force equation:
dv/dt = - (e/gm) [ B ]  v
For pure vertical field: Spin rotates Gg times faster than motion, nsp = Gg
For spin manipulation: At low energy, use longitudinal fields At high energy, use transverse fields

## Slide 4: Spin tune and Depolarizing Resonances
Depolarizing resonance condition:
Number of spin rotations per turn = Number of spin kicks per turn
Spin resonance strength e = spin rotation per turn / 2p
Imperfection resonance (magnet errors and misalignments):
nsp = n
Intrinsic resonance (Vertical focusing fields):
nsp = Pn ± Qy
P : Superperiodicity [AGS: 12]
Qy : Betatron tune [AGS: 8.75]
Weak resonances: some depolarization
Strong resonances: partial or complete spin flip
Illustration by W.W. MacKay

## Slide 5: Spin Resonance Crossing
Froissart-Stora: [a: crossing speed]
Non-adiabatic (e2/a << 1)  Adiabatic (e2/a >> 1)
Pf /Pi = 1 Pf /Pi = - 1
e
K-Gg
e
Gg-K
e
Gg-K
e
K-Gg
Gg=K

## Slide 6: Spin Resonance Crossing
Non-adiabatic (e2/a << 1)
Pf /Pi = 1
Imperfection resonances:
  Correction dipoles (e small)
Intrinsic resonances:
  Pulsed quadrupoles (a large)
  Lattice modifications (e small)
Adiabatic (e2/a >> 1)
Pf /Pi = - 1
Imperfection resonances:
  Partial Siberian snake(s) (e large)
Intrinsic resonances:
  RF Dipole (e large)
  Strong partial Siberian snake(s) (e large)

## Slide 7: Siberian Snakes (Local Spin Rotators)
cos(180 nsp) = cos(d/2) · cos(180 Gg)
d  0  nsp  n
No imperfection resonances
Partial Siberian snake (AGS)
d = 180  nsp = ½
No imperfection resonances and
No Intrinsic resonances
Full Siberian Snake
(Ya.S. Derbenev and A.M. Kondratenko)
Two Siberian Snakes (RHIC):
nsp = (a2-a1)/180 (a1,2: angles between snake axis and beam direction)
Orthogonal snake axis: nsp = ½ and independent of beam emittance (SRM, S. Mane)

## Slide 8: Beam Polarization Near a Single Strong Intrinsic Resonance
Without snakes:
  Full spin flip, width ~ ± 5e
With snakes:
  Opening/closing of “spin cone”, nodes at ± 2
  Resonance crossing during acceleration is adiabatic with no polarization loss.
Resonance strength:
e = 0.3, 0.6
DGg

## Slide 9: BNL - High intensity polarized H- source
Developed as BNL, TRIUMF, KEK, INR collaboration
1.0 mA in 300 ms (1.8 x 1012 protons per pulse); 83% polarization
One source pulse is captured and accelerated for one bunch in RHIC
With inefficiencies and scraping to lower emittance and higher polarization bunch intensity in RHIC is 2.5 x 1011 polarized protons

## Slide 10: RHIC polarimetry
Absolute polarimeter (Pol. Hjet)
  Polarized hydrogen jet target allows for absolute beam polarization measurement:
  Jet target thickness of ~ 11012 cm-2 achieved
  Jet pol. 92  2 % measured with Breit-Rabi polarimeter
  Analyzing power AN ~ 0.044 (24 – 255 GeV)
Relative polarimeters (proton-carbon)
  Measure horizontal and vertical polarization profiles
  Fast measurements (~ 2 minutes)
Local IP polarimeters (forward neutron production)
  Significant asymmetry, calibrated with Hjet
  Used to adjust transverse polarization component to zero
(polarized)
proton beam
scattered
proton
polarized
proton target
or Carbon target
recoil proton
or Carbon

## Slide 11: Polarized proton acceleration in the AGS
During acceleration in AGS polarization flips 40 times
To avoid intrinsic resonances vertical betatron tune is placed very close to 8.98!
10%
5.9%
warm snake
cold snake
9.00
8.90
8.95
8.85
nsp and Qy
Gg
36+Qy
0+Qy
24-Qy
12+Qy
36-Qy
24+Qy
48-Qy

## Slide 12: Horizontal spin resonances
Partial snakes generate ~ 80 weak horizontal spin resonances
Use two fast quadrupoles, pulsing them 40 times during the half second ramp, to overcome all the horizontal resonances.
Reached 90% polarization transmission and 70% polarization at high intensity (2 x 1011 ppb)
N
N+1

## Slide 13: Spin Resonances in RHIC w/o Snakes
Intrinsic resonance strength for 10 p mm mrad particle
Imperfection resonance strength for corrected orbit (s = 0.15 mm)
Imperfection resonance strength for uncorrected orbit (s = 28 mm)

## Slide 14: Beam Polarization Near a Single Strong Intrinsic Resonance
Without snakes:
  Full spin flip, width ~ ± 5e
With snakes:
  Opening/closing of “spin cone”, nodes at ± 2
  Resonance crossing during acceleration is adiabatic with no polarization loss.
Resonance strength:
e = 0.3, 0.6
DGg

## Slide 15: Snake Resonances
Higher order resonance condition nsp + mQy = k (m, k = integer) driven by interaction of intrinsic resonance Gg + Qy = k with large spin rotations of dipoles and snakes.
No non-linear drive term necessary – combination of rotations is already non-linear.
“Snake resonance strength” depends on intrinsic resonance strength and therefore energy
For nsp=1/2+Dnsp  Qy = (2k-1)/2m-Dnsp/m
  First analytical solution of isolated resonance with snakes by S.R. Mane, NIM A 498 (2003) 1
single snake or two snakes with orbit errors
two snakes (m: odd)
RHIC tune working point
1/6
3/14
3/10
1/10
0.6
0.7
0.8
0.9
Stable polarization
on resonance, e = 0.3
1/4
3/8
1/6
1/10
1/8
1/12
3/10
0.6
0.7
0.8
0.9
Stable polarization
on resonance, e = 0.3
Qy
Qy

## Slide 16: Accelerating polarized protons in RHIC
Tune/coupling feedback on every ramp allows for:
  Acceleration between Qy = 0.667 and Qy = 0.7 with best polarization transmission
Slow orbit feedback on every ramp allows for:
  Smaller yrms (smaller imperfection resonance strength)
  Ramp reproducibility (have 24 h orbit variation)
Continuous fast 10 Hz orbit feedback eliminates effect of vibrating triplets
x,yrms ≈ 25 mm (!)
7/10
11/16
15/22
19/28
Snake resonances:
RHIC vertical tune during acceleration

## Slide 17: Polarized proton collisions at 255 GeV beam energy
Reached ~57% average polarization in 14 best stores
Little polarization loss on ramp and during store
Peak luminosity: 2.5 × 1032 cm-2 s-1
Requires excellent control of orbit, tune and coupling

## Slide 18: Depolarization and polarization profiles
Polarization loss from intrinsic resonances: polarization lost at edge of beam → polarization profile
  Impact of polarization profile on beam polarization at collisions Pcoll.:
  For RH ≈ RV ≈ R and small: P0 = <P> (1+R)2; Pcoll. ≈ <P> (1+½R)
  <P> measured with H jet polarimeter; R measured with pC polarimeter
  Typical values at RHIC 255 GeV: P0= 80%; <P>=57%, R=0.18, Pcoll.=62%
Note that P0, the polarization of the core particle, should be equal to the maximum achievable polarization.
Loss of average polarization is compatible with development of polarization profiles → all remaining polarization loss in AGS and RHIC is due to intrinsic resonances. (no coherent polarization loss)

## Slide 19: Summary
RHIC – the most flexible, high luminosity hadron collider
World’s only polarized proton collider
Amplitude dependent intrinsic depolarizing resonances will produce polarization profiles

## Slide 20: High brightness polarized 3He source
Optically pumped polarized 3He gas in high field EBIS solenoid
Feed into electron beam of EBIS for ionization to 3He2+ without depolarization: ~ 2 x 1011 polarized 3He2+ per bunch
3He+
Ionization to 3He++
Optical pumping in
High magnetic field
5.0 T
5.0 T
Up to 2×1011
3He++ ions/pulse
J. Maxwell, C. Epstein, R. Milner, MIT
J. Alessi, E. Beebe, A. Pikin, J. Ritter
A. Zelenski, BNL

## Slide 21: Polarized 3He in RHIC
Polarized 3He possible from new EBIS (J. Maxwell, Tue., 3:30 pm)
Max. energy in RHIC: 170 GeV/n
Depolarizing res. are stronger, however no depolarization expected with six snakes in RHIC
Accelerated unpolarized 3He from EBIS in AGS
Relative pol.: 3He-C CNI polarimeter; successfully tested with unpolarized 3He
Absolute pol.: 3He-3He CNI polarimeter using polarized 3He jet?
STAR
PHENIX
AGS
LINAC
BOOSTER
Pol. H- Source
Spin Rotators
(longitudinal polarization)
Siberian Snakes
He3-C Polarimeter
Abs. Pol. (He3 jet)
He3-C Polarimeter
20-50% Helical Partial Siberian Snake
15 % Helical Partial
Siberian Snake
Spin Rotators (long. pol.)
Spin flipper
Siberian Snakes
Pol. He-3 Source (EBIS)

## Slide 22: CeC for RHIC: High Luminosity with large Piwinski angle
  If head-on collisions are at beam-beam limit large Piwinski angle collisions with very small emittance can increase luminosity (Super B factory)
  Needs strong cooling: synchrotron rad. or CeC
  Separate bunches outside high luminosity region to avoid beam-beam from low luminosity region.
  Reducing beam emittance back to beam-beam limit
  Smaller emittance and shorter overlap region allows for smaller beta-star
  RHIC: overlap length ~ 10 cm, en (95%) ~ 1 p mm , b* ~ 10 cm  ~ x10 luminosity increase ( ~ 5 x1033 cm-2 s-1 !)
Head-on collisions
Collisions with crossing angle
Gun 1
Gun 2
Beam dump 1
Beam dump 2
ERL dual-way electron linac
2 Standard eRHIC modules
Modulator for Blue
Modulator for Yellow
FEL for Blue
FEL for Yellow
Kicker for Blue
Kicker for Yellow