## Slide 1
Single Photon Detection with the CLAS12 MAROC Readout
M. Contalbrigo – INFN Ferrara
EIC PID Workshop
9th July 2019, Stony Brook
Notes: Vanno messi studi innovativi e pubblicazioni

## Slide 2
2
Contalbrigo M.
Cherenkov angle (mrad)
7 Gev/c
6 Gev/c
8 Gev/c
p
k
INSTITUTIONS
INFN (Italy) Bari, Ferrara, Genova, L.Frascati, Roma/ISS
Jefferson Lab (Newport News, USA)
Argonne National Lab (Argonne, USA)
Duquesne University (Pittsburgh, USA)
George Washington University (USA)
Glasgow University (Glasgow, UK)
Kyungpook National University, (Daegu, Korea)
University of Connecticut (Storrs, USA)
UTFSM (Valparaiso, Chile)
p
Goal kaon-pion separation up to 8 GeV/c (prototype results):
EIC PID Workshop, 9th July 2019, Stony Brook
CLAS12 RICH
Notes: Vanno messi studi innovativi e pubblicazioni

## Slide 3
3
Photon Sensor: MA-PMT
MA-PMT
< 1 cm spatial resolution
< 1 ns time resolution
Compatible with the low torus fringe field
Average MA-PMT gain ~ 2.7 106
Corresponds to SPE ~ 400 fC
✓ 64 6x6 mm2 pixels cost effective device
✓ High sensitivity on VIS towards UV light
✓ Mature and reliable technology
✓ Large Area (5x5 cm2)
✓ High packing density (89 %)
✓ Fast response
✓ Expensive technology
~ 1 m2 active surface
EIC PID Workshop, 9th July 2019, Stony Brook
Notes: Dire meglio chi fa cosa.

## Slide 4
4
RICH Readout Electronics
Contalbrigo M.
Readout Electronics
Compact (matches sensor area)
Modular Front-End (Mechanical adapter, ASIC, FPGA)
Scalable fiber optic DAQ (TCP/IP or SSP)
Tessellated (common HV, LV and optical fiber)
HV
LV
Optical
Fiber
Tile power dissipation ~ 3.5 W
EIC PID Workshop, 9th July 2019, Stony Brook
Notes: Immagine electronic panel e scheda ottica

## Slide 5
5
Contalbrigo M.
Analog: Charge (1 fC)
Digital: Time (1 ns)
Trigger latency (8 ms)
Optical ethernet (2.5 Gbps)
Trigger: external
internal
self
On-board pulser
Contalbrigo M.
Charge
Test
Test pulse
Slow shaper
Slow shaper
Digital pulse
Linear response
Multiplexed readout
Limited holding time delays
Used for calibrations
RICH Front-End Electronics
EIC PID Workshop, 9th July 2019, Stony Brook
Notes: Aggiungere range di validita’ per fattorizzazione GPDs

## Slide 6
6
ADC Charge Measurement
Multiplexed readout up to 50 kHz
High resolution SPE spectrum
Viable for efficiency and gain monitors
In conjunction with timing, allows the
study of PMT discharge and cross-talk
Contalbrigo M.
Gain
EIC PID Workshop, 9th July 2019, Stony Brook
Notes: Dire meglio chi fa cosa.

## Slide 7
7
Contalbrigo M.
Analog: Charge (1 fC)
Digital: Time (1 ns)
Trigger latency (8 ms)
Optical ethernet (2.5 Gbps)
Trigger: external
internal
self
On-board pulser
Contalbrigo M.
Start time
Stop time
Test
Test pulse
Slow shaper
Slow shaper
Digital pulse
Digital response
Working in saturated regime
64 parallel channel readout
8 ms FIFO and delays
1 ns time resolution
RICH Front-End Electronics
EIC PID Workshop, 9th July 2019, Stony Brook
Notes: Aggiungere range di validita’ per fattorizzazione GPDs

## Slide 8
8
Contalbrigo M.
Optical ethernet (2.5 Gbps)
Small setups:
TCP/IP
Optical bridge / PC Desktop
Full experiment:
SSP protocol
SSP board / VSX crate
Next:
Ethernet Switches
Contalbrigo M.
RICH Back-End Electronics
EIC PID Workshop, 9th July 2019, Stony Brook
SSP board / VSX crate
2 RICH sectors ~ 50 k channels
Optical bridge / PC Desktop
Few FPGA units ~ 500 channels
Notes: Aggiungere range di validita’ per fattorizzazione GPDs

## Slide 9
9
TDC Digital Readout
Pedestal rms as seen by a test-point
As seen by RICH readout
During Acceptance tests
During Internal Pulser Calibration
Discrimination down to 20 fC, i.e. few % of SPE, allows sensor characterization
Contalbrigo M.
EIC PID Workshop, 9th July 2019, Stony Brook
Notes: Vedere presentazione Matteo

## Slide 10
10
Sensor
Electronic
Gain x 4
THR ~ 1/80 SPE
Signal
Cross-talk
Sampling time
Optical and Electronic Cross-talk
EIC PID Workshop, 9th July 2019, Stony Brook
Notes: Dire meglio chi fa cosa.

## Slide 11
Threshold
Eff. ratio
0 0.5 1 2 4
Eff. ratio
Maroc
Gain
Single-photon Discrimination
Relative efficiency map
Relative gain map
11
Contalbrigo M.
x ¼
x ½ MAROC
x 1 GAIN
x 2
x 4
EIC PID Workshop, 9th July 2019, Stony Brook
Notes: Mettere relazione con blue luminosity ?

## Slide 12
12
Single Photon Electron Timing
± 3ns
Typical time-walk with charge
Channel by channel time calibration: no offsets no walk
Laser
PMT
Time (ns)
Occupancy (#)
Contalbrigo M.
Time over threshold relates to charge
Duration [ns]
Tme [ns]
ADC amplitude [DAC]
Time over THR [ns]
1
Cherenkov
angle
EIC PID Workshop, 9th July 2019, Stony Brook
Notes: Fare una immagine del PMT sulla risoluzione

## Slide 13
13
RICH Installation
Contalbrigo M.
EIC PID Workshop, 9th July 2019, Stony Brook
Notes: Fare una immagine del PMT sulla risoluzione

## Slide 14
14
Electronic Pedestals
Contalbrigo M.
Pedestal rms [DAC unit]: without and with grounding grid
Jan 18
-- off
-- 1000 V
Mar 18
-- off
-- 1000 V
Pixel #
Pixel
Pixel #
Pixel #
Pixel
Pixel
EIC PID Workshop, 9th July 2019, Stony Brook
Notes: Fare una immagine del PMT sulla risoluzione

## Slide 15
15
Online Equalization
Contalbrigo M.
After equalization: distributions narrower and less sensitive to the common threshold
saturate signals and cross-talk well separate
EIC PID Workshop, 9th July 2019, Stony Brook
Notes: Fare una immagine del PMT sulla risoluzione

## Slide 16
16
Single Photon Time Analysis
Contalbrigo M.
Dark counts
Other bunch
CLAS12 Reconstructed Time and Position:
Photons are traced using information
from other CLAS12 detectors
RICH Measured Time and Position:
Defined by the RICH DAQ
Good photons should match
in time and space
Time analysis allows to
separate spurious signals
EIC PID Workshop, 9th July 2019, Stony Brook
Notes: Fare una immagine del PMT sulla risoluzione

## Slide 17
17
Time Calibration
Contalbrigo M.
Time vs Duration
after offset correction
Time vs Duration
after walk correction
Cross-talk
EIC PID Workshop, 9th July 2019, Stony Brook
Notes: Fare una immagine del PMT sulla risoluzione

## Slide 18
18
Single-photon Time Resolution
Contalbrigo M.
PMT 270
s = 0.58 ns
PMT 52
s = 0.66 ns
before time-walk correction
after time-walk correction
Single-photon time resolution better than the 1 ns specification
EIC PID Workshop, 9th July 2019, Stony Brook
Notes: Fare una immagine del PMT sulla risoluzione

## Slide 19
19
Cherenkov Photon Reconstruction
Contalbrigo M.
Example of signal hits identified by time consistent with CLAS12 reconstruction
Direct ring
Half recflected ring
EIC PID Workshop, 9th July 2019, Stony Brook
Notes: Fare una immagine del PMT sulla risoluzione

## Slide 20
20
Direct Cherenkov Photons
Contalbrigo M.
About 18 photons for a center
ring (no reflection accounted for)
Consistent with the TDR projection
Preliminary single photon Cherenkov
angle resolution = 6 mrad
Close to the 4.5 mrad goal despite
No alignment
Nominal (no real) optical property
Enough for a Cherenkov resolution at track level of s = s1/√N ~ 1.5 mrad
EIC PID Workshop, 9th July 2019, Stony Brook
Notes: Fare una immagine del PMT sulla risoluzione

## Slide 21
21
Hadron ID
Contalbrigo M.
Hadron separation, direct photon, RGA data
PRELIMINARY
EIC PID Workshop, 9th July 2019, Stony Brook
Notes: Fare una immagine del PMT sulla risoluzione

## Slide 22
22
Contalbrigo M.
Application: DIRC @ GlueX
H12700 +
CLAS12
readout
Hadron discrimination up to 4 GeV/c
EIC PID Workshop, 9th July 2019, Stony Brook
Notes: Dire meglio chi fa cosa.

## Slide 23
23
Contalbrigo M.
Application: Gas Cherenkov @ SOLID
Heavy Gas Cherenkov
Momentum range 2.5-7.6 GeV/c
Cover 8o to 15o angular range
Kaon contamination goal < 1%
Light Gas Cherenkov
Momentum range 1-5 GeV/c
Cover 7o to 15o angular range
Pion contamination goal < 1%
EIC PID Workshop, 9th July 2019, Stony Brook
H8500 + CLAS12 readout with analog SUM output
Notes: Dire meglio chi fa cosa.

## Slide 24
24
Application: Modular RICH @EIC
Contalbrigo M.
Aerogel
Fresnel lens
Sensor plane
Compact and modular RICH indipendent elements
H13700 to reach the 3 mm spatial resolution
See Xiaochun He talk
EIC PID Workshop, 9th July 2019, Stony Brook
Notes: Fare una immagine del PMT sulla risoluzione

## Slide 25
25
Application: H13700 Readout
Contalbrigo M.
EIC PID Workshop, 9th July 2019, Stony Brook
Derived from CLAS12 RICH readout:
1024 channels
MAROC 64 channel parallel digitalization
FPGA generated 1 ns timestamp
DAQ protocol based on VME/VSX SSP
Custom adapter boards
- Compact distribution
Use of existing MAROC boards
Light and gas tightness
Notes: Fare una immagine del PMT sulla risoluzione

## Slide 26
26
Application: SiPM Arrays
Contalbrigo M.
Pixel #
Pixel #
Peltier cell cooling
Down to -30o in N2
EIC PID Workshop, 9th July 2019, Stony Brook
Notes: Fare una immagine del PMT sulla risoluzione

## Slide 27
CLAS12 RICH designed to provide hadron identification in the 3 to 8 GeV/c momentum range
A hybrid-optic design has been adopted to minimize the instrumented area to about 1 m2
The MAROC readout electronics is designed to offer
Discrimination down to few % of SPE
Time resolution of 1 ns
Negligible dead time at 30 KHz
Trigger latency up to 8 ms
Featuring:
Compatibility with various sensors and applications
Modular Front-End (Mechanical adapter, ASIC, FPGA)
Scalable fiber optic DAQ (TCP/IP or SSP)
Compact and tessellated geometry (common HV, LV and optical fiber)
Flexible trigger logic (external, auto, self)
Charge measurement (multiplexed ADC or time-over-threshold)
Multi purpose electronics: in use also for GlueX DIRC and available for EIC R&D
27
Conclusions
Contalbrigo M.
EIC PID Workshop, 9th July 2019, Stony Brook
Notes: Dire meglio chi fa cosa.