## Slide 1: Low Energy RHIC electron Cooling (LEReC): Status and Plans
Alexei Fedotov
on behalf of the LEReC team
RHIC Science and Technology Review 2019
September 17-19, 2019

## Slide 2: LEReC Project Overview
LEReC project was successfully completed on schedule and on budget, with all project KPPs achieved September 2018.
LEReC is world’s first electron cooler based on the RF acceleration of electron bunches (all previous coolers used DC beams). Such cooling approach opens a possibility of using this technique to high beam energies.
All key elements and experimental demonstrations required for this new approach were successfully achieved:
Building and commissioning of new state of the art electron accelerator 
Produce electron bunches with beam quality suitable for cooling
RF acceleration and transport maintaining required beam quality
Achieve required beam parameters in cooling sections
Commissioning of bunched electron beam cooling
Commissioning of electron cooling in a collider 
2

## Slide 3
May 2015: LEReC project approved for construction
December 2016: DC gun installed and successfully conditioned in RHIC tunnel
February 2017: Gun test beamline installed
April-Aug., 2017: Gun tests with beam
July-Dec., 2017: Installation of full LEReC accelerator
Jan.-Feb., 2018: Systems commissioning (RF, SRF, Cryogenics, Instrumentation, Controls, etc.)
March-Sept. 2018: Commissioning of full LEReC accelerator with e-beam
September 2018: All project Key Performance Parameters achieved
Oct.-Dec., 2018: Scheduled upgrades and modifications
Jan.-Feb., 2019: Restart operation with electron beam
March 2019: Start commissioning with Au ion beams
April 2019: First cooling demonstration. Cooling in both RHIC rings using e-bunches
at 76kHz frequency.
May 2019: Simultaneous cooling of all ion bunches with high-current 9MHz CW e-beam
June 2019: Cooling optimization at 1.6MeV, cooling of beams in collisions (3.85GeV/n ions)
July 2019: Cooling commissioned at higher electron energy of 2MeV (4.6GeV/n ions)
LEReC project timeline

## Slide 4: LEReC electron accelerator (100 meters of beamlines with the DC Gun, high-power fiber laser, 5 RF systems, including one SRF, many magnets and instrumentation)
COOLING
in Blue RHIC ring
COOLING
in Yellow RHIC ring
High-Power Beam Dump
Extraction beam line
DC e- Gun
704 MHz SRF
Booster Cavity
2.1 GHz Cu Cavity
9 MHz Cu Cavity
704 MHz Cu Cavity
Injection beam dump
RF Diagnostic Beamline
RHIC TRIPLET
RHIC DX
180°
Bending
Magnet
e-
e-
e-
* NOT to scale
Cathode
loading system
LF solenoid
HF solenoid
Transport solenoid
ERL solenoid
Quad corrector
Trim corrector
Corrector 3.8 ID
Corrector 6.0 ID
BPM 2.4 ID
BPM 4.8 ID
Bellows
Ion pump
Merger
Beamline
Transport
Beamline
704 MHz Cu Deflector Cavity

## Slide 5: LEReC electron beam parameters
Electron beam requirement for cooling |  |  | 
Kinetic energy, MeV | 1.6 | 2 | 2.6
Cooling section length, m | 20 | 20 | 20
Electron bunch (704MHz) charge, pC | 130 | 170 | 200
Effective charge used for cooling | 100 | 130 | 150
Bunches per macrobunch (9 MHz) | 30 | 30 | 24-30
Charge in macrobunch, nC | 4 | 5 | 5-6
RMS normalized emittance, um | < 2.5 | < 2.5 | < 2.5
Average current, mA | 36 | 47 | 45-55
RMS energy spread | < 5e-4 | < 5e-4 | < 5e-4
RMS angular spread | <150 urad | <150 urad | <150 urad
Two energies commissioned 

## Slide 6: LEReC beam structure in cooling section
110 nsec,
f=9 MHz
Ions structure:
120 bunches
f_rep=120x75.8347 kHz=9.1 MHz
N_ion=5e8, I_peak=0.24 A
Rms length=3 meters
1.42 nsec
30 electron bunches per ion bunch
Electrons:
f_SRF=704 MHz
Q_e=100 pC, I_peak=0.4 A
Rms length=3 cm
9 MHz bunch structure
Ion bunches
with new 9MHz RF
Electron Macro-bunch

## Slide 7: LEReC Critical Technical Systems
1. High-voltage photocathode electron gun
2. High-power fiber laser, transport and stabilization
3. Cathode production deposition and delivery systems
4. 704 MHz SRF Booster cavity
5. 2.1 GHz and 704 MHz warm RF cavities
1
1
2
3
4
5
5

## Slide 8
LEReC construction started in 2016
DC Gun

## Slide 9: LEReC Gun test beamline (2017)
Cathode insertion system
Gun transport section
Injection beamline
Injection beam dump

## Slide 10: Full LEReC installation (October 2017)
LEReC transport
beam line
SRF Booster
stand
DC Gun

## Slide 11: LEReC cooling sections fully installed (2018)

## Slide 12: Attainment of “cold” electron beam suitable for cooling
LEReC is based on the state-of-the-art accelerator physics and technology:
Photocathodes: production and delivery system
High power fiber laser and transport
Laser beam shaping to produce electron bunches of required quality
Operation of DC gun at high voltages (around 400kV) with high charge and high average current
RF gymnastics using several RF cavities and stability control
Energy stability and control
Instrumentation and controls

## Slide 13: Gun performance
Beam current in CW operation (red line) over 8 hours, and QE (blue line) with a fitted cathode current lifetime of 142 h.
Typical CW beam current ramp-up for cooling optimization.
To support 24/7 operations, cathode production and exchange systems were developed which include two cathode deposition systems, three multi-cathode (up to 12 cathodes) carriers, and a mechanism allowing for cathode exchange in RHIC tunnel in less than 1 hour.
DC gun with high QE cathodes and stable laser provided reliable beam
operation over a period of 7 months.

## Slide 14: Transverse phase-space measurements of electron beam
Movable slit and downstream beam profile monitors are installed at the beginning of each cooling section.
Bunch charge 75 pC
Achieved rms normalized emittances
in cooling sections < 2 mm
(requirement: 2.5 mm)

## Slide 15: Longitudinal phase-space measurement of electron beam
1 macro-bunch of electrons (total charge 3nC)
6 macro-bunches, 3 nC each.
704MHz deflecting cavity
First dogleg merger dipole is off
Beam goes to RF diagnostic line
20 degree dipole produces dispersion
704MHz RF deflecting cavity produces time dependent vertical kick
In pulsed mode, subsequent electron macro-bunches have lower energy due to beam loading in RF cavities.
e-beam
(requirement: 5e-4)

## Slide 16: LEReC: First observation of electron cooling using bunched electron beam, April 5, 2019
Ion bunch #2 is being cooled
Bunch length time evolution
for two Au ion bunches in RHIC
Energy of electrons and ions matched
Ion bunch #4 which is not being cooled
Longitudinal profiles
of six ion bunches
In 76kHz mode, subsequent electron macro-bunches have lower energy due to beam loading in RF cavities (can match energy/cool effectively single ion bunch).

## Slide 17: Simultaneous cooling in Yellow and Blue rings (76kHz mode, 6 ion bunches: bunch #1 is being cooled; bunch #6 does not see electrons)
cooled and non-interacting bunches
Yellow
Blue
Blue
Yellow
Cooled, heated and non-interacting bunches
Blue
Yellow
bunch length
bunch intensity
loss rate
Longitudinal bunch profiles
cooled
cooled
cooled

## Slide 18: Cooling of hadron beams under collisions (RHIC store with 111x111 Au ion bunches) @ 3.85GeV/n using 1.6MeV high-current 9MHz CW electron beam
6-D cooling of a 111x111 bunch RHIC store at 3.85 GeV (1.6 MeV electrons, 9 MHz CW current of 15mA).
Top plot - reduction of bunch length. Bottom plot - reduction of transverse beam emittances (two RHIC rings, two planes).

## Slide 19: Cooling of 111x111 ion bunches at 3.85GeV (1.6MeV 9MHz CW electrons)
Cooled vs uncooled store (+/-0.7m trigger)
Electron cooling in a collider:
Cooling of hadron beams in collisions.
Luminosity improvement in test stores
with longitudinal cooling.
Better luminosity improvement requires:
Collecting data with longer vertex cut
Establishing good transverse cooling
and dynamic squeeze of beta*

## Slide 20: Cooling using 2MeV electron beam (ions at 4.6GeV/n)
Cooling on
OFF
No cooling
Cooling on
Longitudinal cooling: ion bunch length
Transverse cooling: vertical beam size

## Slide 21: LEReC roadmap to cooling
Production of 3-D high-brightness electron beams 
RF acceleration and transport of electron bunches maintaining “cold” beam 
Control of various contributions to electron angles in the cooling section to a very low level required for cooling 
Energy matching of electron and ion beams 
First electron cooling demonstration in longitudinal plane
Establishing cooling in 6-D
Matched electron and ion energy in both Yellow and Blue RHIC rings
Achieved cooling in both Yellow and Blue Rings simultaneously using the same electron beam
Demonstrated longitudinal and transverse cooling of several ion bunches (high-current 9MHz CW e-beam operation) simultaneously 
Cooling ion bunches in collisions, in both Yellow and Blue RHIC rings using CW electron beam 

## Slide 22: Observed issues and limitations
With no magnetic field in the cooling sections, focusing of electrons by ions was significant. Adjusting the electron beam optics to take this into account was challenging.
Different focusing on electron bunches distributed at different longitudinal slices of ion bunch.
Using bunched electron beam for cooling at such a low energy led to emittance growth of ions due to modulated focusing from the electrons (called “heating”). Such heating effects were reduced, but not eliminated, by a proper choice of ion beta-function in the cooling section and of a working point. However, to cope with the heating effects, which had strong dependence on electron beam density, we had to operate at electron currents lower than design values.
Ion lifetime limitations at low energy in RHIC: physical aperture, dynamics aperture, beam-beam, space charge and IBS.

## Slide 23: Effects of electrons on ions: “heating” (March 2019)
Even before cooling was established we observed strong “heating” effects of electrons on ions (which are space-charge beam-beam kicks from e-beam on ions).
These “heating” effects were reduced by going to smaller ion beta-function in cooling section and by finding better working point in tune space.
Electrons and ions energies
are NOT matched

## Slide 24: Yellow RHIC Ring (76kHz mode allowing to cool single ion bunch; 6 ion bunches, 5 electron macro-bunches)
Cooled ion bunch
(heating+cooling))
Heating only
(off-energy electrons)
Ion bunch not interacting
with electrons
Heating effects were reduced, but not eliminated,
by a proper choice of ion beta-function in the cooling section and of a working point.
We were able to counteract heating with cooling (see bunch #1, as an example).

## Slide 25: Potential benefits from cooling
lifetime
bunch length
lifetime
bunch length
Cooled bunch is kept shorter, more useful events within trigger window
Minimize ion beam de-bunching and losses from the RF bucket
Peak current significantly higher for cooled bunch
Allows longer stores
Transverse cooling can help with reduction of beta*
Cooled
Non-interacting
Cooled
Non-interacting
Ion bunch profiles
Ion lifetime
(of cooled and non-interacting bunches)
Cooled bunch
Ion bunch profiles
Ion lifetime
(of cooled and non-interacting bunches)
Cooled bunch
BLUE
YELLOW

## Slide 26
LEReC transition to operations by MCR
In 2018-2019 LEReC was in commissioning mode.
During 2019 commissioning already started transition to Ops:
- Various LEReC systems ran successfully 24/7 during 7-month period.
- Tapes and procedures for various systems were developed and already used
by MCR operators.
- MCR already developed tape to ramp up bunch charge and used it
successfully when LEReC e-beam was left to run overnight.
What remains to be done:
Finish commissioning and optimization and freeze e-beam parameters and lattice which works best for cooling
Implement energy and orbit feedbacks
Convert useful commissioning scripts to Ops applications
Update tapes and procedures
Update training of operators on LEReC Ops
Nine LEReC shift leaders are available to provide further training of MCR operators and assist with LEReC running.
26

## Slide 27
November, 2019: Gun conditioning
December, 2019: Once SRF booster is at 2K, restart ops with
electron beam
Dec.’19-Feb.’20: Cooling optimization for 4.6GeV/n ions
(2MeV electrons):
2 weeks of dedicated time –
interleaved with Physics running at 5.75GeV.
March - June, 2020: Physics run with cooling at 4.6GeV/n
(2MeV electrons).
Transition to running LEReC by MCR.
March - June, 2020: Cooling optimization for 3.85GeV/n ions
(1.6MeV electrons):
2 weeks of dedicated time – interleaved with
Physics running at 4.6GeV.
2021 Physics run with cooling at 3.85GeV/n
(1.6MeV electrons).
LEReC upcoming plans
27

## Slide 28: LEReC summary
LEReC project was completed on budget and on schedule.
All commissioning milestones were successfully achieved.
World’s first electron cooling of hadron beams based on RF acceleration of electron bunches was demonstrated. Such cooling approach is new (all previous coolers used DC beam) and opens the possibility of using this technique to high beam energies.
Electron cooling using electron beam without any magnetization on the cathode or cooling section (“non-magnetized” cooling) was demonstrated.
Cooling was commissioned at electron energy of 1.6MeV (ion energy 3.85GeV/n) and at 2MeV (ion energy of 4.6GeV/n)
First electron cooling in a collider (cooling of ion beams in collisions with various effects impacting beam lifetime) was achieved by successfully cooling 111 ion bunches in both RHIC rings.
The next step will be to maximize collision rates with cooling in next year’s RHIC low-energy collisions.
6-D cooling of a 111x111 bunch RHIC store at 3.85 GeV (1.6 MeV electrons, 9 MHz CW current of 15mA).
Top plot - reduction of bunch length. Bottom plot - reduction of transverse beam emittances (two RHIC rings, two planes).
LEReC cooling sections

## Slide 29: Acknowledgement
LEReC project greatly benefits from help and expertise of many people from various groups of the Collider-Accelerator and other Departments of the BNL.
As well as FNAL, ANL, JLAB and Cornell University.
Thank you!