## Slide 1
Andrew Johnson
ASD/Controls Group 2019-10-05

## Slide 2
EPICS 7 Status

## Slide 3
Recent Releases
Final releases, supported series, release frequency.
Core Development Work
Build simplification, joining threads, faster time, access security.
PVA Module Development
Major clean-ups, C++11, JSON, access security.
Future Directions
Rewrite of pvData & pvAccess, discontinuing target OS’s.
Talk Outline
Talk Outline What’s he going on about this time?

## Slide 4
Recent Releases

## Slide 5
7.0.3
The latest tagged version of EPICS, contained some IOC enhancements, bug fixes, and API changes to the pvAccess, pvData, normativeTypes and pvDatabase modules.
Released on 2019-07-31
Recent Releases EPICS 7 Series
Latest EPICS 7 Release

## Slide 6
Final Releases
  Base-3.14.12.8 on 2018-09-14 was the last 3.14 release
  Base-3.16.2 on 2018-12-12 was the last 3.16 release
The Base-3.15 series is still being maintained (bugs, build, documentation)
  Base-3.15.7 should be out in about a month
Development continues on the 7.0 series
  EPICS 7.0.4 should be out soon after Base-3.15.7
Other Releases
Recent Releases Older Series

## Slide 7
Since the EPICS 7.0.2 release we have been making more frequent releases of EPICS 7, roughly every 3 months with new features, more often when there are important bug fixes to distribute.
I would appreciate some feedback on this new policy:
Is 4 or more times a year too often?
We have been asked to issue patch files for important bug fixes:
Would sites prefer to apply patch files instead of install new patch releases?
Release Frequency
Recent Releases EPICS 7 Series

## Slide 8
Software Development

## Slide 9
libcom, ca and database are now source trees, not embedded modules
  We had recombined their git branches into 7.0 for EPICS 7.0.2 (Dec 2018)
The epicsThread C API now provides epicsThreadMustJoin()
  A parent thread can wait for a child to finish its work
  Thread must be flagged as joinable at creation
Short-cut speeds up getting the current time when only one time provider is registered with generalTime; saves taking a lock and scanning a linked-list
Access security code can now check a CA client’s IP address instead of the hostname supplied by the client at connection time
  Does DNS lookups if necessary when loading the AS rules file
Core Development Work
Software Development Recent Work

## Slide 10
pvData, pvAccess
  Deprecations, API removals & simplifications, leaks and deadlocks fixed
  Introducing some C++11 features (optional, e.g. move semantics)
  Conversion between pvStructures and JSON strings
QSRV – Supports access security
Normative Types – compatibility checks relaxed to “convertably-equivalent”
pvaClient – clean-ups; multi-channel API’s for doing I/O to groups of channels
pvDatabase – can now support plugins, and record processing
PVA Module Development
Software Development Recent Work

## Slide 11
Future Directions

## Slide 12
Documentation
  Lots to do in the near term, help always welcome (email us!)
PVA Modules
  Rewrites of pvData and pvAccess are under way (both Java and C++)
IOC Database
  Want record types to be able to have pvStructure fields
Drop support for old RTOS’s
  VxWorks 6 and RTEMS 4 don’t support C++11
Future Directions
Future Directions Older Series

## Slide 13
ANY QUESTIONS?
A similar talk going back to the 2017 ICALEPCS meeting in Barcelona will be given on Wednesday – WECPR01