## Slide 1: Projections for Run-14 and Run-15 Wolfram Fischer
25 July 2013
RHIC Retreat, BNL
Notes: 25 July 2013, 09:10, 15 min (incl. questions)

## Slide 2: Contents
Recent performance, limits
PAC recommendations for Run-14 and Run-15
Upgrades
Projections for Run-13 and Run-14

## Slide 3: Run-13 luminosity
New: OPPIS, AGS survey, upgrade 9 MHz, upgrade pC, new STAR Be pipe, e-lens lattice tested, e-lens hardware commissioning, longitudinal damper injection and ramp, …
Best weeks
(50 pb-1/week) close to max projected (56 pb-1/week)

## Slide 4: Run-13 polarization (preliminary)
50%
 | Run-12 | Run-13
Blue | 50.3% | 49.8%
Yellow | 53.5% | 53.2%
Transverse emittance reduction after optimization of AGS transition crossing
H-jet measured polarization (average over intensity, time, run)
H-jet measures intensity-averaged P
LP2 and LP4 are luminosity-averaged
Luminosity-averaged values are higher than intensity-averaged values

## Slide 5: Delivered Integrated Luminosity and Polarization
Nucleon-pair luminosity: luminosity calculated with nucleons of nuclei treated independently; allows comparison of luminosities of different species; appropriate quantity for comparison runs.

## Slide 6: Performance measure: setup time
Setup time: - for 1st species in run: from both rings cold to 1st physics store - for following species: from beginning of setup to 1st physics store
TRANSPARENT: low energy
INTRANSPARENT: high energy
BLUE: heavy ion runs
RED: polarized proton runs
Example: Setup of 250/255 GeV polarized proton operation as 1st species most demanding operating mode Gain of 2 weeks in setup from 2009 to 2013 savings of ~$1M (incremental operating cost ~$0.5M/week) major upgrade: beam based feedbacks (orbit, tune, coupling)
Setup time [d]
Notes: ----- Meeting Notes (7/24/13 10:42) -----
go to 40 days on scale

## Slide 7: Store-to-store time, time in store
RED: polarized proton runs
BLUE: heavy ion runs
TRANSPARENT: low energy
INTRANSPARENT: high energy
Time in store = store time / calendar time (denominator includes scheduled maintenance, failure, setup, beam experiments)
Time in store goal: 60%
Notes: ----- Meeting Notes (7/24/13 10:42) -----
Fermi and CERN data

## Slide 8: Run-13 test: He-3 acceleration in AGS
Polarized He-3 source under development at MIT (R. Milner, J. Maxwell, C. Epstein)
Accelerated unpolarized He-3 nuclei (helions) in AGS: 3.3x more intensity at AGS extraction than 2012 4x1010/bunch in reach at AGS extraction [EBIS intensity increase from 3.4 to 3.9x1010; 2 bunch merges in Booster, can do 2 more merges in AGS; better Booster injection field regulation; for polarization preservation have demonstrated: vertical tune at Booster injection of 4.09, AGS tune of 8.97]
2013: test of transfer depolarization of 3Heh into EBIS (spare) magnet
H. Huang et al.
CAD of new polarizer and test transfer line
Transfer path simulation
New Helmholtz pair

## Slide 9: RHIC luminosity and polarization goals
parameter |  | unit | achieved |  | goals | 
Au-Au operation |  |  | 2011 |  | ≥ 2014 3D stochastic cooling + 56 MHz SRF | 
energy | GeV/nucleon |  | 100 |  | 100 | 
no colliding bunches | … |  | 111 |  | 111 | 
bunch intensity | 109 |  | 1.3 |  | ≥ 1.1 | 
avg. luminosity | 1026 cm-2s-1 |  | 30 |  | 40 | 
p-p operation |  |  | 2013 |  | ≥ 2014 source + e-lenses | 
energy | GeV |  | 100 | 255 | 100 | 255
no colliding bunches | … |  | 107 | 111 | – 107 – | 
bunch intensity | 1011 |  | 1.6 | 1.85 | 1.8 | 2.5
avg. luminosity | 1030 cm-2s-1 |  | 33 | 135 | 60 | 300
avg. polarization* | % |  | 59 | 53 | 62 | 56
*Intensity and time-averaged polarization as measured by the H-jet. Luminosity-averaged polarizations, relevant in single-spin colliding beam experiments, are higher. For example, for intensity-averaged P = 48% and Rx = Ry = 0.2 (255 GeV, 2013), the luminosity-averaged polarization is P = 53%.

## Slide 10: Recommendation of the Program Advisory Committee
11-12 June 2013

## Slide 11: 7.3 GeV/nucleon Au+Au projection for Run-14
Scaled from operation at 5.75 (Run-10) and 9.8 GeV/nucleon (Run-11)
AGS extraction close to (and below) transition energy Store times ~30 min, frequent refills require good loss control in AtR

## Slide 12: 100 GeV/nucleon Au+Au projection for Run-14
Run-11
Improvements compared to Run-11: 3D cooling, new longitudinal pick-up and kicker for stochastic cooling, higher bunch intensity (long proton run with high intensity provided scrubbing – expect higher instability threshold at transition), 56 MHz SRF commissioning

## Slide 13: 100 GeV ph+ph projection for Run-15
Run-11
Improvements compared to Run-11: OPPIS performance, e-lenses

## Slide 14: 100 GeV/nucleon ph+Au projection for Run-15
DX (beam splitting dipoles next to experiments) and ZDC move needed

## Slide 15: Preparation for Run-15: asymmetric ph-Au operation
time
Lorentz factor g
107.4
25.4
10.5
injection Au
injection ph
store Au (close to gtr)
acceleration Au (cross transition)
acceleration ph, Au
collision ph+Au
Note: now tolerate ion beam instabilities at transition to obtain higher intensity (can be cooled down again), not possible with p+Au since have smaller aperture available
maintains same frev for both beams

## Slide 16: Summary
Very successful Run-13 new records for Lpeak, Lavg, Pavg, almost 0.5 fb-1/experiment used up tolerable tune space completely (g electron lenses) total intensity limited by abort kicker heating (g upgrade) polarization loss driven by emittance (g source + injectors) increased 3He intensity in AGS 3.3x (g 0.4x1011 with 2 more merges)
Run-14 Au+Au 7.3 GeV/nucleon [ 3 wks] (AGS extraction close to gtr) Au+Au 100 GeV/nucleon [14 wks] (3D cooling, maximization of bunch intensity, minimization of non-luminous losses, 56 MHz SRF commissioning) possibly d+Au or 3He+Au preparation for p-Au (DX move, shielding modification)
Run-15:
ph+ph 100 GeV (source + injectors + electron lenses) ph+Au 100 GeV/nucleon (DX move) ph+Si(Al), ph+Cu, d+Au, 3He+Au (setup time)