Developments in Optics Measurement and Correction
C. Liu
Jul. 25th, 2013

---
Outline
1. BPM data quality
2. Optics measurement
3. Optics correction
4. Ramp optics measurement
5. Ramp optics correction
6. Summary

---
BPM data quality

---
SNR of TBT BPM data
Courtesy by P. Thieberger
SNR < 2% for turn-by-turn BPM data with 1 mm oscillation amplitude, the reported number for CERN SPS is ~10%.

---
BPM TBT Improvements
BPM TBT Improvements
- 2009 - 2011
  - Time stamp and Interrupt Bugs Fixed
  - Firewire Optimization and Staggering of Data
- 2012 - 2013
  - Rewrite of ADC Interrupt Handler to Improve Timing
    - Verified that no turns are skipped due to CPU latency
  - 2K and 4K Turn Options Added
    - Verified again that no turns are missed during data acquisition
By R. Hulsart, R. Michnoff

---
Optics measurements

---
Measurement techniques
        – Data taking
AC dipole, sustained driven oscillation
Artus, free oscillation
Injection oscillation
AC dipole
Artus

---
Measurement techniques
        – Data analysis
- 1. Fitting in time domain, M. Bai (Loptics), P. Thieberger/A. Marusic (tbtOpticsAnalysis)
- 2. Interpolated FFT in frequency domain, C. Liu (tbtOpticsAnalysis)
- 3. ICA (Independent Component Analysis), X. Shen

---
Measurement results
        --from AC dipole
By AC dipole optics team

---
Measurement results
        – from Artus data
Tune
S (m)
S (m)
1. Precision tune measurement, rms of the tune distribution of a single measurement is 1.3 × 10−5, the rms of the tunes is 1.6 × 10−5 from multiple data sets acquired during 1 min
2. Precision phase measurement, the rms of phase measurement is ~0.2 deg
3. Option of less model dependent and amplitude scaling beta function measurement
4. Interpolation of phase between BPMs, phase advance between IPs and e-lens
5. Interpolation of beta function for STAR, PHENIX, IPMs, Schottky...

---
Optics measurement for low E run
        – injection oscillation
W/O window
W window
Tune
1. w/o window, the spectrum looks like pure noise; w Gaussian window, two peaks are visible due to residual coupling
2. Peaks for x/y are distinguished by tweaking one tune at a time in RampEidtor
3. Tune spread is ~10-4, beta beat is ~20% (the outliers are excluded)
S (m)

---
Optics correction

---
Correction technique
error
correction
= R
correction
error
= SVD(R)
1. The vector to be corrected in above can be phase error or beta beat, phase correction == beta correction?
2. Weighting can be applied in above to balance x/y correction; manipulation of eigenvalues can reduce excessive correction strength
3. Blue injection: No gammaT quads in model & machine; Yellow injection: GammaT quads not in model but machine; Snakes on at injection, but not in model for both rings
4. R calculated by OptiCalc and MAD-X are compared, huge differences are observed at injection; nice agreement for store
Injection, Yellow
Store, Yellow

---
Phase beat correction
        – with Artus
#02/26/13, blue ring at injection energy with pp13e-v4 (E-Lens) lattice
Phase error and beta beat:
Before
Phase error and beta beat:
After

---
Beta beat correction
        – with Artus
Blue, pp13b-v2, store
Yellow, pp13b-v2, store
The beta beat was reduced significantly in both planes for both rings based on Artus turn-by-turn data despite the s-shapes due to coupling

---
Beta beat correction
        – with AC Dipole
By AC dipole optics team

---
Beta beat correction
        –	global + orbit bump in sextupole
By AC dipole optics team

---
Ramp Optics Measurement

---
Measurement procedure
By M. Minty
1. No interference of TBT data acquisition with average orbit acquisition for orbit feedback
2. Horizontal and vertical kick is 510 turns apart, cross-talk is marginal due to decoherence even with coupling
3. At full energy, sufficient oscillation amplitude can be achieved with adjustment to the number of kicks and Artus tunes (by A. Drees)

---
Beta beat
pp13e-v4, Blue
pp13b-v2, Blue

---
Beta at IPMs
Symptom: Yellow vertical profile at IPM stays more or less constant during beta squeeze, design vertical beta function at that IPM increases, thus the calculated emittance decreases as shown lower left, which is unphysical
Diagnosis: With ramp optics measurement, the beta functions at yellow horizontal and vertical IPMs are interpolated (shown below), beta function at vertical IPM is slowly decreasing contradict to the design
Further development: Implement measured beta for IPM emittance calculation (by M. Minty)

---
Beta at IPMs
BH
BV
YV
YH
Beam loss
Beta function on the ramp at any location is available.

---
Ramp optics correction

---
Ramp optics correction test
Physics ramp
12 by 12 ramp
1. Back-propagated optics corrections at store into the rotator ramp in both rings
2. Tested 12 by 12 ramp, pp13b-v2 with standard protocol
2. Beam loss (left) is same as usual
3. IPM emittance (up right) is the same
4. Calculated emittance (by StoreAnalysis) is as good as good physics store
5. ZDC scaled rate reached 1070 kHz for STAR, ~15% increase of L

---
Rotator ramp correction
Implementation
Starting on May 2nd, 2013, fillno 17451, optics correction for yellow rotator ramp has been implemented, it stayed in the machine without any complication

---
Energy ramp correction
Plan: 12 by 12 ramp for ramp optics measurement, run script to select the TBT orbit file near stones and calculate optics corrections, run script to send correction strength to RampEditor, activate and ramp again
Problem #1: each time a set of strength was sent to RampEditor, it recalculates everything for the whole ramp, too time consuming
Solution: Send correction strengths for a stone once, not separately, or pre-anchor stones
Problem #2: Anchoring stones change the current curve for magnets dramatically, which causes magnet exceeding limits
No anchoring
W anchoring

---
Summary
- TBT BPM data quality significantly improved evidenced by optics analyses
- Three types TBT data (Artus data, AC dipole, injection oscillation), three analysis techniques (fitting, Interpolated FFT and ICA) in function
- Breakthrough of global optics corrections based on both Artus and AC dipole data
- Ramp optics measurement with Artus in operation
- Rotator ramp optics correction operational since May 2013
- Energy ramp optics correction in progress