## Slide 1: Physics Requirements for Zero-Degree Electromagnetic and Hadronic Calorimetry: Spectator Tagging in light systems and Impact Parameter Tagging in heavy systems
Charles Hyde
Old Dominion University
Joint CFNS & RBRC Workshop : Physics and Detector Requirements at Zero-Degree of Colliders (24-26 September 2019)

## Slide 2: Physics Near Zero Degrees
Spectator/Fragment tagging in light nuclei.
DVES on heavy nuclei: (≥ C)
  The challenge of true exclusivity
Target Fragmentation in DIS
  Flavor/pT correlations with current fragmentation region
  Baryon multiplicity as impact parameter tag
Fission Fragments in both photo- and electro-production
  Search for exotic nuclei?

## Slide 3: HaDRONIC Calorimetry: I. Light Systems
D(e,e’pS)X
  Proton tracking determines pT ,
  Probe neutron structure function for nearly on-shell neutron
  Probe EMC effect in the deuteron with strongly off-shell neutron
D(e,e’nS)X
  Calibrate “nearly on-shell neutron” with “nearly on-shell proton”

## Slide 4: D(e,e’nS)X ≈ pbound(e,e’)X 200 GeV/c D  100 GeV/c spectator neutron
Hadronic Calorimeter at 45 m (JLEIC)
Impact point resolution 1.5 cm rms:
  mrad  𝛿pT = 33 MeV
  Equivalent to rms beam spread
If energy Resolution
   𝛿pnD-rest ≈ 35 MeV/c
  If  𝛿pnD-rest ≈ 100 MeV/c

## Slide 5: Hadronic Calorimetry II: Evaporation
Evaporation neutrons
  Thermal Distribution T ~ 10MeV (Nuclear Rest frame)
  95% within in angular cone 3mrad
  HCal must separate shower profiles separated by ~7 cm to count neutrons.
See also talks by M. Baker, F. Hauenstein

## Slide 6: Far-Forward Hadronic Calorimeter: Technology
ZEUS: Depleted Uranium:
High Segmentation e.g. FeSci sampling (longitudinal and transverse)
  < 1 cm transverse spatial resolution
  Require 50cm lateral size beyond active area.
    Wrap around Dipole 3? Wedge into space at 50 m between D & Q?
      Some resolution-loss on beam side may be inevitable

## Slide 7: Far-Forward EM Calorimetry & Gluon Saturation
DVES as a signature for saturation
Veto Incoherent by nuclear break-up
What about Nuclear Bound states?
Based on elastic AZ(e,e) AZ and inelastic AZ(e,e’) AZ* data:
  Expect even first diffractive minimum to be washed out by excitation diffraction: AZ(e,e’ V) AZ*bound
  VETO DECAY GAMMAs!

## Slide 8: Forward EM CalorimeTRY
Proposed signature for gluon saturation:
  Comparison of low-x deep virtual exclusive J/Psi vs phi production.
  Both are sensitive to gluon density, but with different spatial averaging: 𝜙-production sensitive to saturation at larger xB then J/Psi
Signature is a shift in the diffractive minima
  Inelastic production to bound excited states will wash-out the sharp diffractive minima and obscure the saturation signal
Solution is to detect the gamma-decays to veto bound-state excitation

## Slide 9: Gamma-Ray veto
Requires doubly magic nucleus, e.g. 208Pb
  Every gamma-cascade of 208Pb has least one photon above 2.6 MeV (in nuclear rest-frame).
  Compare to Au, gamma decay chains with energies < 0.2 MeV
208Pb

## Slide 10: ForwARD 𝛾 BOOST/ ACCEPTANCE
JLEIC: PA = Z (200 GeV/c),
  EA / MA ~ 80
  50% of (2.6 MeV) photons are emitted in forward hemisphere of rest frame with detector energy from 220 MeV to 440 MeV
    50% of photons are in angular cone ± 1/80 = 12.5 mrad.
    ±10 mrad aperture would capture 42% of decay photons
    ±5 mrad aperture would capture only 15% of decay photons

## Slide 11: ForwARD BOOST/ACCEPTANCE
eRHIC: PA = Z (275 GeV/c),
  EA / MA ~ 116
  50% of photons are in angular cone ± 8.5 mrad.
    At least one photon ≥ 300 MeV (if detected)
    ±4 mrad aperture captures 18% of decay photons

## Slide 12: Far-Forward EM Calorimetry
PbWO4
  X0 = 8.9 mm, rM = 2.2 cm, 𝜏=25 nsec
  5% resolution at 300 MeV (https://arxiv.org/pdf/hep-ex/9907047.pdf)
LYSO:
  X0 = 11.4 mm, rM = 2.1 cm, 𝜏=40 nsec
  SuperB prototype: NIM A 718 (2013) 10
  2.6% @ 300 MeV
Both tolerant to fluence from 100 fb–1 at IP ≤ 1013 neutron/cm2

## Slide 13: Quark-Gluon Imaging of 4He
Highest Central Density of any nucleus
  J=0, I=0
  Hg(ξ, t |Q2), Hu(ξ, t |Q2) = Hd(ξ, t |Q2)
Elastic Charge Form Factor
0.4 GeV/c 0.8 GeV/c 1.2 GeV/c 1.6 GeV/c

## Slide 14: 4He DVES : 𝛾, 𝝆0, 𝜙, 𝜔, J/𝛹
Diffractive minimum @ |Δ| ≈ 0.64 GeV/c
4He Beam: 400 GeV/c
  σ(p) ≈ 0.6∙10–4 p = 240 MeV/c
  σ(p⟘) ≈ 0.3∙10–4 p = 120 MeV/c
  0° recoil nucleus detectable for
    xA = xBj /A > 0.01 (Dispersion = 1m)  xBj >0.04,
    Raw resolution σ (Δ⟘) ≈ 120 MeV/c (improvable via over-complete kinematics)
0.4 0.8 1.2 1.6 GeV

## Slide 15: Conclusions
There is no separation between the accelerator and the detector
The Interaction Region and Detector design process is a series of negotiations and re-negotiations.
We can design and build an accelerator, interaction region and detector that fulfills our science ambitions.

## Slide 16: Elastic vs Inelastic scattering
Fourier-Bessel expansion of inleastic electron scattering from
  J. Heisenberg et al, Phys Rev C v25 (1982) p.2292
Inelastic (e,e’) scattering on Pb to bound excited states.
Deep Virtual excitation will not be identical, but will be similar