## Slide 1: The 2019 Editions of the ICSBEP and IRPhEP Handbooks
This presentation was prepared at Idaho National Laboratory for the U.S. Department of Energy under Contract Number (DE-AC07-05ID14517)
John D. Bess Idaho National Laboratory

## Slide 2: Summary
ICSBEP Handbook available Sep 2019
IRPhEP Handbook available Dec 2019
Key benchmarks of interest to nuclear data:
  LCT099 – Ti cross section
  LCT103 – U7Mo (~20% 235U) plates
  KRITZ-LWR-RESR-004 – Rod lattices 20 – 250 ºC
  MSRE-MSR-RESR-001 – Molten salt & graphite
  TREAT-FUND-RESR-002 – Graphite & hydrogen sensitivity in fuel
See additional slide-pairs for slight additional information as desired

## Slide 3: Extra Slides

## Slide 4: International Handbook of Evaluated Criticality Safety Benchmark Experiments
September 2019 Edition
22 Contributing Countries
~70,000 Pages
577 Evaluations
  4,973 Critical, Near-Critical, or Subcritical Configurations
  45 Criticality-Alarm-Placement/Shielding Configurations
  237 Configurations with Fundamental Physics Measurements
  838 Unacceptable Experiment Configurations
http://icsbep.inl.gov/
https://www.oecd-nea.org/science/wpncs/icsbep/

## Slide 5: International Handbook of Evaluated Reactor Physics Benchmark Experiments
2019 Edition
21 Participating Countries
56 Reactor Facilities
Data from 166 Experimental Series
  162 Approved Benchmarks
  4 DRAFT Benchmarks
Available ~Dec 2019
http://irphep.inl.gov/
http://www.oecd-nea.org/science/wprs/irphe/
Notes: It is available, free of charge, to OECD NEA member countries via the weblinks.

## Slide 6: New Approved Evaluation 1: LEU-COMP-THERM-99
Sandia National Lab
  UO2 fuel in water
  4.31 wt.% U-235
  17 critical configurations
  Ti and/or Al sleeves around fuel
Results
  Calculations with various modern codes/libraries within 1𝝈 to 2𝝈.

## Slide 7: Titanium Improvements
Results
  Calculations with various modern codes/libraries within 1𝝈 to 2𝝈.
ENDF/B-VII.0
ENDF/B-VII.1
Ti

## Slide 8: New Approved Evaluation 2: LEU-COMP-THERM-103
MB-01 Reactor
  IPEN (Brazil)
  LWR w/ UO2 rods (4.346 wt.% 235U)
  U7Mo (19.80 wt.% 235U) plates in core center
Part of an extensive series of benchmarks for this reactor facility

## Slide 9: Results
Evaluated
  3 critical configurations
  MCNP5.1 w/ ENDF/B-VII.0 results within 1s-2s

## Slide 10: New Approved Evaluation 3: LEU-COMP-THERM-104
Studsvik KRITZ-1
  Sweden
  Various LWR lattices with T = 20 to 250 ºC
  Zr-2-clad UO2 (1.35 wt.% 235U)
  Marviken Boiling Heavy Water Reactor (BHWR) fuel

## Slide 11: Example Results
Evaluated
  Criticality
  Reactivity Worth
  Reactivity Coefficients
Criticality
  MCNP6 and ENDF/B-VIII.0
    Within 0.5 %
  SCALE 6.2.3 and ENDF/B-VII.1
    Within 0.7 %
  MONK 11A DEV and ENDF/B-VII.1
    Within 0.7 %

## Slide 12: New Approved Evaluation 4: MSRE-MSR-RESR-001
Molten Salt Reactor Experiment – ORNL
  U.C. Berkeley & ORNL (US)
  62.5LiF-31.6BeF2-5.1ZrF4-0.8UF4
  1.408 wt.% 235U
  Graphite moderated
First MSR benchmark in IRPhEP Handbook
DOE-NE NEUP MS-NE-1

## Slide 13: New Approved Evaluation 4: MSRE-MSR-RESR-001
Evaluated
  Criticality
Most sensitive uncertainties
  Graphite density
  Li-6 enrichment
  Fuel salt density
Sensitive to graphite thermal scattering law data
Unknown if missing significant data biasing the model

## Slide 14: New Approved Evaluation 5: TREAT-FUND-RESR-002
Transient Reactor Test Facility – INL
  U. Michigan (US)
  M8CAL Series
  Dilute HEU in graphite
  CP-2 graphite reflected
  Relevant to current TREAT core configurations
DOE-NE IRP

## Slide 15: New Approved Evaluation 5: TREAT-FUND-RESR-002
Evaluated
  Criticality
  Serpent w/ ENDF/B-VII.1 results within 1s
  Large uncertainties in graphite boron and hydrogen content
Also sensitive to thermal scattering law data for graphite