## Slide 1: Cumulative Fission Yield Correlations
G. Fabricante, R. Lorek, A. Mattera, E.A. McCutchan, A.A. Sonzogni, M. Vorabbi, S. Zhu
National Nuclear Data Center

## Slide 2
Cumulative fission yields
In a reactor, the fission products form a decay network satisfying
dNi / dt = -li Ni + r IFYi + S lk pki Nk,
Under equilibrium, that is dNi / dt = 0, then
Ni= r CFYi / li
Fission rate
Independent fission yield
Decay probability from k to I product
ln(2)/T1/2i

## Slide 3
Fission as a tool to study weak interactions
It was realized early on that the large antineutrino flux generated by a nuclear reactor, > 1020/second, could be used to detect antineutrinos
Detection of the Free Neutrino: a Confirmation
C.L. Cowan, F. Reines, F.B. Harrison, H.W. Kruse, A.D. McGuire, Science 124, 3212 (1956).
LANL team working at the Savannah River Site
25 years after first postulated by Pauli
Antineutrinos are produced in the b-minus decay of neutron rich fission products

## Slide 4
Reactor Antineutrino Anomaly
Since 2011 we learned that we are missing about 6% of electron antineutrinos near the reactor (model dependent)
F.P. An et al, PRL 116, 061801 (2016).

## Slide 5
0.2% precision points!!!!
IBD Antineutrino Yield measurements
Daya Bay, F.P. An et al, PRL 118, 251801 (2017).
239Pu DB value agrees with Huber-Mueller value, 235U does not, therefore no sterile neutrinos
Nucleus | Daya Bay Yield | D | H-M Yield | D
235U | 6.17 | 2.8% | 6.69 | 2.2%
239Pu | 4.27 | 6.1% | 4.36 | 4.4%
Yields in 10-43 cm2/fission units

## Slide 6
RENO contradicts Daya Bay, sterile neutrinos back in the market
Nucleus | RENO Yield | D | Daya Bay Yield | D | H-M Yield | D
235U | 6.15 | 3.1% | 6.17 | 2.8% | 6.69 | 2.2%
239Pu | 4.18 | 6.2% | 4.27 | 6.1% | 4.36 | 4.4%
G. Bak et al, PRL 122, 232501 (2019).
IBD Antineutrino Yield measurements
RENO results
Can we use our databases to shed some light?

## Slide 7
Sterile antineutrinos?
Production cross section for the Z boson,a resonance, is only compatible with 3 active neutrino families.

## Slide 8
Summation Method
Using nuclear databases, the IBD antineutrino yield under equilibrium conditions can be calculated as
where Ci is the cumulative fission yield and Si(E) the antineutrino spectrum for the fission products. The uncertainty can be calculated as
Nucleus | Summation Yield | Sum. Dyield
235U | 6.37 | 1.76%
238U | 9.69 | 2.04%
239Pu | 4.39 | 2.08%
241Pu | 6.25 | 2.36%
We use the ENDF/B-VIII.0 decay data and JEFF-3.3 yields
Uncertainties are unrealistically low

## Slide 9
Summation Method
Uncertainties can be calculated as
Unfortunately, the fission yield databases don’t contain any correlation data.
The GEF1 code will be used to obtain Y(Z,A) correlations, which will be converted to Y(Z,A,FPS) correlations, and then using decay data, we will obtain Cor(Ci,Cj)
1 "General Description of Fission Observables: GEF Model Code", K.-H. Schmidt, B. Jurado, C. Amouroux, C. Schmitt, Nucl. Data Sheets 131, 107 (2016).

## Slide 10
Summation Method
Some examples of correlations will be given for the most important contributors to the IBD antineutrino spectrum:
92Rb,
96Y,
and so on

## Slide 11
Summation Method
The largest correlations will be for nearby nuclides as well as for nuclides with Z=92-37 and A=236-92-2.
Positive correlations among nuclides in the same fission mode: symmetric, asymmetric (S1), very asymmetric (S2).
Negative correlations among different fission modes.
Independent fission yield correlations for 92Rb in 235U(n,f).

## Slide 12
Summation Method
Using ENDF/B-VIII.0 decay data, we can calculate cumulative yield correlations:
Ci = Ii + S bik Ik , where bik are decay probabilities and Ik are independent yields.
For instance, C(92Rb) = I(92Rb)+I(92Kr)+0.0195 x I(93Kr)+0.67 x I(92Br) + 0.68 x I(93Br)

## Slide 13
Summation Method
CFY correlation matrix for fission products that contribute to the IBD antineutrino yield.
The grey areas are due to statistics issues for very low fission yield values in JEFF-3.3
Preliminary

## Slide 14
Summation Method
Yield results (10-43 cm2) using ENDF/B-VIII.0 decay data, JEFF-3.3 yields and GEF IFY correlations.
Nucleus | Summation Yield | Sum. DYield | Sum. Dyield No Corrs.
235U | 6.37 | 2.58% | 1.76%
238U | 9.69 | 2.89% | 2.04%
239Pu | 4.39 | 3.01% | 2.08%
241Pu | 6.25 | 4.07% | 2.36%
Conclusion: summation calculations must include the correlations among Cumulative Fission Yields!

## Slide 15
Summation Method
We can use the same technique for other delayed radiation types, for instance delayed neutron multiplicity per fission, AKA delayed nu-bar
Nucleus | Summation | DSum. | DSum. No Corrs. | ENDF/B-VIII.0
235U | 1.567E-2 | 6.67% | 5.45% | 1.585E-2
238U | 4.01E-2 | 5.92% | 4.03% | 4.4E-2
239Pu | 6.767E-3 | 6.31% | 6.77% | 6.45E-3
241Pu | 1.454E-2 | 5.21% | 4.43% | 1.62E-2
Correlation effects seem to be stronger in IBD antineutrino yields than in delayed nu-bars. Do we understand that?

## Slide 16
Systematics for all fissioning systems
3Z-A

## Slide 17
Delayed nu-bar vs (3Z-A)
More selectivity in IBD antineutrino yield than in delayed nu-bars

## Slide 18
Another Summation Calculation
Ei: Energy converted into heat in the reactor following fission, used to calculate a nuclear reactor’s antineutrino spectrum:
Target | Ei(Kopeikin 2004) | %D | Ei(Ma 2013) | %D
235U | 201.92+-0.46 | 0.22% | 202.36+-0.26 | 0.12%
238U | 205.52+-0.96 | 0.47% | 205.99+-0.52 | 0.25%
239Pu | 209.99+-0.60 | 0.29% | 211.12+-0.34 | 0.16%
241Pu | 213.60+-0.65 | 0.30% | 214.26+-0.33 | 0.15%
Eis are derived using nuclear data. Uncertainties seem unreasonably low.

## Slide 19
Another Summation Calculation
Ei is calculated as
M: mass excess
C: cumulative fission yield for the most stable fission product
Np: prompt neutron multiplicity
Eni: energy carried away by the antineutrinos
Will briefly discuss S CM next
Summation!

## Slide 20
Another Summation Calculation
Target | Y (MeV) | DY (MeV) no CFY cors.
235U | -173.27 | 0.73
238U | -173.06 | 2.11
239Pu | -173.56 | 2.41
241Pu | -173.57 | 3.29
You will need strong anticorrelations to bring down diagonal uncertainties by a factor of 10!

## Slide 21
Summation Calculations
Target | DY (MeV) JEFF-3.3 | DY (MeV) ENDF/B-VIII.0 | DY (MeV) Kopeikin 04 (E&R) | DY (MeV) Ma 13 (JEFF-3.1)
235U | 0.076 | 0.927 | 0.050 | 0.062
238U | 0.298 | 0.593 | 0.100 | 0.058
239Pu | 0.115 | 0.416 | 0.070 | 0.060
241Pu | 0.240 | 0.409 | 0.100 | 0.070
Kopeikin came up with a clever way to obtain uncertainties, from mass conservation:
Mt + 1 = S Ci Ai + nu-bar
Then perform an uncorrelated Monte Carlo simulation varying Cis assuming a Gaussian shape, and keep those events that give nu-bar within its known, low uncertainties.

## Slide 22
Reason for disagreement between Kopeiking and ENDF/B-VIII.0
Large uncertainties for 90Zr and 135Cs

## Slide 23
Reason for disagreement between Kopeiking and ENDF/B-VIII.0
Isomeric ratios uncertainties were not propagated well
Issue appears in ENDF/B-VI.8, was absent in ENDF/B-V.2

## Slide 24
Target | DY (MeV) JEFF-3.3 | DY (MeV) ENDF/B-VIII.0 | DY (MeV) ENDF/B-VIII.0 Corrected | DY (MeV) Kopeikin 04 (E&R) | DY (MeV) Ma 13 (JEFF-3.1)
235U | 0.076 | 0.927 | 0.040 | 0.050 | 0.062
238U | 0.298 | 0.593 | 0.082 | 0.100 | 0.058
239Pu | 0.115 | 0.416 | 0.116 | 0.070 | 0.060
241Pu | 0.240 | 0.409 | 0.101 | 0.100 | 0.070
Propagating IR uncertainties properly
Is it possible that CFY and DCFY in ENDF/B-V.2 were adjusted to the nu-bar uncertainties?
This Monte Carlo method also yields correlation matrices, which should never be taken as true fission yield correlation matrices!

## Slide 26
Spin-off
Energy values in Mf=1 Mt=458 for 238U
The 1.07 MeV reduction in prompt gamma energy has improved the agreement with the summation calculation

## Slide 27
Conclusions
We introduced fission yield correlation matrices in summation calculations.
We observe sensible changes in the uncertainties if these matrices are included.
Only low-fidelity, best model based correlations could be developed for ENDF/B-VIII.0 (also perhaps for JEFF-3.3) as correlations induced by the experimental data used to obtain the library are not available.
These correlations should be thoroughly tested in uncertainty calculations.