## Slide 1: Some ENDF-6 Format Proposals in Support of the IRDFF-II Dosimetry Library
Andrej Trkov, Skip Kahler

## Slide 2: File 10 General Description
ENDF-6 Manual says:
“File 10 is allowed only for evaluations that represent the data for single isotopes.”
MF10/MT5 is used for radionuclide production in IRDFF-II Dosimetry library for natural elements where the same residual is produced by different reactions from different isotopes.
Example:
58Ni(n,p), 60Ni(n,nd), 60Ni(n,2np), 60Ni(n,t), 62Ni(n,2nt), 62Ni(n,4np), 62Ni(n,3nd) all lead to 60Co
Above 20 MeV the 60Ni(n,2np) reaction represents the dominant contribution to 58Co production.
Proposal:
Remove the last sentence in the first paragraph of Section 10.1 mentioned above, which administratively excludes the use of MF=10 for elemental data.

## Slide 4: Define MT-261 for dosimetry spectra
Standard and reference neutron fields are essential for cross section validation
Operations on spectra are similar to those on cross sections (group-averaging, plotting, covariances)
Non-cross section data exist in MF=3 (e.g. 251, 252, 253…)
Proposal
Formalize and legalize the use of MT=261 to represent neutron fields in special purpose libraries

## Slide 5: URR Interpolation
Currently in the ENDF-6 Manual:
“In such cases, if two adjacent grid points differ by more than a factor of three, the processing code should add additional intermediate energy points at a spacing of approximately ten-per-decade and compute the cross sections at the intermediate points using parameter interpolation.”
This is a contradiction and nonsense that leads to ambiguous cross section reconstruction
Proposal:
Admit the wrong decision and prescribe interpolation of resonance parameters