## Slide 1: ATF Electron Beam Capabilities
Mikhail Fedurin
ATF Science planning workshop
October 15 – 17, 2019

## Slide 2: Outline
ATF main beam parameters
ATF beam diagnostics
  Beam profile measurements
  Transverse deflector cavity (TDC)
  Spectrometry
ATF beam manipulation capabilities
  Mask
  Compression
  10 um microbunching with CO2 laser
Future plans for linac and beamlines
  Second TDC for BL1
  Linac energy upgrade
  Advanced compression scheme
More details about advanced e-beam compression
  Zig-zag scheme with two chicane combo (by Yichao Jing)
  New scheme: DWF plates and chicane combo

## Slide 3: ATF main beam parameters
Parameter | Typical value / range | Best value
Energy | 30-60 MeV | 80 MeV
Charge | 0.1 – 1 nC | 3 nC
Repetition rate | 1.5 Hz | 10 Hz
Electron spot size on cathode | 2.86 mm | 0.2 – 4 mm
Bunch length | 1-8 ps | 100 fs with compression
Average bunch current | 100 A | 1.5 kA with compression
Emittance | 1 – 3 mm mrad | 0.8 mm mrad @ 0.5 nC

## Slide 4: Facility Overview (Bldg. 820)
CO2 Laser Area
Electron Accelerator Area
Beamline 2:
Experimental station with
plasma cell capillary
Insertion device section
Differential pumping (1 stage)
CO2 & e-beam IP
X-band Deflector cavity (TDC)
Beamline 1:
Experimental stations:
1) Inverse Compton,
2) LWFA with gas jet cell,
3) IGS (big in vacuum space)
Differential pumping (2 stages)
CO2/YAG & e-beam IP

## Slide 5: ATF beam diagnostics
  Beam profile measurements
Radiabeam PMQ triplet assembly:
G=50 T/m, triplet focal length ~20 cm
UCLA PMQ triplet assembly:
G=500 T/m,
triplet focal length ~8 cm
Microscope (25-0506 X15 Reflecting Objective NA 0.28, F~13 mm)
Basler Gigabit camera (scA 1400-17gm, F=135 mm).

## Slide 6: ATF beam diagnostics
  Transverse deflector cavity (TDC)

## Slide 7: ATF beam diagnostics
Transverse deflector cavity measurements
Image at mask
Images after deflector
X-band Deflector cavity by Radiabeam
for longitudinal bunch profile characterization

## Slide 8: ATF beam diagnostics
  E-beam spectrometry
S. Antipov, S. Baturin, C. Jing, M. Fedurin, A. Kanareykin, C. Swinson, P. Schoessow, W. Gai, and A. Zholents, Phys. Rev. Lett. 112, 114801 (2014)
Measurement: spectrometer
0.95 THz structure
0.76 THz structure
Original chirped beam
S. Antipov, C. Jing, M. Fedurin, W. Gai, A. Kanareykin, K. Kusche, P. Schoessow, V. Yakimenko, A. Zholents, Phys. Rev. Lett. 108, 144801 (2012)
Observation of energy modulation

## Slide 9: ATF beam manipulation capabilities
  Mask technique
Muggli, P., et al., Simple method for generating adjustable trains of picosecond electron bunches. Physical Review Special Topics-Accelerators and Beams, 2010. 13(5): p. 052803
Muggli, P., et al., Generation of trains of electron microbunches with adjustable subpicosecond spacing. Phys Rev Lett, 2008. 101(5)
30 μm bunches
bunch current 100 A

## Slide 10: ATF beam manipulation capabilities
  Beam compression
~1 Tesla magnetic field
50 mm magnetic length
Permanent Magnet Chicane
Electromagnet chicane

## Slide 11: ATF beam manipulation capabilities
  10 um microbunching with CO2 laser
N. Sudar, P. Musumeci, I. Gadjev, et al., PRL 120, 114802 (2018)

## Slide 12: Future plans for Linac and beamline
  Deflector cavity for BL1
TDC BL1
TDC BL2

## Slide 13: Future plans for Linac and beamline
  Linac energy upgrade
Plan to feed linac acceleration sections with separated klystrons to push maximum operational energy to 110-120 MeV
Gun klystron
Linac
klystron #1
Linac klystron #2

## Slide 14: Future plans for Linac and beamline
Advanced compression scheme
DWF plates and
second bunch compressor

## Slide 15: Advanced e-beam compression
  Zig-zag scheme with dual chicane (by Yichao Jing)
Yi.Jin, et al. Phys. Rev. ST Accel. Beams 16, 060704 (2013)

## Slide 16: Advanced e-beam compression
Zig-zag scheme with dual chicane (by Yichao Jing)

## Slide 17: Advanced e-beam compression
  Zig-zag scheme with dual chicane combo (by Yichao Jing)
beam phase space distribution at initial and after zigzag chicane (two PMCs) shows almost perfect compression (beam was rotated by close to 90 degree in phase space). The twist at the core of the beam (right plot) is caused by CSR effect.

## Slide 18: Advanced e-beam compression
  Zig-zag scheme with dual chicane combo (by Yichao Jing)
FWHM bunch length < 20 fs is achievable for higher charge (100 pC in this case) with the combination of the zigzag chicane together with CSR shielding

## Slide 19: Advanced e-beam compression
New scheme: DWF plates and chicane combo
G.Andonian, et. al., Phys. Rev. Lett. 113.264801 (2014)
Hint: In many DWFA experiments conducted at the ATF, beam energy self-modulation was observed. This feature can be used to tune beam chirp!

## Slide 20: Advanced e-beam compression
New scheme: DWF plates and chicane combo
Simulations by Irina Petrushina

## Slide 21: Advanced e-beam compression
New scheme: DWF plates and chicane combo
DWF chirper
PM chicane
DWF chirper
PM chicane
EM or PM chicane
A selected portion of the beam can be transmitted through energy collimator between 2nd and 3rd magnet poles in magnet chicane
Collimating slit
Collimating slit
Zig-zag configuration with DWF chirper plates:

## Slide 22: Summary
Beam parameter | Present | Future plans
Transverse bunch size (sigma) - operational: - smallest achieved: | 50-100 mm 5 mm | 50-100 mm 5 mm
Bunch length/peak current - operational: - compressed: | 0.5-7 psec / 100 A 90 fsec / 1000 A | 0.5-7 psec / 100 A 20 fsec / 2000 A
Beam energy | 50-65 MeV | 110 – 120 MeV
New equipment:
Add X-band deflector cavity on beamline #1 and have bunch length diagnostic on both beamlines
Add second klystron for Linac sections to push beam energy up

## Slide 23: Thank you!