## Slide 1: ATF Science Planning Workshop Facility Upgrade Thrusts
Chris Cullen, ATF Upgrades Project Manager
October 15, 2019

## Slide 2: Topics
ATF CO2 laser configuration
ATF CO2 laser upgraded configuration
CO2 amplifier upgrades
In-vacuum CO2 laser upgrades
  CPA
  NLPC
  Flexible polarization rotator
  Circular polarization
  Beamline 2
ATF Ebeam configuration
ATF Ebeam upgraded configuration
EH Comparison
Ebeam upgrades summary

## Slide 3
Present CO2 Laser Vacuum Transport
Final Amplifier
CPA
Plasma Shutter
Ion Chamber
Vacuum CO2 laser transport

## Slide 4: CO2 Laser Vacuum Transport
CPA
NLPC Development
Flexible Polarization Rotator
Circular or Linear Polarization Mirror
Vacuum Transport to BL2
Proposed
Final Amplifier from B912
Vacuum Transport from CPA to BL1 and BL2 shown

## Slide 5: New Final Amplifier & Output Window
Final amplifier and end caps in B912
Gain from:
  ~ 40% increase in volume
  40% pressure increase (116 to 162 psi)
Peak fluence on window limits output
Window viewing area can be doubled (i.e. energy output can be doubled)
  Window structural analysis already performed
  End cap to be modified for new window
  Downstream optics require evaluation to verify peak power adequacy
Amplifier can be prepared offline in parallel with ATF operations in the B912 clean room
Installation requires re-opening a wall section

## Slide 6: CPA in Vacuum Chamber
Preliminary design & analysis complete
Mirrors and gratings vibration isolated
  Breadboard mounted to concrete footing
Front panel hidden for clarity
Concrete footing
Bellows
Vacuum chamber
Vacuum chamber supports

## Slide 7: Flexible Polarization Rotator
Provides linear polarization control
Rotation range -2° to 92°
Procurement in progress
In vacuum configuration planned

## Slide 8: Additional Proposed In-Vacuum Capabilities
NLPC
  To provide sub-ps pulse compression
Circular polarization
  Dedicated chamber supporting mirrors for linear, CW, & CCW polarization
  Mirrors switched out to support the required polarization
CO2 laser vacuum transport to BL2

## Slide 9: ATF Experimental Hall as Presently Configured
Deflector
cavity
Beamline 1
Experimental stations
Beamline 2
Experimental stations

## Slide 10: ATF as Presently Configured
Photocathode gun
Accelerator sections
Reconfigure this region for stronger bunch compression
Deflector
cavity
Beamline 1
Experimental stations
Beamline 2
Experimental stations

## Slide 11: Planned BL Configuration
Proposed
Existing
Slit & Transverse Deflection Cavity (TDC)
Spectrometer arm & spectrometer added to BL1

## Slide 12: EH Comparison
Current Configuration
Planned Configuration

## Slide 13: Experimental Hall Upgrades Summary
Slit and Transverse Deflector Cavity already on BL2
  Slit improves spectrometer image
  TDC for beam diagnostics
Slit and Transverse Deflector Cavity planned for BL1
Spectrometer planned for BL1
  Provides spectrometer images for all experiments
  Shielding and hall access needs to be reconfigured to allow for this capability
In-vacuum CO2 laser transport planned for BL2
LINAC reconfigured for stronger bunch compression

## Slide 14: Thank you! Questions or Comments?

## Slide 15: Backup

## Slide 16: Shielding and Access

## Slide 17: ATF Experimental Hall as Presently Configured

## Slide 18: Planned