## Slide 1: The Relativistic Heavy Ion Collider RHIC Operations
RHIC overview
Recent performance of RHIC
Low energy RHIC electron cooling
Capital and accelerator improvement projects
Action items from previous S&T review
Michiko Minty
DOE NP RHIC Science & Technology Review
17 – 19 September 2019

## Slide 2
Summary
Operation of RHIC: met or exceeded integrated luminosity goals in the last 3 years
  Run-17 p+p at 255 GeV and Au + Au 27.2 GeV/n
  Run-18 Zr + Zr / Ru + Ru at 100 GeV/n, Au + Au at 13.5 GeV/n
  + fixed target runs (at 3.85 GeV/n)
  Run-19 Au + Au at 9.8 GeV/n, 7.3 GeV/n, 3.85 GeV/n
  + fixed target runs (multiple energies)
New and unique operation (e.g. Ru+Ru / Zr+Zr) enabled by previous upgrades
Flexibility of operations substantially increased: many and interleaved modes is now routine
Operation of RHIC: exceeded accelerator availability goals
First (in the world) electron cooling with RF accelerated electron bunches demonstrated in support of Beam Energy Scan II - LEReC, presentation by A. Fedotov
Facility upgrades and maintenance ongoing to maintain high accelerator availability
Future BES-II operations will employ the newly developed LEReC technology
2

## Slide 3: Relativistic Heavy Ion Collider (RHIC) Overview
RF
ERL
RHIC
NSRL
LINAC
Booster
AGS
Tandems
STAR
sPHENIX
Electron lenses
Polarized Jet Target
Electron cooling
EBIS
BLIP
ATF II
TPL
ATF
Circumference : 3.8 km
Max dipole field : 3.5 T Energy : 255 GeV p : 100 GeV/nucleon Au
Species : ph to U (incl. asymmetric) Experiments : STAR, PHENIX (g sPHENIX)

## Slide 4
RHIC Overview - all colliding-mode physics runs to date (2001 to 2019)
2019-21 BES-II with LEReC and operation below nominal RHIC injection energy
Wolfram Fischer
The RHIC facility provides unparalleled flexibility in terms of ion species and energies for nuclear physics research in the US
4

## Slide 5
RHIC overview - time evolution of unit cost to operate RHIC
Ru+Ru/Zr+Zr
Wolfram Fischer
Productivity gain of RHIC operations (>1E3) is comparable with
state-of-the-art developments in industry
5

## Slide 6
c
Recent performance of RHIC: Run-17
STAR Lmax limited to ≈ 1.4x1032 cm-2s-1 => 1st p+p run with L-leveling
Met integrated luminosity goals of 400 pb-1 (p + p) and 300 mb-1 (Au + Au)
p + p at 255 GeV 15 weeks
Au + Au 27.2 GeV/n 3 weeks
p + p at 255 GeV for RHICf 0.9 weeks
Run-17 p + p at 255 GeV
Run-17 Au + Au at 27.2 GeV/n
3 modes of operation
6
+ CeC and LEReC gun commissioning

## Slide 7
Recent performance of RHIC: Run-18
Zr + Zr and Ru + Ru at 100 GeV/n (interleaved) 12 weeks
Au + Au at 13.5 GeV/n 4 weeks
Au + Au at 3.5 GeV/n (fixed target) 0.6 weeks
Au + Au at 3.85 GeV/n, LEReC commissioning 13 weeks
Au + Au at 26.5 GeV/n, Coherent electron Cooling (CeC PoP) 1.1 weeks
4 modes of operation
Run-18 Zr + Zr / Ru + Ru at 100 GeV/n
Exceeded integrated luminosity goals
7

## Slide 8: Recent performance of RHIC: Run-18, Zr+Zr / Ru+Ru
Zr
Ru
Zr
Ru
Ru
Zr
Ru
Zr
CeC PoP dedicated
scheduled maintenance
Unique operations / flexibility of RHIC met challenging requirements:
flat and equal conditions for Zr + Zr and Ru + Ru
constant (levelled) luminosity of 21.5×1026 cm-2s-1
turn-key, store-by-store species changes
8

## Slide 9
New and unique operation (e.g. Ru+Ru / Zr+Zr) enabled by previous upgrades
Zr-96
  Natural abundance: 2.78%
  From LION/EBIS (sintered ZrO2) => M. Okamura et al.
  Enriched ZrO2 powder commercially available, processing using RIKEN technology
  MIRP chemists could recycle unused ZrO2
Ru-96
  Natural abundance: 5.52%
  From Tandem (metallic) => P. Thieberger et al.
  Enriched Ru-96 not commercially available, provided by DOE using new isotope separation facility at ORNL (500 mg)
ZrO2 tablet (RIKEN)
Ru-96 (ORNL)
Recent performance of RHIC: Run-18
Zr-96 and Ru-96 preparation
Unique isobar run enabled with support from DOE, ORNL and Riken
9

## Slide 10
Recent performance of RHIC: Run-18
Zr-96 and Ru-96 preparation
Unique isobar run enabled with support from DOE, ORNL and Riken
10

## Slide 11
Recent performance of RHIC: Run-19
Au + Au for Beam Energy Scan II (BES-II)
LEReC cooling commissioning
Au on Au at 31.2 GeV/n (18.5 hours), 7.3 GeV/n (13 hours),
4.59 GeV/n (4 days), 3.85 GeV/n (2 hours)
Colliding beam modes
Au + Au at 9.8 GeV/n 6.1 weeks
Au + Au at 7.3 GeV/n 8.7 weeks
Au + Au at 4.59 GeV/n 0.9 weeks
Au + Au at 3.85 GeV/n 3.4 weeks
Au + Au at 100 GeV/n (accelerator studies) 0.4 weeks
Fixed target modes
LEReC cooling commissioning (dedicated)
Au at 3.85 GeV/n 24 weeks
Au at 4.59 GeV/n 2.6 weeks
Multiple modes of operation per year (11 modes in Run-19) now routine
11

## Slide 12
Recent performance of RHIC: Run-19
intrabeam scattering (IBS) – causing rapid emittance growth with
beam energy below transition energy (~24 GeV/n for Au beam)
space charge – causing large incoherent and incoherent tune shifts
persistent current in the superconducting magnets
Main challenges
4.59 GeV/n
Low Energy RHIC Electron Cooling (LEReC) to mitigate IBS
new 9 MHz cavities to reduce space charge effects (longer bunches)
new lattice to accommodate larger tune shifts
new magnet demagnetization cycle to reduce persistent current effects
Highlights
3.85 GeV/n
12

## Slide 13
Run-19 new magnet demagnetization cycle
reduced sextupole components in dipoles reduced
reduced orbit, tune and chromaticity drifts
13
A demagnetization cycle was developed and implemented to reduce persistent current effects in the RHIC superconducting magnets
regular cycle
demagnetization cycle
demagnetization cycle provided stable and reproducible conditions and enabled frequent energy changes needed for operations and LEReC commissioning

## Slide 14
Recent performance of RHIC: Run-19 (BES-II)
Run-19 Au + Au at 9.8 GeV/n
Run-19 Au + Au at 7.3 GeV/n
Integrated luminosity for highest priority colliding beam modes
Met integrated luminosity goals
14

## Slide 15
Beam Energy Scan II --- beam delivery overview
+ FXT at √ SNN = 7.7 GeV (2.9M)
√ SNN = 9.2 GeV (1.0M)
acquired parasitic to LEReC commissioning
582M
324M
51M
53M
15
201M
3.7M
+ 300 M (run18)

## Slide 16
RHIC availability reported to DOE (2002-2019)
availability = beam time / scheduled beam time (scheduled time excludes scheduled maintenance)
Typical time allocations 50K to 4K cool-down 0.5 week
initial set-up 1-2 weeks
changing species 0.5 week
accelerator studies (APEX) 16h every 2 weeks
maintenance 14h every 2 weeks
warm-up 0.5 week
Exceeded availability goal (80%) for 8 consecutive years (goal will be raised)
86
16
93

## Slide 17
LEReC was a $8.3M AIP, completed on schedule and within budget.
(Close-out report was signed by J. Gillo on 1/17/19.)
COOLING
in Blue RHIC ring
COOLING
in Yellow RHIC ring
64 m to IP2
Beam Dump
20° Bending Magnets
DC e- Gun
704 SRF
Booster Cavity
2.1 GHz Cu Cavity
9 MHz Cu Cavity
704 MHz Cu Cavity
Commissioning
Diagnostic Line 1
Commissioning
Diagnostic Line 2
RHIC TRIPLET
RHIC DX
180° Bending Magnet
e-
e-
LEReC Solenoids
Compensating (LF)
Matching (HF)
Merger/Transport
e-
Low Energy RHIC electron Cooling (LEReC)
(not to scale)
energies E 1.6, 2.0 MeV average current Iavg 27 mA momentum dp/p 5×10-4
luminosity gain factor 4
A. Fedotov
17
LEReC completed on schedule and within budget (8.3M$ AIP)

## Slide 18: LEReC accomplishments in Run-19
World’s first electron cooling with rf-accelerated bunched beam for BES-II
first “non-magnetized” electron cooling (all previous coolers used magnetization on the cathode, i.e. solenoid field)
first cooling of ion bunches in two rings using the same electron beam
first electron cooling of colliding beams
electron cooling was commissioned at
electron energy of 1.6 MeV with ion energy 3.85 GeV/n
electron energy of 2 MeV with ion energy of 4.58 GeV/n
electron cooling of RHIC stores with 111 ion bunches in both rings demonstrated at both 3.85 and 4.59 GeV/nucleon ion beam energies
18

## Slide 19: Effect of cooling at 4.59 GeV/nucleon
without cooling
with cooling
With cooling demonstrated 22% increase in STAR event integral over ~ ½ hour

## Slide 20: Colliding mode projections for Run-20
5.75 x 5.75 GeV/n
Lavg improvement factor, total = 2.4x Run-10
Lavg improvement factor, +- 70 cm = 2.3x Run-10
bunch intensity Nb : 1.1 → 1.35e9
rms emittance en : 2.5 → 2.5 mm
bunch length ss : 1.4 → 1.4 m
envelope function b* : 6.0 → 4.0 m
electron cooling : OFF
4.59 x 4.59 GeV/n
Lavg improvement factor, total = 1.5x Run-19
Lavg improvement factor, +/- 70 cm = 2.4x Run-19
bunch intensity Nb : 0.8 → 0.9e9
rms emittance en : 1.5 → 1.6 mm
bunch length ss : 3.8 → 2.3 m
envelope function b* : 4.5 → 4.5 m
electron cooling : ON

## Slide 21: Improvements for increased efficiency in Run-20
reduced filling times reduction
reduced number of mode changes
shortest possible bunches at space charge limit (x = -0.06 ?)
fixed and reliable Au beam parameters for cooling at 4.59 GeV (requires some intensity margin)
beam conditions that allow STAR to stay on during injection
longer STAR beryllium beam pipe (4 m) for increased longitudinal acceptance (deferred)
21
Run-20 will be very challenging with
Au + Au at 5.75 GeV/n (without cooling)
Au + Au at 4.59 GeV/n (with cooling)
up to 6 fixed - target energy runs
continued cooling commissioning at 3.85 GeV/n

## Slide 22
↓
complete
complete
complete
complete
Plan
2018: complete LEReC electron beam commissioning (DONE)
2019: LEReC cooling commission interleaved with physics (DONE)
2020: Use cooled beams at 2 (possibly 3) lowest energies
2021: contingency if event number goals not met
in progress
in progress
RHIC Run-20 and beyond
LEReC/BES-II plan from 2015 still holding
22

## Slide 23: Capital and accelerator improvement projects
Extended EBIS (CP) 2nd sc solenoid + gas cell completion for Run-20
RHIC cryo control system upgrade (CP)
RHIC quench detection (CP)
Linac vacuum system upgrade (AIP)
RHIC turbo pump upgrade (AIP)
RHIC cryo plant cold expander train upgrade (AIP)
Booster AC dipole (He-3↑)
PS: Booster sextupoles, Booster RF tuning (band III), AGS quad and sextupoles, H10/L20, BtA and LtB, RHIC IR8 tq (sPHENIX)
Siemens fire suppression system
AGS MM evaporation cooler
Vacuum lab equipment (ultrasound cleaner, oven)
trap length extension
Ongoing facility upgrades and maintenance for high accelerator availability

## Slide 24: Capital and Accelerator Improvement Projects Funding (FY2017-2025)
Previous upgrades in 2 categories:
  Performance upgrades
  Maintenance/upgrades of technical infrastructure
New upgrades now focus on 2. category
M&S+25 FTE is approx. 0.5% of RHIC hadron complex replacement value
remaining performance upgrade (until 2020)
24
Notes: AIP funding in place before start – DOE Financial Handbook, Chap. 24, issued May 2018 (also raises AIP max to $20M)

## Slide 25
Action items from 2014 and 2016 S&T reviews
Detailed response submitted in August, 2016. Upgrade with two principle components identified:
2014 no accelerator related recommendations
2016
“Develop a plan to improve the machine protection system for operation at ultimate luminosity and intensity of ion and proton beams. Submit to DOE NP by January 1, 2017.”
Implementation of slow (30-40 ms – now 6 ms) mechanical switch in series with the existing fast (<1 ms) thyratron high-voltage switch (DONE)
Additional MPS inputs to provide added protection
beam loss monitors (DONE)
fast orbit correctors power supplies (will be completed in Run-20)
beam position monitors (DONE)
radiofrequency cavities (DONE)
To complete prior to resuming high energy operation:
test delayed dump and energy extraction in operation (reduced risk in low energy operation)
test delayed energy extraction with higher intensity and full energy (end of run)
Notes: 2016 recommendation: MPS upgrade
“Develop a plan to improve the machine protection system for operation at ultimate luminosity and intensity of ion and proton beams. Submit to DOE NP by January 1, 2017.”

## Slide 26
Summary
Operation of RHIC: met or exceeded integrated luminosity goals in the last 3 years
  Run-17 p+p at 255 GeV, run coordinator Vahid Ranjbar
  Au + Au 27.2 GeV/n, run coordinator: Greg Marr
  Run-18 Zr + Zr / Ru + Ru at 100 GeV/n, Au + Au at 13.5 GeV/n
  + fixed target runs (at 3.85 GeV/n), run coordinator: Greg Marr
  Run-19 Au + Au at 9.8 GeV/n, 7.3 GeV/n, 3.85 GeV/n
  + fixed target runs (multiple energies), run coordinator Chuyu Liu
New and unique operation (e.g. Ru+Ru / Zr+Zr) enabled by previous upgrades
Flexibility of operations substantially increased: many and interleaved modes is now routine
Operation of RHIC: exceeded accelerator availability goals
First (in the world) electron cooling with RF accelerated electron bunches demonstrated in support of Beam Energy Scan II - LEReC, presentation by A. Fedotov
Facility upgrades and maintenance ongoing to maintain high accelerator availability
Future BES-II operations will employ the newly developed LEReC technology
26

## Slide 27
Back-up material

## Slide 28
Operational efficiency setup time
TRANSPARENT: low energy
INTRANSPARENT: high energy
BLUE: heavy ion runs
RED: polarized proton runs
Setup time: - for 1st species in run: from both rings cold to 1st physics store - for following species: from beginning of setup to 1st physics store
Run-19
7 days Au+Au 9.8 GeV
1 day for Au+Au 7.3 GeV
Run-17

## Slide 29
Operational efficiency availability reported to DOE
Facility Operations | FY2002 | 2003 | 2004 | 2005 | 2006 | 2007 | 2008 | 2009 | 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016
Research (physics, machine development) | 1379 h | 1238 | 1611 | 2282 | 1920 | 1117 | 1198 | 1352 | 2194 | 1563 | 1752 | 1290 | 2116 | 1909 | 1775
Beam Studies (APEX) | 58 h | 92 | 136 | 158 | 129 | 104 | 103 | 163 | 173 | 64 | 118 | 75 | 90 | 112 | 70
Setup/Tuning | 739 h | 2111 | 1439 | 1422 | 775 | 820 | 1228 | 1639 | 1163 | 1486 | 1202 | 1291 | 852 | 1368 | 851
Total Operating Hours | 2176 h | 3441 | 3186 | 3862 | 2824 | 2041 | 2529 | 3154 | 3530 | 3113 | 3072 | 2655 | 3060 | 3389 | 2696
Failure | 461 h | 975 | 791 | 696 | 699 | 882 | 516 | 773 | 721 | 762 | 526 | 517 | 466 | 485 | 554
Availability (%) | 82.5% | 77.9 | 80.1 | 84.7 | 80.2 | 69.8 | 83.1 | 80.3 | 83.0 | 76.3 | 85.4 | 83.7 | 86.6 | 87.5 | 83.0
Scheduled shutdown (maintain cool-down) | 252 h | 378 | 287 | 803 | 509 | 604 | 158 | 273 | 451 | 262 | 301 | 187 | 195.3 | 254.8 | 528
Injectors/RHIC Beam Operations | 17.2 wks | 28.5 | 25.4 | 31.9 | 24.0 | 21.0 | 19.3 | 25.0 | 28.0 | 25.5 | 26 | 20.0 | 22.1 | 25 | 25
Cryogenic Operation | 17.0 wks | 30.4 | 26.7 | 31.4 | 21.2 | 18.4 | 19.0 | 22.0 | 27.1 | 24.4 | 22.9 | 17.0 | 22.0 | 22.4 | 22
Availability = beam time / scheduled beam time (denominator excludes scheduled maintenance)
Availability goal: 80%
Typical times:
50K to 4K cool-down : 0.5 weeks
Initial set-up : 2 weeks
Changing species : 0.5 weeks
Beam studies (APEX): 16h / 2 weeks
Maintenance : 14h / 2 weeks
Warm-up : 0.5 weeks
Need to update through 2019

## Slide 30
RHIC Run-17 detail
p+p at 255 GeV, 15 weeks (2/12/17-5/30/17) STAR only
luminosity leveling
larger aperture beampipes at STAR and PHENIX
MPS tests
9 MHz cavity commissioning
Au + Au at 27.2 GeV/nucleon, 3 weeks (5/30/17 – 6/19/17) energy selection for concurrent operation with Coherent Electron Cooling Proof of Principle (CeC PoP)
p+p at 255 GeV – RHICf, 6 days (6/21/17 - 6/27/17)
radial polarization using spin rotators
CeC and LEReC gun commissioning 90 hours dedicated CeC PoP time
3 modes for physics

## Slide 31: Run-17 p+p at 255 GeV Notable items
all DX magnets moved back to symmetric position
only one experiment STAR (PHENIX being converted to sPHENIX)
STAR experimental beam pipe changed (from 4 cm ID Be NEG coated to 8 cm ID Be without coating; adjacent Al pieces are NEG coated on both cases); PHENIX experimental beam pipe changed (from 4 cm ID Be to 12.2 cm ID SS, both NEG coated)
1 of 3 new 9 MHz cavities installed in each ring and made operational (60 kV/cavity design, operated at 26 kV/cavity)
new ion optical system increases OPPIS beam by 20% (03/01/2017)
lens cryo upgrade - both superconducting solenoids run stably at 6 T
use of dual harmonic acceleration in AGS to reduce space charge near injection
MPS upgrade with additional permit inputs: RF, orbit correctors, 10 Hz orbit feedback, fast BPM readings (coherence signal); also lowered BLM thresholds at store
only transversely polarized beams at IP6 (no rotators)
many Yellow quenches after 4 of 5 new mechanical serial switches failed to close after beam dump (03/13/2017); as a result yi7-d6 shows small bypass current in a quench protection diodes - reduced ramp rate by factor of 2 to reduce the bypass current
β* squeeze from 1.5 to 1.2 m nominally 3 h into the store (beginning 03/13/2017)
special Yellow Au ramp for CeC PoP (γ = 29.229); 90 h dedicated CeC PoP time
beam from LEReC DC gun to gun line beam dump

## Slide 32
RHIC Run-18 detail
5 modes for physics
Zr + Zr and Ru + Ru at 100 GeV/nucleon, 12 weeks (3/8/18 – 5/10/18) store-by-store changes in ion species with Zr from LION/EBIS
Ru from Tandem
Au + Au at 13.5 GeV/nucleon, 4 weeks (5/10/18 – 5/30/18 and 6/4/18 – 6/18/18) 133 hours dedicated CeC PoP time (parasitic fixed target operation in parallel)
LEReC electron beam commissioning in parallel
Au at 3.85 GeV/nucleon on fixed target Au foil inside STAR, 4 days (5/30/18 - 6/4/18) BBQ for constant STAR event rate
BES-II preparation (injection and abort kicker tests, new hysteresis cycle)
Au in Yellow ring for CeC PoP at 26.5 GeV/nucleon, 186 hours
parasitic fixed target operation in parallel
Dedicated LEReC electron beam commissioning at 1.6 MeV
CeC electron beam development, 13 weeks (6/19/18 – 9/17/18)

## Slide 33
Mode 1A: LEReC cooling commissioning with 197Au79+ at 3.85 GeV/nucleon
Mode 1B: 197Au79+ on 197Au79+ at 9.8 GeV/nucleon particle energy
Mode 1C: 197Au79+ on 197Au79+ at 7.3 GeV/nucleon particle energy
Mode 1D: 197Au79+ at 7.3 GeV/nucleon particle energy on fixed target 197Au foil inside STAR (3.93 GeV/nucleon COM energy)
Mode 1E: 197Au79+ on 197Au79+ at 3.85 GeV/nucleon particle energy
Mode 1F: 197Au79+ at 3.85 GeV/nucleon particle energy on fixed target 197Au foil inside STAR (3.22 GeV/nucleon COM energy)
Mode 1G: LEReC cooling commissioning with 197Au79+ at 4.59 GeV/nucleon
Mode 1H: 197Au79+ at 4.59 GeV/nucleon particle energy on fixed target 197Au foil inside STAR (3.00 GeV/nucleon COM energy)
Mode 1I: 197Au79+ on 197Au79+ at 4.59 GeV/nucleon particle energy
Mode 1J: 197Au79+ at 31.2 GeV/nucleon particle energy on fixed target 197Au foil inside STAR (7.74 GeV/nucleon COM energy)
Mode 1K: 197Au79+ on 197Au79+ at 100 GeV/nucleon particle energy
RHIC Run-19 detail
11 modes for physics

## Slide 34
11 modes for physics (largest number to date)
Mode 1A: LEReC cooling commissioning with Au at 3.85 GeV/nucleon, 168 days
Mode 1B: Au on Au at 9.8 GeV/nucleon, 43 days
Mode 1C: Au on Au at 7.3 GeV/nucleon, 61 days
Mode 1D: Au at 7.3 GeV/nucleon, fixed Au target, 13 hours
Mode 1E: Au on Au at 3.85 GeV/nucleon particle energy, 24 days
Mode 1F: Au at 3.85 GeV/nucleon particle energy, fixed Au target, 2 hours
Mode 1G: LEReC cooling commissioning with Au at 4.59 GeV/nucleon, 18 days
Mode 1H: Au at 4.59 GeV/nucleon, fixed target, 4 days
Mode 1I: Au on Au at 4.59 GeV/nucleon, 6 days
Mode 1J: Au at 31.2 GeV/nucleon, fixed target, 18.5 hours
Mode 1K: Au on Au at 100 GeV/nucleon for APEX, 3 days
Run-19 Au+Au for Beam Energy Scan II (BES-II) and LEReC cooling commissioning
To do – make chart and timeline like on slide 7 (standardize presentation method)
To do – standardize plots
Run Coordinator: Chuyu Liu

## Slide 35
Extended EBIS
Scope
Add superconducting solenoid for trap length extension, expect +40% Au intensity
(early completion would shorten time for 2 highest energies in BES-II; also allows for next step in polarized 3He R&D)
Cost and funding
Schedule
2016 started solenoid acquisition
2020 planned completion largest risk (cost, schedule and performance): superconducting solenoid magnet
FY2016 | 2017 | Total
$475k | 1350k (P) | 1.8M
High-field 3He cell for polarization (collaboration with R. Milner et al. MIT)
trap length extension
Need to update

## Slide 36: Linac / BLIP upgrades
RHIC provides main support (takes ~10% of pulses, polarized) Isotope program is incremental user (~90% of pulses)
RHIC upgrades
Reliability – D. Raparia (RHIC funded CE) 5 kW solid state amplifiers, instrumentation, LLRF $1.5M – complete FY2016 as planned
Vacuum upgrade (planned RHIC AIP, FY2017/18) replacement of 50 original ion pumps, power supplies and controllers, $3.0M total cost, completion in 2021
First beam 1970
Need to update
Notes: 6 tube amplifiers in operation at Linac:
7651: 1 per tank, 5 kW pulsed power, need about 15/year (total $35k/year w/o overhead)
4616: 1 per tank, 200 kW pulsed power, need about 4/year (total $135k/year w/o overhead)
7835: 1 Per tank, 2.5 MW pulsed power, need about 4/year (total $520k/year w/o overhead)
8616: 1 Per tank, ?? kW pulsed power, need about 9/year (total $80k/year w/o overhead)

## Slide 37: RHIC MPS upgrade Run-18 progress
Serial switches
  shortened closing time from 30 ms to 7 ms (2350 to 550 turns)
  installed redundant trigger units in Blue and Yellow (prevents a failure mode observed in Run-17 test)
  modified hardware test protocol
Delayed energy extraction from sc magnets
  measured orbit and tune without and with delayed energy extraction (9 ms) – single bunch at store
New beam permit inputs
  All implemented except fast corrector PS input
  Control board designed – in production, alcove cable installation under way, software being developed
Test delayed dump and energy extraction in operation (reduced risk in low energy operation)
Test delayed energy extraction with higher intensity and full energy (end of run)

## Slide 38: RHIC Machine Protection upgrade Background
10-20 abort kicker pre-fires per year
Some pre-fires have damaged detector components, notably in asymmetric Cu+Au and p+Au operation
In Run-16, large orbit bumps installed to protect experiments concentrated off-momentum losses, QP diode damaged after beam abort and quench, required warm-up and replacement. Another QP diode damaged in MPS upgrade test in Run-17 (did not affect run).
Problem most severe with Au+Au at highest energies (~90% of beam loss from off-momentum secondary BFPP and EMD created beams)
Need a solution for sPHENIX (stored beam energy reduced in BES-II)
M. Purschke
PHENIX MPC start of run
after Yellow pre-fire 05/11/15
after Yellow pre-fire 06/01/15
Notes: orbit bumps first installed in Run-14
bo6-qd3-ps failure on 03/18/2016 led to beam abort, quench, and damaged diode in Run-16

## Slide 39: RHIC MPS upgrade Approach
PFN
abort kicker
thyratron tube
redundant mechanical relays (added)
slow (550 turns) no pre-fires
fast (< 1 turn) pre-fires
closes 1st not synchronized
closes 2nd synchronized with abort gap
Abort kicker pre-fires can be greatly reduced by moving HV switches out of tunnel, and by momentum collimation (also protects the QP diodes) => would be expensive upgrades (several $M)
More cost effective upgrade:
  Add serial switches to RHIC abort kickers to suppress pre-fires (+7 ms delay)
  Delay energy extraction from sc magnets after quench (necessity not recognized initially)
  New and modified inputs to permit link detecting precursors of large losses lower BLM thresholds at store, RF systems, Orbit corrector PS (fast and slow), fast BPM readings (coherence signal from 10 Hz feedback system)
  Monitor QP diode condition (measure voltage when diode becomes conductive) with sPHENIX run plan expect ~3-4x increase in distributed losses due to secondary beams from Au+Au luminosity over lifetime of RHIC
Abort kicker switches schematic

## Slide 40: RHIC MPS upgrade Run-18 progress
Serial switches
  shortened closing time from 30 ms to 7 ms (2350 to 550 turns)
  installed redundant trigger units in Blue and Yellow (prevents a failure mode observed in Run-17 test)
  modified hardware test protocol
Delayed energy extraction from sc magnets
  measured orbit and tune without and with delayed energy extraction (9 ms) – single bunch at store
New beam permit inputs
  All implemented except fast corrector PS input
  Control board designed – in production, alcove cable installation under way, software being developed

## Slide 41: RHIC MPS upgrade Run-18 tests
average orbit
rms orbit
tunes
7 ms delay in energy extraction of superconducting magnets is acceptable
No avg orbit changes with QS delayed
orbit and tunes after pulling quench link

## Slide 42: RHIC Quench Protection (QP) diodes monitoring
One QP damaged each in Run-16 and Run-17 became partially conductive due to radiation damage after heavy beam loss exposure, weakened dipoles strength
Continue program to test diodes measure voltage when diode become conductive (forward bias voltage)
900 QP diodes total => tested 18/166/168 in Run-16/17/18 (all dipole)
Only B10-D9 not in 3-10 V range (2.1V, 1.8V)
Diodes repeated: B10-D19 and B10-D9
After 18 years of operation no sign of systematic radiation damage, 2 diodes damaged in special events
Also work on measuring spacial distribution of forward bias voltage (warm complete, cold in preparation)
<= segmented damaged diode
Dewar for cold measurement =>

## Slide 43: RHIC MPS upgrade Run-19/20 Plans
Add outstanding permit input (fast corrector PS)
Complete cold measurements of damaged diode (spacial distribution of forward bias voltage)
Test delayed dump and energy extraction in operation (reduced risk in low energy operation)
Test delayed energy extraction with higher intensity and full energy (end of run)

## Slide 44
Summary
Operation of RHIC: met or exceeded integrated luminosity goals in the last 3 years
  Run-17 p+p at 255 GeV, run coordinator Vahid Ranjbar
  Au + Au 27.2 GeV/n, run coordinator: Greg Marr
  Run-18 Zr + Zr / Ru + Ru at 100 GeV/n, Au + Au at 13.5 GeV/n
  + fixed target runs (at 3.85 GeV/n), run coordinator: Greg Marr
  Run-19 Au + Au at 9.8 GeV/n, 7.3 GeV/n, 3.85 GeV/n
  + fixed target runs (multiple energies), run coordinator Chuyu Liu
New and unique operation (e.g. Ru+Ru / Zr+Zr) enabled by previous upgrades
Flexibility of operations substantially increased: multiple modes / year is now routine
Operation of RHIC: exceeded accelerator availability goals
First (in the world) electron cooling with RF accelerated electron bunches demonstrated in support of Beam Energy Scan II - LEReC, presentation by A. Fedotov
Facility upgrades and maintenance ongoing to maintain high accelerator availability
Future BES-II operations will employ the newly developed LEReC technology
44