## Slide 1
Experiment ID: AE-93
Title: Direct Measurements of Fields and Radiation in the Self-Modulated Plasma Wakefield Regime
PIs: V.N. Litvinenko, N. Vafaei-Najafabadi, C. Joshi, M. Downer
Funding source: DOE (Received)
Irina Petrushina
on behalf of AE-93

## Slide 2
AE-93 Collaboration
I. Petrushina, J. Yan, P. Iapozzuto, P. Kumar, R. Samulyak, V. N. Litvinenko, and N. Vafaei-Najafabadi | @ Stony Brook University, US
I.V. Pogorelsky, R. Kupfer, M. Babzien, Y. Jing, K. Kusche, M. Polyanskiy, M. Fedurin, M. Palmer | @ Brookhaven National Laboratory, US
J. Welch, R. Zgadzaj, M. Downer | @ University of Texas at Austin, US
W.B. Mori and C. Joshi | @ University of California Los Angeles, US
Acknowledging funding from DOE Grant DE-SC0014043
CORI @ NERSC facility operated under Contract DE-AC02-05CH11231
SEAWULF @ Stony Brook University

## Slide 3
Bubble Regime of LWFA Remains the Long-Term Goal
If compressed to ≈200 fs, it will drive plasma wakefields with bubbles as long as 170µm
Enabling external injection of ATF’s e- beam into accelerating phase with ≈25 GeV/m
Unique ATF’s CO2 laser system has
λ0≈10 µm and TW-class pulses

## Slide 4
Meanwhile: Self-Modulation Regime
Current 2 ps, 2 TW laser enables the exploration of LWFA in the self-modulation regime (SM-LWFA)!
Zhang, C. J. et al. Capturing relativistic wakefield structures in plasmas using ultrashort high-energy electrons as a probe. Sci. Rep. 6, 29485; doi: 10.1038/srep29485 (2016).

## Slide 5
Timeline proposed last year
2019
2019/2020
2020
2021
Direct measurement of the fields in a self-modulated (SM) laser wakefield accelerator (LWFA) using linac electron beam as a transverse probe.
Parametric study of laser evolution in the SM regime and study of novel physics predicted by simulations in this interaction.
Coordinate electron characterization, wake visualization and simulations to achieve comprehensive understanding of CO2-laser-driven wakefield acceleration in nonlinear regime.
Characterization of radiation-generation capability of the channel region in SM-LWFA using longitudinal probe. In particular, the role of direct laser acceleration (DLA) in enhancing the gamma radiation will be investigated

## Slide 6
Gas Jet
CO2 in
CO2 out
CO2 mirror
CO2 parabolic mirror
Electron Beam Probe
“Low Resolution”
BPM
“High Resolution”
BPM

## Slide 7
CO2 in
CO2 out
CO2 mirror
CO2 parabolic mirror
Gas Jet
Electron Beam Probe
“Low Resolution”
BPM
“High Resolution”
BPM

## Slide 8
Preliminary results:
typical image observed at the “Low Resolution” BPM
Laser
15 mm

## Slide 9
Preliminary results:
typical image observed at the “Low Resolution” BPM
Laser
Laser propagation
No gas released
EL = 4 J
15 mm

## Slide 10
Preliminary results:
typical image observed at the “Low Resolution” BPM
Laser
15 mm
Laser propagation
19.6 psi, EL = 2.5 J, e-beam 0.25 ps

## Slide 11
Electron probe beam has revealed periodic focusing and defocusing structures as well as unique features that potentially point to new physics for relativistic picosecond LPI
Laser
19.6 psi, EL = 2.5 J, e-beam 0.25 ps
Laser propagation
Focusing
Defocusing
Laser
Wakefield
Preliminary results:
typical image observed at the “Low Resolution” BPM

## Slide 12
Preliminary results: time evolution
Laser

## Slide 13
Channel Formation and Ion Collapse:
The electron probe is able to resolve the long term evolution of the ion channel
13
Ion collapse
Channel edges
Wake region
The electron probe is able to resolve the longer term evolution of the ion channel
5e17, EL = 15 J, 2 ps
t = +1 ps
t = 0
t = +3 ps
13
z (mm)
0
2
0.5
1
1.5
0
0.1
0.2
-0.2
-0.1
x (mm)
t = 0
0
2
0.5
1
1.5
0
0.1
0.2
-0.2
-0.1
x (mm)
z (mm)

## Slide 14
Plan for next year
14
The electron probe is able to resolve the longer term evolution of the ion channel
Implement high resolution BPM measurement for detailed study of fields in SM-LWFA with spatial resolution on the scale of the laser wavelength
Improve gas targets and diagnostics to enable simultaneous observation of e-beam probe diagnostic, YAG laser diagnostic, and forward electron spectrum
Obtain required data for a complete analysis of density and laser power scaling in SM-LWFA
Prepare plans for longitudinal CO2 injection of linac e-beam in preparation of blowout regime experiments

## Slide 15
Parameter | Units | Typical Values | Comments | Requested Values
Beam Energy | MeV | 50-65 | Full range is ~15-75 MeV with highest beam quality at nominal values | Nominal (50-65 MeV)
Bunch Charge | nC | 0.1-2.0 | Bunch length & emittance vary with charge | ~1
Compression | fs | Down to 100 fs (up to 1 kA peak current) | A magnetic bunch compressor available to compress bunch down to ~100 fs. Beam quality is variable depending on charge and amount of compression required. NOTE: Further compression options are being developed to provide bunch lengths down to the ~10 fs level | 100 fs
Transverse size at IP (s) | mm | 30 – 100 (dependent on IP position) | It is possible to achieve transverse sizes below 10 um with special permanent magnet optics. | 100 um (longitudinal probe) 1 mm (transverse probe)
Normalized Emittance | mm | 1 (at 0.3 nC) | Variable with bunch charge | 1
Rep. Rate (Hz) | Hz | 1.5 | 3 Hz also available if needed | Up to 1.5
Trains mode | --- | Single bunch | Multi-bunch mode available. Trains of 24 or 48 ns spaced bunches. | Single bunch
Electron Beam Requirements

## Slide 16
Configuration | Parameter | Units | Typical Values | Comments | Requested Values
CO2 CPA Beam | Wavelength | mm | 9.2 | Wavelength determined by mixed isotope gain media | 9.2
Note that delivery of full power pulses to the Experimental Hall is presently limited to Beamline #1 only. | Peak Power | TW | 2 | ~5 TW operation is planned for FY21 (requires further in-vacuum transport upgrade). A 3-year development effort to achieve >10 TW and deliver to users is in progress. | 2
 | Pulse Mode | --- | Single |  | Single
 | Pulse Length | ps | 2 |  | 2
 | Pulse Energy | J | ~5 | Maximum pulse energies of >10 J will become available in FY20 | 5
 | M2 | --- | ~2 |  | ~2
 | Repetition Rate | Hz | 0.05 |  | 0.05
 | Polarization |  | Linear | Adjustable linear polarization along with circular polarization will become available in FY20 | Linear
CO2 Laser Requirements

## Slide 17: Special Equipment Requirements and Hazards
Electron Beam
  Please indicate any special equipment that you expect to need, including (but not limited to) the transverse deflecting cavity, shaped bunch using mask technique, plasma capillary discharge system, bolometer/interferometer setup etc.:
CO2 Laser
  Please note any specialty laser configurations required here:
Ti:Sapphire and Nd:YAG Lasers
  Please note any specialty non-CO2 laser configurations required here: N/A
Hazards & Special Installation Requirements
  Large installation (chamber, insertion device, etc.): N
  Cryogens: N
  Introducing new magnetic elements: Magnetic Spectrometer
  Introducing new materials into the beam path: Y (Yag BPM & Mirror)
  Any other foreseeable beam line modifications: Y (Permanent magnet chicane for beam compression)

## Slide 18: Experimental Time Request
Capability | Setup Hours | Running Hours
Electron Beam Only | 0 | 0
Laser* Only (in FEL Room) | 0 | 0
Laser* + Electron Beam | 80 | 240
CY2020 Time Request
Capability | Setup Hours | Running Hours
Electron Beam Only |  | 
Laser* Only (in FEL Room) |  | 
Laser* + Electron Beam | 240 | 720
* Laser = Near-IR or LWIR (CO2) Laser
Time Estimate for Remaining Years of Experiment (including CY2020)

## Slide 19
Thank you for listening!

## Slide 20
20191105 Estimate of the general scale at the GPOP10 and the gas jet.
Laser energy: 2.4 J
Backing pressure: 18.3 psi
1 mm
1.3 mm
Corresponds to 0.375 mm and 0.506 mm @ the gas jet

## Slide 21
20191105 Estimate of the general scale at the GPOP10 and the gas jet.
0.94 mm
1.15 mm
Corresponds to 0.352 mm, 0.431 and 0.446 mm @ the gas jet
1.19 mm
Laser energy: 2.5 J
Backing pressure: 19.6 psi

## Slide 22
20191107: LWFA eProbe. Delay 12.1 mm. Energy dependence.
16:36:09
2.65 J
16:40:18
3.58 J
16:44:18
1.84 J
16:45:31
1.98 J
16:54:54
1.73 J
16:57:32
0.94 J
50 m