## Slide 1
Proposal ID: UED 306056
Proposal title: Structural phase transition and phonon excitation in non-equilibrium Cu2S
PI: Jing Tao
Condensed Matter Physics & Materials Science Division
Brookhaven National Laboratory
Funding Source (Received): U. S. DOE, BES, Division of Materials Science and Engineering, and Early Career Award
ATF Users’ Meeting 2019
Co-PI: Junjie Li, Yimei Zhu
Collaborators:
Brookhaven National Laboratory
PM: L. Wu, W-G. Yin, R. Konik, M. Dean, I. Robinson
ATF: M. Babzien, M. Fedurin, R. Malone, M. Palmer
CFN: D. Lu
University of Arkansas
J-Y. Chen
American Physical Society
Y. Li
Princeton University
R. J. Cava
University of Michigan
K. Sun

## Slide 2
Outline
Objective: understanding the mechanism of structural phase transition in Cu2S
Introduction: a background of the material
Justification: 1) why UED; 2) experimental plan
Benefit to DOE and potential impact
ATF Users’ Meeting 2019

## Slide 3
Reversible structure manipulation in Cu2S
T = 20 C
T = 90 C


Room temperature: low-chalcocite phase (L-phase; space group P21/c; semiconductor)
Above 90 C: high-chalcocite phase (H-phase; space group P63/mmc; insulator)
100 nm
100 nm
ATF Users’ Meeting 2019

## Slide 4
Reversible structure manipulation in Cu2S
J. Tao et al., PNAS 114, 9832 (2017)
ATF Users’ Meeting 2019

## Slide 5
Ultrafast x-ray absorption work suggests the transition is not governed by electronic mechanisms but by the copper ion self-diffusion rate.
TEM study implies an intimate interplay between electronic degrees of freedom and the lattice during the structural phase transition.
Solution:
Direct probes of the structural evolution using momentum-resolved techniques in the ultrafast time domain.
Motivation for UED study in Cu2S
ATF Users’ Meeting 2019

## Slide 6
A comparison of UED and ED patterns
H phase
L phase
t = 80 ps
t = -10 ps
(110)
(120)
The peak width (reflecting the change of crystal symmetry) and peak center (reflecting the change in lattice constants)
UED patterns
ED patterns
ATF Users’ Meeting 2019

## Slide 7
Peak width and peak center position measurements
Time constant ~ 2.3 ± 0.2 ps for the peak width and ~ 10.2 ± 0.3 ps for the peak center for the (120) peak. The temporal characteristic in crystal symmetry change is the same as in electronic structures.
Illustrated that crystal symmetry changes first, followed by lattice expansion.
Suggested the transition mechanism in Cu2S to be electron-phonon coupling.
ATF Users’ Meeting 2019

## Slide 8
Outline
Objective: understanding the mechanism of structural phase transition in Cu2S
Introduction: a background of the material
Justification: 1) why UED; 2) experimental plan
Benefit to DOE and potential impact
ATF Users’ Meeting 2019

## Slide 9
Ultrafast electron diffraction: the pump-probe method
Pump
Probe
Sample
Detector
Time Delay
Pump: initiate the process and set the time zero
Probe: take snapshot at different delay times
Delay time: optical length difference, 1um ~3.3fs
Camera speed: 1000 frame/s = 10-3 s Ultrafast: 100 fs = 10-13 s
Optical pump
Electron probe
electrons
spins
phonons
~100ps
~10fs
~1ps
ATF Users’ Meeting 2019

## Slide 10
Acceleration voltage ~ 3 MeV
106 electrons per pulse
Temporal resolution ~ 130 fs
SPECS
MeV UED at Brookhaven
800 nm laser pumping
Room temperature to liquid nitrogen cooling
ATF Users’ Meeting 2019

## Slide 11
H phase
L phase
H phase
L phase
Ring patterns vs. single-crystal patterns
Using single-crystal UED results:
Pros – better momentum sensitivity and structural characterizations.
Cons – less precision for lattice-constant measurements and more difficulty in UED sample preparation.
ATF Users’ Meeting 2019

## Slide 12
UED sample prep from 3D single crystals
A Fe3O4 UED sample prepared by FIB
Challenges in MeV-UED sample preparation from single crystals:
Uniformly thin for electron transparence (< 100 nm along beam direction)
Large lateral size of thin area (> 100 µm as diameter)
Approaches:
Mechanical polishing, focused ion beam milling, noble-gas ion sputtering
Nano-fabrication, lithography, and plasma etching
ATF Users’ Meeting 2019

## Slide 13
UED patterns from 3D single crystals
Single crystal VO2
Single crystal Fe3O4
MeV-UED, BNL-ATF
MeV-UED, SLAC
ATF Users’ Meeting 2019

## Slide 14
An XFEL pattern
M. Trigo et al., Nat. Phys. 9, 790 (2013)
An MeV-UED pattern
submitted
A comparison
T = 26 K
Capabilities enabled by single-crystal UED patterns
Single-crystal 1T-TaSeTe
ATF Users’ Meeting 2019

## Slide 15
From J. M. Zuo’s Group, http://cbed.matse.illinois.edu
Large cross sections from electron scattering
ATF Users’ Meeting 2019

## Slide 16
Momentum sensitivity to distinct atomic displacements
Our results indicate the primary role of the chalcogen sublattice during the dynamics.
J. Li, … J. Tao, submitted
ATF Users’ Meeting 2019

## Slide 17
Capabilities enabled by single-crystal UED patterns
A MeV-UED pattern
The pattern symmetry is corresponding to structure symmetry.
The intensity distributions are sensitive to atomic displacements / structure distortion.
The role of phonon excitation or relaxation in structural phase transition can be revealed during photoexcitation.
UED results and structural interpretations will be correlated to time-resolved observations of electron dynamics to understand the charge-lattice interactions.
ATF Users’ Meeting 2019

## Slide 18
Special Equipment Requirements and Hazards
Sample Cu2S and Setup
  Experimental setup is normal. No special equipment is needed.
Pump Laser Requirements
  800 nm (1.55 eV) with various pump fluence.
  Up to 9 m (140 meV) using OPA for selective phonon excitation.
Hazards & Special Installation Requirements
  Double-tilt sample stage.
  Cryogens: liquid nitrogen.
  No new magnetic elements.
  No new materials into the beam path.
  No beam line modifications.
ATF Users’ Meeting 2019

## Slide 19
Experimental Time Request
ATF Users’ Meeting 2019
Capability | Setup Hours | Running Hours
UED Facility | 2 - 3 days (48 – 72 hours) | 1 - 2 weeks (40 – 80 hours)
CY2020 Time Request
Capability | Setup Hours | Running Hours
UED Facility | 10 days (240 hours) | 3 – 6 weeks (120 – 240 hours)
Time Estimate for Remaining Years of Experiment (including CY2020)

## Slide 20
Timeline
ATF Users’ Meeting 2019
Year 1: Single-crystal Cu2S UED samples would be prepared and MeV-UED patterns with good quality will be obtained. Time-resolved UED results will be tested.
Year 2: Complete sets of time-resolved UED results will be collected. Data analysis and the structural interpretation(i.e., how are the intensity measurements associated with the structures, atomic displacements, and phonon modes)will be done.
Year 3: Time-resolved UED results will be collected and data analysis will be completed in a parameter space, i.e., under various temperatures and pumping fluences for a better understanding of photoexcitation mechanism.

## Slide 21
Cu2S is an energy-related material since it can be used in super-ionic conductors, memory, battery and thermoelectric devices. The outcomes of the project, i.e., a future understanding of the transition mechanism, will incubate additional applications in multiple areas by taking advantage of the extreme sensitivity in Cu2S structures/properties to certain external stimuli such as electric currents and fields.
Cu2S is also a quantum material, in which strong interplay between competing degrees of freedom, such as charge and lattice, is essential in the materials' functionality. The understanding of the electron-phonon coupling in this material will shed light in a wide group of materials in the future.
Benefit to DOE
ATF Users’ Meeting 2019

## Slide 22
Thank you!
ATF Users’ Meeting 2019
Notes: Thank you very much!