## Slide 1: Partow Electro-Optic Bunch Characterization
CEO: Payam Rabiei
Partow Technologies LLC, Vista, CA

## Slide 2: Project description
Title:
  Lithium niobite thin film modulators for electron beam characterization
DOE SBIR Phase I funded
DOE SBIR Phase II pending
Collaborators
  Rensaelear Polythechnic Institute, Prof. Ingrid Wilkei
  Argonne Wakefiled Accelerator, Dr. John Power

## Slide 3: Existing beam characterization method
Using electro-optic crystals a femtosecond pulse is modulated by electron beam electric field
The beam duration is characterized non-destructively
E-O crystal used
ZnTe(4pm/V),
or GaP (0.5pm/v)

## Slide 4: Proposed Electro-optic Mach-Zehnder modulator
An optical waveguide is used.
By applying electric field light phase is modulated
The circuit convert phase to intensity signal

## Slide 5: Proposed idea
Lithium niobite has much higher electro-optic coefficient (30pm/V) -> much better sensitivity
However it has not been used due to limitation for phase matching between electron-beam velocity and optical signal
Using our thin film lithium niobate on quartz this problem can be solved
It is fiber based so is much cheaper and easier to operate
Detection scheme is a simple spectrometer
  Allows characterization of beams as short as 0.1psec

## Slide 6: Calculated field profile in sensor

## Slide 7: Fiber-attached modulator (on Silicon)
6mm

## Slide 8: Calculated sensor bandwidth

## Slide 9: Proposed sampling device for DOE
Quartz substrate
E
Lithium niobate
E
E
Fiber coupler
Fiber coupler
Modulating arms
Poling direction

## Slide 10: Vacuum feedthrough
Available form several suppliers

## Slide 11: Measurement system
F-sec laser
Detector
Optical fiber
Synchronization
Variable delay

## Slide 12: Measurement system
Laser
High resolution spectrometer
Optical fiber

## Slide 13: Time-line for experiment
Last quarter of 2020
Beam parameters
  We should be able to characterize most beams but higher charge and higher repetition rate is advantageous
No hazard for oue equipment
Estimated beam time is 40-80 hours.
Need help from ATF to setup and perform tests