## Slide 1: eRHIC Accelerator Design V. Ptitsyn for the eRHIC design team

## Slide 2: RHIC – a High Luminosity (Polarized) Hadron Collider
RHIC
NSRL
LINAC
Booster
AGS
Tandems
STAR
6:00 o’clock
PHENIX
8:00 o’clock
Electron lenses
10:00 o’clock
Polarized Jet Target
12:00 o’clock
RF
4:00 o’clock
(Electron cooling)
2:00 o’clock
Operated modes (beam energies):
Au – Au 3.8/4.6/5.8/10/14/32/65/100 GeV/n
U – U 96.4 GeV/n
Cu – Cu 11/31/100 GeV/n
p – p 11/31/100/205/250/255 GeV
d – Au* 100 GeV/n
Cu – Au* 100 GeV/n
Planned or possible future modes:
Au – Au 2.5 GeV/n p – A* 100 GeV/n (A = Au, Cu, Al)
3He – A* 100 GeV/n (A = Au, Cu, Al)
p – 3He* 166 GeV/n (*asymmetric rigidity)
Achieved peak luminosities:
Au – Au (100 GeV/n) 195  1030 cm-2 s -1
p – p (255 GeV) 245  1030 cm-2 s -1
Other large hadron colliders (scaled to 255 GeV):
Tevatron (p – pbar) 110  1030 cm-2 s -1
LHC (p – p) 493  1030 cm-2 s -1
EBIS
BLIP

## Slide 4: eRHIC: QCD Facility at BNL Add an electron accelerator to the existing $2.5B RHIC including existing RHIC tunnel and cryo facility
e-
p
80% polarized electrons: 6.6 – 21.2 GeV
Pol. light ions (He-3) 17 - 167 (184*) GeV/u
Light ions (d, Si, Cu)
Heavy ions (Au, U)
10 - 100 (110*) GeV/u
70% polarized protons
25 - 250 (275*) GeV
Center-of-mass energy range: 30 – 145 GeV
Any polarization direction in electron-hadron collisions
protons
electrons
* It is possible to increase RHIC ring energy by 10%

## Slide 5: Lepton-nucleon scattering
Deep Inelastic Scattering (DIS) of electron, muon and neutrino beams on nucleons (fixed targets) has been a vital scientific exploration tool for several decades.
Experiments at SLAC (late 60s) led to the quark-parton model of nucleons, and ultimately to establishing QCD theory.
Numerous DIS experiments in 70-80s uncovered the momentum and spin distribution of quark constituents of proton and neutron
HERA (1991-2007): first electron-proton collider
Higher CME -> reach to the momentum distribution of quark and gluons at very low momentum fraction (x)
Selection of physics results:
precise data on details of the proton structure
the discovery of very high density of sea quarks and gluons present in the proton at low-x
detailed data on electro-weak electron-quark interactions
precision tests of QCD (as measurements)
Notes: In the process of DIS, a lepton particle penetrates into a nucleon and interacts in electroweak way with the constituents of the nucleon. Scattering of electron, muon and neutrino beams on fix targets has been a vital tool …
Then in 1991 the first electron-proton collider HERA started its operation. It brought DIS experiments to the area of very high CME which allowed to study with high resolution the momentum distribution of quark and gluons down to very low momentum fraction (x). Here is shown the selection of HERA physics results demonstrating…
HERA program was very successful, but as it often happens in science the results and discoveries made at HERA and in fixed target experiments opened new puzzles and put new questions.
Presently several designs of the future electron-hadron colliders (they are also often called electron-ion colliders) are developed in Europe and United States laboratories to address those questions.

## Slide 6: From HERA to future EICs
Heavy ion beams
Polarized e-,e+ (27.5 GeV)
Unpolarized protons (920 GeV)
Peak luminosity: 5⋅1031 cm-2 s-1
Polarized protons and light ions
(in addition to polarized electrons)
p
e-
e+
HERA
Much higher luminosity:
1033-1034 cm-2 s-1
Future colliders
Different (and variable) Center-of-Mass Energy range
Notes: Having mentioned the physics goals for future electron-ion colliders let’s see what the features of those colliders that should help to realize the goal. What the differences compared with HERA?

## Slide 7: Major physics objectives of eRHIC
Parton distributions and interaction in nuclei
eRHIC
Probing the nucleon’s spin structure
3-dimensional imaging of the nucleons
Mapping the gluon content of ions and protons;
High-density gluon state
In vacuum
Inside the nucleus
Notes: So, let’s look at the major objectives of future electron-ion colliders.
While, from previous experiments, we have rich information on the momentum structure functions of nucleon constituents, a high-luminosity EIC will be able to get data also on spatial distribution of the nucleon constituents, thus doing the imaging of the nucleons.
The proton spin puzzle needs to be fully answered. With EIC’s using polarized proton and electron beams the contribution from gluons to the proton spin can be measured in the region of low momentum fraction not accessible by RHIC polarized proton experiments. The contribution to proton spin from the orbital momentum of quark and gluons also can be measured.
One of the important (and somewhat surprising) results from HERA was the discovery of increasing gluon density at low x values. Mapping the gluon content of the ions and protons, verification whether it is saturated at some level and understanding the properties of this high-density gluon state is important task for future EICs. More efficiently the high-density gluon studies can be done with heavy ion beams. Because of that the use of the heavy ion beams is important feature of future EICs.
The physics objectives shown her mainly characterize the EIC’s as big microscopes (or femtoscopes) for study of nucleon structure
But with very high luminosity or with very high CME (on TeV scale) one can also effectively search and get better understanding of new physics:…

## Slide 8: eRHIC History Line
I. Ben-Zvi, J. Kewisch, J. Murphy, S.Peggs, “Accelerator Physics Issues in eRHIC”, Nuclear Instrumentations and Methods in Physics Research A 463 (2001), p.94.
eRHIC ZDR (the ring-ring design with L~1032 cm-2 s-1; ERL linac-ring as backup) (2004).
ERL-based eRHIC with separated re-circulating passes
  L~1034 cm-2 s-, high hadron beam intensity, upgrades in hadron ring, Space Charge Compensation
  Energy staging. First stage eRHIC: 4-5 GeV electron machine.
2012-2013: Work on cost optimized machine design.
Bottom-up cost estimate and optimization: minimal cost first stage (5 GeV) eRHIC with separated re-circulating passes: $530 mln. (detector(s) not included).
FFAG re-circulating passes + permanent magnets
  construction and operational cost savings
  No energy staging. Using FFAG passes widens the energy reach at moderate cost.
10 GeV FFAG design has been evaluated by Machine Advisory Committee (Nov. 2013) :
  ”The MAC congratulates the eRHIC design team for its ingenious and novel use of the FFAG concept.”
The “eRHIC Design Study” report includes the Accelerator Design Chapter presenting main features of eRHIC FFAG design.

## Slide 9: FFAG eRHIC Design
Up to 21.2 GeV electron beam accelerated with Energy Recovery Linac (ERL) inside existing RHIC tunnel collides with existing 250 GeV polarized protons and 100 GeV/n HI RHIC beams
Single collision of each electron bunch allows for large disruption, giving high luminosity and full electron polarization transparency
Use 2 FFAG magnet strings in RHIC tunnel to transport up to 16 beams
Considered permanent magnet design for FFAG lattice magnets
Cool hadron beam 10-fold in all directions using coherent electron cooling (CeC) at reduced intensity of hadron beam
IR design with β*= 5 cm using SC magnet technology and crab-crossing scheme
Average polarized electron current of 50 mA
1.32 GeV

## Slide 10: eRHIC beam parameters and luminosities
  Future luminosity upgrade
  The proton beam intensity is only at ~15% of present level.
  Open path to the moderate cost luminosity upgrade the future by increasing the hadron beam intensity (by an order of magnitude) and related hadron ring improvements:
  copper coating of beam pipe, beam diagnostics upgrade, RF system upgrade
  Luminosity above 1034 cm-2 s-1 can be reached

## Slide 11: Luminosity vs CEM
© T. Roser
Factors defining eRHIC luminosity:
Electron source current
Electron synchrotron radiation
Hadron beam-beam limit
Hadron space charge limit
Detector energy asymmetry requirements

## Slide 12: Why FFAG eRHIC?
Operation cost saving: potential of using permanent magnet technology for FFAG beam lines.
Dejan Trbojevic
Campaining for NS-FFAG eRHIC approach for many years.
Main arguments for using FFAG for beam recirculation:
Until 2013 the high luminosity ERL-based eRHIC has been designed with individual recirculation passes.
25.1 GeV
20.2 GeV
15.3 GeV
10.4 GeV
30.0 GeV
5.50 GeV
Construction cost saving: 2 FFAG beam lines instead of numerous separate recirculation passes .
Other view: Possibility to reach higher electron beam energy at the same cost.

## Slide 13: Demonstrating feasibility of NS-FFAG lattice design approach
Optimization of FFAG cell design to minimize synchrotron radiation, orbit spread, path length spread, …
Development of the lattice solutions for detector bypasses, straight sections, arc-to-straight matching sections, a technique for extraction into the IR beamline from the FFAG beamline.
Beam orbit measurements and corrections in the FFAG beam lines
Theoretical analysis methods and simulation tools have been developed to resolve the listed tasks.

## Slide 14: NS-FFAG approach for eRHIC
Non-Scaling Fixed Field Alternating Gradient (NS-FFAG) approach is used for eRHIC recirculation passes. It can transport large energy range.
eRHIC FFAG cell is comprised of two quadrupoles (F & D) whose magnetic axes are shifted horizontally with respect to each other by an offset Δ .
It can be considered as strongly focusing, bent FODO cell
  Small quadrupole offsets bend the beams adiabatically if bend radius is much larger than cell length
Orbit and optics dependence on the energy can be accurately found in paraxial approximation
High energy FFAG cell
© D.Trbojevic
© V. Litvinenko

## Slide 15: FFAG Recirculation Passes
Cell parameters for both FFAGs
© D.Trbojevic, S. Brooks
FFAG lattice was thoroughly optimized on several factors:
  energy acceptance
  orbit spread
  time-of-flight spread
  synchrotron radiation power
Transition from arc section to straight section is done by
gradual reduction of quadrupole offsets

## Slide 16: Synchrotron Radiation Effects
Energy loss compensation schemes :
  2nd harmonic (844 MHz) cavities; or
  main linac RF phase offset + high harmonic cavities
Total SR power 12 MW:
operation at 15.9 GeV top energy -> 50 mA
operation at 21.2 GeV top energy -> 18 mA
SR power loss per recirculation pass
Accumulated energy spread
Transverse emittance growth
© S. Brooks, F. Meot, V. Ptitsyn, O. Tchoubar
Ie=50 mA
Ie=18 mA

## Slide 17: Permanent Magnet Design
Sm2Co17
low-carbon magnetic steel
© W. Meng
FFAG lattice can be realized with permanent magnets
Expected construction and operational cost savings
Expected field quality < 10-2
SmCo: acceptable Br, good temperature stability, exceptional radation resistance
Different designs of 50 T/m permanent magnet
have been under consideration.
Including 1% dipole and quadrupole
correction coils.
Hybrid magnet
© N. Tsoupas
Halbach magnet

## Slide 18: e-Beam Bunch Pattern
The bunch pattern is defined by the length of electron circumference.
Presently one RF bucket shift between the bunches. Half-bucket shift at the top energy pass.
~ 900 ns gap to eliminate ion accumulation
For orbit measurements of individual passes: bunches in the gap are introduced. Every 16 RHIC revolution periods inject one bunch into the gap.
BPM bunches
Bunch pattern
in the Linac

## Slide 19: Beam Spreader and Combiner
© N. Tsoupas
Linac
Arcs
Placed on either side of the linac to separate/combine the 16 beams with different energies between FFAG arcs and CW Linac
Match optical function from the arc to the linac
Ensure isochronous one turn transport:
path length and R56 corrections
Betatron phase advance adjusters
15 cm horizontal separation between individual lines
Some of the lines are folded into the vertical plane to reduce path length difference
Vertical magnet chicanes are used for pathlength correction

## Slide 20: Electron Polarization in eRHIC
90% longitudinally polarized e-beam from DC gun with super-lattice GaAs-photocathode with polarization sign reversal by changing helicity of laser photons.
Only longitudinal polarization is needed in the IPs.
eRHIC avoids lengthy spin rotator insertions. Cost saving.
Integer number of 180-degrees spin rotations between the gun and IPs
With the linac energy of 1.322 GeV the polarization is longitudinal at both experimental IPs
To achieve 80% polarization up to 21.2 GeV harmonic cavities are used for the energy spread reduction
Polarized
e-gun
jd, gd
j0, g0
j
stays in horizontal plane
and rotates in arcs around
vertical direction
protons
electrons
with energy spread compensation
without energy spread compensation
Dashed – 21.2 GeV
Solid – 15.9 GeV

## Slide 21: Hadron-Electron Synchronization
Presently solution:
Hadron delay
Radial orbit offset in hadron ring:
Up to 16 cm path lengthening ability.
The RF harmonic switching method;
Used to operate with the hadron energies <50 GeV/n
Main synchronization condition:
the electron and hadron bunch repetition frequencies at the collision points have to be the same:
fbe = fbh
The hadron bunch frequency (at the fixed circumference) depends on the hadron energy
Hadron circumference lengthening

## Slide 22: SRF Linac
Multipass beam-breakup thresholds
for 16 pass operation (simulation results)
HOM frequency spread
Energy Recovery Linac:
422 MHz SRF cavities
120 m cold length
no quadrupoles
The beta function in the linac for 16 passes.
The horizontal and vertical optics are identical.
The grid lines separates the optics of each pass.
© Y. Hao
Additional SRF systems:
Energy loss compensation
(2nd harmonic)
Energy spread reduction
(3rd or 5th harmonic)

## Slide 23: Beam Dynamics
Beam-beam
e-beam disruption (emittance increase by ~30%)
Luminosity enhancement by e-beam pinching: 33%
Kink instability of hadron beam:
the feedback system (50-300 MHz) damps the instability
Hadron beam heating by electron parameter noise
Multi-pass BBU
Single bunch BBU
Electron-ion interactions
  Gap is introduced to prevent ion accumulation
  Fast ion instability simulations
Energy spread due to impedances: ~18 MeV
Compensation schemes are under studies
Kink instability threshold
Circulant matrix method
Two particle model
eRHIC parameter area
© Y. Hao
© G. Wang
e-ion instability

## Slide 24: Interaction Region with b* = 5 cm
10 mrad crossing angle with crab-crossing
Large enough aperture IR SC magnets for forward collision products and with field-free passage for electron beam
Recent IR design improvements on the magnet design with electron passage and integration of
detector components
90 degree lattice and beta-beat in adjacent arcs (ATS) to reach b* of 5 cm and provide effective chromatic corrections
Crab-cavities
p
e
Electron passage is arranged between SC coils of hadron magnet
© B. Parker
Forward detector components

## Slide 25: eRHIC R&D
  Prototyping of Gatling Gun polarized electron source
  Coherent electron Cooling PoP using 40 GeV/n Au beams in RHIC
  High average current ERL to support operation with high current e-beam
  Prototype eRHIC ERL with FFAG arcs (@ Cornell ?)
  Development of high gradient crab cavities within LARP
  Development of polarized He-3 (underway in collaboration with MIT)
Gatling gun
CeC PoP
QWR crab-cavity design (BNL)

## Slide 26: 50 mA polarized electron source R&D
Prototype with 20 potential cathodes has been built
Photo current from two cathodes during first test at Stangenes Industries (CA)
End of 2014: test with two cathodes in Stony Brook
BNL Gatling Gun:
the current from multiple cathodes is merged
I. Ben-Zvi
V. Litvinenko
J. Skaritka

## Slide 27: Proof-of-principle CeC Experiment in RHIC IP2
Helical Wiggler
Kicker Section
Modulator Section
Beam Dump
Accelerator
Section
Buncher
Cavities
@ A. Fedotov
© V.N. Litvinenko, I. Pinayev, G. Wang …
Proof-of-principle demonstration planned with 40 GeV/n Au beam in RHIC (2016)
Aim : to demonstrate longitudinal cooling of 40 GeV/u Au ion bunch in RHIC
Gun
Coherent Electron Cooling:
Idea proposed by Y. Derbenev in 1980, novel scheme with full evaluation developed by V. Litvinenko.
Fast cooling of high energy hadron beams is necessary for eRHIC luminosity
Made possible by high brightness electron beams and FEL technology

## Slide 28: Energy Recovery Linac Test Facility
ERL test facility at BNL.
E=20 MeV
Test of high current, high brightness ERL operation
SC RF gun was tested at 2MV
The beam from the gun expected by the end of 2014
Recirculation: 2015/16
Cryo-module
e- 15 – 20 MeV
SC RF Gun
e- 2.5MeV
Beam dump
50 kW 700 MHz
transmitter
Magnets, vacuum
Controls &
Diagnostics
Laser
1 MW
700 MHz
Klystron
e-
2.5 MeV

## Slide 29: eRHIC Schedule

## Slide 30: Summary
The present cost-effective design of ERL-based eRHIC relies on FFAG lattice of recirculation passes and reaches high luminosity (> 1033 cm-2 s-1) up to 125 GeV CM energy and 145 GeV CM energy for somewhat lower luminosity.
Studies of design issues specific for the FFAG lattice approach have not revealed showstoppers. Solutions have been found for the optimal FFAG lattice, spreader/combiner, orbit measurement and correction, ion gap formation … .
R&D is under way on high current polarized electron source (Gatling Gun), strong hadron cooling (Coherent electron Cooling) and high current ERL with key results coming in next two years.

## Slide 31: Acknowledgements
for their contributions to the FFAG eRHIC Accelerator design:
E.C. Aschenauer, S. Belomestnykh, I. Ben-Zvi, S. Berg, M. Blaskiewicz, S. Brooks, C. Brutus, T. Burton, A. Fedotov, D. Gassner, Y. Hao, Y. Jing, D. Kayran, V. N. Litvinenko, C. Liu, G. Mahler, G. McIntyre, W. Meng, F. Meot, T. Miller, M. Minty, B.Parker, I. Pinayev, V.Ptitsyn, T. Roser, J. Skaritka, O. Tchoubar, P. Thieberger, D. Trbojevic, N. Tsoupas, J. Tuozzolo, E. Wang, G. Wang, Q. Wu, W. Xu

## Slide 32: Luminosity versus Beam Energy
Luminosity versus hadron beam energy
  For 15.9 GeV electron energy or less
  Limited by hadron beam-beam parameter above 100 GeV and space charge below 100 GeV
Luminosity versus electron beam energy
  Limited by maximum SR power of 12 MW above 15.9 GeV

## Slide 33: Crab-crossing
Idea Introduced by R. B. Palmer SLAC PUB 4832
Used at KEK B-factory
Fundamental +3rd + 5th ,
ffund= 183 MHz, Vfund = 24 MV, V3rd=1.3 MV, V5th =0.09 MV
OR
Fundamental +2nd + 3rd
ffund= 244 MHz, Vfund = 22 MV, V2nd=4.4 MV, V3th =0.5 MV
Crab-cavity design on the basis of the quarter wave SRF cavities has been developed
@ V. Litvinenko, I. Ben-Zvi,
S. Belomestnykh, Q. Wu
QWR crab-cavity design (BNL)