## Slide 1: NS-FFAG GANTRY DESIGN
Dejan Trbojevic
Brookhaven National Laboratory

## Slide 2: INTRODUCTION
Future gantries for the ion cancer therapy need to have large momentum acceptance - longitudinal scanning - conclusions from the ion cancer workshop organized in January 2013, by NIH (US National Institute of Health), NCI (US-National Cancer Institute), DOE (US Department Of Energy) and DOD (US-Department of Defense).
Efforts should be put on: reducing the gantry cost, size, and complexity of operation.
Work on markers to be used for in city during the real time of treatment to provide information on ion-tumor interaction but also on the very low intensity beam measurements: precise dose, beam position, profile, and energy. There are some simple ideas at BNL of using the vacuum windows for determining the beam position, beam transverse profile and even the intensity (dose) (Peter Thieberger).
For the reduction of size in both carbon or proton gantries the superconducting magnets are clearly needed. The larger the field the smaller the size.
S.A.D without large magnets (Except the second scanner magent still large 20 (30) cm aperture.

## Slide 3
What is the OBJECTIVE?
- Reduce the size of an accelerator
- Improve its performance
- Reduce the cost
- Allow large energy range
The NEW carbon ion gantry replaces the 135 ton magnets of the Heidelberg gantry with 2 ton small BNL superconducting magnets.

## Slide 4: Lawrence equation
ρ
υ=ds/dt
EoC=0.93149 GeV/u
Eop= 0.938272 GeV
E=Ek + Eo
p/c=√ E 2 – Eo2
pproton 250 MeV =0.729 GeV/c
pcarbon 400 MeV/u=0.95142 GeV/c/u
Bρ proton 250 MeV [Tm] = 2.432 Tm
Bρ carbon 400 MeV/u [Tm] = 6.348 Tm

## Slide 5: Scanning above the patient
0.5 m
0.1 m
0.38 m
H1=1.4 m
q= 0.1/1.4=0.0713
q= 0.1/1.5=0.0667
0.38 m
H=2.5-3 m
0.1 m
CARBON IONS Minimum
H ~1.7 m
q= 1.2*0.38/6.34=0.071
q= 1.2*0.35/6.34=0.066
0.48 m
0.154
H1=2.175 m
Proton
1.2*0.3/2.43 H1= 0.67m
2m
Proton

## Slide 6: Spill extraction
τ ~ 1.63 μs @ 8 MeV/u
E1
E2
E1 ~ 24 cm
E2~ 20 cm
tumor
t1
t2
τ≈10 ms
20,000 turns/62/2
323/2 turns each spill
33.3 ms
~13 layers
~4 cm/ 3 mm=13.3
τ ≈0.298 μs  time of one turn around circumference of 64 m at 400 MeV/u

## Slide 7: Construction of the gantry
h=2.5 m
r=1.809 m
Proton Gantry – Ek=250 MeV  E=250 + 938.27 MeV  p=√E 2 - Eo2
Bρ= p/c = 2.432 Tm q = Bl/Bρ if B ~ 5T  then r = 0.486 m
Bavrg=Bρ/r = 1.344 T  If we raise the field to the superconducting
Φ=72o
l = 2p r =11.37 m
1m

## Slide 8
3.2 m
3.2 m
The state of the art proton gantry at PSI

## Slide 9: The state of the art proton gantry at PSI

## Slide 10: SAD – SOURCE-TO-AXIS-DISTANCE Scanning system: applied for patent by BNL
The maximum dose to the patient surface relative to the dose in the SOBP
increases as the effective source-to-axis distance (SAD) decreases. For a fixed,
horizontal beam, large SAD's are easy to achieve; but not for gantry beam lines. A smaller gantry with a physical outer diameter of less than 2 meters may have important cost implications. Such a gantry would require magnetic optics to ensure that the effective source-to-axis distance is large enough to provide adequate skin sparing.
S
Axis
S
Axis
S
Axis
S
Axis

## Slide 11: SCALING VS. NON-SCALING FFAG
0.03 meters
Orbit offsets are proportional to the dispersion function:
- To reduce the orbit offsets to ±4 cm range, for momentum range of dp/p ~ ± 50 % the dispersion function Dx has to be of the order of:
Dx ~ 4 cm / 0.5 = 8 cm
Dx = Dx * dp/p
0.9 meters
Linear magnetic field:
B = Bo+ r Go
3 cm

## Slide 12: Range of momentum = range kinetic energy
ΔEk carbon=400-195.4 MeV/u [27.3-8.2 cm]
ΔEk carbon=195.4-91.5 MeV/u [8.2–2.2 cm]
ΔEk proton=250-118.81 MeV [37.8-10.4 cm]
ΔEk proton=118.81-54.6 MeV [10.4-2.6 cm]

## Slide 13: State of the art C-gantry at Heidelberg
Weight of the transport components – 135 tons
Total weight = 630 tons - 19 m long. WEIGHT and SIZE

## Slide 15: Carbon Ek=400 MeV/u  Br = 6.35 Tm ( q= Bl/Br ) Warm iron magnets: B=1.6 T then r ~ 4.0 m Superconducting magnets B=3.2 T then r ~ 2.0 m
4.1 m
8.6 m
20.8
DIMENSIONS of the CARBON GANTRY
2.54 m

## Slide 16: Reducing the size and weight of the carbon gantry(135 tons 2 tons) with fixed field
2.543 m
72o
0.612 m
0.3 m
1.4 m
1.1 m
1.84 m
2.3 m
1.27
1.27
1.14

## Slide 17: Three Dimensional picture

## Slide 18: Amplitude functions in the carbon gantry
√βx, √βy (m1/2), Dx (m)
Dx
√βx
√βy
1.45 (2.1 m)
Dmax<8 cm

## Slide 19: Magnetic field required in the pipe and estimated maximum field in the coils
BD max = Bd + GD x = 4.27 - 102 *
BF max = Bf + GF x = -0.52+ 141.8 *
6 cm
insulation
Dipole, quad coils
Beam
r
4.54 mm
7.5 mm
-6.64 mm
-2.90 mm
3.80 T
4.6 T
0.54 T
-1.46 T
R=1.5 cm
Beam size : σT=√σ2 + (D dp/p)2
R=1 cm
Quadrupole Coil
140 T/m * 2 cm = 2.8 T

## Slide 20: AML combined function magnet design

## Slide 21: BNL- combined function magnet design

## Slide 22: Tracking particles in the carbon gantry for the energy range of 210-400 MeV/u

## Slide 23: CARBON GANTRY h=4.091m without magnification
θ=Bl/6.347=0.1/1.586=0.063
l=0.3m  Bmax=1.33 T

## Slide 24: CARBON GANTRY height 4.091m 5X magnification, scanning ±10 cm

## Slide 25: Concepts

## Slide 26: Replacing the large magnet

## Slide 27
3.0503 m
6.84166 m
0.5 m
3.7913 m
2.7607 m
Magnified x10 =±10cm

## Slide 28: CRYO-COOLERS: reliable, maintenance free, easy to operate

## Slide 29: NS-FFAG gantry with permanent magnets
7.375 cm

## Slide 30: Halbach Permanent Magnets
In reality it would be limited by:
The realistic size
The demagnetization effect

## Slide 31: What is innovative? The extreme focusing
29.7 cm
QF/2
QF/2
B
QD
B
LQF/2=6.05 cm
LB=3.8 cm
LQD=9.2 cm
LB=3.8 cm
250 MeV
31 MeV
16 mm
-10 mm
L QD=9.2 cm
L QF/2=6 cm

## Slide 32: Permanent Halbach Magnet NS-FFAG Proton Gantry
84o
r=2.71 m
h1=2.61 m
14 cells-27 cells
162o
h2=3.172 m
Proton kinetic energy range
30 – 250 MeV
ORBITS MAGNIFIED
-10<Dx<16 mm

## Slide 33: SUMMARY:
NS-FFAG gantries provide transfer of carbon ions with Δp/p=± 20% (200-400 MeV – or - 100-200 MeV) allowing longitudinal scanning as fast as the front accelerator can change the energy of the beam because the magnetic field is fixed for the required energy range
Weight is reduced for one or two orders of magnitude
Size of NS-FFAG the carbon gantry is of PSI proton one
Operation is simplified as the magnetic field is fixed
Scanning system is with SAD=∞
Beam size is adjustable with the triplet magnets
Triplet magnets do not need to be superconducting