## Slide 1: SQXF Coil End Part Design LARP-BEND
Miao Yu
05/05/2014

## Slide 2: BEND Design Diagram
Define
FAT and KEY
Input
Modify Code
Geometric:
Outer radius
Inner radius
Outer starting angle
Initial edge angle
Cable mid-thickness
Keystone angle
Run
User Design:
Number of cable on each side of guiding strip (0/n)
A-length
Estimated final edge angle
Minimize strain energy
Shift and Blunt
Output
Cable:
4 corner coordinates
50 cross-sections
End parts:
50 points on both OD spline and ID spline
CAD
Note:
Shift (-2 to 2): redistribute the twist along the guiding strip.
Blunt (0 to 0.5): relief the sharp nose

## Slide 3: Design Parameters
KEY and FAT
  key: keystone angle; fat: mid-thickness; 1/2: midpoint/nose
  Defined based on HQ coil inspection.
  All conductor group share the same key1=0.6, key2=0.3, fat1=1.09 and fat2=1.07
A-length
  Based on Roxie coil end magnetic design
  Defined to meet the first cable of each conductor group at the outer radius position
Final Edge Angle
  Roughly estimate and input to BEND
  BEND automatically calculates the suggested one
  Decision by designer
RE
LE

## Slide 4: L1 A-length
RE | CG1 | CG2 | CG3
A-length (mm) | 27 | 49 | 71
Shift (mm) | 0 | 0 | 38
LE | CG1 | CG2 | CG3 | CG4
A-length (mm) | 31 | 45 | 54 | 78
Shift (mm) | 0 | 0 | 0 | 25

## Slide 5: L2 A-length
RE | CG1 | CG2 | CG3
A-length (mm) | 35 | 49 | 83
Shift (mm) | 0 | 4 | 35
LE | CG1 | CG2 | CG3 | CG4
A-length (mm) | 35 | 54 | 94 | 94
Shift (mm) | 0 | 0 | 0 | 21

## Slide 6: Final Edge Angle
 |  | ROXIE INPUT |  | BEND INPUT |  | Δ
 | Block | # cond | angle | v1 | v1b | 
RE | 1a | 10 | 71 | 25 (65) | - | 6
 | 1b | 7 | 76 | 20 (70) | 14 (76) | 0
 | 2b | 5 | 82 | 9 (81) | - | 1
 | 3 | 16 | 68.5 | 22.5 (67.5) | - | 1
 | 4a | 8 | 76 | 14 (76) | - | 0
 | 4b | 4 | 81 | 11 (79) | - | 2
 |  | ROXIE INPUT |  | BEND INPUT |  | Δ
 | Block | # cond | angle | v1 | v1b | 
LE | 1a | 10 | 71 | 23.5 (66.5) | - | 4.5
 | 1b | 6 | 76 | 20 (70) | 15 (75) | 1
 | 1-2 | 1 | 78 | 13 (77) | - | 1
 | 2 | 4 | 82 | 10 (80) | - | 2
 | 3 | 15 | 68.5 | 22 (68) | - | 0.5
 | 3-4 | 1 | 72 | 19 (71) | - | 1
 | 4a | 8 | 76 | 13 (77) | - | -1
 | 4b | 4 | 81 | 10 (80) | - | 1
* Positive Δ: steeper at CERN

## Slide 7: Flexible End Part
Coil 1, LARP received the solid parts and wire cut the slits.
Well fit the coil, although some are a little tight.

## Slide 8: 1st Practice coil after W&C

## Slide 9: 1st Practice coil after W&C

## Slide 10: Flexible End Parts for Coil 2
LARP received the parts with slits and bridges
We wire cut the bridges to free the needed slits.
Round the edges, tips and corners
Plasma Coating

## Slide 11: Slits Dimension
LARP: 0.4 mm
LARP: 3 mm

## Slide 12: Round tip and edge
R0.5
R3.0
R1.5
R0.5
~ 1mm
R0.5
R1.5
R0.5

## Slide 13: End Parts for Coil 3
16, 14, 10, 0, 10, 14, 18
22, 14, 14, 10, 10, 18, 16
LARP received the parts with slits and bridges
We wire cut the bridges to free the needed slits.
Saddles w slits will be replaced after curing with the ones w/o slits.
Each part has 3 mm pin hole for alignment during winding.
Pin holes to connect LE saddle and its extension are abandoned. They are connected by two M6 screws.
QA and strain relief tap holes on RE saddles are M4 size.

## Slide 14: Slits Comparison
L1 | B1b-IR1 | B1b-IR2 | B1-IR3 | B1-IC1 | B1b-IC2 | B1b-IC3 | B1-IC4
Coil 1 | 7 | 9 | 10 | 0 | 0 | 9 | 10
Coil 2 | 9 | 14 | 18 | 0 | 0 | 14 | 16
Coil 3 | 10 | 14 | 18 | 0 | 10 | 14 | 16
L2 | B1-OR1 | B1-OR2 | B1-OR3 | B1-OC1 | B1-OC2 | B1-OC3 | B1-OC4
Coil 1 | 9 | 11 | 14 | 9 | 11 | 15 | 16
Coil 2 | 9 | 14 | 16 | 9 | 14 | 14 | 20
Coil 3 | 10 | 18 | 16 | 10 | 14 | 14 | 22
From SQXF coil 4, the slits design will be finalized.
The vendor will laser sintering the solid part, and then wire cut the slits.

## Slide 15: Splice Block
LARP has 3 sets of splice blocks
The splice blocks for coil 1 and coil 2 may be a little tight for the lead.
The splice blocks for coil 3 will be modified by offset the surface by 0.2 mm.
Require 4.145 mm for the lead
0.175 mm S2 glass tape
0.15 mm cable insulation
Sum = 4.235 mm

## Slide 16: SQXF Coil Pole
Room for Strain Gauge
LARP has 3 sets of poles. These poles have 6.35 mm pin hole
From LARP coil 4, the pin hole size will be changed to 5 mm
Except pin holes, all the other holes will be used as cooling channels

## Slide 17: Summary
The current end parts design worked well on SQXF coil 1. No more optimization needed until after autopsy of coil 1 ( the end of July)
Number of slits will be finalized after coil 2.
In stock, we have poles and splice blocks up to coil 3, and wedges up to coil 4 (more is coming soon). We will procure 3 more sets of poles and splice blocks in early June.

## Slide 18: Autopsy of Practice Winding Coils

## Slide 19: ROXIE vs. BEND at LE
ROXIE
Coil 1
BEND
Coil 2
90 deg.

## Slide 20: ROXIE vs. BEND at LE
45 deg.
ROXIE
Coil 1
BEND
Coil 2

## Slide 21: ROXIE vs. BEND at RE
90 deg.
ROXIE
Coil 2
BEND
Coil 1

## Slide 22: ROXIE vs. BEND at RE
ROXIE
Coil 2
BEND
Coil 1
45 deg.