## Slide 1: SQXF Coil End Parts Design CERN-ROXIE
Susana Izquierdo Bermudez. 05-05-2014
Joint LARP/HiLumi LHC Meeting (CM22)
QXF Coil Workshop

## Slide 2: Contents
Overview of the design process
  ROXIE differential Geometry Ends Module
  Design Parameters
  Design for the first iteration
Evolution of CERN end spacers

## Slide 3: ROXIE differential geometry ends
The strip is modeled by the base curve and the field of Darboux vectors that define the generators of the developable surface.
The mathematical basis to define these vectors are the same in ROXIE and BEND.
Main objective: minimize hard-way bend squared over entire block.
Base-line curve: ROXIE uses hyper-ellipses on cylinders.
Cable shape changes: ROXIE uses artificial inter-turn spacers. In BEND the cables in a block are packed together with slightly changing cross sections.
Guiding strip: In ROXIE, the guiding surface is the inner surface of the current block but the strain energy minimization can be done considering any conductor of the block.
Main differences among codes:

## Slide 4: Design parameters
PARAMETER | Upper bound | Lower bound
Order of the Hyper-Ellipse | 3 | 2
Ellipticity | 3 | 1
Inclination angle of the innermost turn | 83 | 60
TORS1/TORS2/TORS3/TORS4 | -2 | 2
Ellipticity (f) of the coil-end baseline
Order of the hyper-ellipse (Horder) that defines the baseline
β
Natural angle β for the innermost cable turn
Additional twist around the tangent vector (TORS).
Inter-turn spacers in between compensate for de-keystoning
GROUP A
GROUP B
GROUP C
Selection based on the available data from magnets designed with ROXIE differential geometry module. Feedback from winding to optimize these parameters.
Deterministic optimization algorithm “Extrem” to minimize the geodesic curvature and torsion on each individual block. Explored boundaries
Longitudinal position of each block. Optimize to minimize the multipole content of the integrated field and peak field in the conductor

## Slide 5: Design for the first iteration
1. First optimization of parameters that mainly affect to the strain energy on the cable
2. Optimization of parameters that mainly affect to peak field and field harmonics
3. Re-optimization of parameters that mainly affect to the strain energy on the cable
V1
Ellipticity, β , Horder
Ellipticity, β , Horder
Number of blocks, distribution of the conductors, z
Details about magnetic optimization (steps 1&2):
LARP CM20-HiLumi: 3D magnetic analysis and coil end design
Details about mechanical optimization (step 3):
End Parts Mini Review: https://plone.uslarp.org/MagnetRD/qxf/meetings/2013/20131015/

## Slide 6: Evolution of CERN spacers
V1
SPC1 IL
Cu
Oct-2014
V2
SPC1 OL
Cu
Oct-2014
V3
SPC2 and SQXF1
Cu
Jan 2014 April 2014
V4
SQXF2
Bad Nb3Sn
June 2014
V5
SQXF3
Nb3Sn
End July 2014
WP3 meeting
Review End Parts Design
Increase de Harmonic Order of the baseline ellipse (more roundish)
Pole converged to BEND design
Change angle last block IL
Minor changes:
Radius on the edges
Flexible features
Modify spacing among cables last block IL
2013 |  |  |  |  |  |  |  |  |  |  | 2014 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
October |  |  | November |  |  |  | December |  |  |  | January |  |  |  |  | February |  |  |  | March |  |  |  | April |  |  |  |  | May |  |  |  | June |  |  |  |  | July |  |  |  | Aug | 
42 | 43 | 44 | 45 | 46 | 47 | 48 | 49 | 50 | 51 | 52 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25 | 26 | 27 | 28 | 29 | 30 | 31 | 32 | 33
 | SPC1 |  |  |  |  |  |  |  |  |  |  |  |  | SPC2 |  |  |  |  | Preparation |  |  |  | SQXF1IL |  |  |  |  | OL |  |  |  |  | SQXF2 |  |  |  |  |  |  |  | SQXF3 |  | 
71.5˚67.3˚
68.5˚71˚
Now
CM22
Shorter coils with plastic end spacers to optimize ends
SQXF coils

## Slide 7: Remark!
Short coils with plastic end spacers (SPC1&SPC2) and first SQXF coil (SQXF1) are made with COPPER CABLE
Similar behaviour (in terms of end-spacer fitting, not in terms of cable mechanical stability) was observed in LBNL when using Nb3Sn and Cu cable
https://plone.uslarp.org/MagnetRD/qxf/meetings/2013/2013-12-17/

## Slide 8: From V1 to V2
2. Increase the harmonic order of the hyper-ellipse that define the baseline of the inner-most turn on the mandrel (Horder) to have more “roundish” spacers
Roxie
Bend
Roxie
Bend
Roxie
Bend
Roxie
Bend
Chart: z (mm)
| 0 | 33.63900000000001 | 40.816000000000003 | 47.499000000000024 | 53.689000000000021 | 59.386000000000024 | 64.592000000000013 | 69.306000000000012 | 73.529000000000025 | 77.259000000000015 | 80.496000000000009 | 83.240000000000009 | 85.495000000000005 | 87.295999999999992 | 88.634999999999991 | 89.588000000000022 | 90.182999999999993 | 90.494000000000028 | 90.580000000000041
Horder=2 | 43.184 | 40.308 | 38.852 | 37.159 | 35.251 | 33.147 | 30.868 | 28.432 | 25.86 | 23.176 | 20.406 | 17.585 | 14.757 | 11.936 | 9.23 | 6.617 | 4.193 | 1.959 | 0
Horder=3 | 43.184 | 43.018 | 42.664 | 42.036 | 41.093 | 39.807 | 38.167 | 36.176 | 33.85 | 31.224 | 28.345 | 25.275 | 22.088 | 18.864 | 15.65 | 12.559 | 9.593 | 6.828 | 4.293 | 2.037 | 0
SQXF | IL RETURN |  |  | OL RETURN |  | 
 | Block 1.A | Block 1.B | Block 2 | Block 3 | Block 4.A | Block 4.B
Harmonic order V1 | 2.1 |  |  |  |  | 
Harmonic order V2 | 3.2 | 3.0 | 2.8 | 3 | 2.8 | 2.3
Input Parameters | V1 |  | V2 | 
 | IL RE | OL RE | IL RE | OL RE
β | 82 | 81 | 81 | 79
Ellipticity | 1.8 | 1.8 | 2.23 | 1.804
Harmonic Order | 2.1 | 2.1 | 2.8 | 2.3
TORS1 | 0.0991 | 0.8879 | -0.3 | -0.6
TORS2 | -0.0286 | 1.0625 | -1.2 | -2.3
TORS3 | -1.0225 | -1.6606 | -1.8 | -2.3
TORS4 | -0.6854 | -1.1157 | -0.5 | -0.5
1. Modify ROXIE pole to have surfaces as close as possible to BEND design
Lower ellipse
Upper ellipse
IL RE V1
IL RE V2
OL RE V1
OL RE V2

## Slide 9: From V2 to V3
During the winding of the first short coil (SPC1) made with plastic spacers, there was a small gap (about 1 mm)
zoom
We decided (based on what we see and feedback from Shlomo) to increase the angle from 68.5° to 71°  0.65 mm steeper spacer
(both in lead and return end)

## Slide 10: V3
V3 was used in:
Second CERN short with plastic spacer (SPC2)
First (LE) and Second (RE) LARP coil with plastic spacers
First CERN SQXF coil (SQXF1)
Autopsy Second Short CERN coil with plastic spacers
Autopsy Second Short CERN coil with plastic spacers

## Slide 11: From V3 to V4
6
8
8
6
IL
6
8
6
6
0
0
0
0
0
OL
Flexibility
Radius on the edges
R = 0.5 mm
R = 0.2 mm
R = 0.5 mm
R = 0.5 mm
V3
V4
Number of cuts were defined based on SQXF1. SLS vendor to perform the cuts (from V4 on) instead of CERN
Alignment pins, holes and pockets for instrumentation  LARP design
QA hole M4
Strain relief hole M4
Threaded holes M6
Alignment pin D=3 mm

## Slide 12: From V4 to V5
Feedback from IL winding with V3 end spacers:
End saddles: small gap close to the straight section, big gap in the tip
V3-IR2: non negligible gap in one side
Chart: Turn #
Measured SQXF_1 | 71.9967 | 71.2345 | 70.5119 | 70.6755 | 70.61 | 69.9578 | 69.4399 | 68.7975 | 68.351 | 68.351 | 67.2783
QXF_V4 | 71 | 71.5478 | 71.5381 | 71.5284 | 71.5188 | 71.5091 | 71.4994 | 71.4897 | 71.4801 | 71.4704 | 71.4607
QXF_V5 | 71 | 71.547 | 71.0736 | 70.5994 | 70.1252 | 69.6509 | 69.1767 | 68.7025 | 68.2283 | 67.7541 | 67.3
Block # | wo | wi | Hwed
1.a V4 | 0.02 | 0.2 | 18.5
1.a V5 | 0.02 | 0.35 | 18.5
Original End Saddle (V4)
Test V5 (in-house printed end saddle)
Change the spacing between conductors in the last block to adapt spacer to the measured cable angle

## Slide 14: REFERENCES
Strain energy minimization in SSC magnet winding. J. M. Cook. IEEE transactions on magnetics, vol. 27, no. 2, march 1991
Coil End Design for Superconducting Magnets Applying Differential Geometry Methods. B. Auchmann and S. Russenschuck. IEEE transactions on magnetics, vol. 40, no. 2, march 2004
Field Computation for Accelerator Magnets: Analytical and Numerical Methods for Electromagnetic Design and Optimization. S. Russenschuck. Wiley-VHC 2010
Summary of the end part design process using BEND. R. Bossert. February 14, 2013. QXF WG meeting. https://plone.uslarp.org/MagnetRD/DesignStudies/QX-CD/Meetings/14022013/

## Slide 15: Coil length
 | Length (mm)
L1 | 195.463-0.250 = 195.213
L2 | 999
L3 | 315.537-0.250 = 315.287
L1
L2
L3
L_total = L1+L2+L3=1510-2*0.250=1509.5
Distance between end saddle and splice box = 2*0.250=0.500mm

## Slide 16: V1

## Slide 17: GROUP b: Inter-turn spacer
Block | # cond | wi | wo | Hwed
2.a | 2 | 0.17 | 0.02 | 15.00
2.b | 3 | 0.18 | 0.02 | 15.00
1.a | 6 | 0.20 | 0.02 | 15.00
1.b | 6 | 0.20 | 0.02 | 15.00
4 | 2 | 0.15 | 0.02 | 15.00
3.a | 7 | 0.15 | 0.02 | 15.00
3.b | 10 | 0.15 | 0.02 | 15.00
Selected parameters
Block | # cond | wi | wo | Hwed
4 | 2 | 0.17 | 0.02 | 14.70
3 | 3 | 0.18 | 0.02 | 14.70
2 | 8 | 0.20 | 0.02 | 14.70
1 | 9 | 0.20 | 0.02 | 14.70
6.a | 8 | 0.15 | 0.02 | 14.70
6.b | 10 | 0.15 | 0.02 | 14.70
5 | 16 | 0.15 | 0.02 | 14.70
Parameters selected based on data available from MQXC and 11T:
MQXC, final parameters
11T, as in v29

## Slide 18: GROUP C Parameters
Minimum Hard-way bending radius:
Inner Layer -> 11 cm
Outer Layer -> 14 cm
Objectives of the optimization: minimize hard-way bending and torsion.
SELECTED PARAMETERS
MAXIMUM CURVATURE VALUES FOR EACH BLOCK

## Slide 19: Hard-way bend on each block
Block 1.a
Block 2
Block 3
Block 4.a
Block 4.b
Additional plots available in the report 1310_QXF_MechanicalEndDesign_v3
Arc length of the conductor vs. geodesic curvature for the first and last conductor of each block
Block 1.b

## Slide 20: V3

## Slide 21: Winding IL
Broken
V3-IC1: Easy to place, nothing done on the spacer (it was slightly broken)
V3-IC2: Easy to place, corners rounded

## Slide 22: Winding IL
V3-IR1: The spacer wets in contact with the lower edge of the cable. A bit of material was removed and the corners were rounded
22
V3-IC3: Corners slightly rounded (negligible material removal)

## Slide 23: Winding IL
V3-IR2: The spacer wets in contact with the cable in the lower edge. A bit of material was removed and the corners were rounded
V3-IC4 No material removed. Non-negligible gap but it seems to be because we are not pushing enough the coil in the mid-plane (the surface of the spacer ≈ parallel to the cable)

## Slide 24: Winding IL
V3-IR3: No material removed. Non-negligible gap but it seems to be because we are not pushing enough the coil in the mid-plane (the surface of the spacer ≈ parallel to the cable)
General Overview lead end before curing

## Slide 25: IL, outer radius after curing
Small gaps except in the end saddle

## Slide 26: IL, inner radius after curing
Big gaps…the coil is not compacted enough during curing?

## Slide 27: IL, inner radius after curing

## Slide 28: Winding OL
V3-OC1:No material removed
V3-OR1:No material removed

## Slide 29: Winding OL
V3-OC2:Corners rounded
V3-OR2:Corners rounded

## Slide 30: Winding OL
V3-OC3:Corners rounded on the wedge side, very easy to place
V3-OR4 No material removed. Non-negligible gap but it seems to be because we are not pushing enough the coil in the mid-plane (the surface of the spacer ≈ parallel to the cable)

## Slide 31: Winding OL
V3-OC4 No material removed. Non-negligible gap but it seems to be because we are not pushing enough the coil in the mid-plane (the surface of the spacer ≈ parallel to the cable)

## Slide 32
OL, outer radius after curing

## Slide 33
OL, outer radius after curing

## Slide 34
V3-IC1: Easy to place, nothing done on the spacer (it was slightly broken [1])
V3-IR1: The spacer gets in contact with the cable in [2], lower edge. A bit of material was removed and the corners were rounded
V3-IC2: Easy to place, corners rounded
V3-IC3: Corners slightly rounded (negligible material removal)
V3-IR2: The spacer wets in contact with the cable in [3], lower edge. A bit of material was removed and the corners were rounded
V3-IC4: No material removed.
V3-IR3: No material removed.
2
2
1
3
3
4

## Slide 35: Second short Cu cable coil LE, right

## Slide 36: Second short Cu cable coil LE, left

## Slide 37: Second short Cu cable coil RE, right

## Slide 38: Second short Cu cable coil RE, right