## Slide 1: Oak Ridge Leadership Computing Facility JETSCAPE Collaboration Meeting
Bronson Messer
Acting Director of Science
Oak Ridge Leadership Computing Facility

## Slide 2: National Center for Computational Sciences Home to the OLCF and the Summit Supercomputer
65K ft2 data space
  Distributed across 4 controlled-access areas
  31K ft2 Very high load bearing (> 625 lb/ft2)
40 MW of high-efficiency highly reliable power
  Tightly integrated into TVA’s 161 KV Transmission system
  High-efficiency 3.0/4.0 MVA transformers
6,600 tons chilled water
  20MW cooling capacity at 21C/70F
  7,700 tons evaporative cooling
Expansion potential:
  Power infrastructure to 60MW,
  Cooling infrastructure to 70MW.
Notes: Approximately 60,000 square feet of unclassified data center floorspace
Approximately 30MW of available power and cooling to these data centers
  Titan Data Center-
    20,000 sq.ft. data center (Titan is roughly 4,500 sq.ft.)
    3 foot raised floor
    42 degree chilled water supply loop
    20 air handlers providing cooling to the equipment
    Operates around 1.25 PUE as a year-round measure
    Titan uses 3 cooling mediums to cool its components: air, R134A, and 42 degree water
  Summit Data Center-
    9,000 sq.ft. data center (Summit is roughly 5,000 sq.ft.)
    Concrete slab flooring with all infrastructure overhead
    72 degree medium-temperature water supply loop
    Has operated as low as 1.02 PUE within this data center
    Chiller-less operation for ~75% of the year
    Summit uses water cooling with direct-to-chip 72 degree water and the remaining heat is picked up by a rear-door heat exchanger that is mounted on each cabinet of compute, storage, and infrastructure inside this data center.
    Summit cabinets can operate as high as 47kW per cabinet
  Other data center space (~32,000 sq. ft.) is capable of housing a limited amount of sensitive systems

## Slide 3: Oak Ridge Leadership Computing Facility – a DOE Office of Science User Facility
Jaguar
2.3 PF Multi-core CPU 7 MW
Titan: 27 PF Hybrid GPU/CPU 9 MW
2009
2012
2017
2021
Frontier
>1,500 PF
Hybrid GPU/CPU 29 MW
Summit
200 PF Hybrid GPU/CPU 13 MW
1015
1016
1017
1018
Mission: Providing world-class computational resources and specialized services for the most computationally intensive global challenges | Vision: Deliver transforming discoveries in energy technologies, materials, biology, environment, health, etc.
Roadmap to Exascale

## Slide 4: ORNL Summit System Overview
Peak of 200 Petaflops (FP64) for modeling & simulation
Peak of 3.3 ExaOps (FP16) for data analytics and artificial intelligence
  2 IBM POWER9 processors
  6 NVIDIA Tesla V100 GPUs
  608 GB of fast memory
    (96 GB HBM2 + 512 GB DDR4)
  1.6 TB of non-volatile memory
  4,608 nodes
  Dual-rail Mellanox EDR InfiniBand network
  250 PB IBM file system transferring data at 2.5 TB/s
System Performance
Each node has
The system includes

## Slide 5: Frontier Overview
Partnership between ORNL, Cray, and AMD
The Frontier system will be delivered in 2021
Peak Performance greater than 1.5 EF
Composed of more than 100 Cray Shasta cabinets
  Connected by Slingshot™ interconnect with adaptive routing, congestion control, and quality of service
Node Architecture:
  An AMD EPYC™ processor and four Radeon Instinct™ GPU accelerators
    purpose-built for exascale computing
  Fully connected with high speed AMD Infinity Fabric links
  Coherent memory across the node
  100 GB/s injection bandwidth
  Near-node NVM storage
Researchers will harness Frontier to advance science in such applications as systems biology, materials science, energy production, additive manufacturing and health data science.

## Slide 6: Comparison of Titan, Summit, and Frontier Systems
System Specs | Titan | Summit | Frontier
Peak | 27 PF | 200 PF | ~1.5 EF
# cabinets | 200 | 256 | > 100
Node | 1 AMD Opteron CPU 1 NVIDIA K20X Kepler GPU | 2 IBM POWER9™ CPUs 6 NVIDIA Volta GPUs | 1 HPC and AI Optimized AMD EPYC CPU 4 Purpose-Built AMD Radeon Instinct GPU
On-node interconnect | PCI Gen2 No coherence across the node | NVIDIA NVLINK Coherent memory across the node | AMD Infinity Fabric Coherent memory across the node
System Interconnect | Cray Gemini network 6.4 GB/s | Mellanox Dual-port EDR IB network 25 GB/s | Cray four-port Slingshot network 100 GB/s
Topology | 3D Torus | Non-blocking Fat Tree | Dragonfly
Storage | 32 PB, 1 TB/s, Lustre Filesystem | 250 PB, 2.5 TB/s, IBM Spectrum Scale™ with GPFS™ | 2-4x performance and capacity of Summit’s I/O subsystem.
Near-node NVM (storage) | No | Yes | Yes

## Slide 7: Frontier Programming Environment
To aid in moving applications from Titan and Summit to Frontier, ORNL, Cray, and AMD will partner to co-design and develop enhanced GPU programming tools designed for performance, productivity and portability.
This will include new capabilities in the Cray Programming Environment and AMD’s ROCm open compute platform that will be integrated together into the Cray Shasta software stack for Frontier
In addition, Frontier will support many of the same compilers, programming models, and tools that have been available to OLCF users on both the Titan and Summit supercomputers
For CUDA programmers, the obvious course is to switch to HIP.
Summit is a premier development platform for Frontier
…but not for CUDA…

## Slide 8: What is HIP?
AMD’s Heterogeneous-compute Interface for Portability, or HIP, is a C++ runtime API and kernel language that allows developers to create portable applications that can run on AMD’s accelerators as well as CUDA devices.
HIP:
  Is open-source.
  Provides an API for an application to leverage GPU acceleration for both AMD and CUDA devices.
  Syntactically similar to CUDA. Most CUDA API calls can be converted in place: cuda-> hip
  Supports a strong subset of CUDA runtime functionality.

## Slide 9: How to Get Time on Summit
The US Department of Energy provides access to leadership supercomputers to facilitate capability-limited research for significant advances in science and engineering through the INCITE and ALCC User Programs
Access is awarded via annual competitive-proposal calls (requests greatly exceed availability)
  Innovative and Novel Computational Impact on Theory and Experiment (INCITE) aims to accelerate scientific discoveries and technological innovations by awarding, on a competitive basis, time on supercomputers to researchers with large-scale, computationally intensive projects that address “grand challenges” in science and engineering (http://www.doeleadershipcomputing.org/incite-program).
  ASCR Leadership Computing Challenge (ALCC) supports projects of interest to the Department of Energy (DOE) with an emphasis on high-risk, high-payoff simulations in areas directly related to the DOE mission and for broadening the community of researchers capable of using leadership computing resources (https://science.energy.gov/ascr/facilities/accessing-ascr-facilities/alcc/)
ALCC

## Slide 10: Four primary user programs for access to LCF Distribution of allocable hours
Chart: 
 | 50 | 20 | 20 | 10
50% INCITE
20% ALCC
ASCR Leadership Computing Challenge
10% Director’s Discretionary
Up to 20% ECP
Exascale Computing Project