## Slide 1: Mixed Elastic Scattering Format Proposal
M. L. Zerkle
CSEWG – Formats & Processing Committee
November 30, 2020

## Slide 2: Motivation
Selected nuclides exhibit both coherent and incoherent elastic scattering effects in the thermal energy range
More rigorous thermal elastic scattering treatment needed to support advanced moderator development
  Without treatment Bragg peaks either neglected (incoherent approximation) or to deep (coherent approximation)
Mixed Elastic Scattering format is a simple extension to ENDF-6 format
  Provides support for new capability in GNDS
No impact on existing TSL evaluations
Implementation
  7LiD and 7LiH TSL evaluations
  FLASSH TSL evaluation code (to be released)
  NDEX nuclear data processing code
  MC21 neutron transport code
Nuclide |  |  | 
natH | 1.7568(10) | 80.26(6) | 82.02(6)
1H | 1.7583(10) | 80.27(6) | 82.03(6)
2H | 5.592(7) | 2.05(3) | 7.64(3)
natLi | 0.454(10) | 0.92(3) | 1.37(3)
6Li | 0.51(5) | 0.46(5) | 0.97(7)
7Li | 0.619(11) | 0.78(3) | 1.40(3)
natB | 0.354(5) | 1.70(12) | 5.24(11)
10B | 0.144(8) | 3.0(4) | 3.1(4)
11B | 5.56(7) | 0.21(7) | 5.77(10)
23Na | 1.66(2) | 1.62(3) | 3.28(4)
Nuclide |  |  | 
natH | 1.7568(10) | 80.26(6) | 82.02(6)
1H | 1.7583(10) | 80.27(6) | 82.03(6)
2H | 5.592(7) | 2.05(3) | 7.64(3)
natLi | 0.454(10) | 0.92(3) | 1.37(3)
6Li | 0.51(5) | 0.46(5) | 0.97(7)
7Li | 0.619(11) | 0.78(3) | 1.40(3)
natB | 0.354(5) | 1.70(12) | 5.24(11)
10B | 0.144(8) | 3.0(4) | 3.1(4)
11B | 5.56(7) | 0.21(7) | 5.77(10)
23Na | 1.66(2) | 1.62(3) | 3.28(4)
Bound Scattering Cross Sections for Selected Nuclides (b)

## Slide 3: D(7LiD) Mixed Elastic Scattering TSL Evaluation
7LiD coherent and D incoherent elastic scattering cross sections approximately the same magnitude
Both coherent and incoherent elastic scattering effects captured in NDEX total elastic scattering cross sections

## Slide 4: 7Li(7LiD) Mixed Elastic Scattering TSL Evaluation
7LiD coherent elastic scattering component larger than 7Li incoherent elastic scattering
7LiD Bragg scattering more prominent in 7Li(7LiD) total scattering cross sections from NDEX

## Slide 5: ENDF-6 Format Proposal

## Slide 6: D(7LiD) Mixed Elastic Scattering Example
1.150000+2 1.996800+0 3 0 0 0 15 7 2
2.936000+2 0.000000+0 5 0 1 3374 15 7 2
3374 1 15 7 2
1.235573-3 2.67690-34 2.471146-3 5.24780-34 3.706719-3 3.757353-3 15 7 2
4.942291-3 1.386287-2 6.177864-3 1.386287-2 7.413437-3 1.386287-2 15 7 2
9.884583-3 2.595574-2 1.112016-2 2.595574-2 1.235573-2 2.595574-2 15 7 2
1.359130-2 2.992438-2 1.482687-2 3.549502-2 1.606245-2 3.549502-2 15 7 2
⁞
4.399400-2 4.399400-2 4.399400-2 4.399400-2 4.399400-2 4.399400-2 15 7 2
4.399400-2 4.399400-2 15 7 2
2.054202+0 0.000000+0 0 0 1 6 15 7 2
6 2 15 7 2
2.936000+2 8.937898+0 4.000000+2 1.047985+1 5.000000+2 1.213545+1 15 7 2
6.000000+2 1.390890+1 7.000000+2 1.575652+1 8.000000+2 1.765328+1 15 7 2
0.000000+0 0.000000+0 0 0 0 0 15 7 0
1.150000+2 1.996800+0 0 1 0 0 15 7 4
0.000000+0 0.000000+0 0 0 6 0 15 7 4
3.395004+0 1.976285+2 1.996800+0 5.000000+0 0.000000+0 1.000000+0 15 7 4
0.000000+0 0.000000+0 0 0 1 300 15 7 4
300 4 15 7 4
2.936000+2 0.000000+0 5 0 1 200 15 7 4
200 4 15 7 4
2.059042-2 4.931327-4 2.163677-2 5.181545-4 2.273629-2 5.444438-4 15 7 4
2.389168-2 5.720646-4 2.510579-2 6.010840-4 2.638160-2 6.315727-4 15 7 4
⁞
LTHR=3
Coherent Elastic
Incoherent Elastic
Inelastic
Bound incoherent scattering cross section