## Slide 1: Double Quarter Wave Crab Cavity −higher order modes
Binping Xiao
on behalf of the DQWCC team
May 5, 2014

## Slide 2: Outline
PoP
  HOM
  Beadpull for HOM
SPS
  Vertical version
  Issues with vertical version
  L-shape version
  Integration to the cavity
  HOM power for HiLumi
  Prototype
Summary

## Slide 3: PoP HOM
Chart: Simulated Frequency [MHz]
| 400 | 576 | 670 | 700 | 752 | 800 | 915 | 946 | 1077 | 1102 | 1113 | 1202 | 1246 | 1290 | 1352 | 1408 | 1409 | 1488 | 1549 | 1560 | 1626 | 1631 | 1634 | 1668 | 1706 | 1708 | 1725 | 1733 | 1776 | 1863
2-port Cold | 3.93 | 5.44 | 0 | 5.24 | 5.05 | 0 | 0 | 12.73 | 5.97 | 0 | 7.41 | 0 | 14.72 | 8.82 | 0 | 9.4 | 0 | 0 | 12.97 | 19.23 | 0 | 0 | 3.41 | 2.46 | 14.51 | 0 | 0 | 7.26 | 3.27
2-port warm | 3.25 | 3.9688 | 0 | 3.7188 | 3.2812 | 0 | 0 | 10.375 | 4.1562 | 0 | 5.2812 | 0 | 12.5312 | 6.6875 | 0 | 6.25 | 0 | 0 | 9.625 | 16.1562 | 1.7188 | 0 | -0.09375 | -2.125 | 11.4375 | 0 | 0 | 2.2812 | -1.1875
4-port warm | 3.25 | 4.3375 | 5.275 | 3.95 | 3.4875 | 3.5375 | 5.5625 | 0 | 3.625 | 2.375 | 5.125 | 9.25 | 12.125 | 6.25 | 6.125 | 7 | 0 | 7.625 | 9.75 | 16.25 | 1.5 | 0 | -0.875 | -1.75 | 10.875 | 0 | -1.25 | 3.375 | -1.75
2-port configuration
4-port configuration

## Slide 4
PoP Bead Pulling
1080 MHz
@Carlos Marques

## Slide 5
HOM System: Vertical version
Filter design
wide stop band (<80dB, several tens of MHz) at 400MHz, high pass at frequency 570MHz~2GHz
Hook coupler design
471 Qext at 579.8MHz (1st HOM),
507 Qext at 682.6MHz (2nd HOM),
233 Qext at 697.3MHz (3rd HOM).
HOM mapping
frequency, Qext, R/Q, mode configuration etc., up to 2GHz are calculated by Silvia (without filter) and Zenghai (with filter).
10mm x 20mm

## Slide 6
HOM System: issues
3cm longer than required
Some high Qext modes
High magnetic field area
Possible multipacting
Loss on the gaskets
81mT@
3.4MV
3mm thick Cu gasket
7 Watts @3.4MV

## Slide 7
HOM System: L shape filter
Triaxial shielding
HOM filter
136.5mm from
cavity center
Flanges to separate HOM filter from cavity, 3mm Cu gasket.
Slope for multipacting suppression
19.8mm in diameter
Chart: Frequency [GHz]
400±5 MHz
-87dB
580 MHz
-4 dB
683 MHz
-11.9 dB
With 0.3mm assembling error
and 0.1mm machining error
400 MHz
<-57.1dB
580 MHz
>-11.6dB
683 MHz
>-12.3dB

## Slide 8
HOM System: Integration
Compact enough to fit into cryomodule
Peak magnetic field on HOM is 72% of that on cavity.
Loss on the Cu gaskets: 150mW@3.34MV
Multipacting analysis is on going

## Slide 9
HOM System: improving coupling
Chart: Frequency [GHz]
L shape | 2386.4315 | 198.0302 | 1330.0568 | 1430.7781 | 4973.6235 | 6128.3304 | 3069.4875 | 18.4499 | 1040.7305 | 1402.7413 | 294.8264 | 9423369.5089 | 262.2591 | 41.0226 | 43.3357 | 195.1549 | 76.118 | 238957.8086 | 1508.7234 | 5532.6856 | 346.9312 | 215.9926 | 10913.8553 | 577.9275 | 21.9926 | 27.2878 | 28.1861 | 146.8419 | 174.0435 | 1090.5991 | 103367.154 | 8674.4791 | 5552.9557 | 15182.8331 | 2014.1027 | 45902.4108 | 49265.0898 | 1731.4805 | 5703.3578 | 2657.8211 | 30871.0903 | 0.29743 | 29.3854 | 29.9455
Coupling to the HOMs is improved
Impedance calculation will continue

## Slide 10
Chart: Frequency [MHz]
HOM System: Power estimation
 | F (MHz) | 579 | 683 | 697 | 742 | 919 | 943 | 973 | 980
 | Mode Type | m | h | m | v | h | m-shift | h-wg-mix | m
 | Qext | 2119 | 17858 | 7034 | 2422 | 255 | 124 | 89 | 124
Impedance | Longitudinal | 212239 |  | 83215 |  |  | 1274 |  | 939
 | Horizontal |  | 1198213 |  |  | 5360 |  | 569 | 
 | Vertical |  |  |  | 91161 |  |  |  | 
The HOM power is estimated to be 114 Watts.
Assuming the HOM frequencies shift in ±1 MHz range, in the worst case the power is 1003 Watt, 93% from mode at 742 MHz. (assuming the worst case that the beam is 5 mm offset)

## Slide 11
HOM System: Thermal analysis
  Assumes cavity operating at nominal deflecting voltage of 3.3 MV.
  Assumes only cooling by conduction with tube wall at 2K (cooling circuits will be designed later).
  Dissipated power in HOM hook made of SC niobium is 5mW, which leads to maximum temperature of 3K.
  Cooling channel larger than the previous version.
  Active cooling will be applied in the straight section of the HOM hook, and it is possible to extend it till the end of the tip.

## Slide 12
HOM System: prototyping
3-D printing + Cu coating.
Acetone etching for smoother surface.
Evaluating different ways to deal with joint loss.
Will figure out the ports connection based on new design.

## Slide 13
Summary
PoP has been studied to understand the HOMs in DQWCC
HOM system for SPS has been optimized (clearance, cooling capacitance, peak magnetic field, joint loss, multipacting, impedance budget etc)
HOM power has been estimated
Prototyping of the HOM system is on-going

## Slide 14
Thank you!