## Slide 1: SPS Crab Cavity Validation Run (2017-2018)
Alick Macpherson
BE-RF-SRF
Acknowledgments
Marton Ady, Vincent Baglin, Philippe Baudrenghien, Krzyzstof Brodzinski, Rama Calaga, Ofelia Capatina, Frederic Galleazzi, Erk Jensen, Antoine Kosmicki, Phoevos Kardasopoulos, Pierre Maesen, Eric Montesinos, Ghislain Roy, Benoit Salvant, Rogelio Tomas, Giovanna Vandoni.

## Slide 2: Overview
The SPS Installation and Integration Issues
Beam Issues, and Beam time requests
Schedule and planning
  Purpose of the SPS crab cavity validation program
    Validate Crab cavity design for proton beams
    Validate Crab cavity invisibility to proton beams when not on resonance
    Validate operational functionality & Machine protection mechanisms
      Overall goal => set inputs for final design

## Slide 3: General Overview
Crab cavity prototypes
  3 designs being taken forward to the SPS test
SPS Crab Cavity Cryomodule
  2 cavities installed in 1 cryomodule
    cavities of same type
  3 different cryomodules
    should be interchangeable
Baseline parameters
  Voltage = 3.4 MV/cavity
  Frequency = 400.79 MHz
  Cavity aperture: 84 mm diameter
  Operating Temperature= 2 K
  (assuming )
  RF power = 40 kW tetrode/cavity

## Slide 4: Crab Cavities in the SPS
  Cryogenics Infrastructure: Only SPS Pt 4 is feasible
  LLRF ~35 m away: Experimental cavern (ECA4) accessible with beam
  Location Availability: Space is not free end of 2015
  Limited access to SPS zone after SPS long shutdown (2013-2014)
  Features: Location just upstream of SPS Extraction pt for LHC beam 2
ECA4
ECA4
SPS Pt 4
Alcove

## Slide 5: LSS4: Simplified View
LLRF
ECA4( 35m)
RF Power
Cryo
CCM
TCF20
N2

## Slide 6: SPS LSS4: As it is now

## Slide 7: SPS LSS4: Crab Integration
Crab Cavities cannot be installed until COLDEX Installation removed
  COLDEX must be de-installed by end of 2015
LSS4 Alcove: This is now (again) a cryogenic installation.

## Slide 8: SPS Integration Issues
SPS operation must be independent of crab operational availability
  Crab Cavity module switchable from in-beam to out-of-beam position
  Need to increase opening angle of Y-chamber => New Y-chamber design
CM Movement: In out of beam line
  Cryomodule: moved with cavities cold and helium tanks full
  Duration: less than 20 mins. Acceleration: less than 0.2g
  Safety requirement: Movement is a remote operation
Dummy LHC Beam Pipe
SPS Bypass
3000 mm
510 mm
16o

## Slide 9: Y-Chamber Redesign
Model | ZII (mOhms) | Zx (kOhms/m) | Zy (kOhms/m)
Baseline 12 Degree | 2.8 | 0.33 | 0.31
16 Degree | 3.73 | 0.27 | 1.67
16 Degree Undulations | 3.69 | 0.41 | 0.53
Ellipsoid | 1.65 | 0.25 | 0.85
Proposed | 0.43 | 0.21 | 0.85

## Slide 10: Y- Chamber: Changes in shunt impedance
Propagating modes
No significant impedances within beam spectrum ()
Propagating modes do not reach cavity due to aperture reduction
Propagating modes into SPS reduced wrt existing design
Design endorsed by Impedance Working Group
Simulations:
Phoevos Kardasopoulos

## Slide 11: Integration Space
Vertical constraints: 700 mm (max) between beam axis and top of table
  Magnet Busbar + shielding + support Table
In Beam
Out of Beam
Top
Front:
Installation
500 mm
1200 mm
1250 mm
Integration constraints: https://edms.cern.ch/document/1360083

## Slide 12: Integration Space
Vertical constraints: 700 mm (max) between beam axis and top of table
  Magnet Busbar + shielding + support Table
In Beam
Out of Beam
Top
Front
500 mm
1200 mm
1178 mm
Integration constraints: https://edms.cern.ch/document/1360083

## Slide 13: SPS Ambient Magnetic Field
Initial 2D simulation results
  consider only main magnet busbars
  use worst case scenario:
Identify most critical position.
  Pt A: Outer surface of cryomodule
  Pt B: Outer surface of He Vessel
Cavity specifications require a ambient magnetic field
  With busbar shield, cryomodule shield factor = 200 (achievable)
  10mm busbar shielding to be installed (2015)
 | In-Beam Stray field [mT] |  | Out-of-Beam Stray field [mT] | 
Busbar shielding | Pt A | Pt B | Pt A | Pt B
Stainless steel (or no cover) | 0.4 | 0.2 | 0.6 | 0.3
Constructional steel, 2 mm thick | 0.3 | 0.2 | 0.4 | 0.2
Constructional steel, 10 mm thick | 0.1 | 0.1 | 0.2 | 0.1
Details: https://edms.cern.ch/document/1377806
To be confirmed by measurement in September 2014
A
B

## Slide 14: Beam Line Around the Cryomodule
Pressure [Pa]
Pressure drop:
2 orders
Cryotrap
 | No cryotrap | 0.5m cryotrap | 1.0m cryotrap
No pump | 100% | 1% | 0.55%
With pump | 10% | 0.55% | 0.2%
Cryo trap: Transmission ratio
Example: Cryo Trap
Vacuum Conditions: Required case operational conditions = 10-10 mbar
  Present SPS vacuum conditions: ~ 10-9 - 10-8 mbar
  Crab Cavity cryo module should not cryo pump the SPS beam line
Vacuum infrastructure + Standard RF warm-cold transition at CM
  Require: NEG Coating or cold trap or baked aCarbon on each side of CM
  Differential pumping: Implemented at beam pipe transition diameter
With some beam line modification PCavity <10-10 mbar is achievable

## Slide 15: Vacuum Considerations
IN
COLDEX
OUT
V1
DCUM 41731
V3
DCUM 41753
V4
DCUM 41757
V2
DCUM 41737
Vacuum gauge
Sector 430
Sector 431
Circulating beam
Vacuum gauge
Vacuum gauge
Present Situation
IN
CRAB
OUT
V1
DCUM 41731
V4
DCUM 41757
Vacuum gauge
Sector 430
Sector 431
Circulating beam
Vacuum gauge
Vacuum gauge
Vacuum gauge
Differential pumping
Isolated beam pipe zone
NEG or cold trap or aCarbon
What is foreseen

## Slide 16: RF Power and Orbit Drifts
Beam position in Cavity:
Crab Tetrode
  Should provide 40 to 50 kW (to be tested)
Power constraints => beam must stay centred
  SPS closed orbit drift in ramp up to 6mm
  Correctors at SPS Pt 4 in interlock chain
    complicates orbit centering
  Slow orbit drift to be countered by support table adjustment, driven by LLRF
    Support Table no longer simple
Tetrode Power vs Beam offset

## Slide 17: SPS Validation Program: 5 Steps
Cavity setup, conditioning, beam injection and initial cavity operation
Long Term Effects: Coasting Beam [120 -270 GeV]. Low Intensity
  Single + multi-bunch + trains: Emittance growth, Dispersion etc
Short Term Effects: Cycling Beam: [26-450 GeV]. Low intensity
  Direct crabbing measurements: Head tail monitor
  Global and Local Crabbing schemes
Machine Protection Issues and Quench studies
High Intensity Studies
  Impedance Studies and Invisibility of detuned cavities
Cavity operation with beam: Cryo limit of 8-12 hrs operation
  Each MD step: 3 slots of 8hrs of beam => 24 hours of beam per cavity
  Test of 2 cavities: 10 days of dedicated MD time spread over 2 years
      This is ~1/3 of allocated SPS MD beam time

## Slide 18: SPS Beam
Crab cavities need dedicated MD time
  LHC beams:
    cannot be in when LHC beam extracted
  SPS Fixed Target:
    large beams at injection & slow extraction
Coasting Beam: Both crab dispersion and long term emittance growth
  E_Beam > 120 GeV to distinguish crab effects from natural emittance growth
6σ
LHC Beam
SPS Natural Emittance Growth Measurements |  |  |  |  | 
Energy [GeV] | Intensity [x 1011] | Tunes Qx/Qy | RF Voltage [MV] | dεx/dt [%/hr] | dεy/dt [%/hr]
55 | 1 | 0.13/0.18 | 3 | 140-370% | 57%
120 | 0.5 (12b) | 0.13/0.18 | 2.0-4.0 | 100-300% | 40-90%
120 | 0.1 | 0.13-0.33 | 2.0-4.0 | 18% | 17%
270 | 0.4 | 0.13/0.18 | 3 | 20-23% | 14-24%
What’s changed after LS1? => participate in MDs in 2015

## Slide 19: LLRF Operation
Operation:
  RF is ON
  Strong RF feedback + tune controls
  Cavities are on-tune at all time.
Filling, ramping or operation with transparent crab cavities
  Cavities kept on-tune with small voltage (0.5 MV?) + active tuning system
    Effect on beam nullified by counter-phasing the cavities
    RF feedback is used with on-tune cavity to provide stability and keep the beam induced voltage zero if the beam is off-centered.
When crabbing is required (at flat top)
  Drive counter-phasing to zero.
  Degree of local crabbing controlled by synchronously changing voltage or phase in both cavities.
Phase PU
TX
Cavity Controller
Global feedback
TX
Cavity Controller
400MHz RF

## Slide 20: Machine Protection
Closed Orbit with global deflection
  LHC beam: 450 GeV, Cavity Voltage: 3 MV
    Worst Case: In-phase cavities kicking the centre of the beam
    Closed orbit at 90o phase advance: ~1mm offset, no amplitude growth.
Interlock Strategy:
  Hardwired Interlocks: Inputs into BIS (Beam Interlock System)
    Interlock on vacuum valves
  Software interlocks: Inputs into SIS (Software Interlock System)
    Table Position (In/Out of beam positions)
    Power load on tetrodes
LLRF Mitigations and Interlocks
  LLRF FB loop: Timescale of  Time for quench mitigation actions
  SPS test to validate cavity mitigation schemes for failures/quenches
  TX fault: machine operation can continue if cavity detuned above RF freq.

## Slide 21: Schedule Issues
SPS Crab Validation Run: 2017 and 2018
SPS Crab schedule: Available Online
  Please see http://kiwi.web.cern.ch/kiwi/Crab_SPS/index.html

## Slide 22: Schedule: Cavity + CryoModule TimeLine

## Slide 23: Schedule: SM18 + SPS
SM18:
  CavityTesting, Cryo Module assembly and testing, Infrastructure validation
SPS
  Preparation of Infrastructure, Validation of Services, Operations Interface
SPS Activities
SM18 Activities

## Slide 24: SM18 RF Test facility
M9 Bunker: Horizontal Tests
  LHC cryomodule
  HIE-ISOLDE cryomodule
  And later: FCC 400 MHz project
M7 Bunker: Horizontal Tests
  CRAB cryomodule
  SPL half cryomodule
  And later: 800 MHz project
M7
V3
V4
SM18 RF Area

## Slide 25: Summary Comments
Integration
  Integration of Crab infrastructure ongoing. Alcove space fully used
  2015-2016 Christmas stop must be used to remove COLDEX
SPS Beam Time
  Crab Cavity Validation needs dedicated SPS MD time
  Initial estimates of MD time request: 5 x 24 hrs per cavity
  MD program must include:
    Crab functionality, cavity invisibility, LLRF op, failure mitigation
  LLRF conceptual design now advancing
Planning and schedule
  2015-2016 Christmas stop: installation of crab infrastructure in SPS
  1st Crab Cryomodule installed 2016-2017 Christmas stop
  2 Cryomodule Installation periods (Xmas stops): can’t hot swap modules
  Use 2016 for cryomodule “sector test” in SM18

## Slide 26: Integration: Cryo Module Interfaces
3 different cryomodule: Evolving toward consistent interfaces
  Designs not finalised yet, but should be harmonised and made consistent
    Simplifies support table design, cryomodule exchange, alignment steps
Support Table functionality becoming more complex
  Once cryo module design is frozen, support table design can be finalised
Relative Position of power coupler wrt crab cavity reference position |  |  | 
Cryomodule | Longitudinal Distance Between Couplers | Transverse offset wrt beam axis | Height (beam axis to centre of waveguide)
DQW | 900 mm | 0 mm | 960.45 mm
RFD | 1050 mm | -113 mm | 944.94 mm
4-Rod | 890.4 mm | 25 mm | 939.85 mm
Example: Cryomodule designs as of week 18 2014