## Slide 1: Wideband Slotline Kicker, Power Amplifiers, Infrastructure Upgrades
John Cesaratto (SLAC)
J. Dusatko, J.D. Fox, K. Pollock, C. Rivetta, O. Turgut (SLAC)
D. Alesini, A. Gallo, M. Zobov (INFN-LNF)
Stefano De Santis, H. Qian (LBNL)
W. Hofle, G. Kotzian, E. Montesinos, and C. Zanini (CERN)
* Work supported by the U.S. Department of Energy under contract DE-AC01-76SF00515, U.S. LHC Accelerator Research Program, and by the EU FP7 HiLumi LHC – Grant Agreement 284404

## Slide 2: Progress over the last year
Optimization of slotline model for maximum bandwidth AND maximum shunt impedance, port optimization
Comparison of stripline, slotline, and cavity designs
Kicker Design Report completed and published at both SLAC and CERN.
  SLAC-R-1037, http://www-public.slac.stanford.edu/SciDoc/docMeta.aspx?slacPubNumber=slac-r-1037
  CERN-ACC-NOTE-2013-0047, http://cds.cern.ch/record/1639553
Two designs chosen: Array of striplines, slotline designs
Four power amplifiers evaluated, ongoing discussions with vendors to provide amplifiers with characteristics we desire.
Infrastructure improvements and additions in SPS Faraday cage and tunnel.

## Slide 3: Kicker Design Report

## Slide 4: Review Slotline Characteristics
Coaxial type (Faltin)
Fermilab type (McGinnis)
Ridged type

## Slide 5: Coaxial Type Slotline Kicker
Two coaxial waveguides coupled to the beam pipe by slots
Parameters of the model optimized for a bandwidth of 1 GHz
1 m long, with 40 slots, compiles with stay-clear restrictions
Acceptable amount of broadband impedance to the SPS (collaboration with INFN-LNF)
Transfer Function
Gain
Phase

## Slide 6: Slotted kicker in Kicker Design Report
Direction of the beam
0°
180°

## Slide 7
No feedthroughs – Coaxial-type
Gaussian bunch, σz = 2 cm
25 ns
Wake Potential
Longitudinal Impedance
Real
Imaginary
Courtesy of M. Zobov

## Slide 8: S11 Parameter

## Slide 9
With feedthroughs
Real
Imaginary
Longitudinal Impedance
Wake Potential

## Slide 10: Impedance Comparison
Real
Imaginary
Without feedthroughs
With feedthroughs

## Slide 11: Lateral feedthrough
Parameters | Length (mm)
Coax diameter | 5
Coax shield | 11.5
Waveguide height | 66.4
Stripline thickness | 5
50 Ohm: coax and enclosed stripline

## Slide 12: S11 Parameter
Improved matching
Chart: Characteristic impedance along taper
| 0.0 | 25.0 | 50.0 | 75.0 | 100.0 | 125.0 | 150.0 | 175.0 | 200.0 | 225.0
 | 50.165 | 50.1749 | 50.3581 | 50.4772 | 50.6821 | 50.9578 | 51.3489 | 51.8778 | 52.2362 | 49.9425
At stripline
At coax

## Slide 13: Longitudinal Impedance
No feedthroughs
90 deg feedthrough
Improvement in impedance spectrum
With lateral feedthrough ports
However, not mechanically desirable
Because of one degree of freedom
Concern for heating, expansion
Lateral feedthrough

## Slide 14: Slotline Port Geometry
Down selection needed on port design
  CERN mechanical engineering department to weigh in on complexity and feasibility
  3 port layouts
    Tapered, lateral provide best matching
  Currently, waiting for ME resources, following stripline development
Once choice is made on the port layout, another round of EM optimization needed, then mechanical design can begin.

## Slide 15: Estimating Directivity
Beam induced power important to understand and be able to handle
Initial estimates on the directivity of the beam induced power have been performed in HFSS
  Plane wave excitation has been used to estimate the relative power levels in the upstream and downstream ports of the slotline kicker
  Results have shown that at 1 GHz, for the power upstream to downstream is 1:300
  When a port design is chosen for the slotline, additional measurements are necessary, as well as complimentary measurements in GdfidL and/or Particle Studio
Power downstream
Power upstream
Plane wave along beam axis

## Slide 16: Comparison of Stripline and Slotline
At low frequencies, the striplines have slightly higher kick strength.
However, the slotline can effectively cover the bandwidth up to 1 GHz.
MDs with the new kicker prototypes are ABSOLUTELY ESSENTIAL to validate and confirm the technologies, bandwidth and kick strength needed.
CERN plans to install:
2 Striplines
1 Slotline

## Slide 17: Current Efforts
Stripline
  Beam induced power estimation as a pickup (common-mode)
  Construction at CERN
Slotline
  Mechanical design
  feedthrough optimization and port matching
Striplines to be installed before initial beam startup in September 2014
Use first MD times in Fall 2014 for measuring beam induced power to validate estimation and formulate plans for protecting amplifiers.
Slotline prototype not expected until 2015

## Slide 18: Power Amplifiers
As important as a kicker is for the feedback project, so are power amplifiers.
Existing amplifiers from AR Kalmus
  Nominally 100 W, de-rated to 80W
  5 amplifiers purchased in 2011
  Used reliably for MDs 2011 – 2013
  Non-optimal time-domain behavior
  Gain (+/- 4 dB) and phase variation over operating band
Specifications:
  Frequency = 20 – 1000 MHz
  Power = 250 – 500 W
  Instantaneous BW
  100% amplitude modulation
  Linear phase across band
Working with manufacturers to improve impulse response and fidelity of amplifiers
Existing power amplifiers
Gain
Phase
Δ = 90°
Δ = 9 dB

## Slide 19: Power Amplifiers Evaluation
Evaluation of 4 power amplifiers in 2013, loaned to us by manufacturers (work by K. Pollock)
  Amplifier Research 250W1000AM4
  Amplifier Research KAW-2300 (modified)
  MilMega 80RF1000-250
  R&K GA020M102-5454R
Developed testing methods and procedure to characterize amplifiers in both time and frequency domains
  Typical frequency domain measurements with network and spectrum analyzers, measure frequency response, phase linearity
  Time-domain measurements performed with 4 GS/s high speed DAC with the capability of generating arbitrary signals
    Burst signals, much like those needed for feedback
R&K (Japan) seemed to have most desirable characteristics in time-domain, but tests on going
Specifications:
  Frequency = 20 – 1000 MHz
  Power = 250 – 500 W
  Instantaneous BW
  100% amplitude modulation
  Linear phase across band
Time-domain measurements
Time (ns)
Time (ns)
Time (ns)
Time (ns)

## Slide 20: Power Amplifiers Evaluation
Evaluation of 4 power amplifiers in 2013, loaned to us by manufacturers (work by K. Pollock)
  Amplifier Research 250W1000AM4
  Amplifier Research KAW-2300 (modified)
  MilMega 80RF1000-250
  R&K GA020M102-5454R
Developed testing methods and procedure to characterize amplifiers in both time and frequency domains
  Typical frequency domain measurements with network and spectrum analyzers, measure frequency response, phase linearity
  Time-domain measurements performed with 4 GS/s high speed DAC with the capability of generating arbitrary signals
    Burst signals, much like those needed for feedback
R&K (Japan) seemed to have most desirable characteristics, but tests on going
Specifications:
  Frequency = 20 – 1000 MHz
  Power = 250 – 500 W
  Instantaneous BW
  100% amplitude modulation
  Linear phase across band
Frequency-domain measurements (Gain/phase)

## Slide 21: R&K (Japan)
We are working with manufacturers to improve impulse response and fidelity of amplifiers
  Cater to our specifications
  Expect modified amplifier to test from R&K
R&K time-domain test using a 40 MHz burst signal
  Able to remove tail of signal
  Many manufacturers don’t have the capability to make the time-domain measurements we do
  Therefore, we need to use our equipment to fully characterize the amplifiers
Status on R&K
  As of April, they’ve informed us that they need to redesign the 90 degree hybrid combiners
  Seems to be a common issue using several stage amplifiers
  Additional 2.5 months of development
R&K’s impulse response measurements
Before
After

## Slide 22: New Power Amplifier Developments
We’ve reached out to additional amplifier vendors and have had a very positive response of interest in working with us
Additional companies
  Rhode & Schwarz
  AR Pennslyvania
  Intertronic Solutions
Intertronic Solutions (Canada)
  Use many small GaN transistors and combine them.
  Built 5 – 300 MHz, 400 ultra flat phase power amplifiers for SNS
  Written proposal for a 20 – 1000 MHz 25 W prototype, scale power from there.
    20-1000 MHz instantaneous BW
    >20 dB gain, flat to +/- 1 dB
    Flat phase to +/- 10 deg
    Pure class A mode of operation
Transfer function, GaN transistor
SNS amplifiers

## Slide 23: New Power Amplifier Developments
We’ve reached out to additional amplifier vendors and have had a very positive response of interest in working with us
Additional companies
  Rhode & Schwarz
  AR Pennsylvania
  Intertronic Solutions
Rhode & Schwarz
  Most amps are developed for broadcasting transmission purposes
  Berlin development laboratory, a 80 – 1000 MHz, 125 W module, with goal of 1 kW in summer 2015.
  Sent us preliminary result, using 200, 400, 800 MHz continuous input signals at 100 W output
  Another case where the vendor does not have the equipment necessary to properly characterize the amplifier for our needs. They have invited us to Berlin to test the amplifier with our high speed DAC
  Very excited to work with us, “…we will do everything humanly possible to make sure we are your amp of choice.”
Rhode & Schwarz test of BC125
Source Signal
Amp Output
400 MHz

## Slide 24: Location of Kickers, Infrastructure
SPS Sextant 3, LSS3
Housed in the second half of the 321 period of the SPS.
Approximately 8 m of usable space following the dipole magnet
8 new 7/8” cables pulled to kicker location during LS1
Power amplifiers still needed
  Essential for operation of new kickers!
  Critical items for post LS1 operation
Courtesy of E. Montesinos

## Slide 25: CERN’s Efforts Prepping Tunnel
new cables:
1 drive striplines
1 drive slot line
6 returns from loads
option: relay box for amplifier monitoring (needs preparations) using the three old cables to pos. 319
Cable end in SPS Faraday cage
Cable end in SPS tunnel
Courtesy of W. Hofle, G. Kotzian