## Slide 1: Cryomodule Summary & Action Items
Tom Nicol – Fermilab
May 8, 2014
It’s a group effort – Many thanks to
Jean Delayen, HyeKyoung Park, Subashini De Silva, Rocio Olave at ODU
Sergey Belomestnykh, Qiong Wu, Silvia Verdú-Andrés, Binping Xiao at BNL
Zenghai Li at SLAC
Ofelia Capatina, Luis Alberty, Rama Calaga, Giuseppe Foffano at CERN
Tom Jones, Shrikant Pattalwar, Graeme Burt at STFC and Lancaster, UK
and many others...

## Slide 2: Dress Cavity and Cryomodule Highlights
Three cavity designs.
  RF Dipole (Old Dominion University and SLAC)
  Double Quarter Wave (Brookhaven)
  4-Rod (UK)
A single vendor for all US dressed cavity assemblies.
Funding source for US dressed cavities is a $1M 2013 Phase 2 SBIR award to Niowave for the crab cavity cryomodule design and fabrication. Due to changes in the down-select process and SPS testing requirements, the original scope is not relevant.
Niowave built the prototype for all three designs.
No dressed cavities have been built.
The cryomodule for both US cavities will be designed and built at CERN. Daresbury may design and build their own cryomodule.
Goal is to have as much commonality in the three cryomodule designs as possible.

## Slide 3: Dress Cavity and Cryomodule Highlights (cont’d)
Goal is at least two cryomodules tested in SPS to ensure at least one US design.
BNL is coordinating the double quarter wave cavity design.
  Bare cavity design at BNL
  Dressed cavity design in collaboration with CERN
ODU is coordinating the RF dipole cavity design.
  Bare cavity design at ODU
  Dressed cavity design in collaboration with Fermilab
The tuners will be a joint effort between BNL, ODU, and CERN.
The input coupler will be provided by CERN.
CERN will assist with pressure vessel code compliance issues.
In addition to being involved in the RF dipole dressed cavity design, Fermilab will play provide oversight of fabrication at Niowave.
Eventual need for the LHC is 32 cavities + 4 spares.

## Slide 4: Preliminary high level cavity and cryomodule schedule
2013-2014 | 2015-2016 | 2017 | 2018-2021 | 2022
Cavity Testing & Prototype Cryomodule | SPS Cryomodule Fabrication | SPS Beam Tests | LHC Cryomodule Construction | LHC Installation
Current focus of all groups is installation and testing in the SPS

## Slide 5: SPS tunnel location
Cryomodule
Bypass beamline

## Slide 6: SPS tunnel location

## Slide 7: Crab cavities in the LHC

## Slide 8: Sample crab cavity cryomodule in the LHC
4 cm with 2 cavities each
2 cm with 4 cavities each
1 cm with 8 cavities

## Slide 9: RFD dressed cavity (ODU) Waveguide HOM option
Helium vessel
HOM waveguide
Input coupler
Vertical HOM
Pickup port
Dummy
beam tube

## Slide 10: Functional requirements specification

## Slide 11: Ranking criteria (draft)

## Slide 12: RFD dressed cavity (ODU) Coaxial HOM option
Coaxial HOM

## Slide 13: RFD cryomodule (ODU)
FPC
Tuning system
Cryo jumper
Thermal and magnetic shielding not shown
Side loaded vacuum vessel
Waveguide
Beam gate valve
Cold to warm transition
Tuning frame

## Slide 14: RFD cryomodule (ODU)
Vacuum vessel cover

## Slide 15: RFD cryomodule (ODU)
Coaxial HOM

## Slide 16: SPS integration

## Slide 17: DQW dressed cavity (BNL)
Tuner + reinforcement
beam
Space for
adjacent beam pipe
HOM
FPC
HOM
Cryo jumper
Piezo + reinforcement
362.4 mm
400 mm
565 mm

## Slide 18: DQW cryomodule (BNL)

## Slide 19: 4-Rod dressed cavity (Daresbury)
Helium Vessel made from Grade 2 Titanium
Helium 2-Phase line
Input coupler port
Modified Saclay II tuner
Stiffening ribs
Additional beam tube required for LHC installation
UK 4 Rod Cavity
Port for He level probe
194mm
550mm
312mm
Cryoperm (magnetic shield)
Slides from Tom Jones and Shrikant Pattalwar (Daresbury)

## Slide 20
2150mm
800mm
1520mm
Cryomodule Concept
More details in - Conceptual design of a Cryomodule for Crab Cavities for HiLumi-LHC
S. Pattalwar, et al, MOP 087, SRF 2013, Paris
Design Approach
Provide sufficient and easy access to internal components during assembly and after installation
December 2012
August 2013

## Slide 21: Dress Cavity and Cryomodule Status
Final designs for the RF dipole, DQW, and 4-rod cavities are nearly complete at ODU, BNL, and Daresbury respectively.
Dressed cavity helium vessels, tuners, HOM interfaces, etc. are in process at ODU, BNL, Daresbury, CERN, and Fermilab.
The initial release of data from the US labs to Niowave took place in February.
The goal for release of the final design models is June 2014.
Solid model and drawing data is being managed through CERN’s EDMS.
Workflows consisting of inspection criteria, milestones, hold points, etc. are being developed at BNL and ODU in collaboration with Niowave.
A draft technical specs has been released to Niowave from CERN.
CERN will approve all drawings, material and fabrication specs, etc. prior to manufacture.

## Slide 22: Thanks very much
  From Ofelia Capatina:
  “Regardless the outcome of this review, CERN strongly hopes we will continue this fruitful and nice collaboration spirit.”
  and from me too...