## Slide 1: Analysis of Dimensional Tolerances in HQ
F. Borgnolutti (LBNL)
May 7th, 2014
LARP CM22/ HiLumi-LHC Collaboration Meeting

## Slide 2: Outlines
Analysis of the coil turns position uncertainty in HQ: Impact on the field quality.
2) Coil dimension uncertainty & its impact on the field quality of HQ.
3) Conclusion.

## Slide 3: Coil Turns Position Uncertainty in HQ
We analyzed HQ coil 14 Cross-section.
Theoretical model (Roxie, uninsulated cable) superimposed to HQ coil 14:
  “best fit” of the coil model with the photo.
HQ coil14 is a second generation coil (smaller cable). It is therefore representative of HQ02 and HQ03 coils.

## Slide 4: Coil Turns Position Uncertainty in HQ
The coil is not pre-loaded so we do not have azimuthal matching of the coil turns between Roxie and the coil.
  But the photo/Roxie comparison gives us information regarding the radial alignment of the turns

## Slide 5: Coil Turns Position Uncertainty in HQ
Observation (1):
  Turns of the inner layer upper block appear to be less well radially aligned than in other blocks: ± 200 μm
0.2 mm

## Slide 6: Coil Turns Position Uncertainty in HQ
Chart: Stdev. an
| 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10
defect +/- 200 um turns upper block layer 1 | 0.60215 | 0.54439 | 0.33921 | 0.071228 | 0.17794 | 0.1459 | 0.091566 | 0.065623
Chart: Stdev. an
| 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10
defect +/- 200 um turns upper block layer 1 | 0.60215 | 0.54439 | 0.33921 | 0.071228 | 0.17794 | 0.1459 | 0.091566 | 0.065623
Chart: Stdev. bn
| 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10
defect +/- 200 um turns upper block layer 1 | 0.57448 | 0.34949 | 0.35744 | 0.34243 | 0.18817 | 0.092593 | 0.08279 | 0.047366
Monte-Carlo simulation:
  Inner layer upper block turns are radially displaced. The amplitude of the displacement is randomly picked in the range [-200 um; +200 um]
  500 quadrupoles
  Rref = 40 mm
Magnified random displacement of the coil turns

## Slide 7: Coil Turns Position Uncertainty in HQ
Observation (2):
  Radial position of other turns is about ± 100 µm.

## Slide 8: Coil Turns Position Uncertainty in HQ
Magnified random displacement of the coil turns
Chart: Stdev. an
| 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10
defect +/- 200 um turns upper block layer 1 | 0.60215 | 0.54439 | 0.33921 | 0.071228 | 0.17794 | 0.1459 | 0.091566 | 0.065623
defect +/- 100 um other turns | 0.52963 | 0.42235 | 0.27984 | 0.23823 | 0.14384 | 0.10072 | 0.068604 | 0.045711
Chart: Stdev. bn
| 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10
defect +/- 200 um turns upper block layer 1 | 0.57448 | 0.34949 | 0.35744 | 0.34243 | 0.18817 | 0.092593 | 0.08279 | 0.047366
 | 0.48155 | 0.33759 | 0.28536 | 0.18657 | 0.13036 | 0.09649 | 0.069528 | 0.053105
Chart: Stdev. an
| 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10
radial defect +/- 200 um turns upper block layer 1 | 0.60215 | 0.54439 | 0.33921 | 0.071228 | 0.17794 | 0.1459 | 0.091566 | 0.065623
radial defect +/- 100 um other turns | 0.48155 | 0.33759 | 0.28536 | 0.18657 | 0.13036 | 0.09649 | 0.069528 | 0.053105
Monte-Carlo simulation:
  Turns are radially displaced. The amplitude of the displacement is randomly picked in the range [-100 um; +100 um]
  500 quadrupoles
  Rref = 40 mm

## Slide 9: Coil Turns Position Uncertainty in HQ
Observation (2):
  The turn after the inner layer wedge appears to be radially offset by -300 μm.
0.3 mm
0.3 mm
If systematic error  Δb6 = +0.76, Δb10 = +0.21
Not negligible systematic field error.
Look at this particular turn in QXF.

## Slide 10: Outlines
Analysis of the coil turns position uncertainty in HQ: Impact on the field quality
2) Coil dimension uncertainty & its impact on the field quality of HQ
3) Conclusion

## Slide 11: Coil dimension uncertainty in HQ
Azimuthal Coil size measurements show coil to coil reproducibility better than ±100μm (±50 μm per side)
Chart: Stdev. an
| 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10
radial defect +/- 200 um turns upper block layer 1 | 0.60215 | 0.54439 | 0.33921 | 0.071228 | 0.17794 | 0.1459 | 0.091566 | 0.065623
 | 0.52963 | 0.42235 | 0.27984 | 0.23823 | 0.14384 | 0.10072 | 0.068604 | 0.045711
 | 1.1335 | 1.0236 | 0.40389 | 0.31143 | 0.10592 | 0.072491 | 0.023192 | 0.015269
Chart: Stdev. bn
| 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10
radial defect +/- 200 um turns upper block layer 1 | 0.57448 | 0.34949 | 0.35744 | 0.34243 | 0.18817 | 0.092593 | 0.08279 | 0.047366
 | 0.48155 | 0.33759 | 0.28536 | 0.18657 | 0.13036 | 0.09649 | 0.069528 | 0.053105
 | 1.1519 | 0.00059526 | 0.41048 | 0.00034354 | 0.10763 | 0.00015279 | 0.023574 | 5.5345e-05
Chart: Stdev. an
| 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10
radial defect +/- 200 um turns upper block layer 1 | 0.60215 | 0.54439 | 0.33921 | 0.071228 | 0.17794 | 0.1459 | 0.091566 | 0.065623
radial defect +/- 100 um other turns | 0.48155 | 0.33759 | 0.28536 | 0.18657 | 0.13036 | 0.09649 | 0.069528 | 0.053105
mid-plane position +/- 50 um | 1.188 | 0.0025907 | 0.49361 | 0.30988 | 0.062903 | 0.00034429 | 0.014599 | 0.014967
Monte-Carlo simulation:
  Each mid-plane is displaced by an amplitude randomly picked in the range [-50 µm; + 50 µm]
  500 quadrupoles
  Rref = 40 mm
An uncertainty on the coil azimuthal dimension also translate to an uncertainty on the magnet aperture (ΔR = ± 30 µm)  negligible impact (0.03 unit on b6)

## Slide 12: Coil dimension uncertainty in HQ
Azimuthal position of the pole piece specified ± 20 µm.
It is in HQ02 ±100 um (due to undersized pins)
Pole pieces
Chart: Stdev. an
| 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10
radial defect +/- 200 um turns upper block layer 1 | 0.60215 | 0.54439 | 0.33921 | 0.071228 | 0.17794 | 0.1459 | 0.091566 | 0.065623
 | 0.52963 | 0.42235 | 0.27984 | 0.23823 | 0.14384 | 0.10072 | 0.068604 | 0.045711
 | 1.1335 | 1.0236 | 0.40389 | 0.31143 | 0.10592 | 0.072491 | 0.023192 | 0.015269
Pole piece azimuthal position +/- 100 um | 1.188 | 0.0025907 | 0.49361 | 0.30988 | 0.062903 | 0.00034429 | 0.014599 | 0.014967
Chart: Stdev. bn
| 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10
radial defect +/- 200 um turns upper block layer 1 | 0.57448 | 0.34949 | 0.35744 | 0.34243 | 0.18817 | 0.092593 | 0.08279 | 0.047366
 | 0.48155 | 0.33759 | 0.28536 | 0.18657 | 0.13036 | 0.09649 | 0.069528 | 0.053105
 | 1.1519 | 0.00059526 | 0.41048 | 0.00034354 | 0.10763 | 0.00015279 | 0.023574 | 5.5345e-05
 | 1.1749 | 1.2587 | 0.48823 | 0.0014599 | 0.062195 | 0.00052202 | 0.014436 | 1.0165e-05
Chart: Stdev. an
| 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10
radial defect +/- 200 um turns upper block layer 1 | 0.60215 | 0.54439 | 0.33921 | 0.071228 | 0.17794 | 0.1459 | 0.091566 | 0.065623
radial defect +/- 100 um other turns | 0.48155 | 0.33759 | 0.28536 | 0.18657 | 0.13036 | 0.09649 | 0.069528 | 0.053105
mid-plane position +/- 50 um | 1.188 | 0.0025907 | 0.49361 | 0.30988 | 0.062903 | 0.00034429 | 0.014599 | 0.014967
Pole piece azimuthal position +/- 100 um | 1.188 | 0.0025907 | 0.49361 | 0.30988 | 0.062903 | 0.00034429

## Slide 13: Conclusion
We analyzed dimensional uncertainty in the second generation of HQ coil.
Estimated turn radial position uncertainty:
  ±200 µm for the inner layer upper block
  ±100 µm for the other turns
    Impact on the field quality acceptable
Systematic displacement (-0.3 mm) of the inner layer turn which is just before the copper wedge  not negligible effect on b6 but can be accounted for in the coil design.
Mid-plane location known at ±50µm  possible improvement.
The pole piece azimuthal position uncertainty is not negligible (±100 µm). It was due to undersized alignment tooling.  Improvement expected.
This analysis a first step toward characterization and improvement of fabrication tolerances.