## Slide 1: SAD and ASE Development Single Purpose/Few or One Accelerator
R. May
Thomas Jefferson National Accelerator Facility
Work performed under DOE Contract: AC05-06OR23177

## Slide 2: Overview
Recent and Current Jefferson Lab SADs
SAD Structure
Hazard Assessment Methodology
SAD Review Process
ASE
Summary

## Slide 3: Recent and Current SAD
Currently Revision 7 (August 27, 2012)
  Changes from Revision 6 include
    Updated the SAD for 12 GeV operations,
    Provided a more detailed description of accelerator related equipment in Technical Areas
    Extended hazard analysis rigor to Technical Areas
    Consequence evaluation linked to ANSI/ASSE Z590.3 – 2011, Prevention through Design… 01/23/2012.
    Decoupled the ASE from the SAD - helped delineate what was being approved by our Site Office
    Decoupled Shielding Policy; now stand-alone

## Slide 4: Recent and Current SAD, cont’d.
Previous Revision 6 (March 1, 2009)
  Changes from Revision 5 based on 420.2b
  Further revision, 6a (Oct. 1, 2010)
    Clarifications to ASE w/r/t beam power, addition of certain defense-in-depth measures, clarification of terms and units, typo corrections, etc.
  Further Revision 6b (May 1, 2012)
    Lab organizational change
    Update of geographical area to account for new experiment hall construction
    Update to ASE “Beam On” definition clarified

## Slide 5: SAD Structure
Single SAD Document
  Provides a description of the entire facility, including ancillary support facilities, and analysis of associated hazards
  Lists two accelerator (CEBAF and LERF)
  Analysis focuses on accelerator specific hazards (standard industrial hazards)
  Risks are clearly understood and necessary controls identified
Developed in partnership with TJSO
Assisted by Integrated Support Center

## Slide 6: Hazard Assessment Methodology
Assessment focuses on accelerator specific hazards
  hazard unique to accelerator equipment or direct support equipment
  applied to indirect support equipment if it can produce an accelerator specific hazard
Standard industrial hazards identified but detailed hazard analysis and mitigation discussion not in SAD
  are adequately addressed by DOE approved programs related to federal regulations

## Slide 7: Hazard Assessment Methodology, cont’d.
  No standard methodology or industry guidance for quantitative comparison of risk from fundamentally different hazards considered “accelerator specific”
  Typically, a qualitative assignment of risk supported by professional experience is used to bridge such a gap

## Slide 8: Hazard Assessment Methodology, cont’d.
  The consequences (health effects) of credible hazards grouped in Table 4-2 and binned into consequence levels
  The binning is based on the methodology used in FSAD, Rev. 7 which was revised to better align with a recent consensus standard that addresses occupational hazards and risks in process design

## Slide 9: Hazard Assessment Methodology, cont’d.
  The five categories, their estimated range of occurrence probability (per year), and their description provide the basis for qualitative assessment of the likelihood of a hazardous event

## Slide 10: Hazard Assessment Methodology, cont’d.
  Risk matrix in Table 4-4 combines consequence and probability for determination of acceptability of risk

## Slide 11: Hazard Assessment Methodology, cont’d.
Credible hazards evaluated for Risk Rating
“Unacceptable” Risk Rating gets Credited Control
  Credited Passive Engineered Controls
    Permanent Shielding and Labyrinths
  Credited Active Engineered Controls
    PSS Critical Devices
    Access Controls
  Credited Administrative Controls
    Locked Doors and Gates
“Tolerable” Risk Rating still mitigated by Defense-In-Depth Controls

## Slide 12: Hazard Assessment Methodology, cont’d.
Sample from the SAD Summary Table for Mitigated Risk Rating
Maximum Consequence Level of “High” is addressed in the ASE with mitigation as a prerequisite for accelerator operation
Specific events

## Slide 13: SAD Review Process
Each SAD Chapter review by Safety Configuration Management Board (SCMB)
Each SAD Chapter distributed electronically to System/Subject Matter Experts for review and comment
All comments resolved before distribution to Lab management for review and comment
Lab management final signature
On-going and annual review by SCMB
  Documented review and resolution of safety issues
  Determine the need for SAD revision

## Slide 14: ASE
Simple layout and content
  Document description
  Discussion of what constitutes a violation
  List of Credited Controls
Developed in partnership with TJSO and Integrated Support Center
Internally reviewed and approved - same electronic process as SAD
Approved by TJSO
Annually review by SCMB for continued technical accuracy and relevance

## Slide 15: ASE, cont’d.
SCMB administers USI Process
  Structured process for revaluating hazards in light of planned changes against ASE
  Maintains safety configuration management
  Key to identifying and managing emerging issues

## Slide 16: Summary
SAD Credible Hazards under review based on new fault studies conducted on 12 GeV CEBAF
Will be combined with annual and SCMB review on USI to evaluate need for SAD revision
  No anticipated need for ASE revision
Process thorough, systematic, defensible
Meets 420.2C and consistent with DRAFT safety order guidance document