## Slide 1: Consideration of ANSI N13.12 as Pre-approved Authorized Limit
  Andrew Wallo, AU-20
  Office of Environment, Health, Safety and Security
  DOE Accelerator Safety Workshop August 7, 2014

## Slide 2: Summary of Current Standards
DOE O 458.1 - 4.k, Release and Clearance and 4.k.(6), Authorized Limits
Dose constraints for residual radioactive material:
  25 mrem (0.25 mSv) in a year for real property
  1 mrem (0.01 mSv) in a year for personal property
May develop authorized limits based on dose assessment and ALARA or use DOE pre-approved authorized limits.

## Slide 3: Change Being Considered for DOE pre-approve Authorized Limits for Personal Property
Personal Property – including equipment, items and materials (ANSI N13.12-2013)
Real Property-for buildings and structures continue to use DOE Surface Guidelines until newly derived, dose-based, surface criteria

## Slide 4: Background
Changes requested through:
  DOE O 458.1 review/comment
  Several consecutive DOE Work Groups 2008-2013 recommended a change in the surface guidelines
Rationale for considering ANSI N13.12 2013 for personal property
  Dose-based
  National Technology Transfer and Advancement Act of 1995 requirements to use consensus standards where appropriate
  National Defense Authorization Act of 2013 required that DOE make sure that “…the methods for assessing, certifying and overseeing nuclear safety use national and international standards…”
In May 2014 AU-20/HS solicited input on ANSI N13.12-2013 as a possible Pre-Approved Authorized Limit for personal property

## Slide 5: Criteria Characteristics
Criteria | DOE Surface Activity Guidelines | ANSI N13.12-2013
Scope | Personal & real property | Personal property only
 | Surface contamination | Volumetric and surface contamination
Dose constraint (annual) | 1 mrem personal and 25 mrem real | 1 mrem
Flexibility | Limited - Specific surface activity levels and averaging areas | Screening values have specific levels and averaging areas but standard permits alternative levels if supported by ALARA
Screening for Removable | Yes | Not differentiated

## Slide 6: Responses to whether to adopt ANSI N13.12-2013 for personal property ?
28 respondents
70% “yes”; 30% “no” or “other”
Some major issues identified:
  regulatory consistency
  removable criteria and contamination/control
  detectability of radionuclides
  volume to surface activity conversion

## Slide 7: Next Steps
Continue implementing DOE O 458.1
Assess comments – additional dialogue with Field and Program elements
Evaluate impacts of different personal property and structure surface activity limits and possibility of developing a single set of guidelines
Does not impact efforts currently underway or planned.

## Slide 8
THANK YOU!
QUESTIONS ?