## Slide 1: Panel Discussion Mission Transition and Sustainability Sulfur Hexafluoride Use, Current and Planned
R. May
Thomas Jefferson National Accelerator Facility
Work performed under DOE Contract: AC05-06OR23177

## Slide 2: Overview
Questions Regarding Accelerator SF6 use
Laboratory Responses
Summary

## Slide 3: Questions
I asked three questions across the lab complex through the EHS Managers Forum
  If you currently use SF6 to support accelerator operations, how much do you have on-hand
  Do you recover your SF6 after maintenance
  Do you have plans to build an accelerator or accelerator test equipment requiring additional SF6
I have the following information from six laboratories that have accelerators

## Slide 4: Argonne-1
Argonne has a number of accelerators that use SF6 - ATLAS, Wakefield, and the Ion Implantation Accelerators use the largest amount.
  ATLAS has 4 tons of SF6,
  the other two accelerators use a couple of hundred pounds each.
  Along with other smaller users including other accelerators and electron microscopes that would probably account for another 200 lb.
Total of about 9,000 lb. Probably another 2,000 lbs. in cylinders

## Slide 5: Argonne-2
All three accelerators have recovery systems when maintenance is performed to minimize emissions.
There is also a small portable recovery system for use on small recovery jobs (e.g., Van de Graaff generators, electron microscopes).
With the permanent shutdown of ATLAS, there is a project underway next month to have a contractor recover the 4 tons of SF6 for reclamation and resale.
No near-term plans to build any new systems using SF6.

## Slide 6: FERMILAB-1
Fermilab uses SF6 in some systems that support accelerator operations and in some of our R&D facilities
Currently inventory: approx. 1600 lbs. of SF6 on site. The majority of which is in cylinders. I would estimate we have ~200 lbs. in systems and 1400 lbs. in cylinders
In general there is a staged cylinder at each area where SF6 is used. The amount used in each system is generally very low
Most systems use between 2.5 to 12 lbs. each

## Slide 7: FERMILAB-2
Use an SF6 recovery when we need to perform maintenance on systems containing SF6. The recovery unit pumps the used SF6 into a cylinder.
When recovery unit cylinder is full, it is shipped to a vendor for recycling. After maintenance, the systems are filled from existing on hand inventory.
Expect to continue to use SF6 in small quantities in future accelerator components. Most SF6 use is within high power RF waveguide components and high voltage pulsed kicker power supplies.

## Slide 8: Thomas Jefferson-1
Jefferson Lab uses SF6 in the Low Energy Recovery Facility – LERF (formerly Free Electron Laser) photoemission gun and test stand (GTS)
Currently inventory is approx. 350 lbs.
  Approx. 100 lbs. in LERF, 50 lbs. in GTS
  Approx. 200 lbs. in storage
Systems use a recovery process
  We own equipment to purify gas because of air contamination after multiple transfers
Plans include an accelerator test stand, currently not funded, will use approximately 20 lbs. SF6

## Slide 9: Lawrence Berkeley-1
One accelerator in use. It contains approximately 125 pounds of SF6 and has a recycling unit used to capture the SF6 for maintenance (about every 2 years)
Approximately 10-30 pounds of SF6 is usually lost when recycling (amount needed to purge lines and make pipe connections)
We previously had two other accelerators decommissioned years ago; no plans for future use

## Slide 10: Lawrence Livermore-1
PLS operates a number of accelerators:
  MeV Van de Graaf accelerator system at the Center for Accelerator Mass Spectrometry (CAMS) accelerator which uses approximately 13,000 lbs. of SF6
  The system is designed to pump down the accelerator tank into an external holding tank during maintenance
  Recently the program purchased an off-the-shelf recovery system that can retrieve residual gas from the accelerator and pipe transfer system. While there is still some loss, it has been greatly minimized

## Slide 11: Lawrence Livermore-2
  In addition to the main system, there are two smaller accelerators (known as the 1.7 and 1.0 MeV accelerators) each of which holds approximately 300 lbs.
  The same gas transfer system and recovery cart can be used to pump out and hold the SF6 during the infrequent maintenance operations
  PLS also runs the 4 MeV accelerator in a different facility which uses approx. 1,000 lbs of gas
  Like the CAMS accelerator(s), there is an existing transfer system in place that can hold the SF6 while the accelerator is opened during maintenance

## Slide 12: Lawrence Livermore-3
There is another accelerator system that is currently in standby mode. Some SF6 is contained within waveguide connected to accelerator (40 feet below grade) and above grade RF power supply
Approximately 150-200 lbs. of gas. in waveguide runs
  Not accessed during maintenance activities
Tentative plans in same facility, to bring back online a Pelletron system
  May call for an additional 500 lbs.
  Holding tanks, transfer systems already on hand

## Slide 13: Pacific Northwest National Lab-1
PNNL’s EMSL accelerator system uses approx. 4000 lbs. of (SF6 or Freon) in IBMAL (PNNL EMSL accelerator)
When required by maintenance it is pumped to recovery tanks
Although accelerator systems are tested occasionally, no plans for additional installation of accelerators requiring SF6

## Slide 14: SLAC
Current amount of SF6 in use and storage is 1,450 pounds
SF6 is recovered during maintenance and reused
Will be constructing a new electron gun for the linear accelerator that requires SF6

## Slide 15: Summary of Respondents
Laboratory | Approximate Inventory | Reuse, Recycling | Near-term Future Use
Argonne | 11,000 lb. (Approx. 2,000 lbs. in cylinders) | Yes | No
FERMILAB | 1600 lbs. (Approx. 200 lbs. in systems and 1400 lbs. in cylinders) | Yes | Same
Thomas Jefferson | 350 lbs. (Approx. 150 lbs. In systems and 200 lbs. in cylinders) | Yes | Tentative
Lawrence Berkeley | 125 lbs. | Yes | No
Lawrence Livermore | 20,000 lbs. (14,000 lbs. in use. Approx. 6,000 lbs. in cylinders) | Yes | Tentative
Pacific Northwest | 4000 lbs. of (SF6 and Freon total) | Yes | No
SLAC | 1450 lbs. in use for the accelerator and in storage total | Yes | Yes