## Slide 1: Operational Experience Panel Discussion Interlocks, Access Controls, and Configuration Management
John E. Anderson Jr.
2014 Accelerator Safety Workshop
6 August 2014

## Slide 2: Overview
Program and Requirements
Systems in Use
Configuration Management
Cyber Security

## Slide 3: Program
Radiation Safety Interlock System (RSIS) Requirements flow down through the Fermilab Radiological Control Manual (FRCM) Chapter 10 Radiation Safety Interlock Systems
  Defines Scope
  Authorities and Responsibilities
  Hardware Requirements
    Failsafe, Redundancy, Diversity
  Required Procedures
    Key Accountability, Search and Secure, Maintenance, Repair, Certification Testing, Interlock Bypass

## Slide 4: Systems
Radiation Safety Interlocks and Access Controls are an integrated system
Systems cover ~7 miles of beamline enclosures
  86 Access points, 65 Emergency exits, and 56 Enclosure to Enclosure boundary gates
40+ year laboratory history, wide variety of technologies deployed
  Relay logic systems
  Solid State, EPLD and CPLD logic
  Microcontrollers
  Safety Certified Programmable Logic Controllers (PLC)
    PLC systems used to perform safety functions within the overall RSIS

## Slide 5: Systems
Systems designed in a building block model
  From system specification, can pick and choose different modules to assemble and integrate a system
Same system components are used for Laser safety systems
  Provides a consistent look and feel for users

## Slide 6: Configuration Control
Interlock Change request form
  Change requests stored in a database
  Usually initiated by the RSO
  Reviewed by the Interlock Engineer
  Approved by Accelerator Division (AD) ESH Department Head
    Form has an entry for items requiring independent review and approval
    Changes reviewed for possible USID

## Slide 7: Hardware
Enclosure entry doors are locked
Keys for entry obtained through the Main Control Room
Interlock hardware is secured inside locked cabinets
Chassis based modules are clearly labeled as safety system components
Only personnel authorized in writing by the AD Head have access to keys
System drawings maintained by the Electrical/Electronic Drafting Department

## Slide 8: Interlock System Software
Software configuration management
  Source code maintained on server accessible to interlock group personnel only
    PLC, Microcontroller, EPLD, and CPLD Code
  Microcontroller, EPLD, and CPLD Code verified through initial build bench testing
  PLC program signature is verified as part of the semiannual certification testing
  PLC firmware is verified against vendor firmware release prior to beginning certification testing
  PLC programming software is on a subscription
    Vendor sends notification of programming software updates

## Slide 9: Cyber Security
PLC systems use UDP broadcast to transmit internal status information to data acquisition and display computer
PLCs behind the accelerator control system firewall
  Requires two tier authentication to get behind firewall
PLC network does not allow incoming traffic
  Incoming traffic is stopped at the router
Single laptop used for firmware updates and program download