## Slide 1: Configuration Management
Ian Evans

## Slide 2: Configuration Management
  Requirements Developed
    PPS, BCS, Lasers etc.
  Hardware Installed
  Systems
    De-bugged
    Tested
    Certified per procedure
  All science wants is a system that’s functional and will meet science needs.

## Slide 3: Configuration Management
  PPS – Personnel Protection System
    Prevents personnel from entering areas where the possibility of a radiation hazard exists
      Elements such as hutch door interlocks, key enforced searches, beam stoppers
  BCS - Beam Containment Systems
    Prevents beam from deviating from the design channel into spaces occupied by personnel
      Water cooled apertures, water filled beam dumps, vacuum sensors etc.
  Configuration Management
    Also applies to shielding, search barriers, other systems deemed critical – laser components and interlocks etc.

## Slide 4: Configuration Management
Access Control
System (PPS)
Radiation Control
System
Beam Containment
System
(BCS)
Shielding
Radiation Safety System
Burn
Through
Monitors
(BTM)
Beam Shut- Off Ion Chambers
(BSOIC)
ACM, PIC, LIONS

## Slide 5: Configuration Management

## Slide 6: Configuration Management

## Slide 7: Configuration Management
  Beamline Authorizations (BLA’s) define the critical items that need to be in place to operate safely.
    Controls determined via ESH Staff, Radiation Protection Group & Instrument Staff
      Components
        Stoppers, Apertures, Slits, Collimators
      Systems
        PPS, BCS, Vacuum
      Shielding
        Bulk, Local
  Defines Operational Modes
  Checklists for visible items
  Checklists for non-visible items, in vacuum components, metrology, hard stop limits.

## Slide 8: Configuration Management
  Training
    Staff
      Responsibilities – what am I responsible for
      Awareness – who own what systems
      Communication – who do I call if I need help
      Configuration Control – what it means and why its there
      Labeling, Locks, Hardware - Checklists
      Walk through of items with all involved
    Users
      Hutch Orientation – hands on/hands off, who to call if it doesn’t work.
      Perform a Search, key aspects of the PPS system

## Slide 9: Configuration Management
  Controlling established configurations
    Radiation Safety Work Control Forms (RSWCF’s)
      Manages state of critical elements
      Defines work to be performed
      Identifies Hazards
      Defines Requirements (Hazard Controls & Alternative Mitigations) that need to be in place before work can start.
      Defines Requirements (tests, validations, inspections, sign-offs) that need to be in performed once work is complete.

## Slide 10: Configuration Management
  Lessons Learned (the hard way)
    LCLS Hutch 3 laser class IV ops tied to radiation stopper
    LCLS Hutch 5 laser shutter mechanical failure
    Drilling through lead shielding
    Executing work before RSWCF controls have been fully established
    System are different
      PPS fixed/rigid systems
      LSS (lasers) by nature need to be more flexible
  From a safety perspective we want systems (shielding placement, PPS, interlocks etc…) to work as planned and when needed, so managing their configuration is important.