## Slide 1: Backgrounds and detectors for Compton polarimetry
February 4th 2020
Alexandre Camsonne
Hall A Jefferson Laboratory

## Slide 2: Outline
eRHIC
Compton polarimetry
Compton electron detector JLEIC
Counting rates
Diamond and fast amplifier for electron detector
Photon detection
To do list
Conclusion

## Slide 3: Electron Ion Collider designs
Lower luminosity
560 MHz RF
330 bunches
33 ns between bunches
Electron current up to 1.2A
Ion current up to 0.46 A
High luminosity
560 MHz RF
1320 bunches
10 ns between bunches
Electron current up to 2.4 A
Ion current up to 0.92 A
High luminosity polarized electrons on polarized and unpolarized ions
For electron beam asymmetry measurements polarization can be the dominating error.
Aiming for 1% or better electron polarization accuracy
3

## Slide 4: Main Parameters eRHIC ring-ring for Maximum Luminosity
Ep = 275 GeV, Ee= 10 GeV
New eRHIC ring ring design : beam interaction frequency going from initial RHIC 10 MHz to 30 MHz with 330 bunches and 100 MHz with 1320 bunches in a 3.8 km ring
4

## Slide 5: Polarized Compton effect
The polarization of the beam can be measured using the Compton effect.
Polarization of the photons
(measurable)
Asymmetry computed using QED
Measured asymmetry

## Slide 6
Polarized Compton process
Longitudinal polarization asymmetry
Transverse polarization Compton asymmetry

## Slide 7: Polarized Compton process
The hit distributions are used to measure .
LASER ON
LASER OFF
Precision Electron-Beam Polarimetry using Compton Scattering at 1 GeV
ZERO CROSSING
COMPTON EDGE
(Hall C at Jefferson Lab)

## Slide 8: Compton chicane
gc
Laser + Fabry Perot cavity
e- beam from IP
Photon tagger
Compton electron
tracking detector
Compton photon
calorimeter
Photons from IP
e- beam to spin rotator
Luminosity monitor
The electrons that interact lose part of their momentum, therefore they are deflected more by dipolar magnets.

## Slide 9: JLab Hall C Compton Electron detector
Silicon or diamond strip detectors
About 200 to 250 strips 250 mm width
5 cm length to catch zero crossing and Compton edge
A solid state detector directly in the primary vacuum can approach the beam using a movable support.
Present system used at JLAB Hall C :
electronics connected with flat cables
Bad for SNR and speed!

## Slide 10: Challenges at EIC
Large beam current ( 2.4 A vs 200 uA at JLab )
  Wakefield power deposit by beam can be significant
  Synchrotron radiation ( more severe than JLab )
  Background
    Bremstrahlung
    Halo
  Detector radiation hardness

## Slide 11: Proposed EIC Compton electron detector
Use Roman Pot for electron side too
Pros :
  Access to detector without breaking main vacuum
  Electronics can be closer to electronics ( no flex cables )
  Cooling of detector easier
Con :
  Additional material in front of detector
TOTEM Roman Pot

## Slide 12: Synchrotron radiation
gc
e- beam from IP
Low-Q2 tagger for low-energy electrons
Compton electron
tracking detector
Compton photon
calorimeter
Compton- and low-Q2 electrons are kinematically separated!
Photons from IP
e- beam to spin rotator
Luminosity monitor
gc
Compton electron
tracking detector
e- beam to spin rotator
Electron detector not in direct view of synchrotron fan
Can see still see synchrotron X-rays bouncing on the beam pipe
Can add structure and
coating to reduce rate
Beam pipe wall

## Slide 13: Ante-chamber method
151 cm
Study by Mike Sullivan (PEPII)
Surface power density on the photon stop is 62 W/cm
Eliminate single bounce photons

## Slide 14
Software / simulation
Stand alone Compton event generator ( currently generates LUND files )
GEMC geometry
Analysis script for polarization extraction

## Slide 15: Halo background
Halo modeled by a double Gaussian distribution using beam size from PEPII
Halo rates for 1 cm (blue) and 2 cm aperture ( salmon )
Can be used to reevaluate when more realistic halo available

## Slide 16: Compton Electron Rates from IP
Use Pythia event generator
Transport to Compton Detector
Preliminary rate is negligible compared to other backgrounds

## Slide 17: Compton Electron Det. Rates
10 W
1 A of beam
Green laser
Compton and Bremstrahlung
assuming 10-9 Torr
Corresponding radiation dose for signal and background
( typical silicon SNR divided by 2 after 1 Mrad
No change for diamond after 2 Mrad from Qweak )
Halo 1 cm aperture
Halo 2 cm aperture
Bremstrahlung
Joshua Hoskins

## Slide 18: Compton asymmetry with window
Higher statistics MC comparison
No window
500 mm window

## Slide 19: Compton asymmetry with window
Extracted polarization with and without window
Number consistent at 1% level
Need to study systematics with high statistics to evaluate best accuracy possible

## Slide 20: Wakefield study
119 MHz
476 MHz
Around 2160 W at 3A at low and medium energy
And 540 W at 0.75 A for high energy
Doable and will be reduced after optimization
Impedance after 10 days of computation

## Slide 21: Compton counting rates
JLEIC
Only considering Compton cross-section: no background
Total average polarization in 27 ms
1320 or 330 bunches both options ok unless high background

## Slide 22: Electronics for very fast detectors
A two channels board was designed and manufactured for the characterization of different solid state detectors.
Sensors up to 16x13 mm2 can be glued and bonded.
The components can be easily adapted to accommodate:
Diamond sensors: ~1 nA bias current, both polarities, small signal
Silicon sensors: ~100 nA bias current, small signal
UFSD ~100 nA bias current, ~ larger signal
SiPM: ~ 5 uA bias current, large signal
The board was optimized to achieve a good time precision with different sensors, however it can be modified to have an output signal shorter (but less precise)
3x3 mm2 UFSD
MIP beam test @ Fermilab
~40 ps measured time precision
Test of Ultra Fast Silicon Detectors for Picosecond Time Measurements with a New Multipurpose Read-Out Board
TOTEM electronics designed by Kansas University

## Slide 23: Silicon pulsed with laser at 10 MHz
12 ns
100 ns
Amplifier with silicon detector fast enough to separate successive sources for eRHIC Linac Ring at 10 MHz
(New proposal for up to 476 MHz )

## Slide 24: Fast detector R&D
Diamond sensors are among the fastest available
Electrons
Holes
Total
500 μm scCVD diamond @ 800V
Electrons
Holes
Total
80 μm scCVD diamond @ 500V
The collection time depends on the thickness d
NOTE: the collected charge also depends on the thickness d
However, the deep current mainly depends on the carriers’ velocities, i.e. electric field
Charge collection time too long!

## Slide 25
Ultra Fast Silicon Detectors: as fast as diamond, but with a gain layer!
UFSD: 50 μm LGAD
Fast collection time (50 μm thick) and larger signals, thanks to the gain layer
Electrons (Multiplied)
Holes (Multiplied)
Total
Gain layer
Fast detector R&D

## Slide 26: Electronics for very fast detectors
This board was also used to test the performance of a diamond sensor using a Sr90 β- source.
8.55 ns
500 μm pcCVD diamond

## Slide 27
Chart: t (ns)
Chart: t (ns)
Simulated results:
80 μm scCVD diamond sensor
UFSD
NOISE: ~2 mV RMS
NOISE: ~1.5 mV RMS
Chart: t (ns)
Chart: t (ns)
SNR ~ 5
SNR ~ 25
Fast detector R&D
Study by Nicola Minafra

## Slide 28: Photon detector
Same can be done with photon detector
Pro:
  Redundant measurement with electron detector
  Can measure transverse polarization
Con:
  More sensitive to synchrotron background

## Slide 29: Photon detection
Pair spectrometer
Converter
Segmented calorimeter
  PbWO4, PbF2
  Shashlyk
  (scinitillator or quartz fibers )
  Particle flow (?)
Trackers : GEM or MAPS

## Slide 30: Sensors
Radiation hard
Faster than 10 ns ( diamond / maps / Cerenkov + MCP PMT , thin gap GEMs )
Radiation hard where photon flux is high

## Slide 31: HERA TPOL

## Slide 32: HERA transverse polarimeter

## Slide 33: EIC R&D eRD12
Study for eRHIC
Found adequate location
2 minutes measurement
More refined study to come ( background )

## Slide 34: To do list
Location polarimeters
Include in eRHIC simulation
Look background : Brehmstrahlung
Background from halo
Beam induced background
Synchrotron
Wakefield
Effect of bunch replacement on electron detector

## Slide 35: Conclusion
Pretty extensive study for JLEIC, electron detector seemed feasible, should work for eRHIC, need location after a magnet
Event generator can be reused
Detector need to be implemented in eRHIC
Redo background studies : bremsstrahlung, synchrotron, halo, beam induced
Wakefield
Need to look more at photon side
R&D for fast detectors for photon side